## Slide 1: SVD DAQ
25 Jan 2011 Belle2 DAQ meeting @Beijing
T. Tsuboyama (KEK)

## Slide 2: Outline
Outline
FADC
FTB and Timing distribution
Schedule
This talk is based on slides shown in Krakow meeting in Dec. 2010 and B2GM in Nov. 2010, especially by M. Friedl and W. Ostrowicz.

## Slide 3: System Overview
The SVDDAQ consists of Frontend, Junction box, FADC, FTB. The timing and trigger control, nor the link to PXD, is not shown in this slide.
1902
APV25
chips
Front-end hybrids
Rad-hard
voltage
regulators
Analog level translation,
data sparsification and
hit time reconstruction
Unified Belle II
DAQ system
~2m
copper
cable
Junction
box
~10m
Thicker
copper
cable
FADC+PROC
C
O
P
P
E
R
Unified optical
data link (>20m)
Finesse Transmitter Board (FTB)

## Slide 4: Front end --- APV25
The APV25 chips are designed for CMS at LHC
  Intrinsically radiation hard, short-shaping and pipe-lined.
  Suitable for Belle2 SVD.
The analog information can be used for wave form fit and hit time reconstruction for further background reduction.

## Slide 5: More on APV25
APV25 has a 192-cell pipe line in each channel.
32 bit queue for readout.
In order to accommodate the 5 msec trigger latency, APV25 will be operated with 32 MH clock sacrifying 20% slower readout time.
Dead time at front end.
  With a trigger rush, the readout queue may be filled up. Then further triggers can not be treated correctly, which causes dead time. We should send “busy” to CDAQ in a such case.
  For the recognition of “queue full” in APV25, an APV25 queue emulator will be implemented in the FADC timing controller.

## Slide 6: The Belle detector upgrade

## Slide 7: Junction Box
Just connectors and rad-hard voltage regulators (possibly with remote sensing to hybrids)
APV25 --- Operation voltage 2.5V
Absolute maximum voltage 2.7V
Only 20 / 50 pins of hybrid cable are signals  merge 2 front-end cables into one (same) signal cable to FADC
PXD may need a similar box.
Junction box
?

## Slide 8: FADC
We proved that APV25 can drive 100 W twisted line for > 10 m.
  Repeaters are not necessary.
Analog Signal receivers can be very simple.
24 channels/board. (80 boards necessary.)
Integrating repeater (level translation) into FADC boards
24 inputs per board (6 x 4 or 4 x 6 APVs x hybrids)  80+ VME boards in total
Needs to become more compact to fit onto a single board

## Slide 9: FADC Scheme: Baseline
Level Translation at front-end interface
Majority of board operates at ground (earth) levels
Follows existing scheme

## Slide 10: FADC Scheme: Alternative
Level Translation at module rear
Generally I do not consider this scheme very practical
Probably the only kind of advantage is that all translations become digital

## Slide 11: Existing REBO
Optocouplers (slow controls)
  REBO3 uses single optocouplers for digital slow controls
Amplifiers (signals & CLK/TRG)
  REBO3 uses two amplifiers per channel, one on each HV and LV sides
Voltage Level Translation

## Slide 12: Level Translation – Digital
Existing REBO3
  HCPL0701 (1 optocoupler per SO8 package)
  used for digital slow controls (I2C and reset)
Alternative 1
  HCPL0731 has 2 couplers in the same package
Alternative 2
  Use digital isolators such as ADuM1411
  4 couplers in SO16 package (~2 x SO8)
  Faster versions would even allow translation of CLK and TRG
  Need to evaluate noise performance and operation frequency.

## Slide 13: Level Translation – Analog
Existing REBO3
  first amp is actually attenuator and thus unnecessary
Future circuit
  AD8132 to be replaced by simple resistor (or divider)
  EL5173 could be replaced by EL5373 (3 channels), but ~3x bigger

## Slide 14: ADC Input
SVD DAQ Toru Tsuboyama (KEK)
Existing FADC
  AD8128 equalizer to compensate frequency-dependent cable loss
  EL5173 to convert AD8128 output back to differential
  Even more amplifiers on ADC daughter board
  Parallel ADC data output

## Slide 15: FADC Improvements
No need to drive CAT7 cable anymore  reduce overall number of amplifiers in readout chain
Frequency response in the cable will be corrected by a digital FIR filter inside FPGA (feasibility study will be made in soon) in order to retain fully differential signal path.
Dual-ADC (AD9218) with 10 bit parallel outputs  8-channel ADC (AD9212) with serial outputs (has ~same size as the dual ADC)
5 old (but cheap) FPGAs (Altera Stratix 1 – EP1S20)  single powerful FPGA (Altera Stratix 4GX – EP4SGX180KF40C4N
Communication between VME FPGA and other FPGAs was done by parallel busses  serial communication between VME and central FPGA

## Slide 16: Summary
APV25
  Sufficient thinned & non-thinned devices exist
  VDD voltage must be kept ≤ 2.7V
Junction box scheme established
  Connectors and rad-hard voltage regulators
Several improvements suggested for FADC
  Simplification of voltage level translation
  ADC inputs (FIR filter)
  Serial links instead of parallel busses
Location for FADC racks
  On top of yellow rail beams
  Possibly with power supplies

## Slide 17: FTB (Finesse transmitter Board)
1. FTB design:
a. SVD Electronics - general view
b. Two boards - one set
c. Results of meeting with Zhen’an Liu,
Hao Xu and Mikihiko Nakao.
2. Prototype design:
a. Prototype – double functionality
b. Prototype - tests setup

## Slide 18
SVD Electronics - general view
PIXEL
DAQ
Giessen Box
opt
opt
F E E l e c t r o n i c s
TTD
RJ45
RJ45
#1
#81
#80
RJ45
…
RJ45
#2
COPPER#40
opt
FRB
COPPER#2
opt
FRB
COPPER#1
opt
FRB
…
#1
#40
FTB#80
opt
FADC#80
RJ45
RJ45
FTB#2
opt
FADC#2
RJ45
RJ45
FTB#1
opt
FADC#1
RJ45
RJ45
SVD electronics
SVD-CONTROLLER (SVDctlr)
FCRB
RJ45
SVD tracker

## Slide 19
Two boards - one set
HSD Link (k)
k=1..40
From/to TTD (2k-1)
From/to TTD (2k)
To PXD (k)
DATA (2k-1) + (2k)
1. The same PCB
2. The same module
3. The same firmware
DATA (2k-1)
DATA (2k)
DATA (2k) + (2k-1)
FTB#(2k-1)
OpTr
FTB fmw
RJ45
RJ45
Unified core 2
Unified core 1
FPGA
FTB#(2k)
OpTr
FTB fmw
RJ45
RJ45
Unified core 2
Unified core 1
FPGA
From/to FADC (2k-1)
From/to FADC (2k)

## Slide 20
FPGA
CDC readout
FPGA
HSLRB
Line rate=1.5Gbps
CLK_Lk=200MHz,
CLK_FEE=125MHz
CLK_Lk=200MHz,
CLK_CO=42.3MHz
Results of meeting…
1. Belle2Link:
a. Line rate 1,5 Gbps (3 Gbps works)
b. Clock sources (common clock from TTD = 127MHz):
- On-board = 200MHz
- RJ-45 7-8 pair = 127MHz
- FINESSE-C RCK pair = 42MHz
c. Common CLK via RJ45 in case of test without TTD?
There is no ‘busy’ signal via Belle2Link – I prefer to have such signal between FADC and FTB (FTB busy). But …???

## Slide 21
REGISTERS
FTB
FPGA
UNIFIED CORE
COPPER
Belle2Link
Exactly the same protocol & timing for REGS
HSLB
CSB
LRW
LA[6..0]
LD[7..0]
CSB
LRW
LA[6..0]
LD[7..0]
Mandatory Registers implemented on both sides.
It is unique information for every single board (TYPE[15..0], SERIAL#[15..0])
How to keep information after power down? -> nonvolatile memory (EPROM) on FTB.
FADCs do not need user defined registers for parameters loading/reading. It will be used other solution. (Nakao was interested which way…)
Results of meeting…
d. Registers: mandatory and user defined

## Slide 22
Results of meeting…
Future (near???):
- universal firmware? – in plans
- modules for sub-groups for testing? – they plan…
- any NOTE describing rules and requirements – not yet but…

## Slide 23
Results of meeting…
2. TTD link: ACK, TRG, CLK, RSV.
a) ‘ACK signal (1-2 pair) is a serialized response information to the central
timing system’ – is it the same/similar as ‘BUSY’ signal? - similar.
Any description how to manage the ACK signal. – not yet
b) any RESET via TTD link? – yes. As minimum TRGnb = 0, clear Data Fifos,
no reload the firmware.
What does RESET mean for FADC?
c) any firmware? – maybe soon??
d) any NOTE describing rules and requirements – not yet but…
3. JTAG link
e) For firmware loading – one cable per one board? – not decided yet
f) After firmware loading – what with info in mandatory regs? – ext. EPROM

## Slide 24
FTB functionality + tests possibility
FPGA
Spartan6
RJ45
Prototype – double functionality
OpTr
DRIVERS
POWER
OSC
42MHz
160 pin connector
ext POWER
Regs handler
FTB components
+ test components
DRIVERS
Clock distrib
RJ45
RJ45
config

## Slide 25
SVD FINESSE
COPPER in Cracow
Prototype - tests setup
FPGA
Spartan6
RJ45
OpTr
DRIVERS
POWER
OSC
42MHz
160 pin connector
ext POWER
Regs handl
DRIVERS
Clock distrib
RJ45
RJ45
config
FPGA
Spartan6
RJ45
OpTr
DRIVERS
POWER
OSC
42MHz
160 pin connector
ext POWER
Regs handl
DRIVERS
Clock distrib
RJ45
RJ45
config
FTB prototype – FINESSE adapter
SVD FINESSE
42 MHz
Power

## Slide 26: Location for FADCs
At side of KLM
Accessible during running
Or on top of KLM (but then locked)
When I showed this slide at the B2GM, I noticed that Haba-san shook his head…
Approximately here
1 rack on each side (forward, backward) is enough

## Slide 27: Location for FADCs
24 Jan 2011
There is a lot of space on top of the yellow rail beams
No conflict with existing installations so far (probably PXD also think of this space)
Need to build access infrastructure. This is not an obstacle. Although we can not access to this area when accelerator is in operation
We may put FADC racks (1 forward, 1 backward) + power suppplies there

## Slide 28: Schedule