## Slide 1: Elec-TDAQ progress on CEPC Ref-TDR
Wei Wei
On behalf of the Elec-TDAQ system of the CEPC Ref-TDR
2024-02-28

## Slide 2: Outline
Consideration on Elec-TDAQ overall framework
A reference and preliminary consideration of the powering distribution
Wireless communication R&D progress by Jun Hu

## Slide 3: Elec-TDAQ overall framework
To make the Elec-TDAQ system based on a common platform
FEE: customized to sub-det; BEE + Trigger: limited types of common boards;
DAQ: (centralized) data & computing center scaling with data rate or algorithm
Common interface: Powering & Data Link
electronics system

## Slide 4: Elec-TDAQ System Division
X64@10Gb/s
Front-end module
By Jun Hu
Customized
Common Platform

## Slide 5: Ref Framework——CMS Phase-II DAQ
后端电子学(同步低延迟）：
前后端标准协议接口，数据解压，数据对齐
产生触发条件：簇，径迹段，能量等…，触发条件信息的同步发送（所有触发条件都在后端产生）
探测器原始数据及触发条件信息数据读出（DAQ功能）
触发快控制时钟接收及往前端发送，状态信息反馈（快控制）
前端上电控制，阈值等慢控参数配置及读回校验（慢控制）
前端电子学：时钟及快控制信号恢复，ADC，TDC，数据压缩发送
机箱内快控制时钟扇出及数据读出：
为后端电子学提供标准数据读出接口S-Link，
数据汇总及发送，
触发快控制时钟机箱内扇出及后端电子学状态汇总，反馈
TCDS ：
接收L1A，系统状态汇总
触发时钟快控制信息扇出，系统快控制响应
触发系统 ：
接收各探测器触发条件信息
根据物理需求产生L1A并发送给TCDS
By Jingzhou Zhao

## Slide 6: Cost of trigger can be calc. by N-of-boards
By Jingzhou Zhao

## Slide 7: Elec-TDAQ System Framework
Customized FEE
  Including ASIC, common FEE chip, FEE board & power, till serial interface
    Data concentration chips may be needed
  Cost depends on different detector scheme
BEE
  1 common board: a data exchange / storage center between FEE & Trigger
  Cost mainly scaling with FEE data rate
Trigger
  Very few types of common boards: for common functional of trigger
  Cost mainly scaling with detector volume
DAQ
  Cost can be calc. by N-of-cores or N-of-bandwidth
Data Link
  To be designed based on a common communication protocol (lpGBT-like)
Powering
  Common design on power distribution strategy for all sub-det
  Customized based on GaN for DC-DC, non-LDO system

## Slide 8: Diss. On Powering distribution
Commercial Power Supply
CUST DC-DC Power Crate
CUST Pol module + CUST Power Ctrller
480V AC
280V DC
100m
48V/12V DC
20m
1.2V/1.8V DC
FEE Powering
(TBD）
Serial Powering / LDO…?
COTS Power Supply
COTS DC-DC Power
CUST Pol module + CUST Power Ctrller
480V AC
48V/12V DC
40m？
CEPC alt. scheme (TBD)
alt. scheme (TBD)
ATLAS scheme
Detector Hall
Elec room
0 rad
10~100k rad
1M rad

## Slide 9: Backup

## Slide 10: System division
Interposer board
  DC-DC：low power supply provider for front-end
  Data aggregation to high speed link/optical link（lpGBT, VTRX+）
  Chip configuration transmission
  Clock and trigger distribution
FELIX
  Route data between optical link of front-end and the highspeed network of DAQ system
  Connect with TTC and get synced clock, global trigger decision, reset and so on.
  Fanout low speed clock, trigger and reset to front-end
Power supply
  Provide higher voltage to front-end
Clock, trigger, fast control
  Fanout the common information to FELIX
  Sync with FELIX and provide clean clock，
X64@10Gb/s
Front-end module
Back-end
(off detector)
By Jun Hu