## Slide 1: CEPC vertex detector towards TDR
Zhijun Liang,
On behalf of CEPC vertex working group

## Slide 2: Towards TDR
Aim to have a draft of TDR by the end of 2024.
  System level design, choose baseline technology
  Electronics, service and mechanics needs to be included
Major change from CDR to TDR
  Beam pipe diameter: 28mm (CDR)  20mm (TDR) (reduce 30%)
  Instant Luminosity per IP:
    Z pole: 32×1034 cm-2s-1 (CDR)  192 ×1034 cm-2s-1 (TDR, 50MW) (6 times increase)
    ZH: 5.6×1034 cm-2s-1 (CDR)  8.3 ×1034 cm-2s-1 (TDR) (~1.5 times increase)

## Slide 3: Decision on baseline technology
Group Meeting every Thursday afternoon (2nd meeting last Thursday)
  https://indico.ihep.ac.cn/event/21543/
From last meeting, Discussion about the choice of technology
  Discussion with L3 Stitching (Mingyi) and SOI (Yunpeng)
  Agree to focus CMOS pixel for reference TDR baseline

## Slide 4: Hit density
Hit density in TDR design(with safety factor 1.5)
 |  | Bunch spacing (ns) | Hit density From (Hits/cm2/BX) | Data rate per chip @ trigger (Mbps)
TDR | Higgs | 591 | ~0.54 | ~20
 | Z | 23 | 0.45 | ~120
Data rate scaled from Taichu readout scheme

## Slide 5: Key parameters
  Single-point spatial resolution (now and in the next 5 years)
  Time stamp precision requirement (to be discussed with Shengsun Sun)
  Material budget
  Cost estimation
  Occupancy
  Max data rate that can be handled by this technology (now, and in the next 5 years)
  Radiation hardness (now, and in the next 5 years)
  Power dissipation (now, and in the next 5 years)
  Expected Technology availability in the future
  Technology Readiness

## Slide 6: Plan
Got 1st offical background input from MDI group last week
  Need support from software group to interface background into softward framework
  Next step: get background hit density distribution in vertex detector
End of March: Plan to work with electroncs group to finalize the design
  Readout architecture is the key for next step
  Readout speed and buffer size are the major concern
End of March: finalize the detector geometry and mechnical design

## Slide 7: backup