## Slide 1: Scintillator ECAL Digitization update
2024/04/19
Jiaxuan Wang

## Slide 2: Digitization process 1
Physics process:
  Energy deposited in scintillator
  Photon emission :
    Of Poisson distribution
  PDE :
  SiPM saturation :
MC process:
  Input : MC truth hit energy
  Output: photoelectron number
  Process:
    MIP energy : 0.305 MeV
    SiPM gain (ADC/p.e.) and MIP spectrum MPV (ADC/MIP)
    Poisson smear
  Input : photoelectron number
  Output: photoelectron number(after saturation correction)
  Process:
    SiPM type 10um-10000 15um-4489

## Slide 3: Digitization process 2
MC process:
  Input : photoelectron number(after saturation correction)
  Output: calibrated ADC value
  Process:
    SiPM gain (ADC/p.e.)
    Gaussian smear : ADC = p.e. * gain
  Input : calibrated ADC value
  Output: ADC high low gain ADC
  Process:
    Gaussian smear :
      Mean : calibrated ADC / Hl-ratio + pedestal mean
      Sigma : pedestal sigma
    High-low switch point
      High gain saturation: high adc > switch point , let highadc =4000
      Low gain saturation : low adc > 3000, let lowadc = 3000
Physics process:
  Calibrated ADC : p.e. * gain
    Gain error : fit error
    Single photoelectron spectrum Width : statistical error
  ADC converted into high-low gain mode
  ADC saturation

## Slide 4: Layer hitNo
40GeV e-
  Hit: 0.5MIP cut
  Event: >50MeV and >100hits cut
  Dead channel exclusion
Red: data
Blue: MC_truth
Green: MC_digi

## Slide 5: Layer energy deposition
40GeV e-
  Hit: 0.5MIP cut
  Event: >50MeV and >100hits cut
  Dead channel exclusion
Red: data
Blue: MC_truth
Green: MC_digi

## Slide 6: MC settings update
Threshold : 0.5MIP 1.0MIP
Mixed MC mac file setting
  Electron: ~ 3.75*1e5
  Hadron: ~ 9000
  Noise: ~ 40000
pion
electron
noise

## Slide 7: Layer hitNo improvement
40GeV e-
  Hit: 1MIP cut
  Event: >50MeV and >100hits cut
  Dead channel exclusion
Red: data
Blue: MC_truth
Green: MC_digi
Odd layers match better, still difference on even layers

## Slide 8: Summary && Plan
Not too much difference between MC truth and MC digitization
Data has larger deposited energy but less hitNo
Raise of threshold cut would help with hitNo matching, meanwhile odd layers and even layers show different behavior
Digitization needs to be improved
  SiPM gain: Muon data and LED calibration
  Single photoelectron peak width
  Noise model

## Slide 9: BACKUP

## Slide 10: Track Fit - XZ
All hits
First fitting
Third fitting
Second fitting

## Slide 11: Track Fit - YZ
All hits
First fitting
Third fitting
Second fitting

## Slide 12: General comparison
Data with low hitNo but high deposited energy according to energy reconstruction
  0.5MIP cut
  Dead channel cut
  >50MeV and >100hits cut for 40GeV electron data sets
Red: data
Blue: MC_truth
Green: MC_digi
Red: data
Blue: MC_truth
Green: MC_digi

## Slide 13: Layer hitNo
Layer No.16-29

## Slide 14: Layer energy
Layer No.16-29

## Slide 15: HitNo2Energy
Red: data
Green: MC_digi