## Slide 1: Overview of ERL Projects: SRF Issues and Challenges
Matthias Liepe
Cornell University
Overview of ERL projects: SRF issues and challenges

## Slide 2: Outline
Introduction: SRF for ERLs
  What makes it special / challenging?
Challenges for…
  …the cavity
  …the HOM damper
  …the RF power system and control
  …the cryostat and cryoplant
Summary and outlook
Outline

## Slide 3: Introduction: SRF for ERLs What makes it special / challenging?
Introduction: SRF for ERLs

## Slide 4: SRF for Future Particle Accelerators
Cornell ERL
5 GeV, 100 mA, 400 s.c. cavities
XFEL
17.5 GeV, 800 s.c. cavities
Project X (FNAL)
3 GeV, 1 mA
Future: muon collider?
BNL ERL Electron Cooler and eRHIC
50 mA
KEK ERL Light Source
5 GeV, 100 mA
Facility for Rare Isotope Beams (FRIB)
European Spallation Source (ESS)
2.5 GeV,50 mA
International Linear Collider
500 GeV, 16000 s.c. cavities
HZB ERL
100 mA
China Spallation Source (CSNS)
1.6 GeV SRF linac
Accelerator Driven Subcritical Reactor pilot facility
NGLS
Introduction: SRF for ERLs

## Slide 5: Need for Multi-Gev, CW, High Current SRF Linacs
Key technology: Multi-GeV SRF linacs
Only technology that will allow realizing such linacs in the foreseeable future is superconducting radio-frequency
  Operated in continuous wave or long pulse mode
  Accelerating high beam currents of many tens of mA
  Need lower surface resistance to support efficient cw operation (lower cryogenic losses), and better control of unwanted cavity-beam interaction (higher-order cavity modes) to support high beam currents
Introduction: SRF for ERLs

## Slide 6: Example: SRF for the Cornell ERL
ERL main linac: 5 GeV SRF linac, 100 mA with energy recovery, 5 kW RF power per 7-cell cavity
ERL injector: 15 MeV SRF linac, 100 mA without energy recovery, >100 kW RF power per cavity
Introduction: SRF for ERLs

## Slide 7: Cornell ERL SRF Parameters
Parameter | Injector Linac | Main Linac | Note
Total energy gain [GeV] | 15 MeV | 5 GeV | Multi-GeV
Total # cavities | 12 | 384 | ~ CEBAF
CW beam current [mA] | 100 | 2 x 100 | High!
CW Operating gradient [MV/m] | 6 | 16 | Limited by Q0
Cavity intrinsic quality factor Q0 | 11010 | 21010 | Cost driver!!
Total cryogenic load at 1.8K [W] | 60 | 5000 | 5 MW AC power
Cavity loaded quality factor QL | 5104 | >6.5107 | High! (no effective beam loading)
RF field stability | 110-4 / 0.1 deg | 210-4 / 0.1 deg | Very tight!
Significant progress has been made during the last year towards achieving these ambitious goals!
Introduction: SRF for ERLs

## Slide 8: ERL SRF related Challenges
The SRF system for high current ERLs is extremely demanding:
SRF cavities:
  Continues operation at high fields with low cryogenic losses -> high Q0
  Reliable operation with very low trip-rate
  Very low microphonics levels -> optimized mechanical cavity design
  Design optimized for strong HOM damping
Higher-Order-Mode damping:
  Strong HOM damping and efficient HOM power extraction for high beam currents
RF power system and control:
  Low cost, low CW RF power input couplers
  Low cost RF power sources
  Active and fast cavity frequency control
  Very good RF cavity field stabilization at highest loaded Q for energy stability
Cryostat and Refrigeration:
  Cryogenic system for high cryo-loads
  Cryostat design for low mechanical vibrations and vibration damping
  Cryostat design for excellent magnetic shielding (high Q0)
  Very accurate cavity alignment
  Significant progress in these fields is needed for high current ERLs to work!
Introduction: SRF for ERLs

## Slide 9: Challenges for… …the cavity …the HOM damper …the RF power system and control …the cryostat and cryoplant
Challenges for…

## Slide 10: Challenges for…the Cavity (I)
High Q0 at medium (!!) fields
  GeV scale, CW SRF linacs -> MW-scale cryoplants
  Consistent Q0 > 2x1010 highly desirable for cost reasons
    Higher Q0 -> higher cost optimal gradient (2x1010: 15 – 20 MV/m)
    Understanding residual resistance is key! Why does it fluctuate between 1 and > 10 nOhm?
    Medium field Q slope?
    Best surface preparation??
    How to preserve high Q0 in a a cryomodule?
Design optimized for strong HOM damping
  Impacts cell shape, number of cells, frequency…
  Important: Optimized shape must be stable under realistic shape imperfections!
…the cavity
G. Ciovati, et al., IEEE Trans. Appl. Supercond. Vol. 21, No. 3, 2011

## Slide 11: Challenges for…the Cavity (II)
Very low microphonics
  No effective beam loading, so could operate at QL>1x108
  But: High QL needs low microphonics to be effective!!
  -> Mechanical design for low microphonics! (reduce df/dp sensitivity to pressure fluctuation in LHe bath)
Reliable operation with very low trip-rate
  User facilities (especially x-ray) require uninterrupted beam
  Mean time between trip per cavity > months!?
  Trips caused by occasional peak detunings and insufficient RF power
    How frequent? What is the peak detuning over weeks, and how can it be reduced?
…the cavity

## Slide 12: Examples: ERL Cavities
…the cavity
BNL 5-cell, 703 MHz
KEK 9-cell, 1.3 GHz
JLAB 5-cell, 748.5 MHz
Cornell 7-cell, 1.3 GHz

## Slide 13: ERL Cavities: Q0 in Vertical (!) Tests
…the cavity
BCP&120C bake
ERL main linac spec
BNL 5-cell, 703 MHz
KEK 9-cell, 1.3 GHz
JLAB 7-cell, 1.3 GHz
Cornell 7-cell, 1.3 GHz
BCP&120C bake

## Slide 14: RF Optimization of Cornell’s ERL Main Linac Cavity (I)
Dipole mode damping calculated up to 10 GHz with realistic RF absorbers
Worst mode limits beam current!
Franklin Cray XT4
Cell shape optimization:
  ~20 free parameters
  Full Higher-Order Mode characterization (1000’s of eigenmodes)
  Verification of robustness of cavity design
IBBU ~ 1/(worst BBU-parameter)
…the cavity
Notes: optimization used an unconstrained downhill simplex search method.
the simultaneous mini- mization of n-HOMs was treated as the analytic problem of minimizing the worst HOM, under the non-analytic con- straint that each BBU parameter of all other dipole modes in the spectrum be less than the maximal BBU parameter of all the modes ≡ M

## Slide 15: RF Optimization of Cornell’s ERL Main Linac Cavity (II)
Compute BBU current
Generate realistic ERL
(x100)
Compute dipole HOMs to 10 GHz
(1692 modes /cavity)
Introduce realistic shape variations
(400 cavities)
Optimize Cavity
W.R.T. BBU parameter
Optimized cavity with 0.25 mm shape imperfections supports ERL beam currents well above 100 mA!
1mm
0.125mm
0.5mm
0.25mm
…the cavity
Notes: Point out grad student Nick Valles!!!

## Slide 16: Mechanical Design of Cornell ERL Cavity for efficient Cavity Operation
…the cavity
Stiffening rings can vary from ID at iris to OD at equator
Model of Cornell ERL Main Linac Cavity
Small bandwidth cavity vulnerable cavity microphonics (frequency modulation), especially by helium pressure fluctuations
Diameter of cavity stiffening rings used as free parameter to reduce df/dp
ANSYS simulations: large diameter rings and no rings at all have smallest df/dp
No Rings
ID of rings as Fraction of Iris-Equator Distance
No Rings
Cavity optimized!
Notes: Point out grad student Sam Posen

## Slide 17: Cavity: Current Status
Residual resistance and medium field Q0 still mostly a mystery and need much more attention!
  Including performance (degradation) in cryomodules
  -> Test cryomodules at 1.8K!
  -> Cornell Horizontal Test Cryomodule
Several cavities designed specifically for ERLs (BNL, KEK, JLAB, Cornell…), i.e. primarily for high currents. Also some optimization of mechanical design done (Cornell…)
Reliability of long term cavity operation at very high QL needs more study:
  Operate cavities CW for weeks and monitor detuning
    -> International ERL cryomodule to be tested at Daresbury in 2012
…the cavity

## Slide 18: Cornell’s Horizontal Test Cryomodule
TTF, JLAB, Fermilab: see occasional significant degradation of cavity performance once installed in cryomodule. WHY?
Cornell test cryomodule: show that quality factor can be maintained after cavity has been equipped with helium vessel, RF coupler and HOM absorbers
…the cavity
cavity
HOM load
HOM load
HGRP
80K shield
Gate valve

## Slide 19: International ERL Cryomodule
International collaboration:
  ASTeC (STFC), Cornell University, DESY, FZD-Rossendorf, LBNL, Stanford University, TRIUMF
Test staring in 2012
  Focus on long term cavity operation at high loaded Q
…the cavity
Two 1.3 GHz 7 cell cavities (fabrication at test at Cornell)
Cornell-style cold HOM load
Cornell-style input coupler (from ERL injector)
Modified

## Slide 20: Challenges for…the HOM Damper
Strong, broadband HOM damping
  Q’s of < 10,000 typically needed
  2ps bunches excite HOMs to ~100 GHz
Efficient HOM power extraction
  High power handling needed: Few 100 W to >1000 W of HOM power per cavity
  Best temperature to absorb power at?
Antenna, waveguide or beamline load based?
Best RF absorbing material?
  Graphite loaded SiC, Ceralloy, ferrite, CNT loaded ceramic?
Cost
  - 10% to 40% of cavity cost
…the HOM damper

## Slide 21: Beam Current and HOM Damping Requirements
Project | Beam current [mA] | Average HOM power per cavity [W] | Required monopole Q < | Required dipole Q <
CEBAF 12GeV | 0.10 | 0.05 | 1.40E+09 | 1.50E+09
Project X | 1 | 0.06 | 2.00E+07 | 1.00E+09
XFEL | 5 | 1 | 1.00E+05 | 1.00E+05
SPL | 40 | 22 | 1.00E+04 | 1.00E+07
BERLinPro | 100 | 150 | 1.00E+04 | 1.00E+04
KEK-CERL | 100 | 185 | 1.00E+06 | 1.00E+04
Cornell ERL | 100 | 185 | 5.00E+03 | 1.00E+04
eRHIC | 300 | 7,500 | 1.00E+04 | 4.00E+04
High beam current requires high power handling capabilities of HOM damping scheme
Risk of resonant mode excitation and beam stability require strong HOM damping by HOM damping scheme
…the HOM damper

## Slide 22: HOM Dampers
BNL 5-cell: antenna
KEK, Cornell, DESY: Beamline
JLAB 5-cell: waveguides
RF absorber Rings
…the HOM damper

## Slide 23: HOM Damper: Current Status
Lots of activity worldwide
  Antenna HOM couplers
  Waveguide HOM couplers
  Beamline loads
Some good RF absorbing materials are available for operation at room temperature and cryogenic temperatures
  Reproducibility of properties needs to be addressed
Cost remains an issues
…the HOM damper

## Slide 24: Challenges for… the RF Power System and Control
Active and fast cavity frequency control
  Desirable to further reduce microphonics
  Also needed to compensate Lorentz-force detuning during field camp up
  Tuner design / stiffness also impacts microphonics level
Very good RF cavity field stabilization at highest loaded Q
  Very tight field stability needed at very high loaded Q
Low cost, few kW CW input coupler (main linac)
  Currently 30 to 40% of cavity cost!
High CW input coupler (injector)
  Voltage in injector cavities limited by coupler RF power
Reliable, efficient, low cost 5 - 15 kW RF source
  Need low trip and failure rate
  Need lower cost/Watt (<10$/Watt for full system)
…the RF power system and control

## Slide 25: RF Power System and Control: Current Status (I)
Active compensation of Lorentz-force detuning works well
Initial steps taking in active microphonics control, but very challenging and still limited in effectiveness. Note: peak detuning most important!
…the RF power system and control
Reduces rms microphonics by up to 70%!
Lorentz-force detuning and microphonics compensation at the Cornell ERL injector module

## Slide 26: S1 Global Cryomodule: Detuning change during 2 hour operation
quench
He pressure
Shin MICHIZONO (KEK)
…the RF power system and control
Significant differences in df/dp sensitivity! Need more data!

## Slide 27: RF Power System and Control: Current Status (II)
Excellent field stability at very high loaded Q demonstrated:
…the RF power system and control
Tests of Cornell’s novel LLRF system
  At JLAB ERL-FEL, CEBAF, HZ-Berlin horizontal test cryostat
  Demonstrated highly efficient operation at record high loaded quality factors up to 2108
  Exceptional field stability: σA/A <110-4, σ ~ 0.01 deg

## Slide 28: RF Power System and Control: Current Status (III)
Various CW RF input coupler developed for ERLs:
  Also waveguide couplers (JLAB)
But: High cost remains major issue
…the RF power system and control
2K
5K
80K
300K
Coax
-
waveguide
transition
2K
5K
80K
300K
Coax
-
waveguide
transition
RF power
Warm window
80K
5K
bellows
vacuum
Cold window
KEK, >50 kW, 1.3 GHz
Cornell, 50 kW, 1.3 GHz
Cornell, 5 kW, 1.3 GHz
KEK, 20 kW, 1.3 GHz

## Slide 29: RF Power System and Control: Current Status (IV)
Solid state amplifier start to emerge as best choice for a few kW CW RF power source
    Reliable, linear, good efficiency at all power levels
    Cost competitive with IOT, klystron
…the RF power system and control
W. Anders, HZB

## Slide 30: Challenges for… the Cryostat and Cryoplant (I)
Cryogenic system for high CW cryo-loads: Optimization
  Large number of significant dynamic heat loads: cavity, HOM loads, CW input couplers
  Cool in series, parallel? How to ensure uniform cooling?
  Huge difference in cooling power between RF and beam on and standby. Cryoplant must have sufficient flexibility!
  Optimal temperatures:
    Shield temperature? 80K?
    Cavity operating temperature? Large cryoplant stability at 1.6K and below
  Cryoplant contributes >50% to total wall plug power
    Improvements in coefficient of performance desirable
…the cryostat and cryoplant

## Slide 31: Challenges for… the Cryostat and Cryoplant (II)
Cryostat design for low mechanical vibrations and vibration damping
  How do external vibrations get to the cavities?
  What matters, i.e. drives microphonics?
Excellent magnetic shielding
  Excellent magnetic shielding essential for high Q0 in cw operation (B < few mG at cavities)
  How many layers of shield needed?
Accurate cavity alignment (0.5 – 1mm)
…the cryostat and cryoplant

## Slide 32: Cryostat and Cryoplant: Current Status
Experiences with DESY, LHC, JLAB, and SNS cryoplants provide excellent opportunities to learn from
  Need to explore operation below 1.8 K
…the cryostat and cryoplant
80K distribution to heat exchanger
5K distribution to heat exchanger
5K supply
80K supply
Test / prototype modules important to verify module cryogenic manifold sizing and layout

## Slide 33
Excitation Point | Excitation Force | Detectable With Cavity Accelerometer | Detectable On Cavity RF Frequency (>0.1Hz modul.)
Coupler Waveguide | 110 N (25 lbs) | No | No
Coupler | 110 N (25 lbs) | No | No
Cryomodule Saw-Horse Support | 110 N (25 lbs) | Yes | No
Helium Gas Return Pipe Support | 110 N (25 lbs) | Yes | Yes
Beam Line | 10 N (2 lbs) | No | No
Helium Supply/Return | 110 N (25 lbs) | No | No
Ground vibrations and other mechanical vibrations do not strongly couple to the SRF cavities
Main contribution to cavity microphonics comes from fast fluctuations in the He-pressure and the cryogenic system
Mechanical Coupling Characterization Measurements with a Modal Shaker at Cornell Injector Module
…the cryostat and cryoplant

## Slide 34: Cryostat and Cryoplant: Current Status
Sufficient magnetic shielding and cavity alignment has been demonstrated
…the cryostat and cryoplant
ERL Injector Cooldown WPM Horizontal
-1.00
-0.50
0.00
0.50
1.00
4/29/08 0:00
4/30/08 0:00
5/1/08 0:00
5/2/08 0:00
Date-Time
X position [mm]
X1 [mm]
X3 [mm]
X4 [mm]
X5 [mm]
B < 3 mG
Cornell ERL injector cryomodule: Cavity string is aligned to 0.2 mm after cool-down!

## Slide 35: Summary and outlook
Summary and outlook

## Slide 36: Summary and outlook (I)
Challenges that have been resolved:
  Cavity design for strong HOM damping
  Operation at very high loaded Q (5x107 to >1x108) with excellent RF field stability
  Cryomodule providing excellent cavity alignment and magnetic shielding
Challenges that need some additional work:
  Long term cavity operation at high loaded Q with very low trip rates
  Microphonics reduction by passive and active means
  Broadband HOM dampers
  Low cost, reliable RF power sources (few kW range)
  Cryostat design for large number of significant dynamic loads supporting wide range in loads
Summary and outlook

## Slide 37: Summary and outlook (II)
Challenges that need much more work:
  Reliably achieving high Q0>2x1010 at medium fields
  Reducing cost of lower CW power RF input couplers (few kW range)
How you can help:
  Routinely test cavities at 1.6K, 1.8K, and 2K
  Test full modules at 1.6K, 1.8K, and 2K
  Study microphonics in cryomodules, especially long term, sensitivity to LHe pressure…
  Test operation of cryoplants below 1.8K
Summary and outlook

## Slide 38
The End
Thanks for you attention!