## Slide 1: Flexible data transport for the online reconstruction of FAIR experiments
Mohammad Al-Turany
Dennis Klein
Alexey Rybalchenko
(GSI-IT)

## Slide 2: Contents
Introduction to FAIR
  CBM and Panda Experiments
Why to use Message Queues
Current status
Results
Summary

## Slide 3
FAIR
Darmstadt (Germany)
GSI
Facility for
Antiproton and
Ion
Research
Observer:
EU, United States, Hungary, Georgia, Saudi Arabia

## Slide 5
~400 Physicists
50 Institutes
15 countries
Physics program:
Equation of state at high baryonic density
QCD phase transition
Critical end point of QCD phase diagram
Restoration of Chiral Symmetry

## Slide 6: Anti-Proton ANnihilation at DArmstadt
Physics Programm:
Charmonium Spectroscopy
Search for Glueballs & Hebrides
Hyper nucleus
Drell-Yan Physics
Electromagnetic form factors
Rare decays
Data rate ~107 Event/s
Data volume ~10 PB/yr
~450 Physicists
52 Institutes
17 Countries

## Slide 7: The Online Reconstruction and analysis
300 GB/s
20M Evt/s
< 1 GB/s
25K Evt/s
How to distribute the processes?
How to manage the data flow?
How to recover processes when they crash?
How to monitor the whole system?
……
1 TB/s
1 GB/s
> 60 000
CPU-core
or Equivalent
GPU, FPGA, …
> 60 000
CPU-core
or Equivalent
GPU, FPGA, …

## Slide 8: Trigger-less Data Acquisition

## Slide 9: Design constrains
Highly flexible:
  different data paths should be modeled.
Adaptive:
  Sub-systems are continuously under development and improvement
Should works for simulated and real data:
  developing and debugging the algorithms
It should support all possible hardware where the algorithms could run (CPU, GPU, FPGA)
It has to scale to any size! With minimum or ideally no effort.

## Slide 10: Before Re-inventing the Wheel
What is available on the market and in the community?
  A very promising package: ZeroMQ is available since 2 years
Do we intend to separate online and offline? NO
Multithreaded concept or a message queue based one?
  Message based systems allow us to decouple producers from consumers.
  We can spread the work to be done over several processes and machines.
  We can manage/upgrade/move around programs (processes) independently of each other.

## Slide 11: ØMQ (zeromq)
A socket library that acts as a concurrency framework.
Carries messages across inproc, IPC, TCP, and multicast.
Connect N-to-N via fanout, pubsub, pipeline, request-reply.
Asynch I/O for scalable multicore message-passing apps.
30+ languages including C, C++, Java, .NET, Python.
Most OS’s including Linux, Windows, OS X, PPC405/PPC440.
Large and active open source community.
LGPL free software with full commercial support from iMatix.

## Slide 12: Why ØMQ?
A messaging library, which allows you to design a complex communication system without much effort
Presents abstraction on higher level than MPI programming model is easier
Is suitable for loosely coupled and more general distributed systems

## Slide 13: Zero in ØMQ
Originally the zero in ØMQ was meant as "zero broker" and (as close to) "zero latency" (as possible).
In the meantime it has come to cover different goals:
zero administration,
zero cost,
zero waste.
More generally, "zero” refers to the culture of minimalism that permeates the project. Adding power by removing complexity rather than exposing new functionality.

## Slide 14: ZeroMQ sockets provide efficient transport options
Inter-thread
Inter-process
Inter-node
  which is really just inter-process across nodes communication
PMG : Pragmatic General Multicast (a reliable multicast protocol)
Named Pipe: Piece of random access memory (RAM) managed by
the operating system and exposed to programs through a file descriptor and a named mount point in the file system. It behaves as a first in first out (FIFO) buffer

## Slide 15: The built-in core ØMQ patterns are:
Request-reply, which connects a set of clients to a set of services. (remote procedure call and task distribution pattern)
Publish-subscribe, which connects a set of publishers to a set of subscribers. (data distribution pattern)
Pipeline, which connects nodes in a fan-out / fan-in pattern that can have multiple steps, and loops. (Parallel task distribution and collection pattern)
Exclusive pair, which connect two sockets exclusively

## Slide 16: Current Status
The Framework deliver some components which can be connected to each other in order to construct a processing pipeline(s).
All component share a common base called Device (ZeroMQ Class).
Devices are grouped by three categories:
  Source: Sampler
  Message-based Processor:
    Sink, BalancedStandaloneSplitter, StandaloneMerger, Buffer
  Content-based Processor: Processor

## Slide 17: Design
Experiment/detector specific code
Framework classes that can be used directly

## Slide 18: Example for CBM online reconstruction hierarchy
STS data
Mvd data
Clusterer
Clusterer
Tracker
Global Event Reconstruction
Trigger event selection
TRD data
TOF data
Clusterer
Pre-Processing
TRD Tracker

## Slide 19: Example for CBM online reconstruction hierarchy Simulation
STS Sampler
Mvd Sampler
Clusterer
Clustrer
Tracker
Global Event Reconstruction
Trigger event selection
TRD Sampler
TOF Sampler
Clustrer
Pre-Procceing
TRD Tracker

## Slide 20: Message-based Processor
All message-based processors inherit from Device and operate on messages without interpreting their content.
Four message-based processors have been implemented so far

## Slide 21
TRD data
Clusterer
TRD Tracker
TRD data
FairMQBalancedStandaloneSplitter
Clustrer
Clustrer
Clustrer
FairMQStandaloneMerger
Tracker
Tracker
Tracker
Example for Fan-out/Fan-in
the data path for load balancing

## Slide 22: Content-based Processor
The Processor device has at least one input and one output socket.
A task is meant for accessing and potentially changing the message content.

## Slide 23: Example for CBM online reconstruction hierarchy (scenario)
Detector
Simulation
STS data
Mvd data
Clusterer
Clusterer
REQ
REP
REP
REP
REP
Tracker
REQ
REQ
SUB
PUB
SUB
SUB
Parameter database
PUB
SUB
SUB
PUB
SUB
REP

## Slide 24: Results
Throughput of 940 Mbit/s was measured which is very close to the theoretical limit of the TCP/IPv4/GigabitEthernet
The throughput for the named pipe transport between two devices on one node has been measured around 1.7 GB/s
Each message consists of digits in one panda event for one detector, with size of few kBytes

## Slide 25: Payload in Mbyte/s as function of message size
Chart: 
| 128 Byte | 256 Byte | 512 Byte | 1 kByte | 2 kByte | 4 kByte | 8 kByte | 16 kByte | 32 kByte | 64 kByte | 128 kByte | 256 kByte | 512 kByte
10 Gbit | 101 | 192 | 366 | 584 | 1064 | 936 | 902 | 975 | 1170 | 1172 | 1172 | 1179 | 1177
56 Gbit IB | 76 | 141 | 212 | 357 | 445 | 538 | 583 | 651 | 881 | 1070 | 1248 | 1332 | 1328
ZeroMQ works on InfiniBand but using IP over IB

## Slide 26: Native InfiniBand/RDMA is faster than IP over IB
Implementing ZeroMQ over IB verbs will improve the performance.

## Slide 27
ZeroMQ
Root (Event loop)
FairRootManager
FairRunAna
FairTasks
Init()
Re-Init()
Exec()
Finish()
FairMQProcessorTask
Init()
Re-Init()
Exec()
Finish()
ROOT Files, Lmd Files, Remote event server, …
Integrating the existing software:

## Slide 28: Summary
ZeroMQ communication layer is integrated into our offline framework (FairRoot)
On the short term we will keep both options ROOT based event loop and concurrent processes communicating with each other via ZeroMQ.
On long Term we are moving away from single event loop to distributed processes.
          Thanks you !

## Slide 29: Device
Each processing stage of a pipeline is occupied by a process which executes an instance of the Device class

## Slide 30: Sampler
Devices with no inputs are categorized as sources
A sampler loops (optionally: infinitely) over the loaded events and send them through the output socket.
A variable event rate limiter has been implemented to control the sending speed

## Slide 31: Message format (Protocol)
Potentially any content-based processor or any source can change the application protocol. Therefore, the framework provides a generic Message class that works with any arbitrary and continuous junk of memory (FairMQMessage).
One has to pass a pointer to the memory buffer, the size in bytes, and can optionally pass a function pointer to a destructor, which will be called once the message object is discarded.

## Slide 32: New simple classes without ROOT are used in the Sampler (This enable us to use non-ROOT clients) and reduce the messages size.