## Slide 1: Closeout of Lattice Design Session in Workshop on Accelerator R&D for Ultimate Storage Ring
Working Group
H. Ohkuma(SPring-8), G. Xu(IHEP),
A. Nadji(SOLEIL), A.Franchi(ESRF),
D.H. Ji(IHEP), L. Liu (LNLS), Y. Shimosaki(SPring-8)
Huairou, Beijing, Nov. 1, 2012

## Slide 2: Summary of Talks(1)
“Lattice Design for the MAX IV 3 GeV Storage Ring” by S. Leemann (MAX-Lab)
E = 3 GeV, 7BA, εx = 326 pm.rad w/o IDs. I = 500mA
|DA| = 7-10mm with error
Number of straight = 20×~5m
Circumference = 528m
“Upgrade of the ESRF Light Source : Achievements and Perspectives” by P. Raimondi (ESRF)
  Accelerator Upgrade Phase I (6m, 7m straight sections), Top-up project
  E=6GeV, C=844, 7BA, ε = 130 pm.rad, SS 32x5m
“Lattice Design for SPring-8 II” by Y. Shimosaki (SPring-8)
  E=6GeV, C=1436m, 6BA, ε = 67.5 pm.rad, SS: 44×4.5m, 4×27m with FODO
“Possible USR Upgrade of the ALS” by C．Steier (LBNL)
ALS-II: 5BA-7BA, 50-100pm.rad, ….
E=2GeV, C=250m(?)

## Slide 3: Summary of Talks(2)
“Study of Lower Emittance Lattice at SOLEIL” by A. Nadji (SOLEIL)
(Short term path) :
Robinson Wiggler in a non-zero horizontal dispersion straight section
Beam Adapter in the 12 m long straight section
(Long term path) :
USR is also considered (εx ≈400pm.rad)
“BAPS Lattice Design” by G. Xu (IHEP)
  E=5GeV, C=1364.8m, 7BA, ε = 51 pm.rad, SS: 10×7m, 36×7m
  (15BA, 6BA also considered)
“A compact low emittance lattice with superbends for Sirius” by L. Liu (LNLS)
  E=3GeV, C=518.2m, 5BA+SB(2T), εx = 280 pm.rad, SS: 10×7m, 10×6m
  DA = +-10mm(AC20 mode), +-5mm(AC10 mode) with align-error.
  Permanent magnet dipoles
“Future Synchrotron Light Sources Based on Ultimate Storage Rings” by (Y. Cai) M. Borland (ANL)
PEP-X : E=4.5GeV, 7BA, C=2199.32m, εx = εy = 12 pm.rad, SS: 5m
DA = +-10mm with error of 20 μm

## Slide 4: Summary of Talks(3)
“Exploration of a Tevatron-Sized Ultimate Light Source” by M. Borland (ANL)
  E=9GeV, C=6210m, 180 IDs, ε = 2.98pmrad, Coupling factor ~ 100%
  |DA|=+-0.8mm (that may improve with more running time of MOGA).
  APS-II E=6GeV, 7BA, ε = 147 pm.rad,
“Overview of optics corrections at Diamond and plans for Diamond-II” by R. Bartolini (DLS)
DLS-II : E=3GeV, C=561.6m, modified 4BA, ε = 314.7 pm.rad, 9.7m, 6.7m, 3m
5BA, ε = 142.5 pm.rad, SS: 9.5m, 6.5m
7BA, ε = 45.7 pm.rad, SS: 8.0m, 5.0m
“Round beams experience at BINP … and other ideas” by E. Levichev (BINP)
Round beam mode in the sense of VEPP-2000 (1D motion at IP) seems has no advantage for USR
Equal emittances concept to reach a diffraction limit emittance in both planes seems promissing and should be studied in details.
Damping wigglers with horizontal magnetic field look attractive for “rounding” the emittances and to suppress additionally any heating of the beam emittances.

## Slide 5: Main Subjects (1)
What is USR?
: a storage ring having an emittance in both transverse planes at
the diffraction limit for a range of wavelength?
: diffracted limited emittance is λ/4π or λ/2π ?
: for example, 1A-USR or 10A-USR or even Soft X-ray USR or
Hard X-ray-USR?
: Very high brilliance or very high coherence?
Target Emittance : 10pm.rad ? , diffraction limited @ 10KeV?
: Damping Wiggler and/or coupling control etc. is needed
: The low field of the dipoles help for low energy dispersion,
also very desired to optimize the brilliance of long insertion device
: The use of defocusing gradient in the dipoles helps
: The use of longitudinally variable field also helps
Energy Spread

## Slide 6: Main Subjects (2)
MBA : Optimized No. ?
: seems to be the best compromise to reach ultra low emittance
and zero dispersion straight sections.
: M is a compromise between the emittance we want to reach
and the number of straights needed
Energy (3GeV-9GeV) : depending on user’s demands and required max. photon energy. Future ID development
Dynamic Aperture: need for Injection and beam lifetime
: Adequate dynamic aperture and beam lifetime should be
possible (push the idea of resonance cancellation and use of
high order multipoles)

## Slide 7: Main Subjects (3)
Modern lattice optimization
: using multi-objective genetic algorithms (MOGA)
: Phase advance between sextupoles
IBS, collective effects & Touschek : most serious issue
Harmonic Cavity for longer lifetime and higher bunch current
(SP8-II, and others).
Combined function magnets : because of compactness
(MAX-IV, others)
Alignment: Requirement < 10μm
Small aperture vacuum chamber : NEG-coated Cu chamber
(MAX-IV, Sirius)

## Slide 8: Main Subjects (4)
Matching between the electron and photon phase space should be a criteria to maximize the brilliance
Can we define a quality factor : How far the lattice is optimized in term of emittance normalized to the energy, circumference and length for straight sections?
It is for specific and exigent users : keep high stability and reliability
The Lattice design has to provide low emittance AND adequate space in straight sections to accommodate Insertion Devices

## Slide 9
We would like to thank all the speakers.
S. Leeman (Max-lab)
P. Raimondi (ESRF)
Y. Shimosaki (SPring-8)
C．Steier (LBNL)
A. Nadji (SOLEIL)
G. Xu (IHEP)
L. Liu (LNLS)
(Y. Cai (SLAC))
M. Borland (ANL)
R. Bartolini (DLS)
E. Levichev (BINP)