## Slide 1: BAPS Lattice Design
XU Gang
IHEP, Beijing, China
Oct. 30, 2012, Huairou, China

## Slide 2: Topics
Goals
Linear lattice design
Damping wiggler
Round beam
Chromaticity correction
Summary

## Slide 3: Design Goals
E=5GeV
Circumference 1200~1500m
High brightness operation mode
Emittance 10pm/10pm(diffraction limit for 10keV X-ray)
Beam current 100mA~150mA
High flux operation mode
flat beam(no damping wiggler)
Beam current 200mA~300mA
Large enough dynamic aperture for injection

## Slide 4: Linear lattice design
7BA*36
25mm magnet pole diameter, combined bending magnet
15BA*16
25mm magnet pole diameter, combined bending magnet
6BA*40
48mm magnet pole diameter, quadrupole with sextuple components
Damping wiggler
31mm period 2.3Tesla damping wiggler about 60m
Round beam
local: solnoid+ID+antisolenoid
global: Mobius ring or other

## Slide 5: 7BA*36 Linear Optics
Circumference: 1364.8 m, 2 superperiods, 36 supercells
Working point: 111.39, 39.30
Natural chromaticity: -184, -181
Natural emittance: 51 pm.rad

## Slide 6: Lattice layout in one superperiod
High-beta 10-m Straight section *2, bx/y = (80, 21) m;
Low-beta 7-m Straight section *36, bx/y = (5,1.11) m ;
Phase advance per supercell: (6p + p/6 + duxp/36, 2p + p/6 + duyp/36)
with dux = 0.39, duy = 0.30.
7-m low-beta straight section

## Slide 7: Dynamic aperture
On-momentum DA
Off-momentum DA
Large enough on-momentum DA, satisfies the requirements of pulsed sextupole injection;
Momentum acceptance is not large, ~ 1.5%, not long Touschek lifetime. However, this can be cured with top-up injection.

## Slide 8
Black: bare lattice, Green: multiple error=10-4,
Blue: multiple error & bending error

## Slide 9: Injection insertion
φxinj= φxstd+2π
φyinj= φystd
Keep the symmetry for linear lattice
Help for dynamic aperture for on-momentum
Straight length>9m for pulse sextupole injection

## Slide 10
PSM: pulse sextupole magnet for injection,
L=0.6m, 1000Tesla/m2 52mm pole diameter
bottom width<4μs
(details ref. KANG Wen also JIAO Yi talk)
SEP: Septum magnet
Straight length 9.2m
>5mm dynamic aperture

## Slide 11: 15BA*16

## Slide 12: Lower β section with double wraists
βx =3m, βy =1m, straight section 7m*2
Canting structure is neccesary

## Slide 13: higher β section for injection
βx =80m, βy =8m, middle straight section 9.2m for injection
φxinj= φxstd φyinj= φystd(hope improve dynamic aperture for off-momentum)

## Slide 14: Middle β section for Mobius ring
βx = βy =7m, straight section 14m
φxMob= φxstd φyMob= φystd
Length between the two arc bending magets is equal to each other for high beta and middle beta section

## Slide 15: Dynamic aperture for 15BA

## Slide 16
6BA*40

## Slide 17: Damping wiggler effects
lu (m)
Lu (m)
Damping wiggler (DW), peak field 2.3 Tesla,
Undulator period 3.1 cm,
40-m DW  20 pm
50-m DW  17 pm
60-m DW  15 pm
70-m DW  14 pm

## Slide 18: Round beam
Local round beam
1.75m 15Tesla solenoid( π/4 x-y rotating )
+2.5m ID(circle polarity EPU is best for decouple)
+ 1.75m 15Tesla anti-solenoid (- π/4 x-y rotating )
at least 6m space
local scheme by A. Chao and P. Raimondi
Global round beam:
π/2 x-y rotating solenoid(Mobius ring)
other method

## Slide 19
εx= (AA DD-BB CC) Cos[(c z)/2]2
εy= (AA DD-BB CC) Sin[(c z)/2]2

## Slide 20: Chromaticity correction
Up to 5th order DA map( polynomial ) with sextupole, octupole, decuple, duodecupole strength variables(can reach to about 30 variables)
Up to 6th order corresponding Hamiltonian
Up to 4th order chromaticity
Up to 2nd detuning coefficients
Up to 6th resonance coefficients
Optimizing chromaticity curve under controlling detuning and resonance coefficients (mainly on 3rd order and 4th order)

## Slide 21
Comparison for different detune coefficient(dq/dx)

## Slide 22: Summary
The lattice design of BAPS is still in progress.
To reach diffraction limit very strong damping wiggler and solenoid is necessary in our design
The dynamic aperture for bare lattice and 10-4 multiple error looks acceptable for pulse sextupole injection
For NBA structure, N=7 is popular in USR design, How large N(>7) is applicable?