## Slide 1: Future Muon Accelerators
Mark A. Palmer
August 21, 2013

## Slide 2: Perhaps this should have been called…
The Potential of
High Intensity Muon Beams

## Slide 3: The Aims of the Muon Accelerator Program
  The MAP accelerator R&D effort is focused on developing a facility that can address critical questions spanning two frontiers…
  The Intensity Frontier:
  with a Neutrino Factory producing well-characterized n beams for precise, high sensitivity studies
  The Energy Frontier:
  with a Muon Collider capable of reaching multi-TeV CoM energies
  and a Higgs Factory on the border between these Frontiers
The unique potential of a facility based on muon accelerators is physics reach that SPANS 2 FRONTIERS

## Slide 4: Why Muon Accelerators?
Muon beams offer unique potential for high energy physics
  Tests of Lepton Flavor Violation
  Anomalous magnetic moment a hints of new physics (g-2)
  Can provide equal fractions of electron and muon neutrinos at high intensity for studies of neutrino oscillations – the Neutrino Factory concept
  Muon collisions offer a large coupling to the “Higgs mechanism”
  As with an e+e− collider, a m+m− collider would offer a precision probe of fundamental interactions

## Slide 5: Why Muon Accelerators?
Of course the potential applications for high intensity muon sources go beyond high energy physics
  Muon radiography
  Atomic and nuclear physics applications, for example…
    Catalysis of atomic and molecular reactions
    Nuclear reactions
    Muon capture studies of radiological materials
  Among others…

## Slide 6: The Issues - I
m – an elementary charged lepton:
  200 times heavier than the electron
  2.2 ms lifetime at rest
The large muon mass strongly suppresses synchrotron radiation
  Muons can be accelerated and stored using rings at much higher energy than electrons
  a Colliding beams can be of higher quality with reduced beamstrahlung
Beamstrahlung in any e+e- collider
E/E  2
3 TeV

## Slide 7: The Issues - II
Impacts of the short muon lifetime
  Acceleration and storage time of a muon beam is limited
  Collider a a new class of decay backgrounds must be dealt with
For a collider, beam energy measurement by g-2 method a precision Higgs mass/width determination
Muon beams produced as tertiary beams:
  Offers key accelerator challenges…

## Slide 8: HEP Motivations: Neutrinos
CP violation physics reach of various facilities
Can we probe the CP violation in the neutrino sector at the same level as in the CKM Matrix?
P. Coloma, P. Huber, J. Kopp, W. Winter
0.025 IDS-NF: 700kW target, no cooling, 2×108 s running time
10-15 kTon detector
Measurement sensitivity in the quark sector

## Slide 9: HEP Motivations: Colliders
E. Eichten
A ~10 TeV muon collider provides discovery potential for BSM processes in the EW sector that can exceeds that of a 100 TeV pp machine

## Slide 10: The Muon Accelerator Program R&D Effort

## Slide 11: The Muon Accelerator Program
By the end of this decade:
To deliver results that will permit the high-energy physics community to make an informed choice of the optimal path to a high-energy lepton collider and/or a next-generation neutrino beam facility
As well as…
To explore the path towards a facility that can provide cutting edge performance at both the Intensity Frontier and the Energy Frontier
To validate the concepts that would enable the Fermilab accelerator complex to support these goals

## Slide 12: The U.S. Muon Accelerator Program

## Slide 13: Key Technologies - Target
The MERIT Experiment at the CERN PS
  Demonstrated a 20m/s liquid Hg jet injected into a 15 T solenoid and hit with a 115 KJ/pulse beam!
  Jets could operate with beam powers up to 8 MW with a repetition rate of 70 Hz
MAP staging aimed at initial 1 MW target
Hg jet in a 15 T solenoid
with measured disruption length ~ 28 cm
1 cm
D. Kaplan (Tues - Plenary)
K. McDonald (Tues – WG3)

## Slide 14: TechnoIogy Challenges – Capture Solenoid
A Neutrino Factory and/or Muon Collider Facility requires challenging magnet design in several areas:
  Target Capture Solenoid (15-20T with large aperture)
  Estored ~ 3 GJ
  O(10MW) resistive coil in high radiation environment
  Possible application
  for High Temperature Superconducting magnet technology
K. McDonald (Tues – WG3)
H. Sayed (Tues – WG3)

## Slide 15: Technology Challenges – Tertiary Production
Neuffer
A multi-MW proton source, e.g., Project X, will enable O(1021) muons/year to be produced, bunched and cooled to fit within the acceptance of an accelerator.
D. Neuffer (Tues – WG3)

## Slide 16: Technology Challenges - Cooling
Tertiary production of muon beams
  Initial beam emittance intrinsically large
  Cooling mechanism required, but no radiation damping
Muon Cooling a Ionization Cooling
    dE/dx energy loss in materials
    RF to replace plong
MICE
Spectrometer Solenoids
RF-Coupling Coil (RFCC) Units
  The Muon Ionization Cooling Experiment: Demonstrate the method and validate our simulations
D. Adey, D. Kaplan (Wed – WG3)

## Slide 17: Ionization Cooling
D. Kaplan

## Slide 18: Technology Challenges - Cooling
Some components beyond state-of-art:
  Very high field HTS solenoids (≥30 T)
  High gradient RF cavities operating in multi-Tesla fields
Development of a cooling channel design to reduce the 6D phase space by a factor of O(106) → MC luminosity of O(1034) cm-2 s-1
R. Palmer
Emittance Reduction via Ionization Cooling
The program targets critical magnet and cooling cell technology demonstrations within its feasibility phase.
D. Stratakis (Wed – WG3)
R. Palmer, K. Yonehara, D. Neuffer (Thu – WG3)

## Slide 19: Elements of the R&D Program
Compressor + refrigerator room
Entrance of MTA
exp. hall
MuCool Test Area
MTA Hall
201 MHz cavity
SC magnet
400 MeV H- beam
400 MeV
H- Beam
Gas-Filled RF cell
20 MV/m in 3 Tesla
Vacuum RF Cavity

## Slide 20: Technology Challenges - Acceleration
Muons require an ultrafast accelerator chain
a Beyond the capability of most machines
Solutions include:
EMMA – FFAG
  Superconducting Linacs
  Recirculating Linear Accelerators (RLAs)
  Fixed-Field Alternating-Gradient (FFAG) Machines
  Rapid Cycling Synchrotrons (RCS)
  RCS requires
  2 T p-p magnets
  at f = 400 Hz
  (U Miss & FNAL)
JEMMRLA Proposal:
JLAB Electron Model of
Muon RLA with Multi-pass
Arcs

## Slide 21: Superconducting RF Development
Cavity going into test pit
in Newman basement (Cornell University)
Pit: 5m deep X 2.5m dia.
400mm BT
Cavity length: 2 m
Major dia.: 1.4 m
201 MHz SCRF R&D

## Slide 22: Technology & Design Challenges – Ring, Magnets, Detector
Emittances are relatively large, but muons circulate for ~1000 turns before decaying
  Lattice studies for 126 GeV, 1.5 & 3 TeV CoM
High field dipoles and quadrupoles must operate in high-rate muon decay backgrounds
  Magnet designs under study
Detector shielding & performance
  Initial studies for 126 GeV, 1.5 TeV, and 3 TeV using MARS background simulations
  Major focus on optimizing shielding configuration
MARS energy deposition map for 1.5 TeV collider dipole

## Slide 23: Backgrounds and Detector
Much of the background is soft and out of time
Nanosecond time resolution can reduce backgrounds by three orders of magnitude
Requires a fast, pixelated tracker and calorimeter.
Non-ionizing background ~ 0.1 x LHC
But crossing interval 10ms/25 ns 400 x
GeV/c
ns
 | Cut | Rejection
Tracker hits | 1 ns, dedx | 9x10-4
Calorimeter neutrons | 2 ns | 2.4x10-3
Calorimeter photons | 2 ns | 2.2x10-3

## Slide 24: Recent Highlights in Cooling Channel Technology R&D

## Slide 25: Recent Progress I - MICE
Currently preparing for MICE Step IV
Includes:
  Spectrometer Solenoids
  First Focus Coil
Provides:
  Direct measurement of interactions with absorber materials
  Important simulation input
MICE
Spectrometer Solenoids
RF-Coupling Coil (RFCC) Units
First Spectrometer Solenoid Now Commissioned!
First Coupling Coil Cold Mass Being Readied for Training
Fermilab Solenoid Test Facility

## Slide 26: Recent Progress II – Cavity Materials
Breakdown tests with Be and Cu Buttons
Both reached ~31 MV/m
Cu button shows significant pitting
Be button shows minimal damage
a Materials choices offer the possibility of more robust operation in mangetic fields
Cu
Be

## Slide 27: Recent Progress III – Vacuum RF
Vacuum Tests at B = 0 T & B = 3 T
  Two cycles: B0 a B3 a B0 a B3
No difference in maximum stable operating gradient
  Gradient » 25 MV/m
Demonstrates possibility of successful operation of vacuum cavities in magnetic fields with careful design
All-Seasons
Cavity
(designed for both vacuum and high pressure operation)

## Slide 28: Recent Progress IV: High Pressure RF
Gas-filled cavity
  Can moderate dark current and breakdown currents in magnetic fields
  Can contribute to cooling
  Is loaded, however, by beam-induced plasma
Electronegative Species
  Dope primary gas
  Can moderate the loading effects of beam-induced plasma by scavenging the relatively mobile electrons
5/22/12
Beam on
E0 = 25 MV/m
28
Pure GH2
1% Dry Air (0.2 % O2) in GH2
1% Dry Air
(0.2 % O2)
in GH2 at B = 3 T
E0 = 25 MV/m
~50× change in
RF dissipation

## Slide 29: Recent Progress V: High Field Magnets
Progress towards a demonstration of a final stage cooling solenoid:
Demonstrated 15+ T (16+ T on coil)
  ~25 mm insert HTS solenoid
  BNL/PBL YBCO Design
  Highest field ever in HTS-only solenoid (by a factor of ~1.5)
BSCCO-2212 Cable -
Transport measurements show that FNAL cable attains 105% Jc of that of the single-strand
Multi-strand cable utilizing chemically compatible alloy and oxide layer to minimize cracks
BSCCO-2212 Challenge:
Damage to wire during reaction
Hyperbaric reaction now a proven solution

## Slide 30: MAP: Recent Technology Highlights
Successful Operation of 805 MHz “All Seasons” Cavity in 3T Magnetic Field under Vacuum
MuCool Test Area/Muons Inc
World Record HTS-only Coil 15T on-axis field 16T on coil
PBL/BNL
Demonstration of High Pressure RF Cavity in 3T Magnetic Field with Beam
Extrapolates to m-Collider Parameters
MuCool Test Area
Breakthrough in HTS Cable Performance with Cables Matching Strand Performance
FNAL-Tech Div T. Shen-Early Career Award
The Path to a Viable Muon Ionization Cooling Channel
Pure GH2
1% Dry Air (0.2% O2) in GH2
E0 = 25 MV/m
~50X reduction in
RF power dissipation
1% Dry Air
(0.2 % O2)
in GH2 at
B = 3T

## Slide 31: The Muon Accelerator Staging Study (MASS) and MAP Timelines
Also see next talk by J.-P. Delahaye

## Slide 32: A Staged Muon-Based Neutrino and Collider Physics Program

## Slide 33: Muon Accelerators
Program Baselines
And Potential Staging Steps

## Slide 34: All proposed muon-based accelerators would easily fit at Fermilab
nSTORM (entry level Neutrino Factory)
Intensity Frontier Neutrino Factory
nSTORM would provide important physics output and critical R&D leverage
The IDS-NF Options

## Slide 35: Neutrinos from Stored Muons (arXiv: 1206.0294 (LOI), Fermilab P-1028)
DOES NOT
Require the
Development of
ANY
New Technology
An entry-level NF?
A.Bross
NuFACT12
3.8 GeV/c
stored m
10-100kW

## Slide 36: nStorm as an Accelerator R&D Platform
A high-intensity pulsed muon source
100<pμ<300 MeV/c muons
  Using extracted beam from ring
  1010 muons per 1 μsec pulse
Beam available simultaneously with physics operation
  Sterile n search
  n cross section measurements needed for ultimate precision in long baseline measurements
nSTORM also provides the opportunity to design, build and test decay ring instrumentation (BCT, momentum spectrometer, polarimeter) to measure and characterize the circulating muon flux.
D. Neuffer, J.-B. Lagrange, A. Bross (Wed – WG3)
J. Morfin (Wed – WG2)
A. Bross (Sat – Plenary)

## Slide 37: The n Sector and NuMAX
We want to provide the option to get here

## Slide 38: Neutrino Factory Staging (MASS)
Preliminary Staging Plan Based on Project Stage 2
* supports multiple detector technologies

## Slide 39: How Could the Staged NF to Homestake Perform?
What if we send beam to LBNE? 1 MW, no muon cooling a 3 MW, w/cooling a 4 MW, w/cooling
What if we were able to have a magnetized LAr detector?
Plots courtesy of P. Huber
Gray bands represent range of possible
detector performance per arXiv:0805.2019
Plots assume
100 kt-years

## Slide 40
One IP in the latest
design
Next: Possibly a muon-based Higgs Factory or Energy Frontier Muon Collider

## Slide 41: Multi-TeV Collider – 1.5 TeV Baseline
Parameter | Unit | Value
Beam energy | TeV | 0.75
Repetition rate | Hz | 15
Average luminosity / IP | 1034/cm2/s | 1.1
Number of IPs, NIP | - | 2
Circumference, C | km | 2.73
* | cm | 1 (0.5-2)
Momentum compaction, p | 10-5 | -1.3
Normalized r.m.s. emittance, N | mmmrad | 25
Momentum spread, p/p | % | 0.1
Bunch length, s | cm | 1
Number of muons / bunch | 1012 | 2
Number of bunches / beam | - | 1
Beam-beam parameter / IP,  | - | 0.09
RF voltage at 800 MHz | MV | 16
Larger chromatic function (Wy) is corrected first with a single sextupole S1, Wx is corrected with two sextupoles S2, S4 separated by 180 phase advance.
Y. Alexahin

## Slide 42: Muon Collider Parameters
Site Radiation mitigation with depth and lattice design: ≤ 10 TeV
Success of advanced cooling concepts a several × 1032
Exquisite Energy Resolution Allows Direct Measurement
of Higgs Width

## Slide 43: MAP Timeline
 | 2010 |  | ~2020 |  | ~2030 | 
Muon Accelerator R&D Phase |  |  |  |  |  | 
Proton Driver Implementation – Project X @ FNAL |  |  |  |  |  | 
Intensity Frontier |  |  |  |  |  | 
Energy Frontier |  |  |  |  |  | 
MAP Feasibility Assessment
Advanced Systems R&D
Muon Ionization Cooling Experiment (MICE)
IDS-NF RDR
Proposed Muon Storage Ring Facility (nSTORM)
Evolution of Long Baseline n Factory
Collider Conceptual  Technical Design
Collider Construction  Physics Program
Pr X Stage I
Pr X Stage II
Pr X Stage III & IV
At Fermilab, critical physics production could build on Stage II of Project X
Indicates a date when an informed decision should be possible

## Slide 44
LBNE
Buncher/
Compressor
Rings
To SURF
Project X Stage I
Project X Stage II
Linac + RLA to ~5 GeV
NF Decay Ring:
ns to SURF
Front End+4D+6D
RLA to 63 GeV +
300m Higgs Factory
nSTORM + Muon Beam R&D Facility
A Muon Accelerator Facility for Cutting Edge Physics on the Intensity and Energy Frontiers
Based on Project X Stage II
44
A 1.5 TeV collider
would fit within the
Tevatron ring
ft
ft
A TeV-scale Collider
at Fermilab
And other potential applications for high quality m beams in the MeV to TeV energy range

## Slide 45: Concluding Remarks

## Slide 46: Some Thoughts…
The unique feature of muon accelerators is the ability to provide cutting edge performance on both the Intensity and Energy Frontiers
  This is well-matched to the direction specified by the P5 panel for Fermilab
  The possibilities for a staged approach make this particularly appealing in a time of constrained budgets
  nSTORM would represent a critical first step in providing a muon-based accelerator complex
World leading Intensity Frontier performance could be provided with a Neutrino Factory based on Project X Stage II
  This would also provide the necessary foundation for a return to the Energy Frontier with a muon collider on U.S. soil
A Muon Collider Higgs Factory
  Would provide exquisite energy resolution to directly measure the width of the Higgs. This capability would be of crucial importance in the MSSM doublet scenario.
  The first collider on the path to a
  multi-TeV Energy Frontier lepton machine?

## Slide 47: Conclusion
Through the end of this decade, the primary goal of MAP is demonstrating the feasibility of key concepts needed for a neutrino factory and muon collider
a Thus enabling an informed decision on the path forward for the HEP community
Muon Collider Concept
A promising R&D program is in progress!

## Slide 48: Muon Accelerator Program Contacts
MAP Web-Site: http://map.fnal.gov/
MAP Management Team:
Mark Palmer, Director: mapalmer@fnal.gov
Robert Ryne, L1 Manager for Design and Simulation: rdryne@lbl.gov
Harold Kirk, L1 Manager for Technology Development: hkirk@bnl.gov
Daniel Kaplan, L1 Manager for Systems Demonstrations: kaplan@iit.edu
Alan Bross, L1 Manager for MICE Construction: bross@fnal.gov
Ron Lipton, L1 Manager for Detectors and Physics: lipton@fnal.gov
US HEP Community Planning Effort
Jean-Pierre Delahaye, Muon Accelerator Staging Study jpd@slac.stanford.edu

## Slide 49: Acknowledgments
I would personally like to thank Steve Geer, Mike Zisman, Bob Palmer as well as the MAP L1 & L2 managers for their help in familiarizing me with the program since I took over as director just over a year ago
The MAP Effort -
Labs: ANL, BNL, FNAL, JLAB, LBNL, ORNL, SLAC
Universities: Chicago, CMU, Cornell, ICL, IIT, Princeton, SUNY-SB, UC-Berkeley, UCLA, UC-Riverside, UMiss, VT
Companies: Muons, Inc; Particle Beam Lasers