## Slide 1: Modifications on ESS for neutrino Super Beam
Marcos DRACOS
IPHC-IN2P3/CNRS Strasbourg
(E. Wildner, T. Ekelof)

## Slide 2: EUROnu Projects (beam facilities)
p
SPL 3.5-5 GeV, 4 MW
Target
~300 MeV nm beam to far detector
decay tunnel
Accumulator
ring
Magnetic
horn capture
(collector)
proton driver
hadrons
n, m
p
Proton
driver
Isol target
& ion source
DECAY
RING
B = 5T
L=6880 m
PSB
EURISOL
Existing at CERN
New RFQ
SPS
PS
Linac
5 GeV?, 4 MW
Target
Linac  2 GeV
Recirculating
Linacs 2  50 GeV
Decay ring – 50 GeV
2000 m circumference
Ionization
cooling
Phase rotation
n beam to far detector
Drift
Accumulator
ring + bunch
compressor
Magnetic
capture
n beam to near detector
SPL Super-Beam
Neutrino Factory
Beta-Beam
6He for ne and 18Ne for ne
proton driver

## Slide 3: European Long Baseline Super Beam Projects
Studied by LAGUNA

## Slide 4: Target Station (EUROν)
beam switchyard
decay tunnel
horn power supply
strip lines
targets/horns

## Slide 5: 4-Target/Horn system (EUROnu)
Packed bed canister in symmetrical transverse flow configuration (titanium alloy spheres)
Helium Flow
Helium Velocity
Maximum flow velocity = 202m/s
Maximum Mach Number < 0.2
Helium Gas Temperature
Total helium mass flow = 93 gr/s
Maximum Helium temperature = 584°C
Helium average outlet Temperature = 109°C
First tests with beam in the new HiRadMat@SPS facility at CERN in 2014

## Slide 6: Physics Performance (CPV) (Enrique Fernantez et al.)
20 kt LAr
100 kt LAr
SPL: CERN to Fréjus (130 km)
CF-1st: CERN to Canfranc (650 km) 1st max.
CF-2nd: CERN to Canfranc 2nd max.
1 Mton WC detector (440 kton fiducial), 5%/10% syst.
100 kt Lar (0.75 MW)

## Slide 7: Physics Performance (MH)
SPL: CERN to Fréjus (130 km)
CF-1st: CERN to Canfranc (650 km) 1st maximum
CF-2nd: CERN to Canfranc 2nd maximum
1 Mton WC detector (440 kton fiducial), 5%/10% syst.
without adding atmospherics

## Slide 8: SPL not any more part of LHC upgrades
Any other intense proton source in Europe?
(in the context of European Strategy for Particle Physics)
f) Rapid progress in neutrino oscillation physics, with significant European involvement, has
established a strong scientific case for a long-baseline neutrino programme exploring CP violation and the mass hierarchy in the neutrino sector. CERN should develop a neutrino programme to pave the way for a substantial European role in future long-baseline experiments. Europe should explore the possibility of major participation in leading neutrino projects in the US and Japan.

## Slide 9: European Spallation Source
under construction
(~1.5 B€ facility)

## Slide 10: ESS proton linac
The ESS will be a copious source of spallation neutrons
5 MW average proton beam power
125 MW peak power
14 Hz repetition rate (2.86 ms pulse duration, 1015 protons)
4% duty factor
linac mostly (>97%) superconducting
2.5 GeV protons (up to 3.0 GeV with linac upgrades)
>2x1023 p.o.t/year

## Slide 11: ESS parameters
ESS Technical Design Report
April 23, 2013
ESS-doc-274
http://europeanspallationsource.se/documentation/tdr.pdf
enough to go up to 3 GeV
198 days
2 GeV at the beginning
62.5

## Slide 12: Linac Sharing
Ion source : Istituto Nazionale di Fisica Nucleare (INFN) – Catania, Italy
Radio Frequency Quadrupole (RFQ): Commissariat à l'énergie atomique (CEA) – Saclay, France
Medium Energy Beam Transport (MEBT): ESS-Bilbao, Spain
Drift tube Linac (DTL): Istituto Nazionale di Fisica Nucleare (INFN) – Legnaro, Italy
Spoke cavities: Institut de Physique Nucléaire (CNRS) – Orsay, France
Elliptical cavities: Commissariat à l'énergie atomique (CEA) – Saclay, France
High Energy Beam Transport: Aarhus University, Denmark
Spoke RF sources: Uppsala University, Sweden
RF regulation: Lund University, Sweden

## Slide 13: What is different from SNS?
The average proton beam power will be 5 MW
  Average neutron flux is proportional to average beam power
  5 MW is five times greater than SNS beam power
The total proton energy per pulse will be 360 kJ
  Beam brightness (neutrons per pulse) is proportional to total proton energy per pulse
  360 kJ is over 20 times greater than SNS total proton energy per pulse

## Slide 14: Well defined ESS Schedule
1st beam before the end of the decade
5 MW by 2023

## Slide 15: ESS Schedule

## Slide 16: Requirements for adding a neutrino facility
We must not affect the neutron program.
Follow their schedule.
Use as much as possible neutron facilities.
For anything added, be synergetic when possible.
Moderate cost.
Kindly ask them to keep their choices compatible with neutrino needs (if this doesn't increase the neutron budget).

## Slide 17: How to add a neutrino facility?
with 2.5 GeV proton: ~300 MeV neutrinos
Linac modifications: double the rate (14 Hz → 28 Hz)
  one pulse for neutrinos and one pulse for neutrinos (5 MW each)
additional RF power to drive the two beams (neutron production and neutrinos)
  upgradable power sources
  or double the power sources (free space has to be foreseen since now)
2.5 GeV protons
flux at 100 km

## Slide 18: How to add a neutrino facility?
Accumulator (ø 143 m) needed to compress to few μs the 2.86 ms proton pulses, affordable by the magnetic horn (350 kA, power consumption, Joule effect)
  H- source (instead of protons)
  space charge problems to be solved
Neutron users have also expressed an interest for the accumulator (increase of neutron brightness).
Other neutrino users using pions (from neutron target) decaying at rest need short pulses.
Target station (studied in EUROnu)
Underground detector (studied in LAGUNA)
Linac and accumulator could be the first step towards the Neutrino Factory
(http://lanl.arxiv.org/abs/1212.5048)
accumulator
target/horn station
Linac
Storage Ring
Target and Instruments

## Slide 19: Existing expertise

## Slide 20: Linac and RF power source tests
A prototype 352 MHz spoke cavity for the ESS linac will be tested in the FREIA Laboratory at Uppsala University already as from July 2014 in a cryostat at 14 Hz pulse frequency and at the full instantaneous power required for ESS proton acceleration.
As part of this neutrino project, the power supplied to the 352 MHz power source would be doubled and the pulse frequency raised to 28 Hz, thus doubling the average power to the cavity.
The influence of this higher power on the operation of the cavity and on the capacity to cool the cavity itself and, in particular, its RF coupler will be studied.
Layout of the 352 MHz RF
source, wave guides and test
cryostat in the FREIA hall
ESS Spoke 352 MHz
Accelerating Cavity

## Slide 21: Accumulator
A problem with the enormous amount of protons stored at comparatively low energy in the accumulation ring is the space charge which leads to a defocusing of the stored beam.
For a charge of 1015 protons stored for 2.86 ms in 450 m circumference storage ring, this defocusing effect is critical.
A way to alleviate this problem is to divide the stored charge on four accumulation rings, thereby reducing the defocusing effect by a factor 4.
Neutron community very interested about this new device.
This trick is already used for the CERN PS Booster ring.
The 4 rings of the CERN PS Booster (1972)

## Slide 22: H- Source
Parameter | Unit | ISIS | SNS | BNL | CERN, L4 | ESS ν | SPL
Beam Energy | keV | 16-35 | 65 | 35,40 | 45 | 75 | 45
Pulse duration | ms | 0.5 | 1 | 0.8 | 0.4 | 3 | 1.2
Repetition Rate | Hz | 50 | 60 | 6.6 | 1 | 14 | 50
H- current | mA | 35 | 60 | 65 | 80 | 62.5 | 80
H- production mode |  | Cs-Arc | Cs-Surf. | Cs-Surf. | Cs-Surf. | Cs-Surf. | Cs-Surf.
Plasma Heating |  |  |  |  |  |  | 
Emmittance In RFQ Norm RMS | mmmrad |  | 0.25 |  | 0.25 | 0.20 | 
Cs-consumption | mg/day | 100 | 0.4 | 12 |  |  | 
Operation MTBM | weeks | 5 | 6 | 36 | 52 |  | 
There exist sources that could give the required performance for EUROSB
Courtesy: J. Lettry

## Slide 23: The LEBT
Or ?
EUROSB Specific
At SNS:
two sources one RFQ !
Could we use the same RFQ for ESS and EUROSB ?
Constraints on RFQ phase?
ESS: 0.2 mmmrad 4D norm Waterbag distribution at entrance RFQ

## Slide 24: Source-LEBT
The Source is feasible (cmp existing developments)
  Estimate price by scaling from existing source developments
  SNS source is close to EUROSB requirements
  Get measurements from existing sources for simulations (SNS, CERN … )
Simulations of LEBT including RFQ
  Can the RFQ work for interleaved H- and H+ pulses (i.e. use of same RFQ)?
  If so, simulation of separate RFQ and common RFQ
  Must not influence neutron performance (Powered dipole only for H-)
  Measurement of the Linac 4 source and of the SPL cavities, exploiting the tools developed in the context of the SLHC-PP project to take into account RF imperfections should be included in the simulations
LEBT Chopper requirements
  Chop unstable part of source pulse
  Ion source rise/fall time 50 ms and RFQ 100 ns
  Gives time for RFQ stabilization

## Slide 25: MEBT
Chopper in MEBT
  Prepare structure of beam for later (ejection of beam from accumulator)
  Advantageous to chop beam at lower energy
  Fast: 2 ns rise-time for 352 MHz
MEBT functions
  Optics of MEBT may cause emittance growth
  However useful for instrumentation, steering, optics tuning…
  Collimation
  Matching of RFQ and DTL in all three planes (10 quadrupoles and three 352.21 MHz buncher cavities)
  MEBT contains a dump for tests i.e. for upgrade work

## Slide 26: Stripping
foil stripping not possible due to the high beam intensity
Laser stripping necessary
Promising tests at SNS

## Slide 27: Target Station General Layout
Split Proton Beam
Neutrino Beam Direction
Collimators
Horns and Targets
Decay Volume (He, 25 m)
Beam Dump
Horn Support Module
Shield Blocks

## Slide 28: Possible Operation Timing
35.7 ms
2.86 ms
2.86/4 ms
28 Hz
1.5 μs
17.85 ms
(71.4/4 ms)
17.135 ms
neutron
neutrino
56 Hz neutrino beam (1.25 MW/target)
(50 Hz for SPL, 1 MW/target)
if only users of the accumulator
empty 1st ring
empty 2nd ring
empty 3rd ring
empty 4th ring
refilling
ring filling

## Slide 29: The MEMPHYS Detector (Water Cherenkov) (LAGUNA)
Mainly to study:
Proton Decay (GUT)
  up to ~1035 years lifetime
Neutrino properties and Astrophysics
  Supernovae (burst + "relics")
  Solar neutrinos
  Atmospheric neutrinos
  Geoneutrinos
  neutrinos from accelerators (Super Beam, Beta Beam)
Water Cerenkov Detector with total fiducial mass: 500 kt:
2 Cylindrical modules 100x65 m
Readout: 22.2k 8” PMTs, 30% geom. cover.
(arXiv: hep-ex/0607026)

## Slide 30: Detector location (LAGUNA)
CERN
ESS

## Slide 31: Physics Performance for Future SB projects (Enrique Fernantez)
CPV
MH
LBNE: 5+5 years, 0.7 MW, 10/35 kt LAr
T2HK: 3+7 years, 0.75 MW, 500 kt WC (5%/10% syst. errors)
SPL: 2+8 years, 4 MW, 500 kt WC (130 km, 5%/10% syst. errors)
ESS: 2+8 years, 5 MW, 500 kt WC (2 GeV, 360/540 km, 5%/10% syst. errors)
C2Py: 20/100 kt LAr, 0.8 MW, 2300 km
unknown MH
360 km
540 km

## Slide 32: Conclusions
ESS is under construction
  very intense source of protons, 5 MW, 2-3 GeV
  more than 1023 protons/year
  well defined schedule
Modifications are needed to transform ESS to neutrino facility
  Double the rate
  Add an accumulator
  Add a target station
  Underground detector (MEMPHYS), mines available
Very promising physics performance using EUROnu optimizations:
  CPV: coverage up to ~60%
  MH: could reach 5 σ combining atmospheric neutrinos
First ESS beam 2019, full power/energy by 2023.
could be the first step towards the Neutrino Factory

## Slide 33: Collaborators are welcome… (just email tord.ekelof@physics.uu.se, marcos.dracos@in2p3.fr )

## Slide 34: Backup

## Slide 35: Possible Detector Locations
Many mines (active or not) are available in Sweden
What is the optimal position for CPV?
How this project could help for MH?
p(nmne)
L/E (km/GeV)
Dm2sun=7.5x10-5 eV2
Dm2atm=2.4x10-3 eV2
q23=41.4°
q12=33.6°
q13=8.8°
E~290 MeV
dCP=-90
dCP=0
dCP=+90

## Slide 36: ESS proton linac
Source: ion (H- ) source, surface-plasma source (magnetron), semi-planatron, surface-plasma source with Penning discharge (Dudnikov-type source), RF volume source, etc. Multi-turn injection from a linac to an accumulator ring.
LEBT: low energy beam transport, matching section between the ion source and the RFQ
RFQ: pre-accelerator, Cockcroft-Walton or RFQ
Chopper: to chop the beam so that it can properly fit into the RF bucket structure in an accumulator. This would greatly reduce the injection loss caused by RF capture.
MEBT: Medium energy beam transport
DTL: Drift tube linac. Low energy part (below 100 MeV, β < 0.4)
Spokes: Spoked Resonator Cavity section
Medium β: Medium energy part (100 MeV - 1 GeV, 0.4 < β < 0.9)
High β: High energy part (above 1 GeV, β > 0.9)
HEBT: Medium energy beam transport
Upgrade: spare space for future upgrades to go up to 3 GeV.

## Slide 37: Spoke Cavities
ESS will transition to superconducting cavities at 88 MeV
ESS will be the first accelerator to use 352 MHz double spoke cavity resonators
Twenty-eight cavities with an accelerating gradient of 8 MV/m are required.
Each cavity will operate at a nominal peak power of 320 kW
What type of power source to choose?
  Tetrode
  Klystron
  IOT
  Solid State

## Slide 38: Elliptical Cavities
Universal Cryomodule
  Cryomodules are expensive and difficult to fabricate
  Pick cavity βg and number of cells
    Optimize power transfer
    Optimize length
  Power in couplers is limited to 1200 MW (peak)
    Medium Beta βg = 0.67
  6 cell cavities
  Cavity length = 0.86 m
  32 cavities packaged in 8 cryomodules
  Maximum peak RF power = 800kW
    High Beta βg = = 0. 86
  5 cell cavities
  Cavity length = 0.92 m
  88 cavities packaged in 22 cryomodules
  Maximum peak RF power = 1100kW

## Slide 39: Elliptical RF System Layout
One cavity per klystron
Two klystrons per modulator
16 klystrons per stub

## Slide 40: Horn Optimization
perfect focusing
present focusing
no focusing
/proton/2GeV/m2
GeV
for 2.5 GeV
the horn is needed
(x7.4 on the ν flux)