## Slide 1: Review of crosstalk between beam-beam interaction and lattice nonlinearity in e+e- colliders
ZHANG Yuan(IHEP), ZHOU Demin(KEK)

## Slide 2: Outline
DAFNE
DAFNE upgrade
KEKB
Super-KEKB
BEPCII

## Slide 3
DAFNE

## Slide 4: DAFNE: Cubic lattice nonlinearity Only one IP
|C11| < 200
M. Zobov, DAFNE Techinial Note G-57, 2001

## Slide 5: DAFNE: Cubic lattice nonlinearity One IP + 2 nearest PC
M. Zobov, DAFNE Techinial Note G-57, 2001
1 IP
1 IP + 2PC
1 IP + 2PC + C11

## Slide 6
DAFNE-Upgrade

## Slide 7
Large Piwinski’s angle F = tg(q/2)sz/sx
Vertical beta comparable with overlap area by 2sx/q
Crab waist transformation y = xy’/q
Crab Waist in 3 Steps
1. P.Raimondi, 2° SuperB Workshop, March 2006
2. P.Raimondi, D.Shatilov, M.Zobov, physics/0702033
physics/0702033
physics/0702033

## Slide 8
Large Piwinski’s angle
F = tg(q/2)sz/sx
2. Vertical beta comparable
with overlap area
by 2sx/q
3. Crabbed waist transformation
y = xy’/q
Crabbed Waist Advantages
Luminosity gain with N
Very low horizontal tune shift
Vertical tune shift decreases with oscillation amplitude
Geometric luminosity gain
Lower vertical tune shift
Suppression of vertical synchro-betatron resonances
Geometric luminosity gain
Suppression of X-Y betatron and synchro-betatron resonances
M.Zobov, C.Milardi， BB’2013

## Slide 9
X-Y Resonance Suppression
Typical case (KEKB, DAFNE etc.):
1. low Piwinski angle F < 1
2. by comparable with sz
Crab Waist On:
1. large Piwinski angle F >> 1
2. by comparable with sx/q
Much higher luminosity!
M.Zobov, C.Milardi， BB’2013

## Slide 10
Dnx
Dnx
Dny
Dny
Crab OFF
Crab ON
Frequency Map Analysis of Beam-Beam Interaction
D.Shatilov, E.Levichev, E.Simonov and M.Zobov
Phys.Rev.ST Accel.Beams 14 (2011) 014001

## Slide 11
DANE Peak Luminosity
NEW COLLISION SCHEME
Design Goal
M.Zobov, C.Milardi， BB-2013
M.Zobov, C.Milardi， BB’2013

## Slide 12
Crabbed Waist Scheme
Sextupole
(Anti)sextupole
Sextupole strength
Equivalent Hamiltonian
IP
M.Zobov, C.Milardi， BB’2013

## Slide 13
Logarithm of the bunch density at IP (z=0).
The scales are  10 sigma for X and Y.
D. Shatilov
M.Zobov, C.Milardi， BB’2013

## Slide 14: Normal form analysis of crabed- wasit transformtaion
One-turn map with beam-beam
One-turn map without beam-beam at IP
There only exist 3rd order generating function：

## Slide 15
KEKB

## Slide 16: Motivation of crab cavity at KEKB
(mA)
Head-on (crab)
First proposed by R. B. Palmer in 1988 for linear colliders.
Crab Crossing can boost the beam-beam parameter higher than 0.15 ! (K. Ohmi)
22mrad crossing angle
Strong-strong beam-beam simulation
nx =.508
Head-on
}
y ~0.15
After this simulation appeared, the development of crab cavities was revitalized.
Luminosity would be doubled with crab cavities!!!
Y. Funakoshi， Beam-Beam Workshop, CERN, 2013

## Slide 17
Y. Funakoshi， Beam-Beam Workshop, CERN, 2013

## Slide 18
Skew-sextupoles
Beam lifetime problem
Y. Funakoshi， Beam-Beam Workshop, CERN, 2013

## Slide 19: General Chromaticity
The chromaticities of Twiss parameters and X-Y couplings
The δ-dependent transverse matrix can be split into the product of two matrices. All the chromatic dependences are lumped into MH(δ)
Generating function F2 is used to represent the transformation of MH(δ). The generating function guarantees the 6D symplectic condition. Hamiltonian which expresses generalized chromaticity is given by
=
+
Alternative way is the direct map for the betatron variables and as
K. Ohmi, ICAP-09
D. Zhou, K. Ohmi, Y. Seimiya etal., PRST-AB 13, 021001, 2010
Y. Seimiya, K. Ohmi, D. Zhou etal,
Prog. Theor. Phys. (2012) 127 (6): 1099-1119

## Slide 21: Scan of first-order chromatic coupling (WS, Crab on)
D. Zhou, et al., PRST-­‐AB 13, 021001 (2010).
Horizontal size
Vertical size

## Slide 22: Chromaticity of x-y coupling at IP
Ohmi et al. showed that the linear chromaticity of x-y coupling parameters at IP could degrade the luminosity, if the residual values, which depend on machine errors, are large.
To control the chromaticity, skew sextupole magnets were installed during winter shutdown 2009.
The skew sextuples are very effective to increase the luminosity at KEKB.
The gain of the luminosity by these magnets is ~15%.
Y. Funakoshi， Beam-Beam Workshop, CERN, 2013

## Slide 23
D. Zhou, 2011

## Slide 27
Super-KEKB

## Slide 29: LER: Simplied IR
Simplified lattice by H. Sugimoto
Sler_simple001.sad: no solenoid but preserve main optics parameters
No significant luminosity degradation at low current
Solenoid is the main source of lattice nonlinearity?
D. Zhou and Y. Zhang(IHEP),
SuperKEKB optics meeting,
Apr.17, 2014

## Slide 30: Lattice nonlinearity from turn-by-turn data
Initial coordinates (x0, 0, 0, 0, 0, 0);
x0 changes from 0 to 5σx
Watch point is at IP, beam-beam is off

## Slide 31: Lattice nonlinearity from turn-by-turn data (Cont.)
Evidence of nonlinear X-Y coupling
COD in Y direction as function of X offset

## Slide 32: Frequency Analysis

## Slide 33: Frequency Analysis (cont.)

## Slide 35: Compensation with a skew-sext map
Test by inserting a map of H=K*x2y into the LER lattice
COD and oscillation amplitude in y are well suppressed as expected

## Slide 36: Compensation with a skew-sext map (Cont.)

## Slide 37: Compensation with a skew-sext map (Cont.)

## Slide 38
BEPCII

## Slide 43: Fringe effect in BEPCII （using SAD）
二极铁
四极铁
超导四极铁
螺线管场
D. Zhou(KEK), 2014

## Slide 44
D. Zhou(KEK), 2014

## Slide 45
原始模型，+边缘场，+LOCO校正
D. Zhou(KEK), 2014

## Slide 46
原始模型，+边缘场，+LOCO校正（cont.）
D. Zhou(KEK), 2014

## Slide 47
D. Zhou(KEK), 2014
亮度： 原始模型 vs 边缘场+LOCO校正
loss~15%

## Slide 48
D. Zhou(KEK), 2014

## Slide 49
D. Zhou(KEK), 2014

## Slide 50: Summary
所有的非线性都已经在“实际”机器中被发现对亮度产生影响：
Detuning
Choromaticity（tune/twiss parameters/coupling）
noraml/skew multipole magnet