## Slide 1
Jean-Christophe Gayde EN/MEF-SU
Guillaume Kautzmann EN/MEF-SU
HIE-ISOLDE
General presentation of the
Monitoring and Alignment Tracking for Hie-IsoLDE
IWAA 2014 – IHEP
October 2014

## Slide 2
Introduction
+
2016

## Slide 3
HIE-ISOLDE SUPERCONDUCTING LINAC
~16m
High Intensity and Energy ISOLDE  Important upgrades of REX-ISOLDE
Goal: Increase the energy and the quality of post-accelerated Ion Beams
Transfer Lines
Introduction
2016
Phase 2

## Slide 4
Alignment specifications
General
Alignment and monitoring of the Cavities and Solenoids in the Cryomodules w.r.to a common nominal beam line (NBL) along the Linac
Permanent system
Common Vacuum and Cryogenics (4.5K) conditions
Precision asked along radial and height axis at 1 sigma level :
  300 microns for the Cavities
  150 microns for the Solenoids
NBL
+/-300 micr
+/-150 micr
~16 m

## Slide 5
RF cavities and solenoid equipped with targets
CONCEPT
Creation of a closed geometrical network continuously measured
Observation and position reconstruction of Cavities and Solenoid in this Network
Pillars
Pillars
Cryo-module
RF Cavity
Solenoid
SYSTEM
BCAM
Metrologic Table
BCAM cameras fixed to inter-module metrological tables
Interface Atmosphere / High Vacuum  Precise viewports
BCAM observations
External Line
External Lines => Position and orientation of metrological tables and BCAMs
Internal Line
Internal Lines => Position of the targets inside the tank
MATHILDE
Proposed Concept

## Slide 6
BCAM
Metrological Table
BCAM to BCAM observations
BCAM to Pillar observations
Pillar
Pillar
Side view
Ext. line
Overlapping
Top view
Overlapping zone of BCAM obs. on external lines
Double sided targets observations on internal lines
=> Redundancy
MATHILDE
Proposed Concept

## Slide 7
Cavity and solenoid support:
  Top Plate Reference
  2 adjustable omega plates per element
  Isostatic interface: hollow Sphere – V-shape
  Cryomodule assembly in ISO Class 5 clean room
     Alignment done with AT401 Laser Tracker + check with MATHILDE
    Once assembled, three levels of alignment:
  Jacks
  Frame
  Independent solenoid
Supporting and Adjustment
Courtesy of: Y. Leclercq (TE-MSC)

## Slide 8
HBCAMs
Developed in 1999 by Brandeis University for ATLAS Muon alignment
OSI (Open Source Instruments)  http://alignment.hep.brandeis.edu/
Original BCAM  HBCAM
Camera focal length: 72 mm  49 mm – 50 mm
Sensor: 336 x 243 pixels 10 micr  659p × 494p, 7.4 microns
Field of view: 40 mrad x 30 mrad  ~ 100 x 70 mrad
Sources: Laser Diodes 650 nm + Calibration of their power to 5mW
Additional synchronized illumination system
Mounting: "Plug-in" isostatic system under the chassis
Double sided model
Cable length BCAM/Driver > 60 m + Connection on the side
From HBCAM2
From HBCAM1
HBCAM vs BCAM Field of view

## Slide 9
HBCAMs
Resolution: 5 micro radians constructor (OSI)  Same range
Accuracy of 50 micro radians to absolute  Same range
Delivered calibrated with respect to the mounting balls
Focus around 1.5m
Tested resolution: 3 micro radians

## Slide 10
Courtesy of: E. Urrutia (EN-MME)
G. Vandoni (TE-VSC)
500mm
1200mm
222mm
318mm
160mm
Integration in a busy space
  Metrology to link the HBCAM mounting balls and fiducial marks
  Special measurable adapter to improve the HBCAMs relative angles obs.
    Table inserted as an ensemble
    Holes to lighten the table (~11kg) whilst keeping rigidity
    Supporting decoupled from the DB and Steerer
Metrologic Table
    BUT…. Still need to be qualified

## Slide 11
20 microns
Distance to target:
1.2 m
Scan over 40% of the field of view
Precision of the reconstructed movement: ~10 microns at one sigma level
Expectation: around 10 urad
Targets
HBCAM Measurement

## Slide 12
Outgassing at background level for an equivalent of 20 Ø4mm balls or 80 Ø2 mm balls.
Cryo-test:
  Down to 5 k and 40•10-6 mbar, HBCAM measurements OK
  No damages or unexpected behavior noticed
    Outgassing test done by Mario Hermann (TE/VSC)
Targets
Cryogenic and Vacuum Behavior

## Slide 13
Based on Ø4mm glass balls
Titanium made narrow silhouette (6mm)
Interface with Omega plate:
  V-Groove  Lateral position
  Pin  Height blocking
  Screw  Fixation
  Double sided
  Flashed by HBCAM Lasers
    Multi-ball targets
    5 different lengths/CM
    Good geometrical results
    High vacuum compatible
    Cryogenic conditions compatible
Targets
Final Design

## Slide 14
Targets need to cross the thermal shield
  Addition of 2 thermalized alignment corridors:
  Holes to allow target envelopes to cross it
  Minimal addition to the heat budget
  Still visible from upstream/downstream HBCAMs
  Walls covered with anodized aluminum plates
Targets
Thermal Shield Crossing
Courtesy of: J. Dequaire (EN-MME)

## Slide 15
A viewport with an angle:
    Viewport with 5 degree angle w.r.t. the HBCAM axis
     Avoiding parasitic reflection for passive target observation
     Viewport mounted with a 5 deg. angle in the flange
    Minimum rotation values:
    Around Y 3 deg.
    Around X 2 deg.
Viewports
Orientation

## Slide 16
Atmosphere / Vacuum interface
6.55 mm thick
Studied and validated for:
  Wedge angle
  Parallel plate effect
  Deformation due to vacuum
Angle w.r.t HBCAM axis ≈ 5 deg
Integrated in the viewport design
Special request to the manufacturer
Effect corrected by software
 Viewport for 2 CM delivered and validated
Viewports
Summary

## Slide 17
Each element has a specific coordinate system atached
even a point or a viewport
Hierarchical scheme of coordinates systems :
  Topmost: HIE system  Link to the NBL
  For each table: Table system  Link between the HBCAMs
  For each HBCAM: Mount system  Calibration parameters
  CDD System  Observation
  Pivot point, lasers sources,....
MATHIS Software
Coordinate Frames

## Slide 18
Translations and rotations for each table need to be estimated: 6 parameters per table in the setup
Relations between mount systems on the same table are fixed
 Tables considered as a floating rigid body
MATHIS Software
Parameter Adjustment
Highly Versatile and Flexible Principle
Can Virtually create any configuration with BCAM type sensors
7 Table conf. reconstruction within 20 micr. at 1 sigma level ( IWWA2012)

## Slide 19
Geometrical conf.
Observation conf.
Description of the full system by 3 XML files
LWDAQ Script
Complete
Geometrical conf.
LGC V2
Automatically generates
Correction for frame thermal retractions
T from CERN DB
LWDAQ
Input file for LGC V2
Only temperature data
Observation and computation scheme
HBCAM calibration parameters
Observations on targets
Pre-Processing:
Viewport crossing correction
Glass ball target center reconstruction
Measurements averaging
- etc…
PRE-PROCESSING
Data formatting
Results sent to DB and to Control room
Sensor Param
Least square adjustment
MATHIS Software
Data Flow

## Slide 20
MATHIS Software
Graphical User Interface

## Slide 21
ALIGNMENT SYSTEM MAINLY VALIDATED
HBCAMs
  Proved and used devices
  HBCAM developed, validated and procured
METROLOGICAL TABLE
  Integrated in the Inter-Tank area
  Close to final design
VIEWPORTS
  Fit well to the theory  Easy BCAM observation corrections
  High optical quality needed
  Delivered and validated
TARGETS
  Passive glass balls
  Targets ordered
SOFTWARE
  Development on-going
  Use of LGC V2
Conclusion

## Slide 22
This research project has been supported by a Marie Curie Early Training Network Fellowship of the European Community’s Seventh Framework Programme under contract number (PITN-GA-2010-264330-CATHI).
Official partners :
Brandeis University, Faculty of Physics (USA): J. Bensinger, K. Hashemi
Top Tec and technical university of Liberec (CZ): M. Šulc
Acknowledgement
Y. Leclercq, J. Dequaire, G. Vandoni, S. Maridor, S. Rokopanos, T. Basilien, F. Klumb, S. Waniorek, D. Duarte Ramos, M. Herrmann, E. Urrutia… All others involved in HIE-ISOLDE Project

## Slide 23
Thanks for your attention
谢谢
MATHILDE

## Slide 24
HBCAMs

## Slide 25
    Studied Target Types
    Silica Silica optical fiber end
      - feed-through needed, one-sided target
    + easy light level control, OK with cold and vacuum (tested)
    Silica ilica optical fiber ended by a ceramic ball
    - feed-through needed, connection fiber/ball
    + visible from all positions, good diffuser
    Retro-reflective targets
        - illumination needed, all targets in one shot
        + double-sided, passive target, no feed-through
Constraints  HIGH VACUUM - CRYO CONDITIONS - SIZE
Targets
Different options

## Slide 26
    Three types of “double sided” targets considered
Double sided retro-reflective target Prototype
But Not High-Vacuum compatible
Test prototype for an illuminated ceramic ball synchronized to the acquisition system
But Active targets
Retro-reflective bi-directional target
Laser illuminated ceramic balls
Retro-reflective Glass ball target
Targets
Different options

## Slide 27
From HBCAM2
From HBCAM1
HBCAM vs BCAM Field of view
Targets
Spatial Distribution

## Slide 28
Targets
Planification of a radiation test
    Collaboration with Institute for Nuclear Research Atomki (Debrecen – Hungary)
Fluka Simulation On-Going
Up to 5kGy
  Real test done in the near future

## Slide 29
1 x
1 x
Stainless steel spring
4 x
2 x
1 x
1 x
Ø4mm Ceramic Ball
Ø4mm glass Ball
Ø2mm Stainless steel pin
Titanium target plug
Titanium target body
Targets
Final Design : Components

## Slide 30
Wedge angle
    10 microrad wedge angle acceptable
    Parallel Plate Effect
    Incident angle change of 1gon (0.9deg)  37 microns radial object “displacement”
    Match the theory by a few microns  Easy observation correction by software
Window | Given wedge angle (microrad) from window’s technical data | Wedge angle observed (microrad) | Influence on target at 1m (micr) | Influence on target at 2m (micr)
A | 25 | 5 | 2.5 | 5
B | 50 | 10 | 5 | 10
C | 500 | 300 | 150 | 300
    Vacuum deformation
    Less than 7 microns deformation at the center
    Less than 0.015 degree of angular deviation
    Deformation measurements Liberec University (CZ):
      Results match the calculated deformations by a few microns
      Same deformation on both side  Parallelism kept
Viewports
Studies

## Slide 31
GUI developed
 Automated generation of the XML Files
Geometrical (frame hierarchy,..)
Observation configuration
…
MATHIS Software
Graphical User Interface

## Slide 32
MATHIS Software
Software checking small Bench

## Slide 33
Σ02=0.0117 | σty [μm] | σtz [μm] | σrx [μrad] | σry [μrad] | σrz [μrad]
0 | 0.49 | 0.53 | 1.54 | 3.51 | 1.2
1 | 9.19 | 10.72 | 34.5 | 4.16 | 3.78
2 | 12.72 | 15.38 | 38.2 | 3.59 | 3.39
3 | 13.67 | 16.87 | 38.02 | 2.82 | 2.69
4 | 12.73 | 15.6 | 38.27 | 3.56 | 3.39
5 | 9.21 | 11.01 | 34.54 | 4.18 | 3.78
6 | 0.9 | 1.07 | 3.18 | 3.93 | 1.23
20 microns
Overlapping improves the results by a factor 2
Still some error budget for the reconstruction of the targets
MATHIS Software
Simulation Results
Test result using a computation shell prototype