## Slide 1: Constraints on the FCC-ee lattice from the compatibility with the FCC hadron collider
Bastian Haerer (CERN, Geneva; KIT, Karlsruhe), Wolfgang Bartmann, Michael Benedikt, Bernhard Johannes Holzer, John Osborne, Daniel Schulte, Rogelio Tomas, Jorg Wenninger, Frank Zimmermann (CERN, Geneva), Michael James Syphers (MSU, East Lanning, Michigan), Ulrich Wienands (SLAC, Menlo Park, California)

## Slide 2: Future Circular Collider Study

## Slide 3: Future Circular Collider Study
Consists of three sub-studies:
FCC-hh: 100 TeV proton collider
FCC-ee: 91-350 GeV lepton collider
FCC-he: electron-proton option
Each study has its own requirements, but technology for FCC-hh is most challenging!

## Slide 4: Constraints on FCC-hh
Magnet technology (Nb3Sn)
Shape (racetrack vs. circle)
Geology
Overlap with LHC (if used as injector)
Injection, beam dump, experiments
Not covered today:
Constraints from housing FCC-hh and FCC-ee in the tunnel at the same time
Constraints from FCC-he

## Slide 5: 1) Bending radius
Proton beam energy: 50 TeV
Beam rigidity: Bρ = p/e ≈ 1.67×105 Tm
B = 20 T:  ρ = 8.5 km
B = 16 T:  ρ = 10.7 km
B = 16 T achievable with Nb3Sn technology!
(FCC-ee: B = 55 mT)

## Slide 6: 2) Circumference
Approx. 67% of circumference C are bends:
B = 20 T, ρ = 8.5 km  C = 80 km
B = 16 T, ρ = 10.7 km  C = 100 km
RF frequency should be a multiple of RF frequency of LHC (bunch to bucket transfer)
 C = 3×26.7 km = 80.1 km
 C = 4×26.7 km = 106.8 km

## Slide 7: 3) Layout objectives
Hadron machine
Max. momentum limited by
 High fill factor
 As few straight sections as possible
Lepton machine
Limited by synchrotron radiation power
 High fill factor
 High bending radius
 Many straight sections for RF to limit sawtooth effect

## Slide 8: FCC-ee: Sawtooth effect
12 RF sections
4 RF sections
Energy loss per turn
(175 GeV beam energy): U0 = 7.7 GeV (4.3 %)

## Slide 9: 4) Shape
Circular shape (like LHC)
Preferred for lepton collider
Racetrack (like SSC)
Most of the infrastructure can be concentrated at two main sites
Chromaticity correction easier
A
Courtesy: John Osborne et al.

## Slide 10: 5) Geology
Boundary Limits:
East: Pre-Alps
South: Rhone, Vuache Mountain
West: Jura
North: Lake Geneva
Courtesy: John Osborne

## Slide 11: Lake Geneva
The lake gets deeper to the North
The Molasse rockhead as well
 The tunnel level must be deeper in the earth
Riverbed
Molasse Rockhead
370
320
210
mASL
Courtesy:
John Osborne

## Slide 12: 80 km circle
Courtesy:
John Osborne, Yung Loo

## Slide 13: 100 km circle
Courtesy:
John Osborne, Yung Loo

## Slide 14: Tilting the tunnel
LEP/LHC: 1.42 %
 Maximize tunnel extend in Molasse, minimize tunnel extend in Limestone and Moraines
 Minimize the depth of the access shafts
P3
P1
P7
(450m)
(359m)
(350m)
Courtesy: John Osborne
Limestone

## Slide 15: 100 km circle with tilt
Courtesy:
John Osborne, Yung Loo

## Slide 16: 6) Location relative to LHC
Required distance L for transfer lines depends on:
Difference in depth d
Magnet technology
Courtesy: W. Bartmann
LHC
FCC
d
L
Beam energy
Max. slope of tunnel 5%
FCC and LHC should overlap, if LHC is used as injector

## Slide 17: Distance for transfer lines
Required length: L = 500 – 1500 m
3.9 T Tevatron dipoles
2.6 T CF JPARC magnets
1.8 T TI 2/8 dipoles
Beam energy: 3.5 TeV
Filling factor: 0.75
8.3 T LHC dipoles
Courtesy:
Wolfgang Bartmann
d
L

## Slide 18: 7) Length of Long Straight Sections
Space for septum, kicker magnet and absorbers for machine protection
Injection: Energy: 3.5 TeV
600 m
Beam dump: Energy: 50 TeV
800 m – 1000 m (?)
Collimation?

## Slide 19: 8) Experiments

## Slide 20: FCC-hh Interaction Region
Interaction region (IR) design for
Huge Detectors
 L* = 46 m !!!
Length of single IR:  ≈ 1100 m
Small crossing angle:  11 μrad
 β* = 1.1 m
Court. R. Alemany, B. Holzer
β (m)

## Slide 21: FCC-ee Interaction Region
βy* = 1 mm, L* = 2 m !!!
Large crossing angle
 30 mrad, 11 mrad
IR even longer
More about IR design:
Roman Martin’s presentation
Local chromaticity
correction scheme

## Slide 22: Current FCC-ee design
Circular shape,
100 km circumference
12 straight sections
 Length: 1.5 km
4 experiments
Length of arcs: 6.8 km
 ρ ≈ 10.6 km
RF
RF
RF
RF
RF
RF
RF
RF
RF
RF
RF
RF
IP
IP
IP
IP
Details of the FCC-ee lattice were presented yesterday in my other talk

## Slide 23: Resume
Magnet technology sets constraints on bending radius and circumference
Injection, beam dump, collimation and experiments define length of the straight sections
Compromise for the layout must be found
Geology and transfer lines define location of FCC

## Slide 24
Thank you for your attention!
Court. J. Wenninger

## Slide 25: Unequally distributed RF

## Slide 26: Experiments FCC-ee
Completely different IR design:
Large crossing angle
βy = 1 mm, L* = 2 m !!!
Local chromaticity correction scheme
IR length: even larger
More about IR design:
Roman Martin’s presentation
Court. R. Martin

## Slide 27: FCC-he design parameters

## Slide 28: LHeC: IR layout
A similar interaction scheme needs to be designed for FCC-he
Courtesy Max Klein