## Slide 1: HF2014 WG4 Summary “Synchrotron Radiation and Shielding”
Marica Biagini (INFN-Frascati)
John Seeman (SLAC)
October 12, 2014
HF2014 IHEP Beijing

## Slide 2: Synchrotron Radiation and Shielding Talks Presented
Z. Ma (IHEP): Monte Carlo Simulations of Synchrotron Radiation for CEPC Vacuum System
R. Kersevan (CERN): Vacuum System requirements for a HF e+e- Accelerator
Y. Papaphilippou (CERN): Synchrotron Radiation Effects in the HF Injector
L. Esposito (CERN): Shielding of Electrons in the Tunnel
M. Maltseva (TENZOR): Infrared Synchrotron Methods and Systems for Monitoring and Controlling Particle Beam in Real Time
M. Boscolo (INFN-Frascati): Lost Particles in the IR and Beam Induced Backgrounds in a Higgs Factory
J. Seeman (SLAC): Synchrotron Radiation Absorption and Vacuum Issues in the IR

## Slide 3: Ma: CEPC Vacuum Layout and Radiation Effects

## Slide 4: Ma: Radiation protection topics:
Synchrotron radiation shielding
The thickness of the main tunnel
Shielding for straight tunnel, beam dump, collimate station, injection section, maze, duct, shielding doors, RF station, etc;
Induced radioactivity analysis: cooling water, ventilation air, accelerator component, local shielding concrete, ground water, environmental samples, etc;
Personal safety interlock system
Radiation dose monitoring system

## Slide 5
Ma: Limits for shielding design of CEPC-sPPC
Area | Design Value | example
Radiation monitored area | < 2.5 μSv/h | Outer of the tunnels, where worker can stay long
Radiation controlled area | < 25 μSv/h | Outer of the tunnels, where worker can stay occasionally
Forbidden area | >>1mSv/h | Inner of the tunnels, worker cannot get in during accelerator operation
Site boundary | 0.08 mSv/year | 
All the areas should be clearly defined after the functional structures are determined.

## Slide 6
Simulation model for beam pipe
Synchrotron radiation source analysis
Solid degree of synchrotron radiaiton：<10-5rad
Bending angle Between beam and SR: 3.1669 mrad
The cros section of vacuum chamber
(Above: Al&Pb Below: Cu)
LEP’s Vacuum chamber was adopted:
But two materials: Composed by a few millimeters of Al covered by 3 or 8mm of Pb or totally by a few millimeters of Cu
Synchrotron radiation hits the vacuum chamber at a grazing angle of 3.1669mrad
Ma: MCNP simulation

## Slide 7
Energy of most of photons is between 100keV and 300keV
The flux out of Cu is obviously lower than Al&Pb’s.
The mass attenuation coefficients of Cu are between Al and Pb
Vacuum chamber fabricated by Cu may instead of Al and Pb
The spectrum of photons in the air
Mass attenuation coefficients
Ma: Simulations

## Slide 8: Ma: Summary and Future Tasks
The dose rate in the tunnel for CEPC is mainly dominated by synchrotron radiation.
Above 65% heat were deposited in the chamber
Cu may be a good material for beam pipe from the point of radiation protection, also have to be consider from the manufacture/price and other point of view
Dose rate, which level to be deduced is depend on the radiation resistant of the electron component
Detailed simulation have to be conducted next: reliability verification, actual structure, thermal analysis, etc.

## Slide 9: Kersevan: Requirements on HF Vacuum Systems

## Slide 10
R. Kersevan, “Vacuum System Requirements for a HF e+e- Accelerator – 55th ICFA – Beijing – 10 Oct 2014
SR fan at FCC-ee 90x30 mm2 1/2x FODO cell (25 m)
Distributed SR fan vs localized absorbers: Ray-tracing (SYNRAD+)
Photon fan profiles converted into outgassing profiles via h(mol/ph)
Pressure profile calculation via 3D Montecarlo code (Molflow+)

## Slide 11
Kersevan: Conclusions
Any design of a Higgs Factory with beam energies in the 45~175 GeV range inevitably makes a powerful source of SR
Comprehensive ray-tracing analysis of SR fans: mandatory! Especially for delicate areas, such as IR, SRF, wigglers!
Careful choice of vacuum chamber material
Vacuum system geometry and pumping system must be carefully analysed and designed
Special care has to be taken for any cross-sectional changes (tapers), and devices (BPMs, stripline kickers, RF cavities, gate-valves, etc…): proper shielding from SR and cooling for HOMs
The operation of LEP and B-factories, and the design of low-emittance light sources can help a lot in the design of a HF’s vacuum system
The chamber vs chamber/antechamber solutions must be carefully evaluated
The distributed vs discrete pumping solutions must be carefully evaluated
Low-SEY coatings for e-cloud in the e+ beam chamber
Although not easy to implement, in-situ bake-out is recommended
R. Kersevan, “Vacuum System Requirements for a HF e+e- Accelerator – 55th ICFA – Beijing – 10 Oct 2014

## Slide 12: Papaphilippou: HF Injector SR Considerations

## Slide 13: Papaphilippou: HF Injector

## Slide 14: Papaphilippou: Injector possibilities

## Slide 15: Papaphilippou: Outlook

## Slide 16: Esposito: Tunnel Shielding-- What are we talking about?
Electronics
Ventilation Units
CV,crane,
fire
Gy per 4.5 1019 p.o.t.
CNGS 2007 physics run, 8 1017 p.o.t. delivered ( 2% of a nominal CNGS year )
Single event upsets in ventilation electronics caused ventilation control failure and interruption of communication
Predicted dose levels
in agreement with measurements
R2E=Rad to Electronics

## Slide 17: Mitigation Options
SHIELDING
RELOCATION
CIVIL ENGINEERING
RAD-TOL DESIGN

## Slide 18: R2E Project Building Blocks
Calculations
Radiation Tests
Production & Implementation
Radiation Monitoring
Developments
Test Facilities

## Slide 19: Esposito: Radiation field in the FCC tunnel
Neutrons from photo-nuclear interactions

## Slide 20: Radiation levels in FCC-e+e-
LHC + Experiments
FCC-e+e-
FCC-e+e-
FCC-e+e-
20
COTS Systems
Hardened Electronics
Electronics
Damage
Custom Boards with COTS

## Slide 21: Esposito: Conclusions
R2E represents a crucial issue to be taken into account as design criterion of any high energy and intensity machine
The R2E project at CERN allowed to create a diffuse knowledge and expertise covering all the aspects of radiation hardening
Total Integrated Dose effect has to be mitigated through a carefully shielding design

## Slide 22: Maltseva: Synchrotron Radiation Diagnostics

## Slide 23: Maltseva: SR Diagnostics
Important to have:
Non-destructive monitors
High resolution IR optical devices
Wide spectral range
Distributions of SR power can be calculated
Use modern devices for infrared and ultraviolet
Computerized optoelectronics (>100 microseconds)
Spectrometric detection systems (0.4 – 40 microns)
Non-cryogenics systems

## Slide 24: Boscolo: IR Particle Losses and Beam Backgrounds

## Slide 25: Boscolo: Energy Acceptance Important

## Slide 26: Boscolo: Touchek

## Slide 27: Boscolo: Beam-Gas

## Slide 28: Boscolo: Radiative Bhabha

## Slide 29: Boscolo: IR SR

## Slide 30: Boscolo: Conclusions

## Slide 31: Seeman: CEPC Horizontal Trajectory near the IR

## Slide 32: Bends (Quads) make X-ray fans: PEP-II IR HER X-ray Fans (M. Sullivan)

## Slide 33: Seeman: Design vacuum chamber masking for power absorption, backgrounds, and HOMs
PEP-II IR masking near BaBar

## Slide 34: WG4: Key Future Topics :SR+Shielding in a Higgs Factory
Stabilize the storage ring parameters so that the injector parameters and power losses will stabilize.
Carryout the next layer of design of the injector chain
Develop a tunnel design with shafts/cranes/CV etc to study surrounding radiation effects and electronics shielding
Design a vacuum system for the hard areas: SCRF, injection, IR, wigglers
Need a next layer (realistic?) of IR design.
Study in detail the SR power lost in the Interaction Region
Develop a vacuum pumping scheme for the IR.
Develop a masking scheme for the detector from x-rays and lost particles.
Develop non-destructive diagnostics with wide spectral range and high sensitivity.