## Slide 1: SuperKEKB background simulations ~including issues for detector shielding~
Hiroyuki Nakayama (KEK), on behave of SuperKEKB/Belle II collaboration
Oct. 10th, 2014
HF2014 workshop in Beijing
This presentation is supported by (公) 高エネルギー加速器科学研究奨励会
7GeV(e-), 4GeV(e-)

## Slide 2: Beam background at SuperKEKB
At SuperKEKB with x40 larger Luminosity, beam background will also increase drastically.
  Touschek scattering
  Beam-gas scattering
  Synchrotron radiation
  Radiative Bhabha event: emitted g
  Radiative Bhabha event: spent e+/e-
  2-photon process event: e+e-e+e-e+e-
  etc…
e-
e+
e-
Beam-origin
Luminosity dependent
Notes: In this slide, I have listed up variety of possible beam background sources at SuperKEKB.
Among these background sources, so-called “Touschek scattering” will be the most difficult one to cope with, which I will explain in more detail in the following slides.

## Slide 3: 1.Touschek scattering
Intra-bunch scattering : Rate∝(beam size)-1,(Ebeam)-3
Touschek lifetime: assume 600sec (required by injector ability)
 total beam loss: 375GHz (LER), 270GHz(HER)
Horizontal collimators to reduce loss at IR (|s|<4m)
  collimators before IP (|s|<200m) are very effective
Collimator width
  Initial values:
  Further optimization to balance IR loss and beam lifetime
  Smaller loss rate on the final collimators (|s|<20m) is preferred
After careful optimization of collimators, IR loss is <0.3GHz now
  3 orders smaller than ring total loss

## Slide 4: 2.Beam-gas scattering
Brems
Coulomb
Scattering by remaining gas, Rate ∝IxP
Due to smaller beam pipe aperture and larger
maximum by, beam-gas Coulomb scattering could be more dangerous than in KEKB
 | KEKB LER | SuperKEKB LER
QC1 beam pipe radius: rQC1 | 35mm | 13.5mm
Max. vertical beta (in QC1): by,QC1 | 600m | 2900m
Averaged vertical beta: <by> | 23m | 50m
Min. scattering angle: qc | 0.3mrad | 0.036mrad
Beam-gas Coulomb lifetime | >10 hours | 35min
66s
85s
Physical aperture
(vertical)
SuperKEKB LER
e+
mm
[m]

## Slide 5: Where we should put vertical collimator?
> 1.44 mA/bunch (LER)
We should put collimator where beta_y is SMALL!
TMC instability should be avoided.
Kick factor
beta[m]
d[mm]
Aperture
TMC:
Collimator position
taken from “Handbook of accelerator
physics and engineering, p.121”
(in case of rectangular collimator window)
Collimator aperture should be narrower than QC1 aperture.
Assuming following two formulae:
For more details , please check out following paper:
H. Nakayama et al, “Small-Beta Collimation at SuperKEKB to Stop Beam-Gas Scattered Particles and
to Avoid Transverse Mode Coupling Instability”, Conf. Proc. C 1205201, 1104 (2012)
Notes: d[mm], beta[m]
beta* 12.5/sqrt(d^3) < 470  sqrt(d^3) < beta * 12.5 / 470  d < (beta*12.5/470)^(2/3)
d/1000/sqrt(8.64e-12*beta)) > 65  d > 65 * sqrt(8.64e-6*beta)
betax8, dx4,Nsigmaxsqrt(2)

## Slide 6: Candidate collimator locations
(r=10.5mm)
r=13.5mm
TMC condition
beta_y [m]
(r=10.5mm)
r=13.5mm
TMC condition
Collimator width d[mm]
beta_y [m]
LER
HER
  V1 collimator @ LLB3R (downstream)
  (s=-90-82m, by=30146m)
  by=125m, 2.23mm<d<2.81mm
  V1 collimator @ LTLB2 (downstream)
  (s=-63-61m, by=81187m)
  by=123m, 1.74mm<d<2.26mm
herfqlc5605
lerfqlc_1604
Collimator position should satisfy beta_y condition above,
need space(at least 1.5m), and the phase should be similar to QC1
Ny(V1)= 42.82, Ny(QC1)= 44.32
Ny(V1)= 1.25, Ny(QC1)= 0.25

## Slide 7: Vertical collimator width vs. Coulomb loss rate, Coulomb life time
her5365,V1=LTLB2 downstream |  |  | 
V1 width[mm] | IR loss [GHz] | Total loss[GHz] | Coulomb life[sec]
2.10 | 0.0007 | 49.6 | 3294.0
2.20 | 0.001 | 45.2 | 3615.2
2.30 | 0.357 | 41.0 | 3951.3
2.40 | 7.99 | 33.0 | 3985.9
2.50 | 13.1 | 27.9 | 3985.9
ler1604, V1=LLB3R downstream |  |  | 
V1 width[mm] | IR loss [GHz] | Total loss[GHz] | Coulomb life[sec]
2.40 | 0.04 | 153.9 | 1469.8
2.50 | 0.05 | 141.8 | 1594.8
2.60 | 0.09 | 131.0 | 1724.9
2.70 | 0.24 | 121.4 | 1860.2
2.80 | 1.65 | 111.4 | 2000.5
2.90 | 11.48 | 100.8 | 2014.3
3.00 | 21.98 | 90.3 | 2014.3
Based on element-by-element simulation considering causality the phase difference (by Nakayama)
IR loss rate is VERY sensitive to the vertical collimator width.
(Once V1 aperture>QC1 aperture, all beam loss goes from V1 to IR
Typical orbit deviation at V1 : +-0.12mm (by iBump V-angle: +-0.5mrad@IP )
Up to 100turns

## Slide 8: SuperKEKB Collimators Location
HER
D12: H1, H2, H3, H4
(V1, V2, V3, V4)
HER
D09: H1, H2, H3, H4
(V1, V2, V3, V4)
D02
D03
D04
D05
D06
D07
D08
D09
D10
D11
D12
D01
LER
D06: H1, H2, H3, H4
LER
D02: H1, H2, H3, H4,
V1 for Beam-gas
LER
D03: H1, H2
(V1, V2)
HER
D01: H1, H2, H3, H4, H5,
V1 for Beam-gas
T. Ishibashi (KEK)
~20 Horizontal collimators and 2 Vertical collimators
Each collimator can be asymmetric
Need to control ~50 parameters!
Hiroyuki Nakayama (KEK)
Higgs Factory 2014, 10th Oct. 2014, Beijing
8

## Slide 9: Collimator Design Concepts
KEKB type
SuperKEKB type
Part of the movable heads is hidden inside the antechambers to reduce the impedance.
Need to get space for installations of HOM absorbers and bellows up/downstream of the collimators.
Have to avoid the trapped-modes.
Total length ~ 1000 mm.
T. Ishibashi (KEK)
Hiroyuki Nakayama (KEK)
Higgs Factory 2014, 10th Oct. 2014, Beijing
9

## Slide 10: Basic Collimator Structure
SLAC PEP-II collimators as a reference.
The chamber and the heads are made from copper.
The strokes of the movable heads are d=5-25 mm in horizontal and 2-12 mm in vertical. (“d” refers to the distance between the central beam axis and the tip of the head.)
Tungsten is jointed at the tip of the head with Hot Isostatic Press(HIP, already succeed in the test).
RF fingers are attached between the heads and chambers.
ramp ~12°
cooling channel
tungsten on tip
tapered beam pipe
bellows
T. Ishibashi (KEK)
Hiroyuki Nakayama (KEK)
Higgs Factory 2014, 10th Oct. 2014, Beijing
10

## Slide 11: Collimator Prototype
A prototype of the SuperKEKB type horizontal collimator was manufactured.
We’ve improved supports for the movable heads, RF fingers and so on through tests.
T. Ishibashi (KEK)
Hiroyuki Nakayama (KEK)
Higgs Factory 2014, 10th Oct. 2014, Beijing
11

## Slide 12: Vertical Collimators
To reduce IR loss of beam-gas Coulomb BG, very narrow (~2mm half width) vertical collimator at by=~100m is required
TMC instability is an issue, low-impedance design of collimator head is important
Only one collimator per ring, so precise (~50um) control of collimator width is important (otherwise IR loss rapidly increases)
Should withstand ~100GHz loss (tungsten)
Secondary shower (tip-scattering) study is important
Hiroyuki Nakayama (KEK)
Higgs Factory 2014, 10th Oct. 2014, Beijing
12

## Slide 13: 3. Synchrotron radiation
Beam pipe design
Ridge structure
f20mm
f9mm
e-
e+
IP beam pipe (Ti/Be/Ti)
incoming/outgoing beam pipe (Ta)
f20mmf9mm collimation on incoming beam pipes (no collimation on outgoing pipes)
Most of SR photons are stopped by the collimation and direct hits on IP beam pipe is negligible
HOM can escape from outgoing beam pipe
To hide IP beam pipe from reflected SR, “ridge” structure on inner surface of collimation part.
13
Notes: Moving on to the next, I would like to show our optimized beam-pipe design to stop SR background.
Incoming part of beam pipe is collimated from f20mm to f9mm, therefore most of SR photons coming from upstream can be stopped by this collimation and direct hits on IP beam pipe, made of Beryllium, are negligible.
We don’t have to worry about HOM trap, since the outgoing pipes are made straight and HOM can escape .
It is also worthwhile to note that “ridge” or “saw-tooth” structure is set on the inner surface of collimation part to avoid the reflected SR hitting the IP beam-pipe.
The expected SR background of the inner detector is much smaller than the minimal requirement, so we are satisfied with this clever design of beam-pipe.

## Slide 14: “Ridge” structure
Al mockup
To hide IP beam pipe from reflected SR

## Slide 15: 4. Luminosity-dependent background
Radiative Bhabha
  Rate∝Luminosity (KEKBx40)
  Spent e+/e- with large DE could be lost inside detector
  Neutrons from emitted g (hitting downstream magnet)
  BBBREM (beam-size effect included)
2-photon process
  Generated e+e- pair might hit PXD (or SVD)
  Confirmed to be tolerable, according to
  KoralW/BDK simulation and KEKB machine study
Notes: Touschek/beam-gas background is coming from each beam.
Next background source is coming from collision of two beams,
proportional to Luminosity.
After radiative Bhabha collision at IP, both spent beam particle and emitted gamma contribute to background.
2-photon process via this Feynman diagram is simulated to be small enough.
The simulation validity is confirmed by machine study at KEKB.

## Slide 16: Final focusing magnets
QC2LE
QC2LP
QC1LE
QC1LP
QC1RP
QC1RE
QC2RP
QC2RE
IRON
IRON
IRON
IP
IP
  q =83mrad
  q =22mrad
Larger crossing angle q
Final Q for each ring more flexible optics design
No bend near IP less emittance, less background from spent particles
Solenoid axis
Notes: Although there are a number of features of the accelerator upgrade, here, let me pick up the design of final focusing magnet.
The crossing angle is changed to be much larger than that of KEKB, so that each rings can have their own final q magnet.
This will lead to flexible adjustment of orbit design.
The another benefit from independent final q magnet is that the bend by downstream Q magnet which existed at KEKB will disappear.
This will realize less emittance without dispersion coming the bend close to IP,
and also lead to less background such as SR at downstream magnet or over-bent spent electron from Radiative Bhabha event, which is expected to be the dominant BG of Italian SuperB.

## Slide 17: Spent e+/e- loss position after RBB scattering
e+
LER(orig. 4GeV)
e-
HER(orig. 7GeV)
If DE is large and e+/e- energy becomes <2GeV,
they can be lost inside the detector (|s|<4m)
due to kick from detector solenoid with large crossing angle

## Slide 18
 | LER (4GeV e+) | HER (7GeV e-)
Rad. Bhabha | 0.74 W (eff. 1.2GHz) | 0.59W (eff. 0.52GHz)
Touschek | 0.078W (0.12GHz) | 0.02 W (0.02 GHz)
Coulomb | 0.18 W (0.28GHz) | 0.001W (0.001GHz)
BG loss distribution
1GeV ,1GHz
= 0.16W
HER
(e-)
LER(e+)
Ver. 2014.6.18
(9th campaign)
Loss wattage
= loss rate
* energy of loss particle

## Slide 19
Background picture
SR
Touschek LER
RBB LER
Coulomb HER
Touschek HER
RBB HER
Ver. 2014.6.18
HER(e-)
LER(e+)

## Slide 20
Tungsten shields inside final-Q cryostat
tungsten (10mm t)
tungsten
QC2RP
QC2RE
QC1RP
QC1RE
tungsten
(20~70mm t)
e+
e-
tungsten(~30mm t)
tungsten (50mm t)
tungsten (10mm t)
e+
e-
Major beam loss position
by Touschek or Beam-gas
Thick tungsten shields can significantly stop background showers originated from |s|>65cm.
1m
-1m
IP
IP

## Slide 21
VXD docks
VXD docks
17°
Neutron shield to protect HAPDs in ARICH
Other shielding
Neutron shield for FPGAs on CDC elec. board.(Polyethylene)
Remote Vacuum Connection structure in front of QCS reduces showers from RBB loss at |s|~60cm (6cm-thick SUS)
ECL shield, for included for (Lead + Polyethylene)
Iron
Iron
Heavy metal shields to protect VXD
from showers generated in cryostat
ECL
CDC
Thick tungsten layers inside cryostat
(Bron-doped Polyethylene)
Notes: <R-side>
ARICH: r>44cm, blue: 38<r<44cm, green: 44<r<50cm, ECL, r>44cm, red: 42<r<47cm, dock: r=39.9+-2.5cm
iron: r=50->36.7cm, QCS: R=39->34.7cm
<L-side>
ECL, r>45cm, red: 46.5<r<51.5cm, dock: r=35.5+-2.5cm
iron: r=50->27cm, QCS: R=39->25cm
Svd-dock: x=-135~103(235), y=-32~56(90), z-210~175(390)

## Slide 22: Full-detector GEANT4 simulation
Whole Belle II detector implemented in our software framework based on GEANT4

## Slide 23: Simulation tools
BG type | BG generator | Tracking (till hitting beam pipe) | Detector simulation
Touschek/Beam-gas | Theoretical formulae [1] | SAD [2] | GEANT4
Radiative Bhabha | BBBREM [3] | SAD (for e+,e-) GEANT4 (for g) | GEANT4
2-photon | Diag36 (“BDK”) [4] | GEANT4 | GEANT4
Synchrotron radiation | Physics model inside GEANT4 | GEANT4 | GEANT4
[1] Y. Ohnishi et al., PTEP 2013, 03A011 (2013).
[2] SAD is a “Home-brew” tracking code by KEKB group, http://acc-physics.kek.jp/SAD/
[3] R. Kleiss and H. Burkhardt, Comput. Phys. Commun. 81, 372 (1994)
[4] F. A. Berends, P. H. Daverveldt and R.Kleiss, Comput. Phys. Commun. 40, 285 (1986).

## Slide 24: Background simulation check list
Degrade data quality
  Tracking precision (CDC hit rates)
  Particle-ID precision (TOP, ARICH rates)
Eat-up readout bandwidth
  PXD occupancy should be <2%
Damage components during years of operation
  Radiation dose on electronics, crystals, etc..
  Neutron fluence on Si devices (HAPD, FPGA error, etc..)
  TOP-PMT photocathode lifetime (aging)
CDC wire hit rate
TOP PMT p.e. flux
PXD occupancy
10Gy/year
Dose on ECL Crystals
Dose on ARICH HAPD

## Slide 25: Summary of beam background impact
Assuming operation at the design luminosity, BG impact on detector performance(occupancy, tracking/PID performance etc..) is tolerable.
Assuming 10 years operation at the design luminosity, most of our detector components are safe for radiation dose and neutron fluence.
  except for TOP PMT photocathode lifetime, which needs further x3 reduction.
    Our PMTs (1C/cm2 life) will be killed in few years and should be replaced with recently-developed new PMTs (~7C/cm2).
Gammas in BG shower reach TOP quartz bar and generate electrons by Compton scattering and etc.. Those electrons emit Cerenkov photons and those photons reach PMT photocathode.

## Slide 26
Beam loss distribution
which creates TOP PMT hits
Beam loss distribution
Thick tungsten shield
Thick tungsten shield
TOP quartz bars
IP
Limited shield
e-
e+
IP
IP
1m
-1m
1m
-1m
2m
2m

## Slide 27: Closer look to IP vicinity area (|s|<65cm)

## Slide 28
IP beam pipe
Be
Ti
Ti
Paraffin flow
Al
Be
SUS
Ti
Light material (Be) inside detector acceptance
Paraffin (C10H22)flow to remove heat from mirror current (~80W)
Gold plating (~10um)
on inner wall to stop SR
Much simpler Be shape (also much cheaper) since we allow Paraffin and vacuum to attach both side of welding
Belle
Belle-II

## Slide 29: Interaction region
Belle
Belle-II
<Belle-II>
Smaller IP beam pipe radius
（r=15mm⇒10mm）
Wider beam crossing angle
（22mrad⇒83mrad）
Crotch part: Ta pipe
Pipe crotch starts from closer to IP, complicated structure
New detector: PXD
（more cables should go out）
Ta
Ta
Ti/Be/Ti

## Slide 30: Tungsten shield
cf. Heavy-metal shield @ Belle
Heavy-metal shield to protect PXD/SVD from showers coming from upstream.
Belle-II IP design (obsolete)
Shield design constrained by cabling space and total weight requirements
SVD
PXD
Ta beam pipe
Notes: Another countermeasure is to use heavy-metal shield to protect inner detectors, which was also used for current Belle.
“Heavy-metal” is specifically referring to Tungsten-alloy, with a very short radiation length and capacity to stop showers created by the Touschek scattered particles.

## Slide 31: PXD cables & pipes

## Slide 32: Summary
Touschek/Beam-gas well reduced by collimators
Radiative Bhabha spent particles are dominant
Thick tungsten shield inside cryostat stop shows
PMT photocathode aging for TOP counter is a remaining issue
Shielding at |s|<60cm is VERY difficult
  Limited space (need cabling path),
  Limited weight to be supported

## Slide 33
Thank you !!
ME
DANGEROUS BEAM
OUR
DETECTOR

## Slide 34: Other related SuperKEKB talks
Friday morning
  WG2: “Dynamic aperture optimization in SuperKEKB” (Y. Ohnishi)
  WG2: “The effect of IR imperfection on dynamic aperture in SuperKEKB / dynamic aperture study of CEPC” (H. Sugimoto)
Friday afternoon
  WG2: “Beamstrahlung and energy acceptance“ (K. Ohmi)
  WG3: “Beam-beam limit vs. number of IPs and energy I: beam-beam simulation” (K. Ohmi)
Sunday morning
  WG9: “Lessons learned from the B-Factories and implications for a high-luminosity circular e+e- Higgs factory” (Y. Funakoshi)

## Slide 35: Schedule, collaboration

## Slide 36: Commissioning schedule
Phase 1 (Autumn 2015-)
  No final Q magnets, no Belle-II detector
  Machine study for low emittance beam
  Vacuum baking with beam (>1month w/ 0.5-1.0A)
Phase 2 (Autumn 2016-)
  Install Q magnets, Belle-II detector except VXD detectors
  Machine study for final focusing, XY-coupling, collision
  Beam background study
Phase 3 (Summer 2017 )
  Physics run

## Slide 38: Belle II Collaboration
23 countries/regions, 97 institutes,
594 collaborators
Sep. 2014

## Slide 39: Machine Design Parameters
parameters |  | KEKB |  | SuperKEKB |  | units
 |  | LER | HER | LER | HER | 
Beam energy | Eb | 3.5 | 8 | 4 | 7.007 | GeV
Half crossing angle | φ | 11 |  | 41.5 |  | mrad
# of Bunches | N | 1584 |  | 2500 |  | 
Horizontal emittance | εx | 18 | 24 | 3.2 | 4.3 | nm
Emittance ratio | κ | 0.88 | 0.66 | 0.27 | 0.31 | %
Beta functions at IP | βx*/βy* | 1200/5.9 |  | 32/0.27 | 25/0.30 | mm
Beam currents | Ib | 1.64 | 1.19 | 3.6 | 2.6 | A
beam-beam param. | ξy | 0.129 | 0.090 | 0.087 | 0.081 | 
Bunch Length | sz | 6.0 | 6.0 | 6.0 | 5.0 | mm
Horizontal Beam Size | sx* | 150 | 150 | 10 | 11 | um
Vertical Beam Size | sy* | 0.94 |  | 0.048 | 0.063 | um
Luminosity | L | 2.1 x 1034 |  | 8 x 1035 |  | cm-2s-1

## Slide 40: Lifetime/ IR loss summary
Life time | Touschek | Beam-gas Coulomb | Rad. Bhabha
LER | 10 min. | 25 min | 28 min.
HER | 10 min. | 46 min. | 20 min.
IR loss ¦s¦<4m | Touschek | Beam-gas Coulomb | Rad. Bhabha
LER | 250 MHz | 90 MHz | 0.6GHz*
HER | 30 MHz | <10 MHz | 0.5GHz*
*Effective rate

## Slide 41: Candidate collimator locations
(r=10.5mm)
r=13.5mm
TMC condition
beta_y [m]
(r=10.5mm)
r=13.5mm
TMC condition
Collimator width d[mm]
beta_y [m]
LER
HER
  V1 collimator @ LLB3R (downstream)
  (s=-90-82m, by=30146m)
  by=125m, 2.23mm<d<2.81mm
  V1 collimator @ LTLB2 (downstream)
  (s=-63-61m, by=81187m)
  by=123m, 1.74mm<d<2.26mm
herfqlc5605
lerfqlc_1604
Collimator position should satisfy beta_y condition above,
need space(at least 1.5m), and the phase should be close to IP
Ny(V1)= 42.82, Ny(QC1)= 44.32
Ny(V1)= 1.25, Ny(QC1)= 0.25

## Slide 42: Vertical collimator width vs. Coulomb loss rate, Coulomb life time
her5365,V1=LTLB2 downstream |  |  | 
V1 width[mm] | IR loss [GHz] | Total loss[GHz] | Coulomb life[sec]
2.10 | 0.0007 | 49.6 | 3294.0
2.20 | 0.001 | 45.2 | 3615.2
2.30 | 0.357 | 41.0 | 3951.3
2.40 | 7.99 | 33.0 | 3985.9
2.50 | 13.1 | 27.9 | 3985.9
ler1604, V1=LLB3R downstream |  |  | 
V1 width[mm] | IR loss [GHz] | Total loss[GHz] | Coulomb life[sec]
2.40 | 0.04 | 153.9 | 1469.8
2.50 | 0.05 | 141.8 | 1594.8
2.60 | 0.09 | 131.0 | 1724.9
2.70 | 0.24 | 121.4 | 1860.2
2.80 | 1.65 | 111.4 | 2000.5
2.90 | 11.48 | 100.8 | 2014.3
3.00 | 21.98 | 90.3 | 2014.3
Based on element-by-element simulation considering causality the phase difference (by Nakayama)
IR loss rate is VERY sensitive to the vertical collimator width.
(Once V1 aperture>QC1 aperture, all beam loss goes from V1 to IR
Typical orbit deviation at V1 : +-0.12mm (by iBump V-angle: +-0.5mrad@IP )
Up to 100turns

## Slide 43
inner
lower
upper
lower
inner
x : positive=ring outer, y: positive=downward
Beam orbit after RBB scattering

## Slide 44: Background reduction history
Lossrate in IR
Sep. ‘10
Dec. ‘10
Mar ‘11
Jun. ‘11
Sep. ‘11
Dec. ‘11
15 GHz
1 GHz
0.2 GHz
Touschek LER
Touschek HER
RBB LER(e+)
Beam-gas
Coulomb LER
Beam-gas
Coulomb HER
110GHz
More horizontal collimators near IP
Vertical collimators at small beta_y
Coulomb BG found to be dangerous
0.7GHz eff
0.9GHz eff
RBB HER(e-)
0.1 GHz
0.2 GHz
0.1 GHz
Extrapolation from machine study
40GHz
Focused review
Joint BG workshop with SuperB

## Slide 45: Tunnel BG (|s|<30m)
Photon dump
Photon dump
Hiroyuki Nakayama (KEK)
KEKB ARC (Mar. 4, 2013)
45
 | LER (4GeV e+) | HER (7GeV e-)
Rad. Bhabha | 61 W (eff. 96GHz) | 23W (eff. 19GHz)
Touschek | 0.08W (0.1GHz) | 3.4W (3.1 GHz)
+ gammas emitted from Rad. Bhabha event
LER last collimator
HER last collimator
Touschek LER loss at the last collimator has been suppressed by collimator optimization
75cm-thick concrete shield
30cm-thick polyethylene shield

## Slide 46: Summary for 9th campaign
 | 9th campaign result | limit | SF
PXD occupancy | 2photon:0.8% , SR:~0.2% | < 3% | 3
CDC wire hit rate | 180kHz | <200kHz | 1.3↓
CDC Elec.Borad n-flux* | 0.58 | <1 | 1.5↓
CDC Elec.Board dose | 72Gy/yr | <100 Gy/yr | 1.4↓
TOP PMT rate | 3MHz/PMT | <1 MHz/PMT | 0.3↓
TOP PCB n-flux* | 0.2 | <0.5 | 3
ARICH HAPD n-flux* (w/ shield) | 0.35 | <1 | 3↑
ECL crystal dose (w/ shield) | 5.2 Gy/yr | <10 Gy/yr | 2
ECL diode n-flux* (w/shield) | 0.3 | <1 | 3↑
ECL pile-up noise (w/shield) | 4.2/1MeV | 0.8/0.2MeV at Belle-I | ?
SF=Safety Factor
*neutron flux in unit of
1011 neutrons/cm2/yr,
NIEL-damage weighted
KLMs studies are not included
listing SF<5 only
With “combined” shield inside ECL

## Slide 47
LER Touschek loss
HER RBB loss
R~
12cm
HER RBB loss at z=60cm is dominant source of TOP PMT background. Quick study shows material for Remote Vacuum Connection (RVC) gives ~20% TOP BG reduction, assuming RVC is equivalent to 60mm thick iron.
Beam loss position which create TOP PMT hits

## Slide 48: =========Notice======== Next WG3 session starts from 13:30, not from 14:00. Please come back early. Thank you!