## Slide 1: Top-Up Injection for PEP-II and Applications to a Higgs Factory
John Seeman,
SLAC
October 11, 2014
HF2014 Beijing

## Slide 2: Abstract: Top Injection for PEP-II
Top-off injection was developed in PEP-II from the linac injector to allow constant luminosity with the BaBar detector being fully operational during injection. The electron beam top-off was developed initially as its lifetime was the shortest and thus made the luminosity nearly constant. Second, the positron beam top-off was developed making the luminosity fully constant. Either electrons or positron could be injection up to 30 Hz if needed, deciding pulse-by-pulse which beam (bunch) was desired. Technical details of PEP-II top-off will be presented. The implications for top-off into a circular Higgs factory will also be discussed. The injected beam emittances and septum parameters are presented.

## Slide 3: Topics for Top-up Injection for Higgs Factory
What is needed for Top-Up injection
PEP-II /BaBar top-up injection
Required injection parameters for a Circular Higgs Factory
Inital injector parameters
Detector masking

## Slide 4: Definitions (for this talk)
Trickle injection = Top-Off = Top-Up

## Slide 5: PEP-II Overview

## Slide 6
PEP-II Parameters for 3.1 GeV x 9.0 GeV
Parameter | Units | Design | April 2008 Best | 2008 Potential
I+ | mA | 2140 | 3210 | 3700
I- | mA | 750 | 2070 | 2200
Number bunches |  | 1658 | 1722 | 1740
by* | mm | 15-25 | 9-10 | 8.5
Bunch length | mm | 15 | 11-12 | 9
xy |  | 0.03 | 0.05-0.06 | 0.07
Luminosity | x1033 | 3 | 12 | 20
Int lumi / day | pb-1 | 130 | 911 | 1300
7 times design
4 times design

## Slide 7: Technical Items Needed for Top-Up injection
Measure each bunch charge in real time and determine when it needs refilling.
In the injector time a bunch to deliver it to the needed particular bunch (bucket) in the ring.
Inject the bunch(es) into the collider with very low losses.
Determine the injected beam backgrounds in the particle physics detector and find cures using collimation.
Develop methods to monitor relevant backgrounds in real time for accelerator operators to tune on.
Develop trigger masking for the detector physics taking by turn and with azimuthal variation.

## Slide 8: PEP-II / BaBar Top-Up (Trickle) Injection
Energy = 3.5 x 9 GeV
Circumference = 2200 m
One collision point (IR) at Lum = 1.2 x 1034
Full energy injection from Linac+Damping Rings
Number of bunches = 1732 / ring
Beam currents = 2.1 A x 3.2 A
Particles = 1.0/1.5 x 1014 / beam (HER/LER)
Lifetimes:
Vacuum = ~10 hours
Touschek = ~3 hours (LER)
Luminosity = ~1 hour
Lost particles per second = 4.2 x 1010 / second
Top-up injection = one bunch / pulse
Injection rate: ~3-15 Hz (30 Hz max)
Particles per injection: 3 to 9 x 109 / pulse
Bunch injection controller: pick the lowest bunch
Injection efficiency = ~ 80%
Injection kicker pulse length = 0.4 msec
Ring path length = 7.3 msec
BaBar
PEP-II

## Slide 9: Running before Trickle (Continuous) Injection

## Slide 10: Continuous Injection for PEP-II

## Slide 11: Trickle Injection lengthened the average fill length

## Slide 12: PEP-II Run Time Changes with Top-Up Injection

## Slide 13: Top-Up Injection increased Higher Average Luminosity

## Slide 14: Trickle or Continuous Injection In PEP-II

## Slide 15: PEP-II/BaBar Top-Up Injection (Accelerator)
Before Top-Up Injection
After Top-Up Injection
Improved peak and average luminosity.

## Slide 16: PEP-II/BaBar Top-Up Injection and Detector Trigger Masking
BaBar trigger masking:
Mask all of ring a few tens of turns.
Mask injected bunch area for 1250
turns or about 0.9 msec.
One
turn

## Slide 17: BaBar Vetoes versus bunch number and turn number.

## Slide 18: CEPC Accelerator Parameters

## Slide 19: CEPC Injection Phase Space
bx at injection septum (stored) = ~200m
bx at injection septum (injection) = ~30m
exstored (stored) =6 nm
exinj (injected) =40 nm
sxstored at septum (stored) = 1.1 mm
sxinj at septum (injected) = 1.1 mm
Xs = Septum blade thickness =~ 5 mm
Xc = septum clearance distance = ~6sx
Xinj < Ax
Xinj = 4sinj+Xs+Xc = ~16 mm
Ax = machine aperture > ~20 mm
Stored Beam Orbit
Injection orbit
Septum blade
Injection bump on
Injection bump off
(~one turn later)
Injection bump
Injected beam
(+/- 2 sxinj)
Stored beam
Ax
xinj
xinj
xc

## Slide 20: Electron and Positron Production
CEPC stores about 2 x1013 e+ per ring.
CEPC with 1 hr lifetime needs 1.25 x1013 e-/e+ per hour or
~3.5 x109 e+ and e- per second at full energy.
Past:
CERN: LEP injection complex delivered ~1011 e+ per second.
SLAC: SLC injection complex delivered ~6 x 1012 e+ per second.

## Slide 21: Option 1: “Ramped Storage Ring” as a CEPC Injector
Top-up injection = 50 bunches / pulse / beam
Slow ramp due to magnet laminations
Injection rate: Once every 4 minutes.
Particles per ring injection: 8.4 x 1011 / pulse
Particles per injected bunch: 1.7 x 1010 / pulse
Bunch injection controller: Fill all bunches at once
Tailor each bunch separately.
Ring path length = 182 msec
Injection kicker pulse length = 182 msec.
Kickers = 13 stronger than PEP-II but long flat top.
 Luminosity varies from 100% to 74% over 8 minutes with 4 minutes per ring.
CERN LEP: 26.7 km
Ramping speed is 0.5 GeV/sec
 120 GeV in 4 minutes.
CEPC
Injector
Storage Ring
DR 1.5 GeV
e+
Linacs
e-
3 GeV
120 GeV

## Slide 22: Option 2: “Synchrotron” as a CHF Injector
Top-up injection = 50 bunch / pulse
Cycle rate = 3 Hz
Injection rate: 1 Hz e+, 1 Hz e-, 1 Hz e- to make e+
Particles per injection:4 x 109 / pulse over 50 bunches
with 90% injection efficiency
 8 x 107 /bunch  means low instability effects and RF.
Bunch injection controller: Tailor the charge of each bunch
Magnet laminations same as AC transformers.
Injection kicker pulse length = 183 msec (= 53 km)
Kickers = 13 stronger than PEP-II but 7 times slower.
Ring path length = 183 msec (53 km)
 Luminosity stays within 0.12% of the peak.
Cornell synchrotron: 768 m
Sine wave-magnet excitation
0.2 GeV to 12 GeV in
8.3 msec at 60 Hz.
Does not affect CESR
storage ring operation just
2 m away.
CHF
Synchrotron
e+
e-
DR
e-
2 GeV
120 GeV

## Slide 23: Detector Masking
Detectors for CEPC need to mask injection bunches.
Ramped storage ring injector:
Mask all of ring for ~10 msec every 4 minutes. But luminosity is only constant to ~16%.
Synchrotron injector:
Mask all of ring for ~10 msec at 1 Hz but injected bunch and injection charge is 200 times smaller and luminosity is constant to 0.1%.
Need to make initial full design of a full energy 1 Hz synchrotron injector.

## Slide 24: Conclusions
Top-up injection will work for a Circular Higgs Factory.
A full energy injector is needed because of beam lifetime.
A synchrotron injector will work the best but is more than is needed. (60 Hz)
A rapidly ramped storage ring is adequate. (4 sec)
A slowly ramped storage ring injector doesn’t make the luminosity constant enough.
The detectors will need to mask out the buckets with damping injected bunches during data taking.