## Slide 1: Overall Considerations, Main Challenges and Goals
Yunhai Cai and Kazuhito Ohmi
October 11, 2014
Higgs Factory Workshop, 2014
Beijing, China

## Slide 2: Main Challenges in Lattice Design
Compared with LEP2, we want a factor of 100 increase of luminosity at beam energy 120 Gev with affordable cost
  Low emittance lattice at high energy
  High packing factor of magnets
  Strong final focusing
  Large momentum acceptance
  Short bunches
Notes: 1) Emphases that there is no major breakthrough in technology.

## Slide 3: Design Parameters
 | LEP2 | HF2014
Beam Energy [GeV] | 104.5 | 120.0
Circumference [km] | 26.7 | 47.5
Beam current [mA] | 4 | 14.4
Number of bunches | 4 | 25
Bunch population [1010] | 57.5 | 32.0
Horizontal emittance [nm] | 48 | 1.7
Vertical emittance [nm] | 0.25 | 0.0043
Momentum compaction factor | 18.5x10-5 | 1.43x10-5
bx* [mm] | 1500 | 200
by* [mm] | 50 | 2
Hourglass factor | 0.98 | 0.76
SR power [MW] | 11 | 50
Bunch length [mm] | 16.1 | 1.5
Beam-beam parameter | 0.07 | 0.07
Luminosity [1034 cm-2s-1] | 0.0125 | 1.01

## Slide 4: Luminosity
Bunch luminosity
where Rh is a geometrical reduction from the hourglass effect and is written as
Total luminosity
Notes: Requires bunch length is equal or smaller than the vertical beta function at the interaction point. There are dynamical effects as well.

## Slide 5: Beam-Beam Limit
Given the beam-beam parameter
The luminosity can be re-written as
where IA=17045 A. Smaller by* is absolutely necessary. For example, in this design we have I=14.4 mA, E0=120 GeV, xy=0.07, Rh=0.76, by*=2mm, gives 1x1034 cm-2s-1 in luminosity. So what is the beam-beam limit for Higgs factory?
Notes: A typical beam-beam parameter is 0.05. So it is very easy to pick you beta function as needed.
Strongly focusing is necessary at the interaction point. Say beta = 1 mm.

## Slide 6: Power Limitation
Synchrotron radiation
Beam power given by RF
Limits the total beam current I
For example, E0=120 GeV, r=5.2 km, U0=3.6 GeV,
I=14.4 mA, lead to Pb=50 MW in this design.
Notes: 1) Larger ring radiate less.

## Slide 7: Scaling of Luminosity
If there is a beam-beam limit as suggested by the simulation and beam power is also limited, the luminosity can be re-written as
where PA = mc2IA/e = 8.7 GW. This scaling was first given by B. Richter, Nucl. Instr. Meth. 136 (1976) 47-60.
Notes: Larger bending radius and more power will leads to higher luminosity. Money talks.
Higher energy reduces the luminosity, for example operating at Z peaks.

## Slide 8: Emittance of Lattice
For an electron ring, the horizontal emittnace is given by
The quantum constant Cq = 3.8319x10-13 m for electron
g is the Lorentz factor (energy)
q is the bending angle of the dipoles.
Lower emittance implies
  More cells, more dipoles and smaller dispersion
  Stronger focusing, more quadrupoles
  Stronger2 of sextupoles reduces dynamic aperture
Notes: 1) Emphasis on reduction of dynamic aperture.

## Slide 9: Space in Arc and Packing Factor
Notes: Extra-Space is valuable to design a good lattice.
The dispersion bumps show here or harmonic sextupoles in small straight sections.

## Slide 10: Final Focus System
at IP:
bx*=200 mm
by*=2 mm
L*=2 m
xy~L*/by*
chromaticity:
Notes: Chromaticity at order of thousands have to be compensated locally.
Compensation is good a linear-order. How about those higher-order ones?

## Slide 11: Beamstrahlung Effects
Beam lifetime due to large single photon emission (for 30 minutes, V.I. Telnov, 2012)
Large RF-buckets and large momentum aperture h
Large sz and sx. Favors longer and larger horizontal beam size.
Limits bunch population Nb
Are there any reasonable solutions?
Notes: Exponential nature of the reduction of beam lifetime.
Momentum aperture of 3%. Otherwise it translate to a significant reduction of luminosity.

## Slide 12: Dynamic Aperture
16 sx
144 sy

## Slide 13: Main Goals
  Clarify where we are and identify main design issues
  Compare different designs and identify their trade-offs
  Collect ideas to resolve the technical blocks such as off-momentum aperture
  Obtain a set of requirements that consistent with other systems (or WGs)
  Define or have a baseline design?
Notes: 1) Do not over specify your system and leave the room to make the job easier for others.

## Slide 14: Important Questions
Is FODO better for high packing factor, or any other possibility?
Is the emittance hard to achieve in the reasonable sextupole strength?
How is the degree of freedom in the design of final focus system?
How is chromaticity correction well done?
Possibility for wider momentum acceptance.