## Slide 1: Summary of WG2
Y Cai and K. Ohmi
HF2014@Beijing

## Slide 2: Thanks to all speakers
(1) Overall consideration, main challenges and goals, Yunhai Cai (SLAC)
(2) Single ring multi-bunch operation and beam separation, Richard Talman (Cornell U.)
(3) Challenges and status of the FCC-ee lattice design, Bastian Harer (CERN)
(4) Status of the CEPC lattice design, Huiping Geng (IHEP)
(5) Analysis of nonlinear dynamics, Yunhai Cai (SLAC)
(6) Dynamic aperture optimization in SuperKEKB, Yukiyoshi Ohnishi (KEK)
(7) The effect of IR imperfection on dynamic aperture in SuperKEKB / dynamic aperture study of CEPC, Hiroshi Sugimoto (KEK)
(8) Beam lifetime and Injection consideration, Cui Xiaohao (IHEP)
(9) CEPC IR optics, Yiwei Wang (IHEP)
(10) Status of the FCC-ee interaction region design, Roman Martin (CERN)
(11) Crab waist interaction region, Anton Bogomyagkov (BINP)
(12) Beamstrahlung and energy acceptance, Kazuhito Ohmi (KEK)
(13) Interaction region magnets, Eugenio Paoloni (INF)
(14) Beam-beam effects in the CEPC, Yuan Zhang (IHEP)
(15) Wide-band long-focus optics for detection systems infrared synchrotron accelerator diagnostics, Marina Maltseva (TENZOR)

## Slide 3: Main challenges and goals Yunhai Cai
  I is limited by synchrotron radiation power.
  Small by and high xy.
  Large r for more I.
  Low emittance lattice at high energy
  High packing factor of magnets
  Strong final focusing
  Large momentum acceptance
  Short bunches

## Slide 4: Important Questions for Optics
Is FODO better for high packing factor, or any other possibility?
Is the emittance hard to achieve in the reasonable sextupole strength?
How is the degree of freedom in the design of final focus system?
How is chromaticity correction well done mainly in IR design?
Possibility for wider momentum acceptance and dynamic aperture.

## Slide 5: FCC-ee arc lattice design Bastian Harer
Design Compatible lattice for Z, W, H and t.
Lattices for H and t are compatible without changes.

## Slide 6
Emittance control is necessary for Z and W.
  Change cell length 50->150m
  Change phase advance per cell.
W(80 GeV) and Z(45.5GeV)

## Slide 7: FCC-ee IR design Roman Martin, Anton Bogomyagkov
L*=2m CERN deign BINP design 30mrad crossing
crab waist for Z and W

## Slide 8
FCC-hh
FCC-ee BINP
FCC-ee CERN
CERN: highest Momentum acceptance from −0.6% to 0.9%
BINP: from −0.6% to 1.2%
Layout of IR
Momentum acceptance

## Slide 9: BINP design for FCC-ee
Optimize b,h at sextupoles
Db/b is also corrected.
A version of interaction region with crab waist is ready.
Synchrotron radiation is low.
Beam lines are symmetrical, making tunnel straight.

## Slide 10: CEPC arc lattice design Huiping Geng
Sufficient dynamic aperture for lattice only arc.

## Slide 11: CEPC IR optics Yiwei Wang
L*=1.5m
Chromaticity correction ; Wx=7, Wy=6(IP)

## Slide 12: Dynamic aperture for CEPC whole lattice
need a lot of optimization to get a reasonable dynamic aperture for the whole ring
  optimize dynamic aperture for on momentum particles
    Optimize the strength of the additional sextupoles
    One more sextupole to cancel x and px simultaneously
  need efforts to achieve bandwidth ±2%
    Match W function and its phase between FFS and the ARC
    with more families of sextupoles in the ARC
    with octupoles
  aberration analysis for the whole ring need to be carried out

## Slide 13: Dynamic aperture studies for CEPC H. Sugimoto
Possible lattice structure except FODO? Keeping packing factor
Which is better Dfx(IP,XLCC)=3p or 2p.
Optimization of b and h at LCC sextupoles.

## Slide 14: Nonlinear dynamics Yunhai Cai
Order by order analysis
2nx-2ny, Jx2 JxJy , Jy2 ….

## Slide 15: Design Issues
Tune shits vs. amplitudes are very large due to interlaced sextupoles in the arcs.
“Second-order dispersion” in the interaction region leads out to the arcs.
Second-order chromatic optics is not yet well matched between the arcs and the interaction region.
Huge geometric-chromatic aberration seen in 5th-order Lie operators in the interaction region. They may well be the bottle neck of the lattice.

## Slide 16: Effects of Pretzel orbit Huiping Geng
Pretzel scheme
Effect of pretzel orbit, interference with sextupoles
Optimizaton of pretzel orbit
Effect and correction of sawtooth orbit due to beam energy variation.
Dynamic aperture with the pretzel and sawtooth orbit is being studied.

## Slide 17: Multibunch beam separation R. Talman
Betatron phase advance(60/60)/cell length and bunch separation.
The scheme used 8 primary separators and 2 trim separators with the separation bumps continuing through the 4 IP’s

## Slide 18: Beam lifetime of CEPC Cui Xiaohao
Beam-Gas Scattering: 10 nTor, 80% H2, 20% CO, 15h
quantum lifetime 2218h
Radiative BhaBha 51min
Beamstrahlung 80min
Touschek lifetime >530h

## Slide 19: Injection consideration of CEPC Cui Xiaohao
Betatron injection
Designing kicker and septum
Bump height
s=4mm
bump height > 12mm
Acceptance length > 15 mm

## Slide 20: Beamstrahlung and momentum acceptance requirement K. Ohmi
Beam-beam simulation with beamstrahlung
Energy distribution and lifetime is calculated.
dmax~2% is preferable for H.
CEPC
TLEP
Control of dynamic beta/emittance may result better lifetime.

## Slide 21: Code benchmark for lifetime, Lifetrack and BBWS Yuang Zhang
dmax=2%
Lifetrack 222 (85: w Gauss fit)
BBWS 250
ymax=40sy
Lifetrack 202 (22: w Gauss fit)
BBWS 250
Lifetime for Energy tail
Lifetiem for Transverse tail
Good agreement without Gaussian fit

## Slide 22: Beam-beam simulation for CEPC Y. Zhang
Dynamic beam-beam effects
b* dependence, possibility of by*=1.2-> 2mm
Current dependence
Error tolerance for IP coupling and dispersion
Beam tilt
Choice of Tune, (0.54,0.61)

## Slide 23: Dynamic aperture optimization at SuperKEKB Y. Ohnishi
X-LCC corrects QC2 chromaticity and Y-LCC corrects QC1 chromaticity locally.

## Slide 24: Difficulty in Large Piwinski Angle scheme
Dynamic aperture shrink due to Beam-beam force
Crab waist helps this difficulty.
However crab waist scheme makes shrink dynamic aperture due to nonlinearity in IR.
BINP approach may help this difficulty.

## Slide 25: How to manage IR multipoles H. Sugimoto
recover dynamic aperture by correction coils

## Slide 26: IR magnet design (SuperB & SuperKEKB) Euginio Paoloni
IR magnet where two beams crosses
SuperKEKB separate magnet, leakage of LER QC1 affects e- beam
SuCanceling coils to null the terms B3,B4,B5 and B6 of the field leaking from the QC1RP: B1 and B2 are retained
Direct winding of collector coil

## Slide 27: SuperB approach
Double Helix Coils
A cold test is done by mod 2015
100T/m double bore

## Slide 28: Broadband long-focusing mirror optical system for infrared diagnostics Marina Maltseva
The system works in the UV and IR ranges of spectrum (Δλ~ 0.3-40 μ m).
Photographic resolutions are: 7Photographic 7-1mm in the focal plane of the tract; 7–1 mm in points shifted at ±5 mm; 7–1mm, at ±10 mm; 7–1mm, at ±15 mm; and 5–1mm, at ±20 mm.

## Slide 29: Conclusions of WG2
Many progresses have been made since the last meeting (Feb, 2014), but the momentum aperture of the collider with realistic arcs is still too small. Possible solutions:
  Add octupoles near the final focusing quadrupole like SuperKEKB Consider asymmetric dispersion at the paired sextupole in the interaction region
  Consider to increase circumference to accommodate other type of cells with non-interlace sextupoles in arcs
  Further to simplify the transition between CCX and CCY to reduce the phase advance from 3p to 2p
2) Consider to increase by* to 2-3 mm since the bunch length is already too long already 2.8 mm
  Not much loss of luminosity
  Help to solve the dynamic aperture problem
  Refinement of the momentum acceptance requirement
3) Technical issues:
  300 T/m gradient of quadupole is feasible but may not easier
  Consider to make a thin septum (2 mm)
  Dipole in the interaction region may be still too strong
  Injected beam may be too large, especially with a pretzel scheme

## Slide 30: Thank you for excellent talks and contributions