## Slide 1: Choice of L* for FCCee: IR optics and DA
A.Bogomyagkov, E.Levichev, P.Piminov
Budker Institute of Nuclear Physics
Novosibirsk

## Slide 2: Outline
Introduction (goals, assumptions, tools)
FF optical blocks
Comparison of nonlinear sources of FF (theoretical)
Simulation results
Conclusions

## Slide 3: Goals, assumptions, tools
Estimate nonlinear features of FCCee final focus as a function of L* and *. Assuming domination of the vertical plane.
Design several lattices of FF (from IP to beginning of the arc) for several L*.
Close the ring with linear matrix providing tunes good for luminosity. Find DA, detuning. Optimize DA.

## Slide 4: IR optics blocks
CRAB
X2
X1
Y2
Y1
FFT
YXCCS
CRAB
-I
-I
IP: Kinematic terms: extremely low IP beta
Chromatic section:
strong sextupoles, large beta
First quad fringes: large strength and beta

## Slide 5: Final focus
D0=0.7 m
Q0: L=4.6 m, G=95 T/m @ 175 GeV
D1=0.4 m
Q1: L=2 m, G=96 T/m @ 175 GeV
IP
L*(D0)
QD0

## Slide 6: Nonlinearity: figure of merit
Final goal is large dynamic aperture. However, DA can’t be calculated for part of the ring. Therefore we took nonlinear detuning coefficient  as FF nonlinearity figure of merit.
Advantages
Perturbations are 3rd order (octupole like) and detuning is calculated by 1st order of perturbation theory:
 is additive for different sources

## Slide 7: Detuning and DA scaling
Naive approach:
where
Octupole resonance fixed point:

 zero Fourier harmonic
h  resonance driving Fourier harmonic (we believe that both are of the same magnitude order)

## Slide 8: Final quad QD0 and chromaticity
Defining the QD0 focusing requirements as o = –I one can find
The beta and its derivative in the end of L* are given by
FF vertical chromaticity(half of FF):
QD0 natural chromaticity
Correction by sextupoles
Note: For FF ’ corresponds to the chromatic function excitation introduced by B.Montague (LEP Note 165, 1979)

## Slide 9: Kinematics
For the extremely low * and large transverse momentum the first order correction of non-paraxiality is given by
The main contribution comes from the IP and the first drift:
where 2L* is the distance between 2 QD0 quads around the IP.

## Slide 10: QD0 Fringe Fields
Quadrupole fringe field nonlinearity is defined by
and the vertical detuning coefficient is given by*)
*) E.Levichev, P.Piminov, arXiv: 0903.3028
A.V.Bogomyagkov et al. IPAC13, WEPEA049, 2615
Or, with above assumptions (k10 is the central strength, 2xQD0):

## Slide 11: Octupole error in QD0
An octupole field error (or corrector) in QD0:
If a field quality at the quad aperture radius ra
One can rewrite the vertical octupole detuning (for 2 QD0) as

## Slide 12: Chromatic sextupoles
Vertical chromatic sextupole pair separated by –I transformer gives the following coordinate transformation in the first order*)
*) A.Bogomyagkov, S.Glukhov, E.Levichev, P.Piminov http://arxiv.org/abs/0909.4872
Pair of sextupoles
Octupole
By analogy to the octupole and using the expression for the FF chromaticity we found for the vertical detuning (1 IR arm)

## Slide 13: yy-test for different lattices
1) CDR
2) K.Oide, FCC Kick-off Meeting, Geneva, 14 Feb 2014
3) T.M.Taylor, PAC 1985
4) H.G. Morales, TLEP Meeting, CERN, 18 Nov 2013
5) A.Chance, SuperB Internal Note, July 30, 2010 (simulation)
6) E.Levichev, P.Piminov, SuperKEKB Internal Report, Feb 11, 2010 (simulation)
Note: Different lattice versions may have different parameters. Black – estimation, blue –simulation.
 | Super C-Tau1) Novosibirsk | SuperB V.161) LER Italy | SuperKEKB2) LER Japan | LEP3) CERN | FCCee/TLEP4) CERN
103 *(m) | 0.8 | 0.27 | 0.27 | 10 | 1
L*(m) | 0.6 | 0.32 | 0.77 | 3.5 | 3.5
-2y | 1500 | 2400 | 5700 | 700 | 7000
-K1(m-2) | 1.3 | 5.4 | 5.1 | 0.11 | 0.19
LQD0(m) | 0.2 | 0.5 | 0.33 | 2 | 2.2
10-6 f (m-1) | 0.07 | 0.4 (0.6)5) | 5.1 (4)6) | 0.008 | 1.3
10-6 k (m-1) | 0.11 | 0.5 (0.62)5) | 1.26 (1.2)6) | 0.004 | 0.42
10-6 sp (m-1) | -0.35(-0.41) | -0.7(-0.7)5) | -0.65 (-0.6)6) |  | 

## Slide 14: Our design, different L*
* = 1 mm, K1 = 0.16 m-1, Ls = 0.5 m, s= 5 cm
K1(QD0)const
This estimation is very approximate and just shows the trend. We did not take into account realistic beta and dispersion behavior, magnets other but QD0, etc. All these issues are included in simulation.
L*(m) | 0.7 | 1 | 2 | 3 | 
-2y | 1400 | 2000 | 4000 | 6000 | 
10-6 k (m-1) | 0.08 | 0.11 | 0.24 | 0.34 | L*
10-6 f (m-1) | 0.009 | 0.025 | 0.21 | 0.71 | L*3
10-6 sp (m-1) | -8 | -16 | -64 | -144 | L*2

## Slide 15: Theoretical conclusions
FF nonlinearities may increase as L* in high power.
Major part of the vertical nonlinearity for the extra-low beta IP comes from chromatic sextupoles due to the finite length effect.
The finite length effect in the –I sextupole pair can be improved by additional (low-strength) sextupole correctors.
Nonlinear errors in the quads with high beta may be a problem. Correction coils (for instance, the octupole one) can help.
Third order aberrations including the fringe field and kinematics can be mitigated by a set of octupole magnets located in proper beta and phase.

## Slide 16: Simulation
Scenario:
We use the following lattice and tracking codes: MAD8 and Acceleraticum1) (BINP home made).
The FF structure is closed optically by a linear matrix .
The tunes are fixed at (0.53, 0.57) to get large luminosity .
Dynamic aperture and other nonlinear characteristics are defined from tracking.
DA is increased by additional sextupole and octupole correctors properly installed.
1) D.Einfeld, Comparison of lattice codes, 2nd NL Beam Dynamics Workshop, Diamond Light Source, 2009

## Slide 17:  comparison for L*=0.7 m
 | Kin | Fringe | Sextupole pair
Simulation |  |  | 
xx (m-1) | 60 | 1100 | -2300
xy =yx (m-1) | 380 | 15300 | -0.07106
yy (m-1) | 0.075106 | 0.1106 | -14106
Estimation |  |  | 
yy (m-1) | 0.084106 | 8700 | -8106
A discrepancy is due to the simulation takes into account all quads fringes (included those strong in the Y chromatic section) and realistic beta behavior

## Slide 18: Initial DA
Black: L* = 0.7 m
Red: L* = 1 m (aperture )
Green: L* = 1.5 m (aperture )
Blue: L* = 2 m (SURPRISE! APERTURE )
x=3.24 10-5m, y=6.52 10-8m, *x=0.5m, *x=0.001m
Finite sextupole length breaks exact cancellation of the geometrical aberrations. Only the second order terms are cancelled while the higher remains and degrade DA.

## Slide 19: Explanation
Y chromaticity correction section is a main source of nonlinear perturbation. Produced aberration is proportional to ηs-2
L*=0.7 m, K2=-12 m-3,
y=5255 m
L*=2 m, K2=-14 m-3 ,
y= 5149 m
L*=1.5 m, K2=-14 m-3 ,
y= 7707 m
ηs  0.05 m
ηs  0.09 m
For L* = 2 m the FF chromaticity increased (~L*) but the dispersion increased also, so to compensate the chromaticity we need the beta and the sext strength the same as for L* = 0.7 m  same DA

## Slide 20: Corrected DA
With correctors
S1 – main (chromatic sextupoles)
S2 – low strength (~10% of the main strength) correction sextupoles can mitigate a finite length effect
Alpha before and after correction

## Slide 21: Conclusion
The major source of the DA limitation for the CW FCCee IR is the –I Y chromatic correction section through the sextupole length effect.
Simple calculation of yy confirms it well, however for details computer simulation is necessary.
DA dependence on L* differs for different nonlinearities: kinematics ~L*, -I sextupole pair ~L*2 and fringes ~L*3.
Large dispersion in the sextupole is welcomed.
Nonlinear corrections works well.
For L*=2 m we have Ax > 100x and Ay > 700y which seems quite enough to start.