## Slide 1: CEPC Partial Double Ring Lattice & SPPC Lattice Design
Feng Su Jie Gao Dou Wang Yiwei Wang
Jingyu Tang Tianjian Bian Sha Bai
Huiping Geng Yuan Zhang Yuanyuan Guo
Yuemei Peng Ye Zou
The first IHEP-BINP CEPC Accelerator Collaboration Workshop
Jan 12-13, 2016
Notes: Good afernoon everyone. My report is
CEPC Partial Double Ring Lattice Design & SPPC Lattice Design

## Slide 2: Outline
CEPC Partial Double Ring Lattice
SPPC Lattice

## Slide 3
CEPC Partial Double Ring Lattice

## Slide 4
CEPC Partial Double Ring Layout
SU Feng
2016.1.4
IP1_ee
IP3_ee
IP2_pp
IP4_pp
3.2Km
RF
1/2RF
1/2RF
1/2RF
RF
RF
RF
1/2RF
IP1_ee/IP3_ee, 3.2Km
IP2_pp/IP4_pp, 1132.8m
4 Short Straights, 141.6m
4 Medium Straights, 566.4m
4 Long Straights, 849.6m
2 Short ARC, 24*FODO, 1132.8m
4 Medium ARC, 112*FODO, 5286.4m
4 Long ARC, 124*FODO, 5852.8m
C=59044m
1/2RF
1/2RF
1/2RF
1/2RF
Bypass
about 42m
Bypass
about 42m
Notes: This is the CEPC Partial double ring Layout. Which was showed many times.
IP1 and IP3 is for ee collider. We choose partial double ring scheme here. The length is about 3200m, the full crossing angle is 26mrad.(milliradian)
IP2 and IP4 is for pp collider. For CEPC, We need a bypass lattice to turn around the pp detectors. It’s about 42m .

## Slide 5
CEPC Partial Double Ring Layout
By MADX and PTC
Blue: Bend
Green: Straight Section
Bypass
Bypass
CEPC Partial Double Ring
CEPC Partial Double Ring
C=59044m
SU Feng
2016.1.4
Notes: It’s not clear to see the distance in bypass part and PDR.

## Slide 6
For CEPC 120GeV beam:
Max. deflection per separator is 66μrad.
Using Septum Dipole after separator to acquire 13 mrad
CEPC Partial Double Ring Layout
B1
B2
B3
B4
B6
13mrad
Full crossing angle 26mrad
Separator
B5
Version 1.0
sufeng
2015.12.20
1642m
12
62.5urad
4.5m
0.75mrad in total
IP
479.1m
614.4m
307.2m
7.852m
54m
Septum Dipole
Septum Dipole
Notes: Deflection angle of each seperator is 62.5 micro radian. Antisymmetry of this part

## Slide 7
Separator with Thin Septum Magnet
Separator： 62.5 urad
12 个
0.75 mrad
Septum Magnet：L=3m
（4.25mrad）thicknes=3-5mm
rho=705.822m B=0.56T
Sigmax=697.8um 20sigma=14mm
20mm
Beam
dump
Notes: Beam size is 700 micrometer。 just in case 以防万一

## Slide 8
Seperator
Chart: 
| 1 | 5.5 | 10 | 14.5 | 19 | 23.5 | 27.999998999999999 | 32.499999000000003 | 36.999999000000003 | 41.499997999999998 | 45.999997 | 50.499996000000003 | 54.999994999999998
x | 0 | 0.000141 | 0.000562 | 0.001266 | 0.00225 | 0.003516 | 0.005062 | 0.006891 | 0.009 | 0.011391 | 0.014062 | 0.017016 | 0.02025
Kicker
Dipole
X=20.25mm
X=20.25mm
X=20.25mm
Orbit difference between dipole separator kicker

## Slide 9
Chart: s（m）
| 1 | 5.5 | 10 | 14.5 | 19 | 23.5 | 28 | 32.5 | 37 | 41.5 | 46 | 50.5 | 55 | 55
dipole | 0 | 0 | -0.00014062 | -0.0005625 | -0.0012656 | -0.00225 | -0.0035156 | -0.0050625 | -0.0068906 | -0.009 | -0.011391 | -0.014062 | -0.017016 | -0.02025 | -0.02025
separator | 0 | 0 | -0.00014065 | -0.00056261 | -0.0012659 | -0.0022504 | -0.0035163 | -0.0050635 | -0.006892 | -0.0090018 | -0.011393 | -0.014065 | -0.017019 | -0.020254 | -0.020254
kicker | 0 | 0 | -0.00014062 | -0.0005625 | -0.0012656 | -0.00225 | -0.0035156 | -0.0050625 | -0.0068906 | -0.009 | -0.011391 | -0.014062 | -0.017016 | -0.02025 | -0.02025
Chart: S（m）
| 1 | 5.5 | 10 | 14.5 | 19 | 23.5 | 28 | 32.5 | 37 | 41.5 | 46 | 50.5 | 55 | 55
dipole | 0 | 0 | 0.000141 | 0.000562 | 0.001266 | 0.00225 | 0.003516 | 0.005062 | 0.006891 | 0.009 | 0.011391 | 0.014062 | 0.017016 | 0.02025 | 0.02025
seperator | 0 | 0 | 0.00014065 | 0.00056261 | 0.0012659 | 0.0022504 | 0.0035163 | 0.0050635 | 0.006892 | 0.0090018 | 0.011393 | 0.014065 | 0.017019 | 0.020254 | 0.020254
kicker | 0 | 0 | 0.000141 | 0.000562 | 0.001266 | 0.00225 | 0.003516 | 0.005062 | 0.006891 | 0.009 | 0.011391 | 0.014062 | 0.017016 | 0.02025 | 0.02025
So we use Dipole instesd Seperator in lattice now

## Slide 10
Beta<150m
SEPARATIONMATCHL

## Slide 11
RING3_DR_IP1_2

## Slide 12
Orbit (RING3_DR_IP1) Version 1.0 without FFS
Chart: 

## Slide 13
Dipole Strength Version 1.0 without FFS
 | Angle(mrad) | L(m) | Rho(m) | Brho(E0/c)(T/m) | B(T) | Ek(KeV) | KeV/m
B0 | 3.232 | 19.6 | 6064.36 | 400 | 0.06596 | 631.625 | 32.226
BSepL | -0.0625 | 4.5 | -72000 | 400 | -0.00556 | 53.2 | 11.822
BSeptumL | -4.25 | 3 | -705.822 | 400 | -0.56667 | 5426.4 | 1808.8
BMatch1L | -0.469 | 4.9 | -10447.8 | 400 | -0.03829 | 366.624 | 74.821
BMatch2L | -3.171 | 19.6 | -6181.02 | 400 | -0.06471 | 619.704 | 31.618
BMatch3L | -4.36 | 19.6 | -4495.41 | 400 | -0.08898 | 852.069 | 43.473
B2 | 2.167 | 19.6 | 9044.76 | 400 | 0.04422 | 423.494 | 21.607
B3 | 2.167 | 19.6 | 9044.76 | 400 | 0.04422 | 423.494 | 21.607
B4 | -2.167 | 19.6 | -9044.76 | 400 | -0.04422 | 423.494 | 21.607
B5 | -2.167 | 19.6 | -9044.76 | 400 | -0.04422 | 423.494 | 21.607
BMatch3R | 4.36 | 19.6 | 4495.41 | 400 | 0.08898 | 852.069 | 43.473
BMatch2R | 3.171 | 19.6 | 6181.02 | 400 | 0.06471 | 619.704 | 31.618
BMatch1R | 0.469 | 4.9 | 10447.8 | 400 | 0.03829 | 366.624 | 74.821
BSeptumR | 4.25 | 3 | 705.822 | 400 | 0.56667 | 5426.4 | 1808.8
BSepR | 0.0625 | 4.5 | 72000 | 400 | 0.00556 | 53.2 | 11.822

## Slide 14
Survey & Dynamic Aperture
（Version 1.0 –without FFS）
0: 20σx 700σy
0.01：16σx 500σy
0.02：10σx 170σy
Bypass part at IP2/4

## Slide 15
Dynamic Aperture Comparation
0: 20σx 700σy
0.01：16σx 500σy
0.02：10σx 170σy
CEPC Partial Double Ring Lattice
(Version1.0-20160104)
0: 50σx 1500σy
0.01：50σx 900σy
0.02：40σx 800σy
CEPC Main Ring Lattice (without pretzel)
(September 30, 2014 Geng Huiping)

## Slide 16
CEPC-Single-Bypass
CEPC-Single
CEPC-PDR-Bypass
CEPC-PDR-Bypass-PDRnPi
Notes: integer multiple of pi.

## Slide 17
FFS Part
Crab sextupoles
IP
Y:2.5Pi X:2Pi
-I
K2=-126.77
Wangdou-20151216

## Slide 18
Wangdou-20151216
Sufeng-20151224
K2=-48.57
K2=-126.77

## Slide 19
Orbit of FFS Part
Notes: Focus on the two plane correction scheme. Following.

## Slide 20
Orbit (RING3_DR_IP1) Version 1.0 + FFS(20151126)
Chart: 

## Slide 21
Tune/DA with FFS
For details：
Energy spread between
-0.8628% and 0.719% has DA, out is 0.
0: 13σx 55σy
0.01：0
0.02：0
Notes: The vertical tune may cross the oscillation line.

## Slide 22
Optimize
1、We tried to add sextupoles here, but not help for DA. Because it’s not easy to match the phase advance between them.
2、Try to add some Sextupoles to correct high order chormaticity here.

## Slide 23
DA Comparation
CEPC-PDR-Bypass
CEPC-PDR-Bypass-Sex

## Slide 24
Summary for part 1
The first version of CEPC Partial Double Ring Lattice was designed (Version 1.0). The whole length of CEPC PDR is 3281.27m, full crossing angle is 26mrad, maximum distance between two ring is 14.913m.
The Dynamic Aperture need to be optimized. Now the DA of CEPC with PDR and Bypass(at IP2/4) and without FFS is better than before, but the DA with FFS is not good enough.
We may add more sextupoles in PDR to correct the high order chromaticity , or use more group of sextupoles in ARC to optimize the DA.
The linear lattice of PDR may also be optimized.

## Slide 25
2. SPPC Lattice

## Slide 26
P.S.
P.S.
P.S.
P.S.
LSS1_ee
LSS7_pp
LSS5_ee
LSS3_pp
C = 55.025 km
LSS2_inj
LSS8_extr
LSS4_coll
LSS6_coll
ARC12
ARC67
ARC81
ARC23
ARC45
ARC34
ARC56
ARC78
arccell1
arccell1
arccell2
arccell1
arccell2
arccell2
arccell1
arccell2
LSS1/5 : 1083m
LSS2/4/6/8 : 938.6m
LSS3/7 : 1070.89m
ARC 5920.4m
SPPC Layout
（Su Feng, Jul. 10, 2015）

## Slide 27: Layout of two CEPC lattices
Huiping Geng
Notes: The circumference and the length of the Straight Section is a little different from thae CEPC layout.
This are the two version lattice layout by Hiping Geng. Wo hope the length of each the closely the better.
We should make it the nearly the better. We can change and adjustment them in the future.

## Slide 28
Consideration of CEPC New Layout with PDR

## Slide 29
P.S.
P.S.
P.S.
P.S.
LSS1_coll
LSS7_pp
LSS5_coll
LSS3_pp
C = 58.983 km
LSS2_inj
LSS8_extr
LSS4_RF
LSS6_RF
ARC12
ARC67
ARC81
ARC23
ARC45
ARC34
ARC56
ARC78
arccell1
arccell1
arccell2
arccell1
arccell2
arccell2
arccell1
arccell2
SPPC Layout
（Su Feng Jan. 10, 2016）
LSS1/5_coll ：3.2Km
LSS2/4/6/8：788.31m
LSS3/7_pp: 973.83m
ARC: 5963.2m
Notes: 8段弧区，90度相移4个FODO Cell可消色散，若每个Cell 8块Dipole，则nB需是256的倍数。
This is the layout of SPPC, we rename the straight section as Long Straight Section 1 /2 and … . Configuration maybe change in the future.

## Slide 30
Parameter Estimate for ARC CELL
High Field Dipole in Pre-CDR ：20T，15m
Notes: 8段弧区，90度相移4个FODO Cell可消色散，若每个Cell 8块Dipole，则nB需是256的倍数。

## Slide 31
FODO CELL in ARC
arccell1
arccell2
L=144.4m
Betax: 244.878/42.57
Betay: 42.569/244.869
Notes: This is the arc cell, we use FODO in the ARC. This is a half deficuous quadrupole,then the sextupole, 4 dipoles, and sextupole, and fucus quadrupole. The length is 144.4m. The maximum and minmun beta function is about 244 and 42.57. as from the different side of the low beta pp IP, the sign of the quadrupoles are opposite. Fucus become defocus, and defocus become focus.

## Slide 32
 | LQ | DQS | LS | DSB | LB | DBB
SPPC | 4m | 1m | 0.5m | 1m | 14.8m | 1m
FCC-hh | 6.3137m | 1m | 0.5m | 2.184m | 14.3m | 1.36m
B max [T] | G max [T/m] | k1 | k2
19.61 | 582.156 | 4.9899E-3 | 0
ARC CELL
Pre-CDR：
Dipole: L=15m B=20T
Quadrupole:
D = 45 mm Bpole=16 T
G=711.1T/m K1=6.097*10^-3
(=4.1um)
E (Collision：35TeV)
(Injection：2.1TeV)
(Collision：1.099*10^-10m=0.1099nm)
（ Injection： 1.83*10^-9m=1.83nm）
σ（Collision：1.66*10^-4m=166um）
（ Injection： 6.76*10^-4m=676um）
R=20*σInj=13.52mm
D=27.04
Betax: 244.878/42.57
Betay: 42.569/244.869
Notes: This is the parameter of ARC FODO. The according K1 is about 5 times 10 to minus 3. the according parameter from SPPC Pre-CDR by the magnets people, the length of dipole is zbout 15m, and the field is about 20T. The aperture of quadrupole is about 45mm,and the pole-tip field is Bpole = 16 T. the graduate is according about 711T/m. K1=6.097*10^-3.acquire.

## Slide 33
ARC （ARCDSPL,36 CELL, ARCDSPR）
ARC23
ARC45
ARC67
ARC81
ARC12
ARC34
ARC56
ARC78
L=5963.2m
Notes: This is the arc part, each has 35 fodo cells. And the length is 5054m. As from the left and right side of the low-beta-pp IR, the quadrupoles are opposite sign ,they are devided into two family.4 arc like this ,and 4 like this.

## Slide 34: Dispersion Suppressor (DS) types
LHC-like
Full Bend
Half Bend (half weak dipoles)
ARC
 IP
Longer DS but less cells in the Arcs
14.3 m
13.5 m
8.33T
7.74T
(1)
(2)
(3)
433.2m

## Slide 35
 | BDSP1L | BDSP2L | BDSP1R | BDSP2R | B0 | 
(1) | 9.93 | 9.93 | 9.93 | 9.93 | 19.86 | (T)
(2) | 18.93 | 18.93 | 18.93 | 18.93 | 19.86 | (T)
(3) | 19.86 | 19.86 | 19.86 | 19.86 | 19.86 | (T)
L=288.8m
L=288.8m
L=288.8m

## Slide 36
Dispersion Suppressor (DS)
382.4m
BDSP1L
 | BDSP1L | BDSP2L | BDSP1R | BDSP2R | B0 | 
B | 18.93 | 18.93 | 18.93 | 18.93 | 19.86 | T
L | 11.5 | 11.5 | 11.5 | 11.5 | 14.8 | m
BDSP2L
BDSP1R
BDSP2R

## Slide 37
Long Straight Section
P.S.
P.S.
P.S.
P.S.
LSS1_coll
LSS7_pp
LSS5_coll
LSS3_pp
C = 58.983 km
LSS2_inj
LSS8_extr
LSS4_RF
LSS6_RF
ARC12
ARC67
ARC81
ARC23
ARC45
ARC34
ARC56
ARC78
arccell1
arccell1
arccell2
arccell1
arccell2
arccell2
arccell1
arccell2
LSS1/5_coll ：3.2Km
LSS2/4/6/8：788.31m
LSS3/7_pp: 973.83m
ARC: 5963.2m
SPPC Layout
（Su Feng Jan. 10, 2016）
Notes: This part is the long straight section design. It’s the LSS1_ee LSS2_inj…

## Slide 38
ARCDSPL, ARC_to_STR, 21.5*STRCELL, STR_to_ARC, ARCDSPR
382.4m, 71.719m, 3104.6m, 66.789m, 382.4m
L=3243.106m
LSS1/5_coll
Notes: Now we just use the simple fodo cell, missing all the dipole to instead. The quadrupole is the same with fodo cell. We will investaga the need and requirement of each Long straight section to redesgin and rematch to satisfy the requirement.

## Slide 39: LSS2_inj/LSS8_extr
-ARCDSPR, ARC_to_STR, 4.5*STRCELL, STR_to_ARC, -ARCDSPL
382.4m, 71.719m, 649.8m, 66.787m, 382.4m
L=788.306m

## Slide 40: LSS4/6_rf
-ARCDSPR, ARC_to_STR, 4.5*STRCELL, STR_to_ARC, -ARCDSPL
382.4m, 71.719m, 649.8m, 66.787m, 382.4m
L=788.306m

## Slide 41: LSS3_pp/LSS7_pp
ARCDSPL, ARC_to_STR, 21.5*STRCELL, STR_to_ARC, ARCDSPR
382.4m, 71.719m, 973.829m, 66.789m, 382.4m
L=973.829m
Notes: The key point for my work is the low beta pp IR design. LSS3_pp LSS7_pp…

## Slide 42: Q Strength
 | K1(m^-2) | G（T/M） | L(M) | βmax
K1.QT.1R | 4.9751e-03 | 580.428 | 6 | 3543.69
K1.QT.A2R | -5.2595e-03 | -613.668 | 9 | 9601.686
K1.QT.B2R | -5.2595e-03 | -613.668 | 9 | 9601.686
K1.QT.3R | 5.3434e-03 | 623.369 | 8 | 9731.53
K1.QM.4R | -2.2804E-04 | -266.04 | 4 | 3798.29
K1.QM.5R | 8.8592E-04 | 103.36 | 4 | 1506.53
K1.QM.6R | -1.2144E-03 | -141.68 | 4 | 587.87
K1.QM.7R | 1.0640E-04 | 124.133 | 4 | 531.25
K1.QM.8R | -4.2431E-03 | -495.028 | 4 | 162.20
K1.QT.1L | -4.9751e-03 | -580.428 | 6 | 3543.69
K1.QT.A2L | 5.2595e-03 | 613.668 | 9 | 9601.686
K1.QT.B2L | 5.2595e-03 | 613.668 | 9 | 9601.686
K1.QT.3L | -5.3434e-03 | -623.369 | 8 | 9731.53
K1.QM.4L | 2.2804E-04 | 266.04 | 4 | 3798.29
K1.QM.5L | -8.8592E-04 | -103.36 | 4 | 1506.53
K1.QM.6L | 1.2144E-03 | 141.68 | 4 | 587.87
K1.QM.7L | -1.0640E-04 | -124.133 | 4 | 531.25
K1.QM.8L | 4.2431E-03 | 495.028 | 4 | 162.20
Pre-CDR：
IR:
D = 60 mm Bpole = 20 T
G=666.7T/m K1=5.716*10^-3
R=30mm
20mm=20σ
σ=1mm
β=σ^2/ε=10.03km
Matching section:
D = 60 mm Bpole = 16 T
G=533.3T/m K1=4.572*10^-3

## Slide 43: Separation Dipole
L=1070.8m
β*=0.75m
RMS bunch length=7.55cm
Normalize emittance= 4.0μrad
Momentum compaction factor=1.4*10^-4
……
Full crossing angle=146μrad

## Slide 44: Separation Dipole

## Slide 45: Summary for part 2
The first version of SPPC Lattice was designed (Version 1.0). The whole length and layout is according to CEPC lattice layout. full crossing angle is 146urad.
Crossing angle and Separation Dipole need to be studied and installation.
LSS3_pp low-β pp optics need to be studied and optimization.
The Dynamic Aperture need to be studied: MADX or Sixtrack.

## Slide 46: Acknowledge
Gang Xu, Qing Qin, Yuan Zhang, Yuemei Peng, Qingjin Xu, Yukai Cui, Xiaohao Cui, Zhe Duan, Yudong Liu, ……
Thanks for your kind help and beneficial discussion!

## Slide 47
[1] CEPC-SPPC Preliminary Conceptual Design Report, The CEPC-SPPC Study Group, IHEP-CEPC-DR-2015-01.
[2] J. Gao, IHEP-AC-Note-2013-012.
[3]Xiao Ming et al, CEPC_bunch_train _ 2015-8-28
[4]Oridy, FCC-ee_150917
[5] P. Raimondi, Status on SuperB effort, La Thuile, March 11, 2006
[6]W. Kalbreier, et al, “Layout, design and construction of the electrostatic separation system of the LEP e+e- collider”, CERN, Geneva, Switzerland. [7] R. Martin, et al, “Status of the FCC-ee interaction region design”, HF2014 Workshop, Beijing, China, 9-12 October, 2014
Reference

## Slide 48
Thank You !