## Slide 1: CEPC Interaction Region design and Dynamic Aperture Optimization
Yiwei Wang, Yuan Zhang, Dou Wang, Huiping Geng,
Xiaohao Cui, Sha Bai, Tianjian Bian, Feng Su, Jie Gao
Institute of High Energy Physics (IHEP, Beijing)
The first IHEP-BINP CEPC Accelerator Collaboration Workshop
IHEP, 12-13 January 2016

## Slide 2: Outline
Lattice design of the interaction region
Optimization of the interaction region nonlinearity
Summary

## Slide 3: Lattice of interaction region
  IR lattice design with local chromaticity correction with
    x*=0.8m, y*=3mm, x=6.12nm, =0.3%, L*=1.5m, 2IPs
    latest lattice for head-on collision: FFS_3.0mm_v3.0_Nov_2015
L*= 1.5m
y*= 3mm
GQD0= -300T/m
GQF1= 300T/m
-I
-I
IP
FT
CCY
CCX
MT

## Slide 4: Lattice of interaction region
Dynamic aperture of whole ring is limited by the strong nonlinearity of IR due to small y*
  An example: DA with only ARC vs. DA with ARC + preliminary IR
Optimization of the dynamic aperture
  Local correction: optimization of IR nonlinearity
  Global correction: with help of ARC (see Yuan Zhang’s talk)
W/ ARC (20140930 by Huiping Geng)
W/ ARC+IR (FFS_3.0mm_v0_Feb_2015 Yiwei Wang)
without radiation damping, error of the magnets, synchrotron motion included
Tracking with 3 times of damping time, Coupling factor =0.003 for emitty
  2% (1.5x , 13.5y)

## Slide 5: Finite length effect of sextupoles
Add additional sextupoles next to the main one*
  Compensate the finite length effect (Lsext=0.3m)
*A.Bogomyagkov et al.
http://arxiv.org/abs/0909.4872
k=1, S1/S2=-0.1

## Slide 6: High order chromaticity
FFS_3.0mm_v1.0_Mar_2015
FFS_3.0mm_v2.2_Sep_2015
remove 2 quads in FT#
additional sext at 1st image point*
tune phase of sextupoles#
*K. Oide, SLAC-PUB-4806, Nov 1988.
R. Brinkmann, DESY M-90-14, Nov 1990.
# Yunhai Cai, private communication.
K. Oide, SLAC-PUB-4806, Nov 1988.

## Slide 7: High order chromaticity (cont.)
Tune shift due to energy deviation
v1.0
v2.2
IR only, from IP to the entrance of FFS
IR + ARC, periodic solution

## Slide 8: High order chromaticity (cont.)
Vertical dynamic aperture vs. dp/p
From v1.0 -> v2.2: DA increased significantly for large off-momentum 20y for 2% (green line)
  W/O error of the magnets
  Synchrotron motion included
  Tracking with 3 times of damping time
  Coupling factor =0.003 for y
x0=0.001x
0
2
-2
-1
1

## Slide 9: High order chromaticity (cont.)
v1.0
v2.2
Dynamic aperture for both planes
v2.2: on momentum (20x, 180 y), off momentum 2% (2.5x , 20y)

## Slide 10: -I break down and high order dispersion
Many additional sextupoles in IR
  Idea from linear collider final focus*
  Six more sextupoles (3,4,5,8,9,10) to correct break down of –I transformation
  Three more sextupoles (2,6,7) help to correct the second order dispersion and so on
-I
-I
IP
FT
CCY
CCX
MT
1
2
3
4
5
6
7
8
9
10
FFS_3.0mm_v3.0_Nov_2015
*R. Brinkmann, DESY M-90-14, Nov 1990.
L*=1.5m
y*=3mm

## Slide 11: -I break down and high order dispersion (cont.)
In practice, dynamic aperture is optimized directly with the additional sextupoles in IR
  W/O error of the magnets
  Synchrotron motion included
  Tracking with ~1 times of damping time
  Coupling factor =0.003 for y
  Downhill simplex algorithm used*
    19 points of dp/p from -2% to 2%
    Optimize with initial phases (phasex, phasey)=(0,0),(pi/2, pi/2), (0, pi/2), (pi/2, 0)
*K. Oide, private communication

## Slide 12
-I break down and high order dispersion (cont.)
+(2,3,4,5) sextupoles
-I
-I
1
2
3
4
5
6
7
8
9
10
FFS_3.0mm_v3.0_Nov_2015
L*=1.5m
y*=3mm

## Slide 13
-I break down and high order dispersion (cont.)
-I
-I
1
2
3
4
5
6
7
8
9
10
FFS_3.0mm_v3.0_Nov_2015
L*=1.5m
y*=3mm
+(2,3,4,5,6,7) sextupoles

## Slide 14
-I break down and high order dispersion (cont.)
-I
-I
1
2
3
4
5
6
7
8
9
10
FFS_3.0mm_v3.0_Nov_2015
L*=1.5m
y*=3mm
+(2,3,4,5,6,7,8,9,10) sextupoles

## Slide 15: Radiation damping
Dynamic aperture is optimized directly with the additional sextupoles in IR
  W/O error of the magnets
  Synchrotron motion and radiation damping included
  Tracking with 1 times of damping time
  Coupling factor =0.003 for y
W/O damping: ~6.5 x  10y for 2%
W/ damping: ~9 x  20y

## Slide 16: Acknowledge
Yunhai Cai, Demin Zhou, Katsunobu Oide, Kazuhito Ohmi, Yingshun Zhu, Ming Xiao, Gang Xu, Qing Qin, Yoshihiro Funakoshi, Yukiyoshi Ohnishi, Hiroshi Sugimoto
Thanks for their kind help and beneficial discussions!

## Slide 17: Summary
To optimize the dynamic aperture of CEPC main ring
  Local correction within IR have been tried
DA incresed significantly, though some prospects needed to be check.
Combine of local and global correction is under going
Multi-object optimization is necessary to get a better solution and quick convergence.

## Slide 18
Thank you for your attention!