## Slide 1: Pretzel scheme of CEPC
H. Geng, G. Xu, Y. Zhang, Q. Qin, J. Gao, W. Chou, Y. Guo, N. Wang, Y. Peng, X. Cui, T. Yue, Z. Duan, Y. Wang, D. Wang, S. Bai, F. Su
IHEP, CAS, China
The first IHEP-BINP CEPC Accelerator Collaboration Workshop
Jan 12-13, 2016

## Slide 2: Outline
Principles of pretzel scheme
Modification of the ring lattice
Pretzel scheme design
Issues remained
Summary

## Slide 3
Principles of pretzel scheme
In single ring collider, pretzel orbit is used to avoid the beam collision at positions except for the IPs
For ideal pretzel orbit, the following relationship should be fullfilled:
i.e. the phase advance between parasitic crossing point should be a integer number of 2*Pi, this relation guarantees that if the beam is properly separated at the first parasitic collision point, then it can be automatically properly separated at other parasitic collision points.

## Slide 4
Principles of pretzel scheme (cont.)
For our lattice, it is comprised of 60/60 degree FODO cells, every 6 cells have a phase advance of 2Pi, so the relationship can be written as:
For 50 bunches, there are 100 collision points in total, thus the ring circumference must be
For a ring with circumference of ~50km, N=2, which means there is one collision point every 4Pi phase advance. The exact length of the ring is 56640m.

## Slide 5: Modifications to ring lattice
To make pretzel scheme works for 50 bunches, a few modifications need to be made to the ring lattice
Two options(assuming phase advance per cell keeps constant):
  Change the cell length, which will result in the change of emittance, circumference etc.
  Change number of cells, e.g. change the circumference
In the following, we take the easy way, i.e. we change the circumference to make the ring lattice works for pretzel orbit of 50 bunches.

## Slide 6: Changes made
ARC length:5852.8m
Short straight: 18 FODO cells, 849.6m
Long straight: 34 (was 20) FODO cells, 1604.8m (was 1132.8m)
Circumference: 56.640km
After making this change, every nearest parasitic collision points will have a phase advance of 4Pi.

## Slide 7: Comparison of DA results before adding pretzel
New version
v20150923
With same working point and chromatic correction scheme
Dramatic drop of DA at ±2% momentum spread

## Slide 8: Pretzel orbit design
Designed for 50 bunches/beam, every 4pi phase advance has one collision point
Horizontal separation is adopted to avoid big coupling
No off-center orbit in RF section to avoid beam instability and HOM in the cavity
One pair of electrostatic separators for each arc

## Slide 9: Pretzel orbit design (cont.)
Separation distance: ~5 sx for each beam (10 sx distance between two beam)
Maximum separation distance between two beams is : ~10 mm

## Slide 10: Issues with pretzel orbit
Estimation of dipole field strength in quadrupole
Estimation of quadrupole field strength in sextupole
Dipole field of the ring 0.066T.
Quadrupole field of the ring K1=0.022.
Dipole field of the ring 0.066T.
This causes the beta function, especially the dispersion function to oscillate as can be seen in the following slide.

## Slide 11
Issues with pretzel orbit
Beta function and dispersion function will oscillate due to pretzel orbit, in which the off-center particles see extra fields in magnets

## Slide 12: Correction of pretzel orbit effects
The distortion of pretzel orbit effects on beta functions
and dispersions can be corrected by making quadrupoles individually adjustable, which can be done by adding shunts on each quadrupoles
A new periodic solution can be found by grouping 6 FODO cells together as one new period

## Slide 13: New lattice after correction
After correction, the lattice regains periodicity
The distortion effects from pretzel orbit is corrected

## Slide 14: Chromatic properties
Tune is quite stable within ± 0.8% momentum spread
Beta function and dispersion function changes a lot within ± 0.8% momentum spread

## Slide 15: DA with pretzel
DA tracking is done with MAD8
240 turns (or 3 times transverse damping time ) is tracked
The DA is (6 sx*420sy) at ± 0.8% momentum spread

## Slide 16: Issues remained&Plan for next steps
DA results with MAD8 need to be checked with other codes, e.g. SAD, MADX etc..
Current pretzel correction scheme breaks the symmetry of lattice, which results in different optics seen by electron and positron beam, and should be corrected
The FFS should be combined with pretzel orbit
DA optimization should be done with pretzel orbit
………

## Slide 17: Summary
A ring lattice is developed for accommodating 50 bunches with pretzel orbit
A primary design of pretzel orbit is done
The primary DA tracking result shows a is (6 sx*420 sy) at ± 0.8% momentum spread
The DA result need to be checked with other codes and DA optimization should be carried out
More work is ahead ……

## Slide 18
Thank you !