## Slide 1: CEPC parameter optimization and lattice design
Dou Wang, Jie Gao, Feng Su, Yuan Zhang, Yiwei Wang,
Jiyuan Zhai, Zhenchao Liu, Bai Sha, Huiping Geng,
Tianjian Bian, Na Wang, Cai Meng, Qing Qin
CEPC-SppC study group meeting, Beihang, Beijing, Sep.3th 2016

## Slide 2: Difficulties of CEPC single ring scheme
 | H |  | Z | 
 | Pre-CDR | Low-HOM |  | 
Number of IPs | 2 | 2 | 2 | 
Energy (GeV) | 120 | 120 | 45.5 | 
Circumference (km) | 54 | 54 | 54 | 
SR loss/turn (GeV) | 3.1 | 3.1 | 0.062 | 
Ne/bunch (1011) | 3.79 | 1.0 | 0.13 | 
Bunch number | 50 | 187 | 4800 | 100
Beam current (mA) | 16.6 | 16.6 | 55.5 | 1.1
SR power /beam (MW) | 51.7 | 50 | 3.45 | 0.072
Bending radius (km) | 6.1 | 6.1 | 6.1 | 
Momentum compaction (10-5) | 3.4 | 3.4 | 3.4 | 
IP x/y (m) | 0.8/0.0012 | 0.06/0.001 | 0.4/0.0012 | 
Emittance x/y (nm) | 6.12/0.018 | 6.13/0.018 | 0.9/0.018 | 
Transverse IP (um) | 69.97/0.15 | 19.2/0.13 | 18.9/0.15 | 
x/IP | 0.118 | 0.031 | 0.072 | 
y/IP | 0.083 | 0.074 | 0.028 | 
VRF (GV) | 6.87 | 6.87 | 0.68 | 
f RF (MHz) | 650 | 650 | 650 | 
Nature z (mm) | 2.14 | 2.13 | 1.5 | 
Total z (mm) | 2.65 | 2.4 | 1.5 | 
HOM power/cavity (kw) | 3.6 | 1.0 | 0.55 | 0.01
Energy spread (%) | 0.13 | 0.13 | 0.05 | 
Energy acceptance (%) | 2 | 1.5 |  | 
Energy acceptance by RF (%) | 6 | 6.1 | 4.5 | 
n | 0.23 | 0.21 | 0.028 | 
Life time due to beamstrahlung_cal (minute) | 47 | 46 |  | 
F (hour glass) | 0.68 | 0.66 | 0.82 | 
Lmax/IP (1034cm-2s-1) | 2.04 | 2.1 | 1.04 | 0.022

## Slide 3
bypass (pp)
bypass (pp)
Advantage:
Avoid pretzel orbit
Accommodate more bunches at Z/W energy
Reduce beam power with crab waist collision

## Slide 4: Machine constraints / given parameters
Energy E0
Circumference C0
NIP
Beam power P0
y*
Emittance coupling factor 
Bending radius 
Piwinski angle 
y enhancement by crab waist Fl ~1.5 (2.6)
Energy acceptance (DA)
Phase advance per cell (FODO)

## Slide 5: Constraints for parameter choice
Limit of Beam-beam tune shift
Beam lifetime due to beamstrahlung
Beamstrahlung energy spread
HOM power per cavity
Fl: y enhancement by crab waist
*J. Gao, emittance growth and beam lifetime limitations due to beam-beam effects in e+e- storage rings, Nucl. Instr. and methods A533（2004）p. 270-274.
BS life time: 30 min
A=0/BS (A3)
V.I. Telnov

## Slide 6: parameter for CEPC partial double ring （wangdou20160325）
 | Pre-CDR | H-high lumi. | H-low power | W | Z
Number of IPs | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5
Circumference (km) | 54 | 54 | 54 | 54 | 54
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 0.59 | 0.062
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 2.5 | 2.6 | 5 | 8.5/7.6
Ne/bunch (1011) | 3.79 | 2.85 | 2.67 | 0.74 | 0.46
Bunch number | 50 | 67 | 44 | 400 | 1100
Beam current (mA) | 16.6 | 16.9 | 10.5 | 26.2 | 45.4
SR power /beam (MW) | 51.7 | 50 | 31.2 | 15.6 | 2.8
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.1 | 6.1
Momentum compaction (10-5) | 3.4 | 2.5 | 2.2 | 2.4 | 3.5
IP x/y (m) | 0.8/0.0012 | 0.25/0.00136 | 0.268 /0.00124 | 0.1/0.001 | 0.1/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.45/0.0074 | 2.06 /0.0062 | 1.02/0.003 | 0.62/0.0028
Transverse IP (um) | 69.97/0.15 | 24.8/0.1 | 23.5/0.088 | 10.1/0.056 | 7.9/0.053
x/IP | 0.118 | 0.03 | 0.032 | 0.008 | 0.005/0.006
y/IP | 0.083 | 0.11 | 0.11 | 0.074 | 0.084/0.073
VRF (GV) | 6.87 | 3.62 | 3.53 | 0.81 | 0.12
f RF (MHz) | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 3.1 | 3.0 | 3.25 | 3.9
Total z (mm) | 2.65 | 4.1 | 4.0 | 3.35 | 4.0
HOM power/cavity (kw) | 3.6 | 2.2 | 1.3 | 0.99 | 0.99
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.09 | 0.05
Energy acceptance (%) | 2 | 2 | 2 |  | 
Energy acceptance by RF (%) | 6 | 2.2 | 2.1 | 1.7 | 1.1
n | 0.23 | 0.47 | 0.47 | 0.3 | 0.27/0.24
Life time due to beamstrahlung_cal (minute) | 47 | 36 | 32 |  | 
F (hour glass) | 0.68 | 0.82 | 0.81 | 0.92 | 0.95
Lmax/IP (1034cm-2s-1) | 2.04 | 2.96 | 2.01 | 3.09 | 3.61/3.09

## Slide 7: Beam-beam simulation
Case: H-low power
Lifetime: 97 min(16)
Case Z
IBB: Strong-Strong Beam-Beam Code with Beamstrahlung effect
Developed by Y. Zhang@IHEP
Case: Pre-CDR
Lifetime: 108 min(16)
Lifetime: 118 min(16)
Case: H-high lum

## Slide 8: CEPC Higgs luminosity vs. crossing angle
54 km ring

## Slide 9: CEPC Higgs Luminosity vs beam power
54 km ring

## Slide 10: CEPC PDR Luminosity vs circumference
* Fabiola Gianotti, Future Circular ColliderDesign Study, ICFA meeting, J-PARC, 25-2-2016.

## Slide 11: 100km CEPC PDR vs Fcc-ee
PHOM,CEPC=11.3 kw
The large difference of Z is due to the constraint for RF HOM power.
* Fabiola Gianotti, Future Circular ColliderDesign Study, ICFA meeting, J-PARC, 25-2-2016.

## Slide 12: ARC lattice
FODO cell
Dispersion Suppressor
Sextupole configuration

## Slide 13: Non-interleave sextupoles in arc (90/90 FODO)

## Slide 14
Partial double ring region (w/o IR)

## Slide 15
Lattice of Interaction Region
IP
FT
CCX
CCY
MT
L*= 1.5m
x*= 0.22mm
y*= 1mm
GQD0= -200T/m
GQF1= 200T/m
LQD0=1.69m
LQF1=0.90m

## Slide 16: Partial double ring FFS design with crab sextupoles
Crab sextupole
Critical energy: Ec=190 keV
Dipole strength: B=0.019 T
Betax=0.25m
Betay=0.00136m
K2hs=26.8 m-3
K2vs=32.2 m-3
IP
The second FFS sextupoles of the CCS-Y section work as the crab sextupoles.

## Slide 17: Combine with partial double ring lattice
30 mrad
10 m

## Slide 18: CEPC IR sextupole strength
Ec=190keV
Ec=190keV
Ec=100keV

## Slide 19: DA of the whole ring (arc+PDR+bypass+FFS(incl. crab))
DA (on-momentum): 27x  58y
DA (0.5%): 2x  4y
Arc sextupole: 2 groups
Crab sextupoles - off
Bandwidth = 0.8%

## Slide 20: DA bandwidth optimization with MODE (knob IR sextupoles)
test15 from Zhang Yuan@IHEP
Bandwidth = 1%.
DA for small energy deviation is better.
On momentum DA is smaller.

## Slide 21: DA bandwidth optimization with MODE (knob arc sextupoles)
test16 from Zhang Yuan@IHEP
Bandwidth = 1.4%.
Both on-momentum and off-momentum DA is better.
Next step:
- Combine arc sextupoles with IR sextupoles.
- Add symmetry in arc

## Slide 22: Dynamic aperture optimization
Dynamic aperture result
  W/O error of the magnets
  Synchrotron motion included, w/o damping
  Tracking with around 1 times of damping time
  Coupling factor =0.003 for y
  Working point (0.08, 0.22)
Many cases of sextupole families tried
  Downhill Simplex algorithm applied
  Some typical results
  Further optimization is possible
    Further optimization with these families
    More families in IR
    y*= 1mm -> 1.36mm
    Larger dispersion for IR sextupoles
From yiwei@IHEP

## Slide 23
CEPC Advanced Partial Double Ring Layout I
SU Feng
2016.5.23
IP1_ee
IP3_ee
IP2_pp
IP4_pp
3Km
RF
1/2RF
1/2RF
1/2RF
RF
RF
RF
1/2RF
IP1_ee/IP3_ee, 2.968Km
IP2_pp/IP4_pp, 1132.8m
APDR, 1052.87m
4 Short Straights, 141.6m
4 Medium Straights, 566.4m
4 Long Straights, 1132.8m
4 ARC1, 124*FODO, 5852.8m
4 ARC2, 24*FODO, 1132.8m
4 ARC3, 79*FODO, 3728.8m
2 ARC4, 24*FODO, 1132.8m
C=62967.86m
1/2RF
1/2RF
1/2RF
1/2RF
Bypass
about 42m
ARC1
ARC3
ARC2
ARC3
ARC2
ARC4
ARC1
APDR
APDR
APDR
APDR

## Slide 24
ARC
CEPC Advanced Partial Double Ring Layout II
SU Feng
2016.6.2
IP1_ee
IP3_ee
3Km
1/2RF
1/2RF
1/2RF
1/2RF
IP1_ee/IP3_ee, 2.968Km
IP2_pp/IP4_pp, 1132.8m
APDR, 1052.87m
4 Short Straights, 94.4m
12 Long Straights, 566.4m
4 Long ARC, 124*FODO, 5852.8m
4 Medium ARC, 104*FODO, 4908.8m
4 Short ARC, 14*FODO, 660.8m
C=65640.2m
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
APDR
APDR
APDR
APDR
APDR
APDR

## Slide 25: Bunch length error with RF phase adjustment
H-high lum
H-low power
Z
For Z, error of bunch length: ~-1.5% (8 ring)
For H-high lum., error of bunch length: ~-3% (8 ring)
For H-low power, error of bunch length: ~-4% (6 ring), ~-3% (8 ring)

## Slide 26: Luminosity change with RF phase adjustment
H-high lum
H-low power
Z
For H-high lum., error of luminosity: ~3% (8 ring)
For H-low power, error of luminosity: ~ 3.5% (6 ring), ~2.4% (8 ring)
For Z, error of luminosity: ~1.7% (8 ring)

## Slide 27: RF voltage change with RF phase adjustment
H-high lum
H-low power
Z
For Z, error of VRF: ~ 2.6% (8 ring)
For H-high lum., error of VRF: ~ 2.6% (8 ring)
For H-low power, error of RF acceptance: ~ 2.8% (6 ring), ~ 2% (8 ring)
RF efficiency will be a little lower than 100%.

## Slide 28: BS life time with RF phase adjustment
For H-high lum., error of BS life time: ~-36% (8 ring)
For H-low power, error of BS life time: ~-37% (6 ring), ~-30% (8 ring)
H-high lum
H-low power
BS life time will be lower than the requirement!!

## Slide 29: CEPC damping ring requirement
Energy: 1.1GeV
Storage time: 20ms
Injected emittance (normalized): 3500 mm-mrad, injected energy spread ~ 0.25%
Extracted energy spread <1×10-3
No strong requirement for the extracted emittance (<0.5inj)!
Transverse acceptance > 3*injection beam size

## Slide 30: CEPC DR design
 | DR V1.0
Energy (GeV) | 1.1
circumference | 58.5
Bending radius (m) | 3.6
B0 (T) | 1.01
U0 (keV/turn) | 35.8
Damping time x/y/z (ms) | 12/12/6
0 (%) | 0.047
0 (mm.mrad) | 302
Nature z (mm) | 1.4 (4.7ps)
Extract z (mm) | ~1.5 (5ps)
inj (mm.mrad) | 3500
ext x/y (mm.mrad) | 434/145
inj /ext (%) | 0.25 /0.047
Energy acceptance by RF(%) | 5
fRF=650MHz

## Slide 31: DR lattice design
FODO length (m) | 2.4
Phase per cell | 60
Dipole length (m) | 0.71
Dipole strength (T) | 1.0
Quadrupole length (m) | 0.2
Quadrupole strength (m-2) | 4.1
Sextupole length (m) | 0.06

## Slide 32: summary
A consistent calculation method for CEPC parameter choice with carb waist scheme has been created. Larger ring has the potential to reach higher luminosity.
Based on partial double ring scheme, we can get higher luminosity (50%) keeping Pre-CDR beam power or to reduce the beam power (30 MW) keeping same luminosity.
FFS with crab sextupoles and lower emittance arc has been designed. On-momentum DA of whole ring is good enough and the optimization of DA bandwidth is underway.
Advanced partial double ring scheme has been proposed in order to improve the RF efficiency. Almost 100% efficiency can be achieved.
First version of CEPC damping ring design for the positron source has been given. Detail injection/extraction optics design and DA study is going on.

## Slide 33
Thanks！