## Slide 1: The Semi-Digital Hadronic Calorimeter for Future Leptonic Collider experiments
I. Laktineh
On behalf of the the
CALICE Collaboration

## Slide 2
SDHCAL technological prototype
Description
Test Beam results
Hadronic shower studies
R&D for large SDHCAL modules
Detectors
Electronics
DAQ
New challenges
Conclusion
Outline

## Slide 3
The structure proposed for the SDHCAL-ILD :
very compact with negligible dead zones
Eliminates projective cracks
Minimizes barrel / endcap separation
(services leaving from the outer radius)
SDHCAL-ILD
The SDHCAL-GRPC is one of the two HCAL options based on PFA and
Proposed for ILD of ILC. Modules are made of 48 RPC chambers (6λI)
equipped with semi-digital, power-pulsed electronics readout and placed
in self-supporting mechanical structure to serve as absorber
as well.
SDHCAL Technological Prototype should
be as much as possible similar to the ILD module
and able to study hadronic showers
Challenges
-Homogeneity for large surfaces
-Thickness of only few mms
-Lateral segmentation of 1 cm X 1 cm
-Services from one side
-Embedded power-cycled electronics
-Self-supporting mechanical structure

## Slide 4
The structure proposed for the SDHCAL-ILD :
very compact with negligible dead zones
Eliminates projective cracks
Minimizes barrel / endcap separation
(services leaving from the outer radius)
SDHCAL-ILD
The SDHCAL-GRPC is one of the two HCAL options based on PFA and
Proposed for ILD of ILC. Modules are made of 48 RPC chambers (6λI)
equipped with semi-digital, power-pulsed electronics readout and placed
in self-supporting mechanical structure to serve as absorber
as well.
SDHCAL Technological Prototype should
be as much as possible similar to the ILD module
and able to study hadronic showers
Challenges
-Homogeneity for large surfaces
-Thickness of only few mms
-Lateral segmentation of 1 cm X 1 cm
-Services from one side
-Embedded power-cycled electronics
-Self-supporting mechanical structure

## Slide 5
10500 64-ch ASIC were tested and calibrated using a
dedicated (ASICs layout : 93% ).
SDHCAL prototype construction
310 PCBs were produced, cabled and tested.
They were assembled by sets of six to make 1m2 ASUs
50 detectors were built and assembled with
their electronics into cassettes.
Self-supporting mechanical structure.
Full assembly took place at CERN.
170 DIF, 20 DCC were built and tested.
DAQ system using both USB and HTML protocol
was developed and used.

## Slide 6
10500 64-ch ASIC were tested and calibrated using a
dedicated (ASICs layout : 93% ).
SDHCAL prototype construction
310 PCBs were produced, cabled and tested.
They were assembled by sets of six to make 1m2 ASUs
50 detectors were built and assembled with
their electronics into cassettes.
Self-supporting mechanical structure.
Full assembly took place at CERN.
170 DIF, 20 DCC were built and tested.
DAQ system using both USB and HTML protocol
was developed and used.
Published: JINST 10 (2015) P10039

## Slide 7
SDHCAL performance
The SDHCAL prototype was exposed to hadron, muon and electron
beams in 2012, 2015 and 2016 on PS, H6 and H6
and these days H8-SPS lines.
Power-pulsing using the SPS spill structure was used to reduce the
power consumption.
Self-triggering mode is used but external trigger mode is possible
The threshold information helps to improve on the energy rec.
by better accounting for the number of tracks crossing one pad
New data were taken in 2015 with an improved DAQ system

## Slide 8
Event selection
No containment selection.
No Cerenkov detector

## Slide 9
The thresholds weight evolution with the total number
of hits obtained by minimizing a χ2
Χ2 = (Ebeam-Erec)2/Ebeam
Erec = α (Ntot) N1 + β(Ntot) N2 + γ(Ntot) N3
N1,N2 and N3 : exclusive number of hits associated to first,
second and third threshold.
α, β, γ are quadratic functions of the total number of hits (Ntot)
Events of H2 runs corresponding to energies : 5, 10, 30 , 60
and 80 GeV were used to fit the 9 parameters.
Then the energy of hadronic events in
both H2( only pions) and H6 (presence of protons)
Energy estimation

## Slide 10
Comparison semi-digital versus binary readout
Erec (binary) = C N tot + D N2 tot + F N3tot
Erec (semi-digital) = α (Ntot) N1 + β(Ntot) N2 + γ(Ntot) N3
Substantial improvement a energy > 30 GeV
Energy estimation
Published: JINST 11 (2016) P04001

## Slide 11
SDHCAL Simulation
A digitizer to describe the RPC response was developed. Parameters tuned using muons and electrons. Detector inefficiencies (dead channels) are included.
Electrons
Muons
Muons

## Slide 12
Comparison data/simulation
Published: JINST 11 (2016) P06014

## Slide 13
SDHCAL High-granularity impact
Hough Transform is an example to extract tracks within hadronic showers and to use them to control the calorimeter in situ
ρxz = z sin(θ) + x cos(θ)
Excellent agreement with results obtained with cosmic and beam-muons.
Excellent agreement data/MC

## Slide 14
SDHCAL High-granularity impact
Good tool to discriminate electron/hadron
It improves on the energy reconstruction by dealing with the hits belonging to the track segments independently of their threshold
The technique could be extended to hadronic showers in the presence of magnetic field.
Published:
JINST 12 (2017) P05009

## Slide 15
SDHCAL high granularity is good
It helps to optimize the connection of hits belonging to the same shower by using first the topology and then the energy information
ArborPFA algorithm*:
It connect first hits and then their clusters using distance and orientation information
Then correct using tracker information
CALICE note CAN054
* Algorithm idea was first developed by ALEPH collaboration
Efficiency
Purity
ΔE

## Slide 16
SDHCAL for future experiments
Detectors as large as 3m X 1m need to be built
Electronic readout should be the most robust with
minimal intervention during operation.
DAQ system should be robust and efficient
Mechanical structure to be similar to the final one
Envisage new features such timing, etc..
Goal: to build new prototype with few but large GRPC with the new components
SDHCAL
ILD Module
GRPC
Glass Resistive Plate Chambers

## Slide 17
2 m
1 m
inlet
outlet
Prototype circulation system
New circulation system
Detector conception
Construction and operation of large GRPC necessitate some improvements with respect to the present scenario.
Gas distribution : new scheme is proposed
Cassette conception to ensure good contact between the detector and electronics is to be improved

## Slide 18
DIF #1
DIF #2
DIF #3
144 ASICs= 9216 channels/1m2
USB
HDMI
ASU1
3072 ch
ASU2
DIF
100 cm
33 cm
HADROC chip
(ASIC)
1m2 board  6 ASUs hosting 24 ASICs
Electronics readout for the 1m3 prototipo
1 DIF (detector InterFace) for 2 ASU (Active Sensor Unit.- PCB+ASICs)  3 DIFs for ONE 1m2 GRPC detector
Electronics readout for the final detector
Only 1 DIF per GRPC (any size) with small dimensions to fit in the small space available at the ILD detector
DIF dimensions
ASUs of 1000 mmx333 mm are being produced
New electronics

## Slide 19
HARDROCR3 main features:
  Independent channels
  Zero suppress
  Extended dynamic range (up to 50 pC)
  I2C link with triple voting for slow control parameters
  packaging in QFP208, die size ~30 mm2
  Consumption increase (internal PLL, I2C)
6,3 mm
4,7 mm
H3B TESTED : 786, Yield : 83.3 %
New electronics: ASIC

## Slide 20: HARDROC3: Analog linearity
FSB0
FSB0: 5σ noise limit= 15 fC
Up to 10 pC
Up to 50 pC
Fast shaper outputs (mV) vs Qinj (fC)
50% trig. Eff. (DAC units) vs Qinj (fC)
Dynamic range: 15fC - 50 pC
FSB1
FSB2

## Slide 21
DIF sends DAQ commands (config, clock, trigger) to front-end and transfer their signal data to DAQ. It controls also the ASIC power pulsing
• Only one DIF per plane (instead of three)
• DIF handle up to 432 HR3 chips (vs 48 HR2 in previous DIF)
• HR3 slow control through I2C bus (12 IC2 buses).
Keeps also 2 of the old slow control buses as backup & redundancy.
• Data transmission to/from DAQ by Ethernet
• Clock and synchronization by TTC (already used in LHC)
• 93W Peak power supply with super-capacitors
(vs 8.6 W in previous DIF)
• Spare I/O connectors to the FPGA (i.e. for GBT links)
• Upgrade USB 1.1 to USB 2.0
FPGA XC7A35TFGG484
TEXAS TM4C1294U
POWER
POWER
POWER
New electronics : DIF

## Slide 22
Improvement on the present system is being made by using Electron Beam Welding rather than bolts to reduce the deformation and the spacers thickness.
Mechanical Structure
Industrial production of flat large absorber plates (3 m X 1 m) by roller leveling process

## Slide 23
Mechanical Structure
Very good flatness (< 1mm)
Chart: 
L1 Before | 1.9 | 2.5 | 2.5 | 1 | 2
L1 After | 0.2 | 0.2 | 0.2 | 0.1 | 0.2
Promising results but better performance is still needed

## Slide 24
Global system architecture
HR2, HR3, Petiroc..
For now, KC705
GBT
GLIB
Front-End control and data collection
Clocking and main FSM
PC
gEth
gEth
GBT
PC
GLIB
DIF
Roc based ASU
Clk
Sync cdes
SLC
Async cdes
Veto, trg
data
Implementation of a GBT-based communication system for ROC chips. This aims to reach higher performance using robust and well maintained system in the future
DAQ system

## Slide 25
Next step : Timing
Multi-gap RPC are excellent fast timing detectors
Several were designed and built . Excellent efficiency when tested with HARDROC ASICs. Next step use PETIROC (< 20 ps time jitters)
Timing could be an important factor to separate showers and better reconstruct their energy

## Slide 26
108 chips
Rectangular section tubes : 2x1 mm
Copper plate over: 1.5 mm
PCB plate under: 1.4 mm
symmetry
symmetry
1.5 m
0.5 m
Flow in
Flow out
Simulation ¼ structure pcb + chips
Water cooling :
h = 10000 W/m²/k
Thermal load :
80 mW/chip without power pulsing
27.147 (max) – 24.591 (min) =2.556 oC
Next step : cooling
Cooling becomes necessary if the power pulsing scheme is not possible (CEPC project)

## Slide 27
Conclusions and perspectives
SDHCAL is the first technological prototype to be conceived
and built for future leptonic experiments.
Results of beam tests validate the concept
New prototype is on the rails and in principle could be achieved before the end of 2017.
New features such as timing and cooling will play important role in future R&D for future colliders.

## Slide 29: Tests of small mechanical structures prototypes
Before assembly the big prototype (~3x1m2), welding tests with smaller prototypes are foreseen
Prototype after welding
First small prototype: 4 plates 1x1 m2
-0.48
+0.06
+0.14
+0.18
+0.54
+0.62
+0.85
+0.57
+0.21
+0.81
+0.1
+0.11
+0.16
-0.49
-0.50
-0.51
+0.53
+0.64
+0.51
+0.53
+0.49
+0.57
+0.49
+0.59
-0.51
-0.54
-0.52
-0.56
+0.07
+0.1
+0.24
+0.43
+0.73
+1.11
+0.5
+0.72
+1.01
+0.22
+0.13
+0.26
After comparing the measurements before and after welding deformations found (~1mm) bigger than expected in X-axis. O.K in Y-axis
 Probably due to the welding sequence used
Differences with respect to the initial status of the plate in Z.
Differences with respect to the initial status of the distance between plates
Measurements have been done AFTER REMOVING the PIECES used FOR RIDIGITY (the picture includes them)
Coordinate measuring machine

## Slide 30
Photogrammetry targets
zoom
2nd Prototype before welding
Second small prototype: 4 plates 1x0.5 m2
Deformations measure using photogrammetry
Welding performed changing a bit the welding sequence with respect to the first prototype

## Slide 31
Gas purifier
-Goal: reduce the gas consumption to reduce the cost.
-Gas renewal of 5-10% rather than 100%
-Conceived by the CERN gas group

## Slide 32
DQM4HEP: Data Quality Monitoring for High Energy Physics
This is a generic C++ framework to perform online data analysis and data quality report. It deals with online application workflow, inter-process communication and memory management.
Main features :
-Event distributed system (client / server architecture)
-Set of user interfaces designed for data quality analysis
-Monitor element distributed system
-Graphical user interface for data visualisation (Qt Gui)
-Large scale remote process management
-Generic IO support for different experiments
-Designed for simple prototype monitoring up
to complex systems like ILD or LHC detectors
-Logbook interface (ELog)
Online monitoring

## Slide 33
Example: Hit map control