## Slide 1: Data transmission system for 2D-SND at CSNS
ZHAO Dongxu1, 3 ZHANG Hongyu2, 3 WANG Xiuku1, 3 TIAN Haolai1 ZHANG Junrong1
1, China Spallation Neutron Source (CSNS), Institute of High Energy Physics(IHEP), Chinese Academy of Sciences(CAS), Dongguan 523803, Peoples Republic of China
2, Institute of High Energy Physics (IHEP), Chinese Academy of Sciences (CAS), Beijing 100049, Peoples Republic of China
3, State Key Laboratory of Particle Detection and Electronics, Beijing 100049, Peoples Republic of China

## Slide 2: Outline
Introduction
  About CSNS
  GPPD components
Implementation of data transmission system
  Data processing framework
  Interface with DAQ
  Interface with data analysis system
An application
  A neutron beam experiment
Conclusion

## Slide 3: Introduction
About CSNS
China Spallation Neutron Source (CSNS) is the first high-performance pulsed neutron source in China.
Facilities:
  Accelerator
    H- linac
    proton rapid cycling synchrotron
  Target
  Instruments(day-one)
    General purpose powder diffractometer(GPPD)
    Board Q-range small angel diffractometer
    Multi-purpose reflectometer
Schematic layout of CSNS facilities

## Slide 4: Introduction
GPPD components
  Scintillator neutron detector(2D-SND)
    4 banks(9 modules in every bank, 36 modules in total)
    192 channels in every module
  Relative systems for 2D-SND:
    Electronics system
    Data acquisition (DAQ) system
    Data transmission system
    Data analysis system
GPPD components
One module of 2D-SND
2D-SND model

## Slide 5: Introduction
Electronic system:
  Components: 36 modules with 192 electronic channels in every module (corresponding 36 modules of 2D-SND)
  Functions: get 2D-SND signals; amplify signals; convert signals to digital data; construct data to raw events; send raw events to DAQ system.
  Technologies: SiTCP
DAQ system:
  Functions: read raw events; save raw events.
  Technologies: QT(user interface); C++; multi threads; NFS
Data transmission system:
  Functions: get raw events from DAQ system; pick good events; transfer good events to data analysis system.
  Technologies: C; multi threads; mutex lock; NFS; DIM
Data analysis system:
  Functions: receive good events; reconstruct events; analyze reconstructed events; display results in the form of charts.
  Technologies: C++; Python; multi threads; DroNE; NEON; DataPilot;

## Slide 6: Implementation of data transmission system
Main tasks:
  getting raw events from DAQ system
  picking good events
  sending these good events to data analysis system
Divided parts:
  package of data process
  interface with DAQ
  interface with data analysis system

## Slide 7: Implementation of data transmission system
Data processing package
  Technologies
    C programming language
    multithreads
    Mutex lock
Head flag 0xFA | Spectrometer ID | Detector ID | Module ID
Run mode | Frequency dividing mode | Data vision number | Reserve 1
T0 Count |  |  | 
Reserve 2 |  |  | 
Channel No | T Data |  | 
Channel No | T Data |  | 
…… |  |  | 
Channel No | T Data |  | 
Filling data flag 0xF0 | Data filled 0x0 |  | 
Tail flag 0xFB | Status |  | 
Byte Count |  |  | 
Event format
Events accord with event format are considered good events and picked out.

## Slide 8: Implementation of data transmission system
Thread 1
Thread n
Flow chart of data process

## Slide 9: Implementation of data transmission system
Interface with DAQ
The interface between DAQ system and data transmission system is adopted Network File System (NFS).
Why is NFS?
provides an environment with capability of mutual interference for multi system architectures.
provides a simple and quick method to programme to fulfil resource access.
Interface with DAQ

## Slide 10: Implementation of data transmission system
Diagram of calling NFS interface in DAQ system
Diagram of calling NFS interface in data transmission system

## Slide 11: Implementation of data transmission system
Interface with data analysis system
Distributed Information Management System (DIM) developed by European Organization for Nuclear Research (CERN) is adopted to be the interface between data transmission system and data analysis system.
Name server
Data transmission system
DIM server
Data analysis system
DIM client
Register
Services
Request
Service
Subscribe to Service
Service events
Commands
Service
Info
DIM architecture
Features of DIM
  providing a network transparent inter-process communication layer.
  based on the client/server paradigm.
  basic concept of "service".
  realizing loose coupling.
  very efficient in data transmission.

## Slide 12: Implementation of data transmission system
Diagram of calling DIM server in data transmission system
Diagram of calling DIM client in data analysis system

## Slide 13: An application
A neutron beam experiment
The data transmission system together with 2D-SND and other relative systems has been applied in neutron beam experiment successfully.
Experiment environment:
  Beam intensity: 106 - 107 c/s
  Event rate of each module: 25 Hz
  Module number of detector in experiment: 3
  Total event rate: 75Hz
Image of neutron imaging on
one module of 2D-SND
In experiment, no event lost in process of data transmission.

## Slide 14: Conclusion
Data transmission system:
  A stable and efficient mechanism to realize credible data transfer.
  With the common framework, can easily be expanded and improved.
What can we do in the future?
To fulfil real-time on data transmission and online data analysis, the interface with DAQ system should be improved.
To improve efficiency further, distributed environment should be involved.

## Slide 15
Thanks!