## Slide 1: Detectors For Electron Ion Colliders
Rik Yoshida
Jefferson Lab
May 22, 2017
TIPP2017, Beijing, China

## Slide 2: Introduction
Current Electron-Ion Collider Concepts

## Slide 3: Electron Ion Collider (EIC)
Electron Ion Collider (EIC)
  It is a Deep Inelastic Scattering Collider
  Point-like probe interacts with p/A
  Science aims of the EIC
    Probe Nuclear and Nucleon Structure
    Laboratory for Quantum Chromo Dynamics.
    Search for certain types of BSM particles (e.g. Leptoquarks)
    Higgs Factory with excellent kinematic control. (Scattered electron fixes the kinematics)
  Which aims play the primary role depends on the parameters of the EIC, such as the center-of-mass energy, luminosity, etc.
NP oriented
HEP oriented

## Slide 4: Concepts for Electron-Ion Colliders
High Energy Physics oriented EICs
  LHeC/FCC-eh: Build 60 (120) GeV electron ERL at CERN and collide with LHC/FCC
  hadrons.
    √s = 1.3/3.5 (1.6/7.0) TeV
    Luminosity = 1034 cm-2s-1
    Information
    Studies continuing to EU2019 planning cycle.
  Very High Energy Electron Proton Collider (VHEeP): Use proton beam driven plasma accelerator (AWAKE) at the LHC to produce 3 TeV electron beams and collide with the LHC beam.
    √s = 9 TeV
    Luminosity = 4 × 1028 cm-2s-1
    Very early concept stage: Workshop, Munich June 1,2 2017
  CepC × SppC?

## Slide 5: Concepts for Electron-Ion Colliders
Nuclear Physics oriented EICs
  EIC@HIAF (Phase 2 HIAF)
    √s = 15 GeV
    Luminosity: 3-5×1032 cm-2 s-1
    Polarized beams
Heavy Intensity Heavy Ion Accelerator Facility (HIAF)
Phase 1 approved 2015
Taken from Xurong Chen talk at the 8th Workshop on Hadron Physics in China
9th Workshop on H.P. in China
Nanjing, July 24-28, 2017

## Slide 6: Concepts for Electron-Ion Collider
The Electron-Ion Collider in the US
  US Nuclear Physics Long Range Planning: has been highly successful.
Every 5-7 years the US Nuclear Science community produces a Long-Range Planning (LRP) Document.
October 2015 -> Latest Report Finalized (Including cost review of EIC)
High Energy Electron-Ion Collider is the highest priority for new facilities in the next decade (after FRIB completion)
USDOE (NP) is acting based on this planning
US National Academy of Science Review on-going
(The EIC case must be endorsed by the larger
science community)

## Slide 7: US EIC Parameters and Realization Plans
US EIC Machine design aims from the EIC Whitepaper
  Highly polarized (~70%) electron and nucleon beams.
  Ion beams from deuterons to the heaviest nuclei (uranium or lead).
  Variable center of mass energies from ~20 - ~ 100 GeV, upgradable to ~140 GeV.
  High luminosity: ~10 33-34 cm-2 s-1
  Possibility of having more than one interaction region.
Two proposed realization plans
  Jefferson Lab: building on the existing 12 GeV CEBAF. JLEIC Design.
  BNL: building on the existing RHIC. eRHIC Design.
  Recent review of acc. R&D
Similar performances, cost according to LRP assessment.
US EIC will likely be down-selected from one of these proposals.
Jefferson Lab
Brookhaven Lab

## Slide 8: US EIC Timeline
A US National Academy of Sciences study has been initiated and the committee is now formed. Charge: “assess the scientific justification for a U.S. domestic electron ion collider facility, “
The NAS committee plans to finalize its report in 7-8 months from now.
  DOE project “CD0” (Establish Mission Need) will be after the NAS study: i.e end 2017, early 2018 most optimistically.
  EIC construction has to start after FRIB completion, with FRIB construction anticipated to start ramping down near or in FY20.
Most optimistic scenario would have EIC construction start (CD3) in FY20, perhaps more realistic FY22-23 timeframe
Best guess for EIC completion: 2025-2030.

## Slide 9: Physics Aims and Detector Requirements
In this talk, I will concentrate on the detectors for Nuclear Physics oriented realizations of Electron-Ion Colliders… and stick to general requirements.
Implications for detectors
  Center of mass energy is lower (15 – 140 GeV) as opposed to (1.3 to 9 TeV)
    The collisions will not be extremely asymmetric (e.g. 60 GeV x 50000 GeV for FCC-eh).
  The most demanding performance requirements will be driven by measurements of the nucleon and nuclear structure.
What about HERA collider (1992-2007) detectors (H1 and ZEUS) as reference?
electrons
protons
ZEUS
H1
HERMES
HERA-b
√s = 300 GeV
Luminosity ~ 1031cm-2s-1
DESY laboratory in Hamburg, Germany
Turns out next generation EICs have
different needs.

## Slide 10: Progress in pQCD Theory (~1980-~2010)
Parton Distribution Functions:
Longitudinal only—
No way to interpret nucleon
partonic structure in rest frame
3D (Transverse) Structure
TMD’s, GPD’s—
Now we know what to measure to
understand the partonic structure of nucleons
Jefferson Lab 12 GeV program based on this progress.
How do we get the complete picture:
origin of mass, spin, nuclear forces…? EIC!
(Q2)
“HERA”
“EIC”

## Slide 11: Detectors for EICs
General Design Considerations

## Slide 12: DIS and Final State Particles
Ion beamline
Electron beamline
Eelectron
Eion
Aim of EIC is nucleon and nuclear structure beyond the longitudinal description.
This makes the requirements for the machine and detector different from all previous colliders including HERA.
Need more than this

## Slide 13: Final State Particles in the Central Rapidity
Ion beamline
Scattered electron
Particles associated with struck parton
Photons
Electron beamline
Eelectron
Eion
Products of the hard
electron-quark collision
Transverse and flavor structure measurement of the nucleon and nuclei:
The particles associated with struck parton must have its species identified and measured. Particle ID much more important than at HERA

## Slide 14: Final State Particles in the Central Rapidity
Ion beamline
Electron beamline
Eelectron
Eion
Boosted towards ion beam
Boosted towards ion beam
Asymmetric collision energies will boost the final state particles in the ion beam direction: Detector requirements change as a function of rapidity

## Slide 15: Particles Associated with the Initial Ion
Ion beamline
Particles Associated with Initial Ion
Electron beamline
Eelectron
Eion
For EIC, particles of the “target remnant” is
as important as the struck parton
Was not considered at HERA initially.
Close to the beamline
Not analyzed by central solenoid.
Aim for ~100% acceptance and good resolution at EIC.
Remember acceptance is equally
important as luminosity!

## Slide 16: Particles Associated with the Initial Electron
Ion beamline
beam electron (or low Q2)
Photons
Electron beamline
Eelectron
Eion
Forward Electron area:
Tag photoproduction (Q2≈0)
Measure Luminosity
Measure electron polarization
Apply lessons from HERA, JLab and elsewhere

## Slide 17: Final State Particles
Ion beamline
Scattered electron
Particles associated with struck parton
beam electron (or low Q2)
Photons
Photons
Electron beamline
Particles Associated with Initial Ion
The aim is to get ~100% acceptance
for all final state particles, and measure
them with good resolution.
Central
Detector
Beam Elements
Beam Elements
Beam elements limit forward acceptance
Central Solenoid not effective for forward

## Slide 18: Interaction Region Concept: eRHIC
Ion beamline
Electron beamline
10 mr
Solenoid
Dipole
NOT TO SCALE!
Large beam crossing angle creates
room for high acceptance forward
detectors.
Beamline magnets analyze the forward particles
Forward
Detectors

## Slide 19: Interaction Region Concept: JLEIC
Ion beamline
Electron beamline
50 mr
Solenoid
Dipole (1 of 3)
Dipole (1 of 4)
NOT TO SCALE!
Very large beam crossing angle
(50 mr) creates room for
forward dipoles
Dipoles analyze the forward particles
and create space for detectors in the forward direction

## Slide 20: Interaction Region Concept
Ion beamline
Electron beamline
Possible to get ~100% acceptance for the whole event
Total acceptance detector (and IR)

## Slide 21: EIC Detector and IR Layout
Extended detector: 80+ m
eRHIC
JLEIC
EIC detectors must be extremely well integrated with the accelerator

## Slide 22: Central Detector

## Slide 23: Final State Particles in the Central Detector
Scattered electron
Eelectron
Eion
Products of the hard
electron-quark collision
Took away the (exaggerated)
beam crossing for simplicity
Particles associated with struck parton
Took away radiated photon
for simplicity

## Slide 24: Basic Kinematic Reconstruction
E’e
Ejet
θe
θjet
Q2  Measure of resolution
y  Measure of inelasticity
x  Measure of momentum fraction
of the struck quark in a proton
Q2 = s x y
E’e,θe ,Ejet ,θjet : any two of these, in principle, sufficient to reconstruct x and Q2.
What are the detector
requirements?

## Slide 25: Reconstruction for Transvers Structure
Looking at out-of –plane component in the final state
Need to identify and measure
these particles
What are the detector
requirements?
Note: multiplicities are low (~20 for ep)
Cross-sec x Lumi < 0.01 x HLLHC
< 0.1 interaction/crossing

## Slide 26: How Boosted is the Final State?
Boosted towards ion beam
Eion= 100 GeV
Eelectron= 10 GeV
No Monte Carlo needed to Determine
E’e,θe ,Ejet ,θjet : any two of these, in principle, sufficient to reconstruct x and Q2.
Given x and Q2, E’e,θe ,Ejet ,θjet are all
fixed

## Slide 27: Electron Isoline Plot
Hadron Endcap
Barrel
Electron Endcap
Far-forward Electron
(out of central detector)

## Slide 28: Quark(Jet) Isoline Plot
Barrel
Hadron Endcap
Far-forward Hadron
(Out of central detector)
Electron Endcap
(Ejet)

## Slide 29: Particle Distribution
E-endcap
Barrel
H-endcap
E'e
Ejet
<8 GeV
8-50 GeV
>50 GeV
~10-50 GeV
<10 GeV
<10 GeV
<15 GeV
~15-50 GeV
low
medium
high
20-100 GeV
E,hadrons
occupancy
π± Energy
GeV
10
100
Pythia MC
η

## Slide 30: Example 1: BNL Reference Detector

## Slide 31: Example 2: Current Jefferson Lab Concept

## Slide 32: Electron-Beam line Detectors

## Slide 33: Chicane for Electron Forward Area for JLEIC
Extended detector: 80+ m

## Slide 34: Luminosity Measurement
Use Bethe-Heitler process to monitor luminosity: same as HERA

## Slide 35: Low Q2 Tagger

## Slide 36: Polarization Measurement
Note the off-momentum electrons from IP does not enter the
Compton tracker for polarimetry.

## Slide 37: Compton Polarimetry
Existing Polarimeter in Hall C at JLab: Achieved 1% Precision

## Slide 38: Luminosity Monitor and Low-Q2 Tagger at eRHIC
Richard Petti: Spin’16

## Slide 39: Forward Hadron Direction

## Slide 40: eRHIC Forward Hadron Detector Concept
Richard Petti Spin 2016

## Slide 41: Ion optics for near-beam detection
Extended detector: 80+ m
A large dispersion at the detection point separates scattered (off-momentum) particles from the beam.
A second focus and small emittance (cooling) allows moving detectors closer to the beam
2nd focus on
Roman pots

## Slide 42: EIC forward detection requirements
Good acceptance for recoil nucleons (rigidity close to beam)
  Diffractive processes on nucleon, coherent nuclear reactions
  Small beam size at detection point (to get close to the beam)
    Secondary focus on roman pots, small beam emmittance (cooling)
  Large dispersion (to separate scattered particles from the beam)
Good acceptance for fragments (rigidity different than beam)
  Tagging in light and heavy nuclei, nuclear diffraction
  Large magnet apertures (low gradients)
  Detection at several points along a long, aperture-free drift region
Good momentum- and angular resolution
  Free neutron structure through spectator tagging, imaging
  Both in roman pots and fixed detectors

## Slide 43: An Example: Diffractive DIS
Signature for Saturation (among other things)
Identify the scattered proton: distinguish from proton dissociation
Measure XL= Ep’/Ep, and Pt (or t) (equiv. to measuring Mx)

## Slide 44: Acceptance for p’ in DDIS
Acceptance in diffractive peak (XL>~.98)
ZEUS: ~2%
JLEIC: ~100%
JLEIC
ZEUS
Leading Proton Spectrometer
Region 2 (Hi. Res)
Region 1
t
XL
1
Pt
0.2
0.994
1
XL
(GeV)
(GeV2)
0
1
2.5

## Slide 45: Conclusions

## Slide 46: Conclusions
Plans for Nuclear Physics oriented Electron-Ion Colliders are advancing in the US and China.
  Currently modest R&D funding available from US DOE NP
    Directed Detector R&D for Electron-Ion Collider
    Call for proposals for FY18 (Due June 16, 2017)
I discussed the general design considerations of a NP oriented EIC detector.
  More specific detector information can be found, for example at
    Richard Petti at SPIN 2016 (here)
    Yulia Furletova at the 3D Modeling Workshop (here)
The physics of EIC demands a total acceptance detector with special characteristics.
  Some features/requirements not discussed:
    Many different ion species
    Variable center of mass energy (20 to 140 GeV)
    Variable solenoid field?
The detector design is still in very early stages. Plenty of scope for you to get involved!

## Slide 47
The EIC Users Group: EICUG.ORG
670 collaborators, 28 countries, 150 institutions... (December, 2016)
(no students included as of yet)
The EIC Users Meeting at Stony Brook, June 2014:
  http://skipper.physics.sunysb.edu/~eicug/meeting1/SBU.html
The EIC UG Meeting at University of Berkeley, January 6-9, 2016
  http://skipper.physics.sunysb.edu/~eicug/meeting2/UCB2016.html
The EIC UG Meeting at Argonne National Laboratory July 7-10, 2016
  http://eic2016.phy.anl.gov
Next meeting:
July 18-22, 2017 Trieste, Italy (Detectors will be one of the topics)

## Slide 49: JLEIC Detector and IR Document
Can be found at the JLEIC Public Wiki page
at: https://eic.jlab.org/wiki
This a short 9-page general introduction
for people new to JLEIC.
More specific and detailed documents
to follow.

## Slide 50: Bunch spacing and identification
Example: CLAS detector at JLab 6 GeV
  2 ns bunch spacing (500 MHz rep. rate)
  0.2 ns TOF resolution (0.5 ns FWHM)
  The figure shows time matching of kaons in CLAS with electrons in the (low-Q2) tagger, in turn matched to the accelerator RF signal
    The 2 ns bunch structure is clearly resolved
  CLAS12 aims at a TOF resolution of 80 ps
Δt [ns]
electron-kaon counts
K-e coincidence time in CLAS 6 GeV data
The bunch spacing in the MEIC is similar to CLAS and most e+e- colliders
  PEP-II/BaBar, KEKB/Belle: 8 ns
  Super KEKB/Belle II: 4 ns (2 ns with all RF buckets full)
  MEIC: 1.3 ns [750 MHz]
  CERN Linear Collider (CLIC): 0.5 ns [2 GHz]
Existing detectors (CLAS, BaBar, etc) at machines with high bunch crossing rates have not had problems in associating tracks with a specific bunch.

## Slide 51: Instantaneous rates
Events (e-p collisions) per bunch crossing | 1.33 ns spacing (MEIC) | 133 ns spacing (~HERA)
DIS @ L=1034 | 10-3 | 10-1
photo @ L=1034 | 10-1 | 10
DIS @ L=1032 | 10-5 | 10-3
photo @ L=1032 | 10-3 | 10-1
Order-of-magnitude estimates of the instantaneous DIS and photoproduction rates based on a 7.5 mb total e-p cross section.
For a given luminosity, increasing the crossing rate reduces the number of collisions per crossing, making it easier to resolve individual events.
  Note that the average collision rate does not depend on the bunch structure
The number of collisions per crossing in the MEIC is comparable to HERA.
Event spacing is particularly important for time matching of tracks in the central and far-forward detectors.
  Only the former pass the vertex tracker
  Photoproduction events also give rise to hadrons at small angles.
Matching is further improved by good resolution in the far-forward detectors.
  Angular for path-length corrections
  Momentum for β corrections
  Timing < 1 ns

## Slide 52: DIS Collider: Beam background
HERA II IR
JLEIC IR
95% of background: proton-(synch-induced)gas from this region.
Electron bends at ~10 m for head-on collision with proton. Synch fan.
The two beams share ~20m beam pipe
Synchrotron from final focus goes in the proton beam direction
HERA II
No electron bend before IP. (last bend 120 m away)
Two beams share only 2 m of beam pipe.
Synchrotron from final focus doe not go in the proton beam direction.
JLEIC
Should be much better but needs quantification and validation