## Slide 1: Design and performances of the Electromagnetic Particle Detector and the prototype array for LHAASO-KM2A
Liu jia
Institute of High Energy Physics, CAS
TIPP2017

## Slide 2: Outline:
Introduction
Experiment set up
Performances of LHAASO-KM2A prototype array
Conclusion

## Slide 3: LHAASO
KM2A
WFCTA
WCDA

## Slide 4
10 photons/year/km2
Background free
Exposure/year:
>2000 km2hr
/p discrimination power:10-4-10-5
1km2 array
Electromagnetic Particle Detector(ED) coverage 0.5%
  ~5000m2
Muon detector (MD) coverage 5%
  ~50000m2
Wide field of view
Energy resolution: 20%@100TeV
Sensitivity: 1%ICrab@100TeV
KM2A: Gamma ray astronomy beyond 10 TeV

## Slide 5: KM2A
5261 EDs, 1 m2 each, 15m spacing
1146 MDs, 36 m2 each, 30m spacing

## Slide 6: ED Specifications
15 m
15 m
15 m
15 m
15 m
15 m
15 m
15 m
15 m
Item | Value
Effective area | 1 m2
Thickness of tiles | ~2 cm
Number of WLS fibers | 32/tile4 tile
Detection efficiency (> 5 MeV) | >95%
Dynamic range | 1-10,000 particles
Time resolution | <2 ns
Particle counting resolution | 25% @ 1 particle 5% @ 10,000 particles
Aging (<20%) | >10 years
Spacing | 15 m
Total number of detectors | 5261
15m

## Slide 7: Electromagnetic Particle Detector (ED)
Steal Case
Lead(0.5cm)
SC Tiles
Steal Case
A sketch map
1 m
0.25 m

## Slide 8: The performance of KM2A array according to the simulation：
For proton and gamma rays, the energy resolution is about 35% at 30TeV and 15% at 1 PeV.
Energy resolution：
For proton and gamma rays, the angular resolution is about 0.5 degree at 30TeV and 0.2 degree at 1 PeV.
When 20 ntrig fired，the angular resolution is about 1.4 degree.
Angular resolution：

## Slide 9: KM2A prototype array @Tibet-YBJ
Introduction of two prototype array：
A 42-ED array fully overlapping with ARGO-YBJ (2010.10---2012.10)
A 42-ED+2MD array with front-end digitization, WR and “triggerless” DAQ (2014.10---2016.10)

## Slide 10: The prototype array overlaps with the ARGO array, so we can match event one by one. (above 95% event of km2a prototype array can match to ARGO’s)
The prototype array of about 1% size of KM2A was built at ARGO Hall
75m
An example shower front observed by ARGO (blue) and the prototype array (red).

## Slide 11
“Triggerless” DAQ
5mm lead plate on the plastic scintillation tiles
ARGO HALL Hall
WR time system
front-end digitization

## Slide 12
Performances of the KM2A prototype array:
Event Rate:
Event rate agrees with MC and ARGO-YBJ

## Slide 13: Energy response ：
Prototype array's number of particles vs. ARGO's number of strips.
The distribution of number of hits (in log-
scale) registered by ARGO-YBJ for ARGO-YBJ events (solid) and hybrid events with prototype array's number of hits > 5 (dotted) and > 20(dashed).
Notes: The reconstructed en-
ergy by ARGO-YBJ is indicated by the upper
scale.

## Slide 14: Shower direction reconstruction
The zenith angle distribution of ARGO(blue) and prototype array(red)
The azimuth angle distribution of ARGO(blue) and prototype array(red)

## Slide 15
Distribution of space angles between the shower directions measured by the KM2A prototype array and the ARGO-YBJ experiment.
Event selection: nhit> =20 hits core reconstructed by ARGO location within 10 m to the center of the array
Space angle:

## Slide 16
Angular resolution in different hit range:
Formula of estimating angular resolution :

## Slide 17
The angular resolution of the prototype array has been estimated by Chess-board
The even-odd space angle before and after the lead was placed. The improvement of the angular resolution is a factor 1.35
The improvement of angular resolution with 0.5cm-thick lead:

## Slide 18: Cosmic ray moon shadow
The significance map of the sky around the Moon. Observed moon shadow by 5.8σ in 2 years.

## Slide 19: Conclusion
The two KM2A prototype arrays stable operation more than two years.
The performances of KM2A prototype array meet design requirement.

## Slide 20
Thanks for your attention

## Slide 22
Long term stability:
The event rate of the prototype array (hollow) and the air pressure (solid) varying with time. Change of event rate (hollow) agrees with air pressure change.
The relative variation of average charge in case of MIPs for an ED (solid) and its ambient temperature (hollow) varying with time. Signal charge (solid) varies <±1%, agrees with PMT temperature coefficient (-0.2%/oC).
Notes: Change of event rate (hollow) agrees with air pressure change.
Signal charge (solid) varies <±1%, agrees with PMT temperature coefficient (-0.2%/oC).
The resulting temperature coefficient of about
0.2% per degree is consistent with that of the PMT.