## Slide 1: CEPC parameter optimization and lattice design
Dou Wang, Yuan Zhang, Yiwei Wang, Chenghui Yu, Na Wang, Huiping Geng, Jiyuan Zhai, Yudong Liu, Sha Bai, Xiaohao Cui, Tianjian Bian, Cai Meng, Weiren Chou, Jie Gao
Many Thanks: K. Oide(KEK), Y. Cai (SLAC), C. Zhang (IHEP), D. Zhou(KEK)
6-8 November 2017, IHEP.
International Workshop on High Energy Circular Electron Positron Collider

## Slide 2: Outline
CEPC CDR parameters
Combined magnet scheme (D+S) based on CDR lattice
Alternative lattice design for collider ring

## Slide 3: CEPC layout
CEPC is a double ring collider with two IPs, shared SCRF for Higgs.
SR power/ beam was limited ~ 30 MW due to the power budget.
Z parameters were designed based on the Higgs factory. No cost increase.
C0=100km

## Slide 4: Constraint for CEPC parameter choice
Limit of Beam-beam tune shift
Beam lifetime due to beamstrahlung
Beamstrahlung energy spread
HOM power per cavity (coaxial coupler)
Fl: y enhancement by crab waist
BS life time: ~30 min
A=0/BS (A5)
SR beam power
SR power for single beam:  30 MW
(Fl=1.7@H 2.0@W, 2.6@Z)

## Slide 5: CEPC CDR parameters
 | Higgs | W | Z
Number of IPs | 2 |  | 
Energy (GeV) | 120 | 80 | 45.5
Circumference (km) | 100 |  | 
SR loss/turn (GeV) | 1.68 | 0.33 | 0.035
Half crossing angle (mrad) | 16.5 |  | 
Piwinski angle | 2.75 | 4.39 | 10.8
Ne/bunch (1010) | 12.9 | 3.6 | 1.6
Bunch number | 286 | 5220 | 10900
Beam current (mA) | 17.7 | 90.3 | 83.8
SR power /beam (MW) | 30 | 30 | 2.9
Bending radius (km) | 10.9 |  | 
Momentum compaction (10-5) | 1.14 |  | 
IP x/y (m) | 0.36/0.002 |  | 
Emittance x/y (nm) | 1.21/0.0036 | 0.54/0.0018 | 0.17/0.0029
Transverse IP (um) | 20.9/0.086 | 13.9/0.060 | 7.91/0.076
x/y/IP | 0.024/0.094 | 0.009/0.055 | 0.005/0.0165
VRF (GV) | 2.14 | 0.465 | 0.053
f RF (MHz) (harmonic) | 650 (217500) |  | 
Nature bunch length z (mm) | 2.72 | 2.98 | 3.67
Bunch length z (mm) | 3.48 | 3.7 | 5.18
HOM power/cavity (kw) | 0.46 (2cell) | 0.32(2cell) | 0.11(2cell)
Energy spread (%) | 0.098 | 0.066 | 0.037
Energy acceptance requirement (%) | 1.21 |  | 
Energy acceptance by RF (%) | 2.06 | 1.48 | 0.75
Photon number due to beamstrahlung | 0.25 | 0.11 | 0.08
Lifetime due to beamstrahlung (hour) | 1.0 |  | 
Lifetime (hour) | 0.33 (20 min) | 3.5 | 7.4
F (hour glass) | 0.93 | 0.96 | 0.986
Lmax/IP (1034cm-2s-1) | 2.0 | 4.1 | 1.0

## Slide 6: luminosity
Luminosity of H & W limited by the SR power 30 MW.
Luminosity of Z limited by TMCI and electron cloud instability.
-- Luminosity @ H: 2.01034 cm-2s-1, 286 bunches
-- Luminosity @ W: 4.11034 cm-2s-1, 5220 bunches
-- 2.6nC/bunch  TMCI
-- Luminosity @ Z: 1.01034 cm-2s-1, 10900 bunches
-- The minimum bunch separation for Z due to electron cloud effect is 25 ns.

## Slide 7: Beam-beam tune shift
definition
 | H | W | Z
x/y/IP | 0.024/0.094 | 0.009/0.055 | 0.005/0.0165
Why not larger y
-- H: y close to the beam-beam limit
-- W& Z : y limited by the single bunch instability
Why not larger x
-- larger x introduce coherent beam-beam instability (x-z resonance)

## Slide 8: Hour glass effect
Hour glass factor:
Effective bunch length: overlap area of colliding bunches

## Slide 9: Beam-beam simulations
H
H
W
Z
Beam-beam simulations agree well with the parameter design.

## Slide 10: y* choice – 2mm
Luminosity can be increased by reducing y*
Why not smaller by*?
Maximum bata-function in the final focusing quadrupole, by,FFQ=L*2/by*, where the L*, defined as the distance from the FFQ to IP, is restricted by the geometry of the detector.
Large byFFQ requires high strength + large aperture of FFQ;
Large byFFQ also generates larger chromaticity, linear Dxy= (bykl)FFQ/4p and higher order term, reduce the energy acceptance of DA.
Nonlinearity of kinematic effects due to small by*, cause dynamic aperture problem

## Slide 11: Beamstrahlung effect @Higgs
Typical issue for energy-frontier e+e− colliders
During collision, the deflected particles will lose part of its energy due to the synchrotron radiation.
Extra energy spread
Beam loss for large energy deviation  life time reduction
Detector background (photons, hadrons…)
Divergence angle  interfere the detection of small-angle events
Constraint for energy spread
Constraint for life time
Large energy acceptance is essential!
Nature energy spread: 0.098%
Beamstrahlung energy spread: ~0.019%
Total energy spread: 0.1%
Requirement for energy acceptance: ~1.2%

## Slide 12: Beam lifetime (Beamstrahlung & Radiative Bhabha)
Beamstrahlung
Radiative Bhabha
*V.I. Telnov, "Issues with current designs for e+e- and gammagamma colliders“, PoS Photon2013 (2013) 070. https://inspirehep.net/record/1298149/files/Photon%202013_070.pdf
-- calculation: ~1 hour @ Higgs
-- simulation: ~40 min @ Higgs (with real lattice)
-- Higgs: bb= 1.6×10-25 cm2, Bhabha lifetime= ~100 min
-- Z: bb= 1.9×10-25 cm2, Bhabha lifetime= ~13 hour
Total lifetime due to beamstrahlung and Bhabha for Higgs at the level: ~ 20 min

## Slide 13: Bunch length choice
The design luminosities include the bunch lengthening effect according to the impedance budget.
A balance of bunch charge and larger Piwinski angle
-- longer bunch accommodate more charge
-- longer bunch  coherent beam-beam instability
-- shorter bunch mitigate luminosity reduction due to large Piwinski angle
Bunch lengthening was calculated by simulations.
-- H: bunch lengthening ~30%
-- W: bunch lengthening ~ 24%
-- Z: bunch lengthening ~ 40%, energy spread increase ~2%
 | H | W | Z
Bunch charge (nC) | 20.6 | 5.8 | 2.6
Nature bunch length z (mm) | 2.72 | 2.98 | 3.67
Bunch length z (mm) | 3.48 | 3.7 | 5.18

## Slide 14: CEPC amplitude-tune dependence
x=0.22 y=0.002 | Cxx (m-1) | Cxy (m-1) | Cyy (m-1)
Kinematic effects | 3.7 | 271 | 44762
Fringe field (QD0+QF1) | 2.0+1.4 | 5788+2444 | 21.3+4.0
x=0.144 y=0.002 | Cxx (m-1) | Cxy (m-1) | Cyy (m-1)
Kinematic effects | 8.6 | 414 | 44762
Fringe field (QD0+QF1) | 3.0+2.0 | 8558+3450 | 21.3+3.7
* Nonlinear effect of sextupole pairs can be corrected by the attached weak sextupole pairs.
Larger x* give help to on-momentum DA.

## Slide 15: Energy acceptance vs. x*
Larger x* reduce the requirement of energy acceptance.

## Slide 16: x* choice – 0.36 m
Parameter modification for x*: 0.171m 0.36m
-- larger x* reduced the amplitude-tune dependence  on mumentum DA
-- larger x* reduced the horizontal chromaticity both for linear and nonlinear term  off mumentum DA
-- larger x* reduce the requirement of energy acceptance  easier DA
Balance between DA and coherent beam-beam instability
-- smaller x* help suppress the coherent beam-beam instability

## Slide 17: Solenoid coupling effect
Vertical emittance growth at Z pole is most serious!
Larger coupling factor (1.7%) at Z pole
Coupling: 0.3% for Higgs and W
 | Higgs | W | Z
Vertical emittance due to solenoid[pmrad] | 0.14 | 0.42 | 2.0
y,solenoid /x (%) | 0.01 | 0.08 | 1.2
Emittance Coupling Budget (%) | 0.3 | 0.3 | 1.7
Detector
Real model

## Slide 18: Principle of combined D+S scheme
The power consumption of the arc sextupoles are too high.
Sextupole : 16.7 MW (copper coils)
Dipole: 6.5 MW (Al coils)
Reducing the strength of the stand-alone sextupoles can make help.
Combined function magnet: dipole + sextupole
Combined sextupoles: correct part (all) of the linear chromaticity
Stand-alone sextupoles: correct higher order chromaticity

## Slide 19: New lattice with combined D+S
SF
SF
SD
SD
Five dipoles between two quadrupoles in the arc
Combined sextupoles are on the first and fifth dipoles (x,y >>y,x)
No additional power sources for SF and SD
-- one dipole is cut into 6 slices
-- 7 thin sextupoles are insert in one dipole

## Slide 20: Primary magnet design for combined D+S
SF
SD
Twin aperture dipole
Separation of two ring: 0.35m

## Slide 21: DA with 50% reduction of independent K2
w/o combined D+S
w combined D+S (50% reduction)
Tracking 200 turns
50 seeds

## Slide 22: DA with 90% reduction of independent K2
w/o combined D+S
w combined D+S (90% reduction)
Tracking 200 turns
50 seeds

## Slide 23: IR lattice and survey
Two kinds of IR design
- left: asymmetrical , right: symmetrical
SPPC need a long straight for collimation at two IR.
Another possibility for IR survey and lattice

## Slide 24: Alternative FFS design
Asymmetric dispersion
Shared sextupole for chromaticity correction and crab waist
1st sextupole correct chromaticity, 2nd sextupole correct the geometric term of 1st sextupole (Oide’s talk on FCCweek17)
Ec < 100 keV within 800m
Crab sextupole
Betax=0.171m
Betay=0.002m
L*=2.2m
K1(QD0)=150T/m

## Slide 25: Final doublet + triplet
x=0.75, y=0.5
Betax=0.171m
Betay=0.002m
L*=2.2
L(QD0)=1.75m
L(QF1)=1.46m
k(QD0)=-150T/m
k(QF1)=106T/m
L0=0.5m

## Slide 26: Final doublet + triplet+CCY+matching+CCX
x=1.5, y=1.25
x=2.5, y=2.375
CCY
CCX
matching
IP

## Slide 27: Correction of the sextupole length effect
S1: main sextupole pair
S2: correcting sextupole pair  0.1*k2(S1)
*A.Bogomyagkov, S.Glykhov, E.Levichev, P.Piminov

## Slide 28: Arc lattice design
90/90 FODO cell
  Non-interleave sextupoles, period N=5cells
  Emittance
  - Higgs: 1.33nm
  - W: 0.57nm
Higgs & W
Z
  Two FODO cells combined into one FODO cell
Geometry of Z compatible with Higgs lattice
Emittance: 1.5nm

## Slide 29: Shared RF section
RF
RF
separator combined with a dipoles
beam
Shared RF cavities for e- and e+ ring (Higgs)
Separator bending cancel that of dipoles for the beam of opposite direction (Oide’s talk on FCCweek17)
Smaller beta in RF section to suppress the multi-bunch instability (max: 55.5 m/min: 9.8 m)
-- x=26cm at first quadrupole
-- Seperation at the end of seperator section: 0.77m

## Slide 30: Whole ring lattice
Circumference：99685m
Emittance from the real lattice：1.33nm
Working point : Qx = 353.10 Qy = 354.22

## Slide 31: DA
phase=0
phase=/2
phase= 
phase=3/2
DA optimization with 234 sex knobs.
Open: Sync oscillation/ Damping/ Sawtooth/tampering/fluctation
Emittance: 1.33 nm
Coupling: 0.3%
Tracking 100 turns
50 seeds
Crab=0

## Slide 32: Summary
A consistent analytical method for CEPC parameter design with carb waist scheme has been created. Crosscheck luminosity with beam-beam simulations
Luminosity of Higgs is limited by power budget and luminosity of Z is limited by bunch charge due to TMCI.
First taste of combined magnet (D+S) looks good.
-- Power for sextupoles  ¼, 50% reduction of independent K2
Alternative lattice for collider ring was explored. DA is comparable with CDR lattice. Far from maturity.