## Slide 1: Luminosity and beam loss monitoring at SuperKEKB
Philip Bambade
LAL-Orsay
10th FCPPL workshop Tsinghua - China 27-30 March 2017
On behalf of LAL group
Cécile Rimbault, P. B., Didier Jehanno (engineer), Yann Peinaud (engineer)
Dima El Khechen (PhD student  CERN/FCC-ee), Pang Chengguo* (PhD student)
Viacheslav Kubytskyi (postdoc  October 2017), N.N. (new postdoc opening in 2017)
*Chinese Scholarship Council

## Slide 2: Luminosity Frontier
KEKB
2×1034/cm2/s
SuperKEKB
80×1034/cm2/s
1km diameter
All future ee circular colliders use novel “nanobeam” collision scheme, which will be tried for 1st time at SuperKEKB in 2018
 essential validation + training for CEPC / FCC-ee

## Slide 3
SuperKEKB / Belle-II & “Machine-Detector Interface”
Control beam induced backgrounds
Luminosity monitoring & tuning
d  300 m
βy = 300 m
 mitigates beam-beam and hour-glass effects
 Luminosity  40
1) Phase 1 : 2016/Feb.  Jun.
- single beam commissioning, vacuum scrubbing
- no luminosity (no final focus), no detector
2) Phase 2 : 2018/Feb.  2018/Jul.
- colliding beam commissioning, no vertex detector
3) Phase 3 : from end of 2018…
- towards full luminosity for physics running




## Slide 4: Beam backgrounds at SuperKEKB
At SuperKEKB with x 40 larger luminosity, beam background will also increase drastically
  Touschek scattering
  Beam-gas scattering
  Synchrotron radiation
  Radiative Bhabha event: emitted g
  Radiative Bhabha event: spent e+/e-
  2-photon process event: e+e-e+e-e+e-
  etc…
e-
e+
e-
Beam-origin
Luminosity dependent
Notes: In this slide, I have listed up variety of possible beam background sources at SuperKEKB.
Among these background sources, so-called “Touschek scattering” will be the most difficult one to cope with, which I will explain in more detail in the following slides.

## Slide 5: Luminosity Fast & slow variations at IP require feedback corrections
Beam-beam deflection (SLC, KEKB) for fast vertical motion
Luminosity feedback by “dithering” (PEP-II) for slower horiz. motion
Luminosity tuning with optical knobs (SLC, FFTB, ATF2) to maintain small spot sizes ( time scales of  hours ? )
Dy at IP=
 5nm  1/10sy*
BPM
IP
BPM
Dy at BPM=  1.3mm
x
Luminosity
Vertical vibration  25-100 Hz
Sampling (BPMs)  32 kHz
Horizontal motion  few Hz
Modulation freq. f0  77 Hz
Sampling (lumi. meas.)  1 kHz
 minimize f0 output component


2f0
f0

## Slide 6
Radiative Bhabha at vanishing scattering angle
luminosity monitoring
major background source from induced particle losses after IP
  250 mbarn (E > 1% Ebeam )
Y. Funakoshi (KEK), background workshop, Feb. 2012
Macroscopic QED effect…
Luminosity monitoring specs
Relative measurements
10-3 in 1 ms over all bunches (“dithering”)
10-3 in  1 s for each 2500 bunch  4ns
(for nominal luminosity)
Non luminosity scaling contamination < 1% (e.g. beam gas bremstrahlung and Touschek losses)
Should also work for initial luminosity
Positron
energy
LAL & KEK

## Slide 7
LAL Luminosity monitor : test setup for Phase 1 commissioning
HER ~ 30 m  photon
LER ~ 11.9 m  positron
500 mm diamond sensors

## Slide 8
Data acquisition for Phase 1 commissioning
beam background measurement  validation
Data processing
→ Define waveforms and save them
→ Extract maximum of signal (total
integrated charge)
→ Position in time
→ FWHM
→ Save in .mat files
→ Merge them to EPICS

## Slide 9
Beam gas Bremsstrahlung
→ Inelastic Coulomb scattering
→ Beam particles pass by EM of nucleus of molecules of residual gas
→ Emission of photon → particle loses energy
→ Particle is lost downstream of emission point
Loss vs (current x pressure)
→ Scattering and loss rates are proportional to beam current and vacuum pressure

## Slide 10
Touschek scattering
→ Scattering of beam particles upon each other
→In CM; pinit1, 2 = (±px,0,0)
pscat1, 2 = (±px sinχ cosφ, ±pxcosχ, ±px sinχ sinφ)
→ In Lab frame: maximum momentum transfer : DE= g x px
→ One particle loses energy and the other gain energy
→ Scattering and loss rates are proportional to I2 and inversely proportional to the beam size
Energy vs emission position
3.7%
analytic calculation

## Slide 11
Physical processes interfaced in SAD tracking code by Y. Ohnishi to simulate overall beam loss in SuperKEKB rings
Simulation improvement: scattering resolution
Scattering @ quad
Scattering @ all elements
Slicing drifts (10 cm) and bends (15 cm)
Default code
Energy
vs emission point

## Slide 12
→ Vacuum bumps were performed upstream of the IP
→ Fraction of losses in the sCVD from scattering regions were calculated and compared to data
→
4-12 m
17-35 m
4-12 m
17-35 m
Vacuum bumps in LER
Pressure profile
Loss profile
total loss simulated in the sCVD, when pressure everywhere in the
ring is equal to that of the maximum of the bump at the given section
is the loss in the sCVD at the maximum of the bump
4~12 m
17~35 m

## Slide 13
→ The vertical beam size sy was varied adjusting
the x-y coupling (“Emittance Control Knob”)
→ Losses in the sCVD were fitted as a function of
the inverse vertical beam size (sy-1)
→ Loss = Bremsstrahlung + Touschek  s-1y
Vertical beam size scans
720 mA
540 mA
180 mA
360 mA
900 mA
1000 mA
(constant term) (slope)

## Slide 14
→ Data is larger than simulation by factor about 3
Bremsstrahlung losses (from constant terms of vertical beam size scans)
simulation
data
→ Factor 3 ± 1.5 was estimated by simulation for KEKB
by vacuum group
→ The pressure measured at Gauges should be multiplied
by  3 to represent the pressure at center of beam pipes

## Slide 15
Touschek losses (from slopes of vertical beam size scans)
Measured slopes combined after quadratic extrapolation to I = 1 A to compare with simulation
→ simulation / data = 1.7 ± 0.74
(preliminary)
Uncertainties
(for future improved comparison)
Statistics (both data and simulation)
Beam size measurement considered reliable in vertical but not in horizontal
Emittance growth with beam current due to intra-beam scattering was neglected

## Slide 16
DAQ status and progress for Phase 2/3

## Slide 17: 140 diamond test for Phase 2/3
Landau distribution of energy deposited and signal amplitude- 140 DS
G4 simulation: 58.2KeV
Experiment: 3.35mV
G4 simulation
Test with Sr-90
May lead to pile up
scintillator
diamond

## Slide 18: Geant4 simulation for Phase 2/3
Energy spectra of
Bhabhas-LER
window G4 model
According to the energy deposited in DS per Bhabha, relative precision with different luminosity can be calculated.
Phase 2:
Target luminosity
Simulated signal sequence to test FPGA algorithm

## Slide 19
Conclusions & Prospects
SuperKEKB: 1st trial in 2018 of new “nanobeam” collision scheme which promises a breakthrough in luminosity ( 40 increase)
Challenge for the controls of the beams + significantly enhances beam related backgrounds
Successful test of LAL and KEK fast luminosity monitor hardware during 2016 single beam commissioning
Measurement of background conditions; validation of simulation to enable extrapolating in the successive luminosity conditions
Preparing on-line train-integrated and bunch-integrated luminosity monitoring for 2018
Background modeling and assessment will need to continue during luminosity operation
 Large impact on future circular ee collider design work
 Rare “real life” training chance for early stage scientists
+ great fun in great atmosphere !

## Slide 20
Backup slides

## Slide 21: LER & HER measurement stations
Outside
HER
e-
LER
e+
 from electron @  30 m
Recoil electron
Recoil positron @ 11 m
g from positron
2 diamonds + 1 Cherenkov + 1 Scintillator
2 diamonds + 1 Cherenkov + 1 Scintillator

## Slide 23: Overall schedule
Summer shutdown
(power saving)
Summer shutdown
(power saving)
phase 1
phase 2 (MR)
phase 3
MR renovation for phase 2, including
installation of QCS and Belle II
w/o QCS
w/o Belle II
w/ QCS
w/ Belle II (no VXD)
w/ full Belle II
DR commissioning
DR installation & startup
MR startup
VXD installation
HER start
LER start
(mid Feb. – mid Jul. 2018)
Summer shutdown
(power saving)
Power saving
after mid July 2018
phase 3 operation
9 months / year
…
2016
JFY2016
2017
2018
2019
JFY2017
JFY2018
JFY2019
Japan FY
Calendar year

## Slide 25
Coulomb scattering
→ Elastic scattering of particle beams on the nucleus of residual gas molecules
→ Particle receives a transverse kick and is lost downstream the emission point
→ Transverse offset of particle lost at position B and emitted at A depends on

## Slide 26
simulation
data
Calibration
→ Maximum of signal of Data were fit by “Landau”
→ A cut at 6 mV separates signal from noise
→ In simulation: minimum of 50 KeV ( > 3s of noise )
→ MPV= 11.6 mV in data
→ MPV= 9.2 mV in simulations
→ 11.6/9.2 = 1.3  threshold is at ~ 4.7 mV for simulations
11.6 mV
9.2 mV