## Slide 1: 100km CEPC parameters and lattice design
Dou Wang, Jie Gao, Chenghui Yu, Yuan Zhang, Yiwei Wang, Feng Su, Bai Sha, Jiyuan Zhai, Huiping Geng, Cai Meng, Tianjian Bian, Na Wang, Xiaohao Cui
27-30 March 2017, Tsinghua University, Beijing.
10th workshop of the France China Particle Physics Laboratory

## Slide 2
Advantage:
Avoid pretzel orbit, more bunches
Correct sawtooth effect
Reduce beam power with crab waist

## Slide 3: CEPC RF distribution

## Slide 4: CEPC bunch distribution
C0=100km
Higgs
W & Z
C0=100km

## Slide 5: Machine constraints / given parameters
Energy E0
Circumference C0
NIP
Beam power P0
y*
Emittance coupling factor 
Bending radius 
Piwinski angle 
y enhancement by crab waist Fl ~1.5 (2.6)
Energy acceptance requirement (DA)
Phase advance per cell (FODO)

## Slide 6: Constraints for parameter choice
Limit of Beam-beam tune shift
Beam lifetime due to beamstrahlung
Beamstrahlung energy spread
HOM power per cavity (coaxial coupler)
Fl: y enhancement by crab waist
*J. Gao, emittance growth and beam lifetime limitations due to beam-beam effects in e+e- storage rings, Nucl. Instr. and methods A533（2004）p. 270-274.
BS life time: 30 min
A=0/BS (A3)
V.I. Telnov

## Slide 7: parameters for CEPC double ring （wangdou20161219-100km_1mmy）
 | Pre-CDR | H-high lumi. | H-low power |  | W | Z | 
Number of IPs | 2 | 2 | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 120 | 80 | 45.5 | 45.5
Circumference (km) | 54 | 100 | 100 | 100 | 100 | 100 | 100
SR loss/turn (GeV) | 3.1 | 1.67 | 1.67 | 1.67 | 0.33 | 0.034 | 0.034
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 2.5 | 2.5 | 2.5 | 3.57 | 5.69 | 5.69
Ne/bunch (1011) | 3.79 | 1.12 | 1.12 | 1.12 | 1.05 | 0.46 | 0.46
Bunch number | 50 | 555 | 333 | 211 | 1000 | 16666 | 65716
Beam current (mA) | 16.6 | 29.97 | 17.98 | 11.4 | 50.6 | 367.7 | 1449.7
SR power /beam (MW) | 51.7 | 50 | 30 | 19 | 16.7 | 12.7 | 50
Bending radius (km) | 6.1 | 11 | 11 | 11 | 11 | 11 | 11
Momentum compaction (10-5) | 3.4 | 0.96 | 0.96 | 0.96 | 3.1 | 3.3 | 3.3
IP x/y (m) | 0.8/0.0012 | 0.3/0.001 | 0.3/0.001 | 0.3 /0.001 | 0.1 /0.001 | 0.12/0.001 | 0.12/0.001
Emittance x/y (nm) | 6.12/0.018 | 1.01/0.0031 | 1.01/0.0031 | 1.01/0.0031 | 2.68/0.008 | 0.93/0.0049 | 0.93/0.0049
Transverse IP (um) | 69.97/0.15 | 17.4/0.055 | 17.4/0.055 | 17.4/0.055 | 16.4/0.09 | 10.5/0.07 | 10.5/0.07
x/y/IP | 0.118/0.083 | 0.029/0.083 | 0.029/0.083 | 0.029/0.083 | 0.0082/0.055 | 0.0075/0.054 | 0.0075/0.054
RF Phase (degree) | 153.0 | 123.3 | 123.3 | 123.3 | 149 | 160.8 | 160.8
VRF (GV) | 6.87 | 2.0 | 2.0 | 2.0 | 0.63 | 0.11 | 0.11
f RF (MHz) (harmonic) | 650 | 650 | 650 | 650 | 650 (217800) | 650 (217800) | 
Nature z (mm) | 2.14 | 2.72 | 2.72 | 2.72 | 3.8 | 3.93 | 3.93
Total z (mm) | 2.65 | 2.9 | 2.9 | 2.9 | 3.9 | 4.0 | 4.0
HOM power/cavity (kw) | 3.6 (5cell) | 0.75(2cell) | 0.45(2cell) | 0.28(2cell) | 1.0 (2cell) | 1.6(1cell) | 6.25(1cell)
Energy spread (%) | 0.13 | 0.098 | 0.098 | 0.098 | 0.065 | 0.037 | 0.037
Energy acceptance (%) | 2 | 1.5 | 1.5 | 1.5 |  |  | 
Energy acceptance by RF (%) | 6 | 1.8 | 1.8 | 1.8 | 1.5 | 1.1 | 1.1
n | 0.23 | 0.26 | 0.26 | 0.26 | 0.26 | 0.18 | 0.18
Life time due to beamstrahlung_cal (minute) | 47 | 52 | 52 | 52 |  |  | 
F (hour glass) | 0.68 | 0.83 | 0.83 | 0.83 | 0.84 | 0.91 | 0.91
Lmax/IP (1034cm-2s-1) | 2.04 | 5.42 | 3.25 | 2.06 | 4.08 | 18.0 | 70.97

## Slide 8: 100km CEPC luminosity potential (1mmy+50MW/beam)
W
H
z
tt

## Slide 9: Strong-strong simulation – 100km
wangdou20161219-100km_1mmy with full crab waist, Higgs
Working point: (0.54, 0.61) with s = 0.0272
Lifetime: 400min
In Phase <xz> oscillation in the first few hundred collisions

## Slide 10: Strong-strong simulation-100km
wangdou20161219-100km_1mmy with full crab waist, Higgs
(0.51,0.55) with s =0.0272 could help suppress the <xz> oscillation

## Slide 11: CEPC Luminosity vs circumference
* Fabiola Gianotti, Future Circular ColliderDesign Study, ICFA meeting, J-PARC, 25-2-2016.

## Slide 12: Parameter for single ring-100km （wangdou20161122）
 | Pre-CDR | New-100km | 
Number of IPs | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120
Circumference (km) | 54 | 100 | 100
SR loss/turn (GeV) | 3.1 | 1.67 | 1.67
Ne/bunch (1011) | 3.79 | 1.79 | 1.79
Bunch number | 50 | 350 | 100
Beam current (mA) | 16.6 | 30.0 | 8.6
SR power /beam (MW) | 51.7 | 50 | 14.3
Bending radius (km) | 6.1 | 11 | 11
Momentum compaction (10-5) | 3.4 | 3.15 | 3.15
IP x/y (m) | 0.8/0.0012 | 0.4/0.0012 | 0.4/0.0012
Emittance x/y (nm) | 6.12/0.018 | 6.18/0.019 | 6.18/0.019
Transverse IP (um) | 69.97/0.15 | 49.5/0.15 | 49.5/0.15
x/IP | 0.118 | 0.055 | 0.055
y/IP | 0.083 | 0.055 | 0.055
VRF (GV) | 6.87 | 4.88 | 4.88
f RF (MHz) | 650 | 650 | 650
Nature z (mm) | 2.14 | 2.41 | 2.41
Total z (mm) | 2.65 | 2.47 | 2.47
HOM power/cavity (kw) | 3.6 | 3.2 | 0.92
Energy spread (%) | 0.13 | 0.098 | 0.098
Energy acceptance (%) | 2 | 0.94 | 0.94
Energy acceptance by RF (%) | 6 | 4.5 | 4.5
n | 0.23 | 0.15 | 0.15
Life time due to beamstrahlung_cal (minute) | 47 | 54 | 54
F (hour glass) | 0.68 | 0.7 | 0.7
Lmax/IP (1034cm-2s-1) | 2.04 | 2.5 | 0.72

## Slide 13: New modifications
y*=2mm (1mm)
L*=2.2m (1.5m)
Crossing angle： 33mrad (30mrad)
Strength of QD0: 150T/m (200T/m)
Strength of detector solinoid: 3T (3.5T)
Strength of anti-solinoid: 7.0T (13T)

## Slide 14: parameters for CEPC double ring （wangdou20170306-100km_2mmy）
 | Pre-CDR | Higgs | W | Z
Number of IPs | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 80 | 45.5
Circumference (km) | 54 | 100 | 100 | 100
SR loss/turn (GeV) | 3.1 | 1.67 | 0.33 | 0.034
Half crossing angle (mrad) | 0 | 16.5 | 16.5 | 16.5
Piwinski angle | 0 | 3.19 | 5.69 | 4.29
Ne/bunch (1011) | 3.79 | 0.968 | 0.365 | 0.455
Bunch number | 50 | 412 | 5534 | 21300
Beam current (mA) | 16.6 | 19.2 | 97.1 | 465.8
SR power /beam (MW) | 51.7 | 32 | 32 | 16.1
Bending radius (km) | 6.1 | 11 | 11 | 11
Momentum compaction (10-5) | 3.4 | 1.14 | 1.14 | 4.49
IP x/y (m) | 0.8/0.0012 | 0.171/0.002 | 0.171 /0.002 | 0.16/0.002
Emittance x/y (nm) | 6.12/0.018 | 1.31/0.004 | 0.57/0.0017 | 1.48/0.0078
Transverse IP (um) | 69.97/0.15 | 15.0/0.089 | 9.9/0.059 | 15.4/0.125
x/y/IP | 0.118/0.083 | 0.013/0.083 | 0.0055/0.062 | 0.008/0.054
RF Phase (degree) | 153.0 | 128 | 126.9 | 165.3
VRF (GV) | 6.87 | 2.1 | 0.41 | 0.14
f RF (MHz) (harmonic) | 650 | 650 | 650 (217800) | 650 (217800)
Nature z (mm) | 2.14 | 2.72 | 3.37 | 3.97
Total z (mm) | 2.65 | 2.9 | 3.4 | 4.0
HOM power/cavity (kw) | 3.6 (5cell) | 0.41(2cell) | 0.36(2cell) | 1.99(2cell)
Energy spread (%) | 0.13 | 0.098 | 0.065 | 0.037
Energy acceptance (%) | 2 | 1.5 |  | 
Energy acceptance by RF (%) | 6 | 2.1 | 1.1 | 1.1
n | 0.23 | 0.26 | 0.15 | 0.12
Life time due to beamstrahlung_cal (minute) | 47 | 52 |  | 
F (hour glass) | 0.68 | 0.96 | 0.98 | 0.96
Lmax/IP (1034cm-2s-1) | 2.04 | 2.0 | 5.15 | 11.9

## Slide 15
Higgs mode and W mode will use the same lattice.
For Z pole, Considering the constraint of 10 ns bunch separation from detector, the maximum bunch number can be increased by only 40% with dedicated RF cavities. So the luminosity of Z is limited by detector speed.
Z mode use different lattice rather than Higgs/W, because Z needs larger emittance which can be realized by closing half quadrupoles in Higgs lattice.

## Slide 16: Higgs Luminosity vs. crossing angle
Keep beamstrahlung life time constant (52min)
luminosity
emittance
100km

## Slide 17: Higgs Luminosity vs. crossing angle
Keep emittance constant (1.56nm)
luminosity
Life time
100km

## Slide 18: Higgs Luminosity vs. y*
Keep beamstrahlung life time constant (52min)
luminosity
emittance
100km

## Slide 19: Higgs Luminosity vs. y*
Keep emittance constant (1.56nm)
luminosity
Life time
100km

## Slide 20: Higgs Luminosity vs. SR power
goal
100km

## Slide 21: Vertical emittance induced by solenoid
Design emittance
Higgs: 1.31/0.004 nm
W: 0.57/0.0017 nm
Z: 1.48/0.0078 nm
Detector
Detector
Vertical emittance at Z pole is most dangerous with solenoid!

## Slide 22: Z parameters with different coupling
 | Z-0.303% | Z-0.527% | Z-0.714% | Z-1%
Number of IPs | 2 |  |  | 
Energy (GeV) | 45.5 |  |  | 
Circumference (km) | 100 |  |  | 
SR loss/turn (GeV) | 0.034 |  |  | 
Half crossing angle (mrad) | 16.5 |  |  | 
Piwinski angle | 4.29 |  |  | 
Ne/bunch (1011) | 0.346 | 0.455 | 0.532 | 0.63
Bunch number | 30870 | 21300 | 15580 | 11120
Beam current (mA) | 513.3 | 465.8 | 398.3 | 336.7
SR power /beam (MW) | 17.7 | 16.1 | 13.7 | 11.6
Bending radius (km) | 11 |  |  | 
Momentum compaction (10-5) | 4.49 |  |  | 
IP x/y (m) | 0.16/0.002 | 0.16/0.002 | 0.16/0.002 | 0.16/0.002
Emittance x/y (nm) | 1.48/0.0045 | 1.48/0.0078 | 1.48/0.0106 | 1.48/0.015
Transverse IP (um) | 15.4/0.095 | 15.4/0.125 | 15.4/0.145 | 15.4/0.172
x/y/IP | 0.006/0.054 | 0.008/0.054 | 0.009/0.054 | 0.011/0.054
RF Phase (degree) | 165.2 | 165.3 | 165.4 | 165.6
VRF (GV) | 0.13 | 0.14 | 0.14 | 0.14
f RF (MHz) (harmonic) | 650 (217800) |  |  | 
Nature z (mm) | 3.99 | 3.97 | 3.96 | 3.93
Total z (mm) | 4.0 |  |  | 
HOM power/cavity (kw) | 1.67(2cell) | 1.99(2cell) | 1.99(2cell) | 1.99
Energy spread (%) | 0.037 |  |  | 
Energy acceptance by RF (%) | 1.1 | 1.1 | 1.1 | 1.1
n | 0.09 | 0.12 | 0.14 | 0.17
F (hour glass) | 0.96 | 0.96 | 0.96 | 0.96
Lmax/IP (1034cm-2s-1) | 13.1 | 11.9 | 10.2 | 8.62

## Slide 23: Z luminosity vs. coupling

## Slide 24: Arc design for 100km CEPC

## Slide 25: Final doublet + triplet
x=0.75, y=0.5
Betax=0.171m
Betay=0.002m
L*=2.2
L(QD0)=1.75m
L(QF1)=1.46m
k(QD0)=-150T/m
k(QF1)=106T/m
L0=0.5m

## Slide 26: FFS optics
x=1.5, y=1.25
x=1.0, y=0.75
Both FFS sextupoles of the CCS-Y section can work as the crab sextupoles.
crab sextupole

## Slide 27: Correction of the sextupole length effect
S1: main sextupole pair
S2: correcting sextupole pair  0.1*k2(S1)
*A.Bogomyagkov, S.Glykhov, E.Levichev, P.Piminov

## Slide 28: W function of FFS
98
98
28
-37
184
98
98
98
98
98
Critical energy Ec < 100 keV within 560m, Ec < 200 keV within 800m.
Horizontal chromaticity leak Wx=90

## Slide 29: Arc + FFS （L*=2.2m,Betax=0.171m,Betay=0.002m）

## Slide 30: Arc + FFS (2 fam) （L*=2.2m,Betax=0.171m,Betay=0.002m）
No damping
Tracking 200 turns
Energy acceptance： 0.5%
2 families sextupole in arc
DA: 60x310 y

## Slide 31: Arc + FFS (112 fam) （L*=2.2m,Betax=0.171m,Betay=0.002m）
With damping
Without damping
Energy acceptance： 1.2%

## Slide 32: DA after optimization (Arc + FFS)
L*=1.5m
Betax=0.22m,Betay=0.002m
k(QD0)=-200T/m
L*=2.2m
Betax=0.171m,Betay=0.002m
k(QD0)=-150T/m
Energy acceptance： 1.5%
Energy acceptance： 1.2%
With damping, crab sextupoles: close
Tracking 200 turns

## Slide 33: summary
A consistent calculation method for CEPC parameter choice with carb waist scheme has been created. Crosscheck luminosity with beam-beam simulations
Based on double ring scheme with 100 km circumference, we can get higher Higgs luminosity (170%) keeping Pre-CDR beam power or to reduce the beam power (19 MW) keeping same luminosity. Luminosity for Z: ~1035cm-2s-1
Requirement for energy acceptance reduced to 1.5% enlarging the ring.
New IP parameters made the FFS design and DA more difficult.
have got 1.5% energy acceptance without crab sextupoles. Further studies of DA with new L* are going on.

## Slide 34
Thanks！

## Slide 35: Back up

## Slide 36: parameter for CEPC partial double ring （wangdou20160325-54km）
 | Pre-CDR | H-high lumi. | H-low power | W | Z
Number of IPs | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5
Circumference (km) | 54 | 54 | 54 | 54 | 54
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 0.59 | 0.062
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 2.5 | 2.6 | 5 | 8.5/7.6
Ne/bunch (1011) | 3.79 | 2.85 | 2.67 | 0.74 | 0.46
Bunch number | 50 | 67 | 44 | 400 | 1100
Beam current (mA) | 16.6 | 16.9 | 10.5 | 26.2 | 45.4
SR power /beam (MW) | 51.7 | 50 | 31.2 | 15.6 | 2.8
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.1 | 6.1
Momentum compaction (10-5) | 3.4 | 2.5 | 2.2 | 2.4 | 3.5
IP x/y (m) | 0.8/0.0012 | 0.25/0.00136 | 0.268 /0.00124 | 0.1/0.001 | 0.1/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.45/0.0074 | 2.06 /0.0062 | 1.02/0.003 | 0.62/0.0028
Transverse IP (um) | 69.97/0.15 | 24.8/0.1 | 23.5/0.088 | 10.1/0.056 | 7.9/0.053
x/IP | 0.118 | 0.03 | 0.032 | 0.008 | 0.005/0.006
y/IP | 0.083 | 0.11 | 0.11 | 0.074 | 0.084/0.073
VRF (GV) | 6.87 | 3.62 | 3.53 | 0.81 | 0.12
f RF (MHz) | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 3.1 | 3.0 | 3.25 | 3.9
Total z (mm) | 2.65 | 4.1 | 4.0 | 3.35 | 4.0
HOM power/cavity (kw) | 3.6 | 2.2 | 1.3 | 0.99 | 0.99
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.09 | 0.05
Energy acceptance (%) | 2 | 2 | 2 |  | 
Energy acceptance by RF (%) | 6 | 2.2 | 2.1 | 1.7 | 1.1
n | 0.23 | 0.47 | 0.47 | 0.3 | 0.27/0.24
Life time due to beamstrahlung_cal (minute) | 47 | 36 | 32 |  | 
F (hour glass) | 0.68 | 0.82 | 0.81 | 0.92 | 0.95
Lmax/IP (1034cm-2s-1) | 2.04 | 2.96 | 2.01 | 3.09 | 3.61/3.09

## Slide 37: parameter for CEPC partial double ring （wangdou20161109-61km）
 | Pre-CDR | H-high lumi. | H-low power | W | Z | Z-5cell
Number of IPs | 2 | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5 | 45.5
Circumference (km) | 54 | 61 | 61 | 61 | 61 | 61
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 0.58 | 0.061 | 0.061
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 1.88 | 1.84 | 4.11 | 5.86 | 5.87
Ne/bunch (1011) | 3.79 | 2.0 | 1.98 | 0.85 | 0.6 | 0.6
Bunch number | 50 | 107 | 70 | 400 | 1100 | 700
Beam current (mA) | 16.6 | 16.9 | 11.0 | 26.8 | 52.0 | 33.1
SR power /beam (MW) | 51.7 | 50 | 32.5 | 15.7 | 3.2 | 2.0
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.2 | 6.2 | 6.2
Momentum compaction (10-5) | 3.4 | 1.48 | 1.48 | 1.48 | 3.1 | 3.1
IP x/y (m) | 0.8/0.0012 | 0.272/0.0013 | 0.275 /0.0013 | 0.16/0.001 | 0.12/0.001 | 0.12/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.05/0.0062 | 2.05 /0.0062 | 0.93/0.003 | 0.87/0.0046 | 0.87/0.0046
Transverse IP (um) | 69.97/0.15 | 23.7/0.09 | 23.7/0.09 | 12.2/0.056 | 10.2/0.068 | 10.2/0.068
x/IP | 0.118 | 0.041 | 0.042 | 0.0145 | 0.0098 | 0.0098
y/IP | 0.083 | 0.11 | 0.11 | 0.084 | 0.073 | 0.073
VRF (GV) | 6.87 | 3.48 | 3.51 | 0.7 | 0.12 | 0.12
f RF (MHz) | 650 | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 2.7 | 2.7 | 3.23 | 3.9 | 3.9
Total z (mm) | 2.65 | 2.95 | 2.9 | 3.35 | 4.0 | 4.0
HOM power/cavity (kw) | 3.6 | 0.74 | 0.48 | 0.47 | 0.59 | 0.93
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.087 | 0.05 | 0.05
Energy acceptance (%) | 2 | 2 | 2 |  |  | 
Energy acceptance by RF (%) | 6 | 2.3 | 2.4 | 1.3 | 1.1 | 1.1
n | 0.23 | 0.35 | 0.34 | 0.28 | 0.24 | 0.24
Life time due to beamstrahlung_cal (minute) | 47 | 37 | 37 |  |  | 
F (hour glass) | 0.68 | 0.82 | 0.82 | 0.89 | 0.92 | 0.92
Lmax/IP (1034cm-2s-1) | 2.04 | 3.1 | 2.01 | 3.5 | 3.44 | 2.2

## Slide 38: Beam-beam simulation-54km
Case: H-low power
Lifetime: 97 min(16)
Case Z
IBB: Strong-Strong Beam-Beam Code with Beamstrahlung effect
Developed by Y. Zhang@IHEP
Case: Pre-CDR
Lifetime: 108 min(16)
Lifetime: 118 min(16)
Case: H-high lum

## Slide 39: Beam-beam simulation-61km
Case: H-low power
Lifetime: 260 min
IBB: Strong-Strong Beam-Beam Code with Beamstrahlung effect
Developed by Y. Zhang@IHEP
Case: w