## Slide 1: DA studies in CEPC by downhill method
Dou Wang, Yuan Zhang, Yiwei Wang, Huiping Geng, Chenghui Yu, Weiren Chou, Jie Gao
Many Thanks: K. Oide(KEK), Y. Cai (SLAC), D. Zhou(KEK)
ICFA Mini-Workshop on Dynamic Apertures of Circular Accelerators
1-3 November 2017, IHEP.

## Slide 2: Outline
Introduction Downhill method & modifications
Application on CDR lattice
Application on new lattice with combined magnets (dipole + sextupole) in arcs

## Slide 3: Dynamic aperture study in CEPC
DA requirement for Higgs (with errors, crab sextupoles and beam-beam)
On-momentum: 20x  30y
Energy acceptance: 1.5%
Multi-sextupole optimization
Two methods:
- Downhill Simplex, K. Oide@KEK
MODE (Multi-Objective optimization by Differential Evolution), Y. Zhang@IHEP
Effects included in DA tracking
- Synchrotron oscillation
- SR Damping
- Sawtooth + tampering
- Quantum fluctation
Difference of two methods
Downhill: local search, quick convergence, need less cpu.
MODE: global search, time consuming, need strong computers.
Both methods were used on CEPC to complement each other.

## Slide 4: Principle of downhill optimization
Scan the strength of sextupoles;
DA tracking for the energy list
Calculate the objective function (DA)
Find the minimum of the objective function by the downhill simplex method
Go to 1.
Optimization stop when
(fmax-fmin)/(abs(fmax)+abs(fmin)) < Tolerance

## Slide 5: Objective function for DA optimization
Case I: wth  0, optimize the energy bandwidth
Case II: wth < 0, optimize the total DA value
-- t: Touschek lifetime
-- Bandwith(n): DA bandwidth according to n* DA reference
-- w & w1: weight for the DA bandwidth
-- DAj(i): DA for i* energy deviation with the jth initial phase (totally 6 phases)
-- w(i) : DA weight for i* energy deviation

## Slide 6: Downhill Simplex modification
DA results not stable while opening fluctuation
Cancel the noise due to fluctuation
Two methods：
Scan whole DA list (5 seeds)  Minimum
Scan DA at center energy (10 seeds)  Minimum  Clip
So far, we used method 2 to save computer time.

## Slide 7: CEPC CDR lattice - arc
  FODO cell, 90/90, non-interleaved sextupole scheme
  224 sextupole pairs in the half ring

## Slide 8: CEPC CDR lattice - IR
  Final Telescope + CCY + CCX + Matching + crab section
  10 sextupole pairs in the half ring
CCY: 4 pairs  linear chromaticity + sextupole length effect
CCX: 4 pairs  linear chromaticity + sextupole length effect
Image points: 2 pairs  third order chromaticity (vertical)
- 
- 
- 
- 

## Slide 9: Sawtooth effect
With only two RF station, the sawtooth orbit : ~1mm
~5% distortion of beam optics and DA reduction
sawtooth orbit after tapering: ~1um
DA study always include sawtooth + tampering

## Slide 10: Initial DA
100 turns tracking
50 seeds
Crab=1
Ax(0): 14 x
Ay(0): 36 y
DA bandwith: 1.2%

## Slide 11: DA-after optimization
Crab=1
Ax(0): 14 x
Ay(0): 33 y
DA bandwith: 1.6%
100 turns tracking
50 seeds
 234 sextupole knobs (no check for variable redundancy)

## Slide 12: Quadrupoles optimization in MODE
12*6 quadrupoles are varied for phase advance tuning
Working points are locked.
Phase tuning sections
Phase tuning sections

## Slide 13: DA optimization with MODE’s K1
100 turns tracking
50 seeds
Crab=1
Crab=1
234 K2 knobs
K1 values from MODE
234 K2 knobs
Optimization with additional K1 knobs give ~20% DA enlargement.

## Slide 14: Principle of combined D+S scheme
The power consumption of the arc sextupoles are too high.
Sextupole : 16.7 MW (copper coils)
Dipole: 6.5 MW (Al coils)
Reducing the strength of the stand-alone sextupoles can make help.
Combined function magnet: dipole + sextupole
Combined sextupoles: correct part (all) of the linear chromaticity
Stand-alone sextupoles: correct higher order chromaticity

## Slide 15: New lattice with combined D+S
SF
SF
SD
SD
Five dipoles between two quadrupoles in the arc
Combined sextupoles are on the first and fifth dipoles (x,y >>y,x)
No additional power sources for SF and SD
-- one dipole is cut into 6 slices
-- 7 thin sextupoles are insert in one dipole

## Slide 16: Primary magnet design for combined D+S
SF
SD
Twin aperture dipole
Separation of two ring: 0.35m

## Slide 17: Case I: 50% K2 reduction
Chromaticity correction with SF & SD
SF =0 m-2
SD =0 m-2
SF =30.4 T/m
SD =-51.2 T/m

## Slide 18: DA before multi-sextupole optimization
50% reduction
Tracking 100 turns
20 seeds
phase=0
phase=/2
phase= 
phase=3/2
Crab=1

## Slide 19: DA after multi-sextupole optimization
50% reduction
Optimization knobs: 234 K2s
Tracking 100 turns
20 seeds
phase=0
phase=/2
phase= 
phase=3/2
Crab=1

## Slide 20: DA comparison
w/o combined D+S
w combined D+S (50% reduction)
Tracking 200 turns
50 seeds

## Slide 21: Strength of independent sextupoles
w/o combined D+S
w combined D+S (Case I)

## Slide 22: Case II: 90% K2 reduction
Chromaticity correction with SF & SD
SF =55.6 T/m
SD =-94.4 T/m
SF =0 m-2
SD =0 m-2

## Slide 23: DA before multi-sextupole optimization
90% reduction
Tracking 100 turns
20 seeds
phase=0
phase=/2
phase= 
phase=3/2
Crab=1

## Slide 24: DA after multi-sextupole optimization
90% reduction
Optimization knobs: 234 K2s
Tracking 100 turns
20 seeds
phase=0
phase=/2
phase= 
phase=3/2
Crab=1

## Slide 25: DA comparison
w/o combined D+S
w combined D+S (90% reduction)
Tracking 200 turns
50 seeds

## Slide 26: Strength of independent sextupoles
w/o combined D+S
w combined D+S (Case II)

## Slide 27: Summary
Both Downhill and MODE were used to complement each other.
Downhill can give almost same results as MODE.
First taste of combined magnet (D+S) looks good.
-- Plan to introduce K1 knobs in Downhill
-- Power for sextupoles  ¼, 50% reduction of independent K2
-- Still need careful check for the DA results