## Slide 1: Emittance Control and Nonlinear Beam Dynamics in JLEIC Electron Collider Ring
Fanglei Lin
on behalf of Jefferson Lab Electron Ion Collider (JLEIC) study team

## Slide 2: Outline
Introduction of Jefferson Lab Electron Ion Collider (JLEIC) design
Electron collider ring design
  Requirements
  Options for low-emittance optics
  Baseline design
Non-linear chromaticity compensation
  Sextupole schemes and performance
Dynamic aperture study
  Energy dependence
  Errors and corrections
  Non-linear field tolerance
  Betatron tunes
Summary

## Slide 3: Electron Ion Collider (EIC)
Recommendations in NSAC LRP 2015:
Continue existing projects: CEBAF, FRIB, RHIC.
“…a U.S.-led ton-scale neutrinoless double beta decay experiment”
“…a high-energy high-luminosity polarized EIC as the highest priority for new facility construction following the completion of FRIB”
“…small-scale and mid-scale projects and initiatives that enable forefront research at universities and laboratories”
EIC Community White Paper arXiv:1212.1701

## Slide 4: Jefferson Lab Electron Ion Collider (JLEIC)
arXiv: 1209.0757
2012
2015
arXiv: 1504.07961
3-12 GeV
8-100(400) GeV
8 GeV
& SRF Linac
May 17 update:
https://eic.jlab.org/wiki/index.php/Main_Page
Electron complex
  CEBAF
  Collider ring
Ion complex
  Ion source / Linac
  Booster
  Collider ring
IP/detectors
  Optimum detector location for minimizing background
  Hori. Crab crossing
Polarization
  Figure-8 shape rings

## Slide 5: Electron Collider Design Requirements
Provide the necessary beam parameters
  3-10 GeV electron
  3A beam current up to 6-7 GeV, small emittance, short bunch length ~1cm, focusing at the IP ( to support luminosity above 1033 cm-2s-1)
  Sufficient beam and luminosity lifetime
  Less than 10MW total synchrotron radiation power
Capability of operating multiple detectors
  One full-acceptance detector (small angle detection) incorporated
  Space for a second detector reserved
Maintain high polarization above 70%
  Longitudinal polarization at the IP
  Sufficient polarization lifetime
Incorporate provisions for non-linear dynamics correction
  Proper chromatic correction scheme using sextupole families
  No emittance growth

## Slide 6: Arc Cell Optics Options
FODO cell w/ PEP-II magnets
FODO cell w/ new magnets (baseline)
TME cell w/ new magnets
HMBA cell w/ new magnets

## Slide 7: Arc Optics Options for Low Emittance
 |  | FODO arc cell w/ PEP-II magnets | FODO arc cell w/ new magnets (baseline) | TME arc cell w/ new magnets | HMBA arc cell w/ new magnets
Ring circumference | m | 2282 | 2336 | 2277 | 2395
Bending angle per arc / figure-8 crossing angle | deg | 261.7 / 81.7 | 261.7 / 81.7 | 261.7 / 81.7 | 259.74 / 79.74
Beta stars at IP *x,y | cm | 10 / 2 | 10 / 2 | 10 / 2 | 10 /2
Hor. / ver. chromaticities x,y |  | -113 / -120 | -127 / -140 | -152 / -150 | 
Momentum compaction factor  | 10-3 | 1.9 | 0.95 | 0.5 | ~0.2
Energy spread @ 5 and 10 GeV | 10-4 | 4.5 / 9.0 | 4.6 / 9.3 | 4.5 / 9.1 | 4.3 / 8.6
Normalized emittance @ 5 and 10 GeV | rad | 93 / 740 | 54 / 433 | 31 / 247 | 10.4 / 83.4
Hori. beam sizes at IP @ 5 and 10 GeV | m | 31 / 62 | 24 / 47 | 18 / 36 | 10 / 21
Energy loss per turn @ 5 and 10 GeV | MeV | 0.82 / 13.1 | 0.89 / 14.4 | 0.89 / 13.4 | 0.67 / 10.7
Total SR power @ 5 and 10 GeV | MW | 2.5 / 9.2 | 2.7 / 10.2 | 2.5 / 9.5 | 2.0 / 7.5
Arc cell length | m | 15.2 | 11.4 | 22.8 | 34.4
Arc dipole length / sagitta | m / cm | 5.4 / 3.3 | 3.6 / 1.65 | 4.0 / 1.83 | 4.2 (2.1) / 2.2 (0.6)
Arc dipole bending angle / radius | deg / m | 2.8 / 110.5 | 2.1 / 98.2 | 2.1 / 109.1 | 2.4 (1.2) / 100
quad length/strength @ 10 &12 GeV | m / T/m | 0.56 / 13 / 15.6 | 0.56 / 17.5 / 21 | 0.56, 1.0 / 20 / 24 | 0.3, 0.5 / 40 / 48

## Slide 8: Summary of Arc Optics Options
Optics with FODO arc cells using PEP-II magnets
  Pros: existing magnets, decent dynamic aperture
  Cons: large emittance, large momentum compaction factor, large sagitta
Optics with FODO arc cells using new magnets (baseline)
  Pros: decent emittance, decent momentum compaction factor, small sagitta, decent magnet strengths, decent dynamic aperture
  Con: new magnets
Optics with theoretical-minimum-emittance (TME) arc cells using new magnets
  Pros: small emittance, small momentum compaction factor, small sagitta
  Cons: new magnets, strong quadrupoles, not-large-enough dynamic aperture
Optics with hybrid-multi-bend-achromat (HMBA) arc cells using new magnets
  Pros: very small emittance, very small momentum compaction factor, small sagitta
  Cons: new magnets, strong quadrupoles, strong sextupoles for chromaticity compensation, need study of chromaticity compensation

## Slide 9: Detector Region Design
Detector region layout
  50 mrad crossing angle
    Fast beam separation, no parasitic collisions
    Improved momentum resolution of the detector solenoid
  Electron beam in a straight line
    Downstream chicane use for spectrometry and polarimetry
  50 mrad up- and downstream bends in ion beam
    Downstream beam lines used for spectrometry, dispersion control and geometry matching
Electron ring detector region optics
IP
e-
forward e-
detection region
FFQs
FFQs
Compton / far-forward e- detection region
Chicane dipoles

## Slide 10: Electron Collider Ring Layout
e-
R=155m
RF
RF
Spin rotator
Spin rotator
Arc, 261.7
81.7
Forward e- detection and polarimetry
IP
Tune trombone & Straight FODOs
Future 2nd IP
Spin rotator
Spin rotator

## Slide 11: Non-linear Chromaticity and Compensation
Non-linear chromaticity from final focusing quads
  Final focus is a large single source of non-linear chromaticity due to very large b and strong focusing
  Left and right FF quads act in the same phase to excite very large Db(d)/b perturbation, Db(d) gives rise to large 2nd and higher order tune shift DQ(d) and creates chromatic beam smear at IP
  These effects enlarge the tune footprint, thus exposing beam to more resonances, resulting in reduced energy range and beam lifetime, and increase the IP beam size s*(d), limiting luminosity
Chromaticity compensation block (CCB)
  The correction strategy is to create another large source of non-linear chromaticity – a local chromaticity correction block (CCB) using dedicated sextupoles – placed in phase with and as close as possible to the FF for local correction
  To compensate residual Db(d) at IP and outside of IR, two CCBs are required, independently correcting the FF on each side of IP

## Slide 12: Low Emittance SuperB-like CCB (SBCC)
Normal CCB based on regular arc cells creates a large emittance in the electron ring due to some of the dipoles located near high peaks of horizontal b
Solution: Super-B type chromaticity correction (SBCC) scheme with
  dipoles removed from high bx locations
  non-interleaved –I pair sextupoles locating at high b-functions
  dipole bending angles are adjusted for low emittance
CCB based on regular arc cells
-I
-I
S2
S2
S1
S1
SBCC based on cells with missing bends
-I
-I

## Slide 13: Electron Collider Ring Layout
e-
R=155m
RF
RF
Spin rotator
Spin rotator
Arc, 261.7
81.7
Forward e- detection and polarimetry
IP
Tune trombone & Straight FODOs
Future 2nd IP
Spin rotator
Spin rotator

## Slide 14: Electron Collider Ring Optics
Betatron tunes x = 59.22, y = 59.16
Chromaticity compensation block
x1
y1
x2
y2

## Slide 15: Electron Collider Ring Parameters
Electron beam momentum | GeV/c | 5
Circumference | m | 2336.18
Straights’ crossing angle | deg | 81.7
Beta stars at IP *x,y | cm | 10/2
Maximum horizontal / vertical  functions x,y | m | 327 / 420
Maximum horizontal dispersion Dx | m | 0.51
Horizontal / vertical betatron tunes x,y |  | 59.22 / 59.16
Horizontal / vertical chromaticitiesx,y |  | -124 / -166
Momentum compaction factor  |  | 9.5  10-4
Transition energy tr |  | 32.39
Normalized horizontal /vertical emittance x,y (un-normalized) | µm rad (nm rad) | 54 / 11 (5.5 / 1.1)
Horizontal / vertical rms beam size at IP *x,y | µm | 24 / 4.8
Maximum horizontal / vertical rms beam size x,y | mm | 1.3 / 0.26

## Slide 16: Baseline Beam Parameters
Beam energy | GeV | 3 | 5 | 6.95 | 9.3 | 10
Beam current | A | 3 | 3 | 3 | 0.95 | 0.71
Total SR power | MW | 0.34 | 2.63 | 10 | 10 | 10
Energy loss per turn | MeV | 0.12 | 0.88 | 3.3 | 10.5 | 14.0
Energy spread | 10-4 | 2.8 | 4.6 | 6.7 | 8.6 | 9.1
Transverse damping time | ms | 385 | 83 | 31 | 13 | 10
Longitudinal damping time | ms | 192 | 41 | 15 | 7 | 5
Normalized Emittance | um | 12 | 54 | 168 | 348 | 433

## Slide 17: Chromatic Tune and *
17
±11s
Betatron tunes are 59.22 and 59.16, * are 10 and 2 cm
Phase advance from SBCC sextupoles to IP is optimized near p/2+np for minimum chromatic tune shift over large energy range
40 x 108 degree cells in each arc for linear chromaticity sextupoles
W-function at IP is cancelled for minimum variation of b*(d)
Adequate chromatic compensation over 11sp range

## Slide 18: Sextupole Non-linear Geometric Effects
The SBCC –I sextupole pairs and the arc sextupole schemes provide compensation of some of the non-linear resonance effects from sextupoles
The choice of arc cell phase advance and number of arc cells Nc with sextupoles such that Ncmc = 2p*integer
  mc = 108 deg  Nc =10k in the electron ring
  yields cancellation of some of the non-linear resonance driving terms due to systematic non-linear field (A. Verdier, PAC’99; Y. Cai, NIM, A645:168–174, 2011)
Potential improvement of dynamic aperture
Cancellation of 3rd order resonance driving terms
SBCC
SBCC
Arc
IP
Arc

## Slide 19: Dynamic Aperture w/ Energy Dependence
DA without errors (shown at IP)
LEGO tracking with 1024 turns, x = +1, ex = 5.7 nm @ 5 GeV (agree with elegant results)
Fractional tune = (.22, .16)
DA ~ 18s for on-momentum
Energy range exceeds
±11σp at 5 GeV

## Slide 20: DA w/ Non-linear Field Errors in FF Quads
DA vs systematic non-linear field components (bn) in FF quads is evaluated
Each QFF bn is scanned, one at a time, while other QFF terms are turned off
PEP-II measured systematic bn in other ring magnets
Relatively strong sensitivity to b4, possibly due to the horizontal tune (59.22) near the 4th order resonance
Assuming the same DA reduction (red line in plots), a set of bn “tolerance” values is obtained
b3
b5
b4
b10
b6

## Slide 21: DA with Evaluated Systematic Errors in FF Quads
Without any errors (blue)
Without errors in FF quads, and with PEP-II systematic bn errors in all other magnets (red)
With evaluated errors in FF quads, based on scan, and with PEP-II systematic errors in all other magnets (green)
  DA reduction of a few x due to the evaluated QFF errors
  b3, b5, b10 values appear too generous, compared to PEP-II table  optimization (reduction) of these terms may improve the DA  to be studied
n | bn [10-3]
3 | 4
4 | 0.2
5 | 10
6 | 1.5
10 | 35
QFF evaluated bn
R = 44.9 mm
PEP-II systematic bn

## Slide 22: DA with PEP-II Measured Field Errors
PEP-II HER measured systematic and random field errors in all magnets (including FF quads)
10 random seeds, 1024 turns
Minimum DA among all seeds and angles is >11s with the average minimum DA of about 13s
Sufficient DA, but other errors (orbit, main field, coupling) and corrections are not yet included  to be studied
PEP-II systematic and random bn

## Slide 23: DA w/ Tune Options
Q = 59.22, 59.16
Q = 59.53, 59.567
On-energy DA near half-integer tune (.53, .567) is larger than at (.22, .16), but energy range is smaller
DA vs integer part of tune
(59/59, 59/60, 59/61, 60/59, 61/59)
No significant sensitivity to integer part of tune
To do  tune scan

## Slide 24: Summary
The baseline design of JLEIC electron collider ring has been completed
  meeting all requirements on the beam parameters, in particular on the emittance
  incorporating provisions for correction of beam nonlinearity without introducing emittance growth
  incorporating dedicated electron polarization and forward detection design
  accommodating up to two detectors
  considering optics design for special elements, such as spin rotator, RF, etc.
To do list for DA study
  perform tune scan to find optimal tunes for maximum DA
  perform tracking with a full set of errors and corrections
  perform tracking with beam-beam and crabbing effects

## Slide 25: Acknowledgment
Thanks to Yuhai Cai and Yuri Nosochkov (SLAC) for help on the detail of study of compensation schemes and tracking simulations
Thanks to Vasiliy Morozov and Yuhong Zhang (JLAB) for discussion
Thank you for your attention !
谢谢 !