## Slide 1
VACREE TECHNOLOGIES CO., LTD
Application and Problem-solution of Helium Purifier
for Cryogenic System
Xuehua Zhang

## Slide 2
Helium Purifier Application in Cryogenic System
1
3
Solution of Helium purifier in Cryogenic System
Contents
2
Helium Purifier Methods and Process Flow
4
Problem Analysis and Discussion

## Slide 3
Application requirements
Helium purifier
Particle Accelerator
Magnetic confinement fusion
Vertical Test Cryostat
Superconducting magnet
Notes: 3
<click> Among others, there are four fundamental questions as Herbert Simon pointed out in his talk at Boulder in 1986: Matter, Universe, Life, and Mind.

## Slide 4
Application requirements
The annual use of helium in China is 2.42×107 Nm3
So helium recovery and purification is necessary.
Proportion of helium consumption worldwide
Main application fields of helium

## Slide 5
Helium Purifier Application in Cryogenic System
1
3
Solution of Helium purifier in Cryogenic System
Contents
2
Helium Purifier Methods and Process Flow
4
Problem Analysis and Discussion

## Slide 6
No | Item | High Pressure Cryo-condensation & adsorption | Membrane Separation | PSA | Freezing Adsorption
1 | Working Pressure bar | 100～150 | 8 | 8、16 | 8
2 | Technique | Technical maturity | Advanced | More advanced | More advanced
3 | Structure | Compact | Compact | Big Size | Compact
4 | He Compressor | Needed | Needed | Needed | Needed
5 | He Recovery | Gas Cyliner Filling | TBA | TBA | TBA
6 | Operation | Easy | Easy | Complex | Easy
7 | Automation | High | High | High | High
8 | LN2 | LN2 Storage Tank | Not Needed | Not Needed | Not Needed
Comparison of Helium Purification Methods
Purification principle

## Slide 7
Cryogenic Liquefaction ( Freezing) & Separation
Principle: Taking LN2 as cold source to cool raw gas to be lower than 77K, and pressurize the gas to HP ,The boil point of He is the lowest 4.2K,Other impurity gases are liquefied and separated out.
Features: Big capacity, High purity, Complex structure
Cryogenic Adsorption
Principle：Adsorption agent has very big specific surface area, which has excellent adsorption to impurity gases under cryogenic temperature
Features: Good adsorption, Regenerative, High purity gas processed.
Cryogenic Purification

## Slide 8
Membrane Separation
Principle: Gases have different permeability across the membrane. It is easier for Helium to pass through the membrane
Permeability Coefficient：P=D×S
Separation Coefficient：α=P1/P2
Feature ：Small size, High-efficiency, Low energy-consumption, But the highest purity of helium is 99%
Gas membrane separation
H2
e

## Slide 9
≥10.0% Crude Helium
Recovery
Unit
Cryogenic gas/ liquid Separation
Membrane Separation
1st stage Purification
Cryocooler Cryogenic Condensation
LN2 HP/MP Cryogenic Adsorption Separation
2nd stage Purification
≥99.0%
Helium
≥99.999%
Helium
Float, Optical Fiber Cooling, Leakage Detection, etc
Cryogenic SC, Protective gas of Optical Fiber, Cryogenic physics
User
Recycling
Adopt Two-stage Separation & Purification
fiber- optical factory
Semiconductor production
Metal arc welding
aerostat
Pipeline replacement
Cryogenic Engineering
Principle diagram of helium recovery and purification
Purification principle

## Slide 10
Helium Purifier Application in Cryogenic System
1
3
Solution of Helium purifier in Cryogenic System
Contents
2
Helium Purifier Methods and Process Flow
4
Problem Analysis and Discussion

## Slide 11
System Process Flow
Recovery & Storage
Purification & Liquefaction
End-User

## Slide 12
Flow diagram
双龙

## Slide 13
Item | Unit | Index | Test Result | Remark
Medium |  | Helium | 95% He （Averaged） | Better
Capacity | Nm³/h | 20～100 | 100 | Compliance
Working Pressure | bar(g) | 100～200 | 120(Averaged) | Compliance
Pressure Loss | bar(g) | ≤2 | 1.8 (Averaged) | Better
Dim. | mm | 2240×2456×3100 （L×W×H） | 2240×2456×3100 （L×W×H） | Compliance
Outlet Impurity | ppm | ≤10 | 2.8PPm and above | Better
Saturation | h | 98% He，≥6.5 | 95% He，≥8 | Better
 |  | 99% He，≥12 |  | 
Typical helium purifier used in cryogenic engineering, He:95%→99.999%
Specifications
Diagram
GCH Series High Helium Purifier

## Slide 14
Process Flow Diagram
GCH Series High Helium Purifier
The system is divided into two groups，each containing a dryer and a purifier , one working and the other activating standby

## Slide 15
Functions
Start-off Compressor
Tank pressure regulate
Inlet Pressure regulate
Start-off Solenoid valves
Helium flow control
Data Display
Operation Status
CP Fault light
Differential pressure
Pressure points
Flow capacity points
Data Exchange
Touch Screen
Controller
Signal indicators，Alarm
Valve operators, mechanical pumps ,etc
Status of Components
Pressure
Temperature
PLC
Control Logic
Equipment Control
Status Display
Curve Generation
Data Storage
Data display
System Control
Control system
The purifier is controlled by PLC to detect ,control,and store the data of T,P,F﹍

## Slide 16
Ave. Capacity：80.354m³/h
Ave. Differential Pressure：1.749bar(g)
Ave. Purity：96.287%
∑ N2+O2+H2O＜5ppm
PIN-POUT＜2bar
Adsorption Volume
5N9: 80.354×（1-96.287%）×8=23.865m³（air）
5N9.5: 80.354×（1-96.287%）×6.5=19.393m³（air）
Requirement：80×0.02×6.5=10.4m³（air）
GCH Series High Helium Purifier
Test graph of the system, including: Capacity/Pressure/Purity/Adsorption Volume

## Slide 17
Third party Test Report
Product photo
GCH Series High Helium Purifier

## Slide 18
Helium Purifier Application in Cryogenic System
1
3
Solution of Helium purifier in Cryogenic System
Contents
2
Helium Purifier Methods and Process Flow
4
Problem Analysis and Discussion

## Slide 19
No | User | Specification | Year
1 | IMP,CAS | Capacity:100Nm3/h；Outlet Purity≥ 99.999% ；Working Pressure：16bar | 2012
2 | IHEP.CAS | Capacity:105Nm3/h；Outlet Purity≥99.9995% ；Working Pressure：150bar | 2013
3 | SINAP,CAS | Capacity:30Nm3/h；Outlet Purity ≥99.995%；Working Pressure：200bar | 2013
4 | CAEP | Capacity:20Nm3/h；Outlet Purity≥99.999% ；Working Pressure：150bar | 2013
5 | Chinese space | Capacity:60Nm3/h；Outlet Purity≥99.999% ；Working Pressure：250bar | 2014
6 | ASIPP,CAS | Capacity:80Nm3/h；Outlet Purity≥99.999% ；Working Pressure：19-30bar | 2015
7 | TIPC,CAS | Capacity：100Nm3 /h：Working Pressure：150bar；Outlet Purity≥99.999% | 2016
8 | Sumitomo Electric | Capacity：25Nm3 /h：Working Pressure：70bar；Inlet Purity 60%，Outlet Purity≥99.999% | 2016
9 | Air Liquide | Capacity:100Nm3 /h；Working Pressure：150bar；Outlet Purity≥99.999% | 2016
10 | Peking University | Capacity:60Nm3 /h；Working Pressure：150bar；Outlet Purity≥99.999% | 2016
Application Reference
Application of helium purifier in cryogenic engineering in China

## Slide 20
Temp. Sensor Damaged
HT & LT
Shock
Select reliable or backup
Problem-solution-1
We had some problems on the purifier during the operations.

## Slide 21
Inlet Gas Analyzer damaged
Water inside
Analyzer was Installed After dryer
Before solution
After solution
Dryer
Problem-solution-2

## Slide 22
Compressed He Contains
a lot of oil
The effect of oil-filter is not good
Add another oil-filter
Problem-solution-3

## Slide 23
Pneumatic Valve Leakage
Valve Disc/Stem
The valve cannot work at low temperature
Exchange LT valve
Problem-solution-4

## Slide 24
The T of Heat exchanger outlet is low
The HE is in the cold LN2 of Dewar
Outlay Heat Exchanger added
Heater to be Added
303K
170K
293K
80K
Problem-solution-5

## Slide 25
Purifier Blocked
Adsorption powder?
Valve leakage?
H2O filtered not completely?
Inlet pressure
Outlet pressure
Solution: Reverse exhaust from vent or replacement of adsorption material
Problem-solution-6

## Slide 26
Model | GCH -20 | GCH -60 | GCH -100 | GCH - 200 | GCH - 300
System handling capacity | 20﻿﻿﻿﻿m3/Hr | 60﻿﻿m3/Hr | 100﻿﻿m3/Hr | 200﻿﻿m3/Hr | 300﻿﻿m3/Hr
Working pressure | 20~200 bar | 20~200 bar | 20~200 bar | 20~200 bar | 20~200 bar
Inlet helium purity | 50%~99% | 50%~99% | 50%~99% | 50%~99% | 50%~99%
Outlet helium purity | 99.999% | 99.999% | 99.999% | 99.999% | 99.999%
GCH Series High Helium Purifier
Through years of improvement and upgrading, We have
a series of standard products

## Slide 27
1
Conclusion
Helium Purifier is extensively used in the cryogenics system
2
3
4
Helium Purification Methods: Membrane separation,cryogenic condensation and adsorption
The outlet Purity can be 99.999%
We should focus on key parts selection and process optimization

## Slide 28
Thanks for your attention!
Contact information
Company: Vacree Technologies Co., Ltd.
Add： No. 189 Haitang Road Hi-Tech Zone ,Hefei, China.
Website：www.vacree.com
Cellphone：13956079943
E-mail： Zhangxh@vacree.com
Welcome to VACREE booth for questions