## Slide 1
Cryogenic system for (SCLF) SHINE Test facility
Zhengrong Ouyang, Shuhua Wang, Jiuce Sun, Lei Zhang, Lei Lei, Xiongzhong Deng
Notes: Good Moring ladies and gentle man, it is my great pleasure to present the new project in front of many cryogenic experts here. My name is Jiuce Sun. Here are all the cryogenic stuff we got so far, a small group, not very well experienced but full of motivation and enthusiasm, That is why Your comments and suggestions are highly welcomed and appreciated. There is a slight change in the title of my talk. Instead of SCLF, difficult to pronounce and remember. a new project name SHINE has been adopted. What this new name stands for will be explained in the presentation later.

## Slide 2: Outline
1. Introduction to SHINE facility
2. Cryogenic system for SHINE facility
  Conceptual design
  Preliminary layout
3. Cryogenic system for SHINE test facility
  Refrigerator process and layout
  Cryogenic distribution system
4. Summary
Notes: In my presentation, the SHINE facility will be briefly introduced in the beginning, and afterwards I will talk a little bit about the conceptual design and preliminary layout of the cryogenic system for the SHINE facility. Next I will concentrate on the cryogenic system for the test facility within SHINE project.

## Slide 3: XFEL: X-ray free electron laser
Eadweard Muybridge, 1892
European XFEL, 2017
Notes: SHINE is a kind of XFEL, which means X-ray free electron laser. And what is this. Technically speaking it is a camera which takes photos and videos. However, it is not an ordinary camera, in fact it is a much much more powerful tools. Take the European XFEL as example, It increases the spatial resolution down to molecule level and it could capture molecule movies regarding time resolution . That is why it is significant for the fundamental research and leads the international competition.

## Slide 4: SHINE comparison
Shanghai XFEL
>2.7m
2.0m
~1.
5m>1.2m
2.0m
ITEM | European XFEL | LCLS-II（HE） | SHINE facility
RF mode | Pulsed | CW | CW
Power source | Klystron | SSA | SSA
Install | Single ac Tunnel | Tunnel + Gallery | Single ac Tunnel
2K heat load/CM | ~20w/CM | ~80w/CM | ~80w/CM
Tunnel slope | ~ | 0.5% | ~
N of modules | ~100 | ~35（+19） | ~75
2K capability | ~3kW | ~ 2 x 4kw | ~ 3x4 kw
Notes: Last year, the European XFEL had been built and started the operation. It is a pulsed type and later on the LCLSII project plans to built a CW type with around 35 cryomodules in the beginning. The nominal 2K cooling capacity is two times 4 kW. The new SHINE projects intends to built also a CW type XFEL with more cryomodules and thus requires a higher 2K cooling capacity.

## Slide 5: SHINE facility
Shanghai HIgh repetition rate XFEL aNd Extreme light facility
Notes: OK, what does SHINE mean. The full name is Shanghai HIgh repetition rate XFEL aNd Extreme light facility .

## Slide 6: SHINE facility
Shaft 1
Shaft 2 Shaft 3 Shaft 4
Shaft 5
8GeV CW Linac
BDS FELs
BLs
NEH
FEH
BLs
SHINE is a newly proposed MHz high rep-rate XFEL, based on an 8 GeV CW SRF linac;
This facility will be built in a 3.2 km long tunnel (30m underground) at Zhang-Jiang High Tech Park, across the SSRF campus in Shanghai;
This XFEL facility includes 3 undulator lines and ~10 experimental stations in phase one;
It can provide the XFEL radiation in the photon energy range of 0.2 -25 keV.
Notes: Here is the rough schematic illustration of SHINE facility. Shine is a newly proposed High repetition rate XFEL, the Superconducting linac will be 1.3 km long and could reach 8GeV.
The entire SHINE facility will be 3.2 km long and built in 30 m underground tunnels at Shang Zhangjiang Hight Tech park.

## Slide 7: SHINE Layout
N
E
W
S
SSRF
SXFEL
SHINE
Full-range (IR to γ) photon science facility cluster in Shanghai
SLEGS
SULF
SEL
SXFEL-γ

## Slide 8: SHINE Layout
N
E
W
S
SC Linac
Injector
Undulators
Beamlines
Beamlines
Near Exp. Hall
Far Exp. Hall
1st plant
2nd plant

## Slide 9: SHINE Superconducting (SC) Linac
1.3 GHz Cryo-Modules: x 75
Cavities: 8
Length 12 m
Weight 8,000 kg
Cryo-Modules: x 77
3.9 GHz Cryo-Modules: x 2
Cavities: 8
Length 6 m
Weight 4,000 kg
Parameter | value | unit
RF | 1.3 | GHz
Max.avg.RF CW gradient | 16 | MV/m
Max.RF gradient | 18 | MV/m
Active length of 9 cell cavity | 1.038 | m
Mean cavity quality factor | >2.7 | 1010
temperature | 2.0 | K
cavities | 8 | -
Heat load(dynamic) | 74.6 ~100 | W@2K
Heat load (static) | 6 | W@2K
pressure | 31 | mbar
Volume of helium | 184 | L

## Slide 10: SHINE Superconducting (SC) Undulators
One of the Undulator lines plans to adopt SC type（4.5K)

## Slide 11: Outline
1. Introduction to SHINE facility
2. Cryogenic system for SHINE facility
  Conceptual design
  Preliminary layout
3. Cryogenic system for SHINE test facility
  Refrigerator process and layout
  Cryogenic distribution system
4. Summary
Notes: In my presentation, the SHINE facility will be briefly introduced in the beginning, and afterwards I will talk a little bit about the conceptual design and preliminary layout of the cryogenic system for the SHINE facility. Next I will concentrate on the cryogenic system for the test facility within SHINE project.

## Slide 12: SHINE facility heat load
Item |  | 2K heat load（kW） | 4.5K Heat load（kW）
1.3GHz SRF Cavities | static | 0.75 | 1.575
 | dynamic | 6.075 | 0.375
 | total | 6.825 | 1.95
Undulator | static |  | 0.4
 | dynamic |  | 4
Distribution | Valve box | 1.0 | 1.0
 | Transfer line | 1.5 | 1.5
Total |  | 9.325 | 8.85
SHINE cryoplant capacity 12kW@2K == 4kW X 3

## Slide 13: SHINE cryoplant layout
GHe Storage
Compressor system
ORS
4.5 K
Cold box
LHe
Dewar
2 K
Cold box
Distribution
Box
LN2 Storage
Purification system
Compressor system
ORS
4.5 K
Cold box
LHe
Dewar
2 K
Cold box
GHe Storage
Compressor system
ORS
4.5 K
Cold box
LHe
Dewar
2 K
Cold box
Distribution
Box
LN2 Storage
Purification system
Shaft 1
Shaft 2
L0 LH L1 BC1 L2(CM4-21) BC2 L3(CM22-CM51) BREAK L4(CM52-CM75)
CP1
CP2
CP3

## Slide 14: Cryoplants at No. 1 Shaft
Shaft120X70
Shaft232X88
Shaft340X30
Shaft455X50
1430m
Shaft555X76
3X400m
3X205m
LuoShan Road
GE R&D center
SSRF
3X760m
Two Cryoplants with 4kW@2K will be installed

## Slide 15: Cryoplant at No. 2 Shaft
One Cryoplant with 4kW@2K will be installed

## Slide 16: Outline
1. Introduction to SHINE facility
2. Cryogenic system for SHINE facility
  Conceptual design
  Preliminary layout
3. Cryogenic system for SHINE test facility
  Refrigerator process and layout
  Cryogenic distribution system
4. Summary

## Slide 17: Cryogenic test facility
HTB1
HTB2
VTC1
VTC2
UTC1
GTC1
CTC1
MTC1
VTC4
VTC3
HTB4
HTB3
UTC2
CTC2
BTC1
VTC: Vertical Test Cryostat
HTB: Horizontal Test Bench
UTC: Undulator Test Cryostat
CTC: Cavity Test Cryostat
GTC: General Test Cryostat
MTC: Magnet Test Cryostat
BTC: Backup Test Cryostat
15
Test cryostats (benches)
17
CAVITIES:
- A: 4K, 3.00 bar
- B: 2K, 0.03 bar
INTERCEPT:
- C: 4.5K, 3.0 bar
- D: 8K, 1.3 bar
SHIELDS:
- E: 35 K, 3.0 bar
- F: 55 K, 1.3 bar
3
Temperature
circuits

## Slide 18: Heat load requirements
Maximum capacity
  1000W @2K
  350W @4.5K
  3750W @35K
  121.8 L/h
Turn-down
  350W @2K
  100W @4.5K
  1000W@35K
Liquefaction
  970 L/h
Item | 2K heat load/W |  |  | 4.6K heat load/W |  |  | 35K heat load/W |  |  | Coolig type | Number
 | Normal | Max. | Min. | Normal | Max. | Min. | Normal | Max. | Min. |  | 
2K Horizontal | 110 | 250 | 10 | 40 | 50 | 15 | 210 | 260 | 130 | bath@2K | 1
 | 180 | 200 | 20 | 80 | 100 | 15 | 420 | 520 | 130 |  | 1
 | 90 | 100 | 10 | 40 | 50 | 15 | 210 | 260 | 130 |  | 2
1.5K-2K Vertical | / | 270 | 5 | / | / | / | / | 50 | / | bath@2K | 1
 | / | 140 | 5 | / | / | / | / | 50 | / |  | 3
2K Single Cavity | 20 | 50 | 10 | / | 30 | / | / | 200 | / | bath@2K | 2
2K SCM | / | 10 | 5 | / | 20 |  | / | 200 |  | bath@2K | 1
2K Heat Exchanger | 500 | / | / | / | / | / | 50 | / | / | bath@2K | 1
4.6K SCM | / | 15 | 8 | / | 20 | ？ | / | 200 | 150 | bath@4.6K | 1
4.5K SCU | / |  |  | / | 80 | 10 | / | 700 | 500 | forced flow | 2

## Slide 19: Cryoplant process for SHINE test facility
3 stages turbine
LN2 precooling
  All in one
  cold box
3 Temperature circuits
  2K loop
  5-8 K
  35-55K
3 stages cold compressor
5 VLP pumps

## Slide 20: Process – Pressure circuits
AmbientHX
Warm
compressor
station
T01
x 5
VP1
VLP->LP
VLP
LP
2K return
(GHe 3.3K)
CS return
(GHe 8.0K)
4.5K supply
(SHe 4.5K)
TS supply
(GHe 35K)
TS return
(GHe 55K)
x 2
C01 LP->HP
T02
T03
Buffer
HX-03
HX-02
HX-01
LHe
Dewar
CDS
HX-05
HX-06
subcooler
HX-04
Warm-up return
A02
H2-Ne
Adsorbers
CC01
CC02
CC03
H2O + N2
+ CnHm
Anlayzer
ORS
cold box
Cool down
（GHe 80K）
A01A/B
Air
Adsorbers
LN2
phase-seperator
LN2
GN2
HP
LP
VLP
Cold compressor

## Slide 21: Process – temperature circuits
AmbientHX
Warm compressor station
x 5
VP1
VLP->LP
VLP
LP
2K return
(GHe 3.3K)
CS return
(GHe 8.0K)
4.5K supply
(SHe 4.5K)
TS supply
(GHe 35K)
TS return
(GHe 55K)
x 2
C01 LP->HP
Buffer
HX-03
HX-02
HX-01
CDS
HX-05
HX-06
subcooler
HX-04
T02
Warm-up return
A02
H2-Ne
Adsorbers
CC01
CC02
CC03
H2O + N2
+ CnHm
Anlayzer
ORS
cold box
T03
Cool down
（GHe 80K)
T01
A01A/B
Air
Adsorbers
LN2
phase-seperator
LN2
GN2
HP
LP
VLP
LHe
Dewar

## Slide 22: Process design – maximum capacity
Cooling capacity | 2K | 1000 | W
 | 4.5K | 350 | W
 | 35K | 3750 | W
 | LHe | 121.8 | L/h
Warm compressors | Suction pressure | 1.05 | bar
 | Discharge pressure | 15 | bar
 | mass flow | 303.2 | g/s
VLP Pumps | Suction pressure | 0.4 | bar
 | Discharge pressure | 1.05 | bar
 | mass flow | 50.5 | g/s
Cold compressors | Pressure to CC1 | 0.03 | bar
 | Pressure from CC3 | 0.48 | bar
 | mass flow | 50.5 | g/s

## Slide 23: Process design – turn down mode
Cooling capacity | 2K | 350 | W
 | 4.5K | 100 | W
 | 35K | 1000 | W
 | LHe |  | L/h
Warm compressors | Suction pressure | 1.05 | bar
 | Discharge pressure | 13.4 | bar
 | mass flow | 196.1 | g/s
VLP Pumps | Suction pressure | 0.11 | bar
 | Discharge pressure | 1.1 | bar
 | mass flow | 17.2 | g/s
Cold compressors | Pressure to CC1 | 0.03 | bar
 | Pressure from CC3 | 0.14 | bar
 | mass flow | 17.2 | g/s

## Slide 24: Process design – Liquefaction mode
Cooling capacity | 2K |  | W
 | 4.5K |  | W
 | 35K |  | W
 | LHe | 970 | L/h
Warm compressors | Suction pressure | 1.05 | bar
 | Discharge pressure | 15 | bar
 | mass flow | 256.4 | g/s
VLP Pumps | Suction pressure |  | bar
 | Discharge pressure |  | bar
 | mass flow |  | g/s
Cold compressors | Pressure to CC3 |  | bar
 | Pressure from CC1 |  | bar
 | mass flow |  | g/s

## Slide 25: Process – test mode
AmbientHX
LN2
phase-seperator
x 5
x 2
Warm compressor station
T01
CC01
CC02
VP1
VLP->LP
VLP
LP
C01 LP->HP
T02
T03
Buffer
HX-03
HX-02
HX-01
CDS
EH02
EH01
HX-05
HX-06
subcooler
HX-04
A02
H2-Ne
Adsorbers
CC03
H2O + N2
+ CnHm
Anlayzer
ORS
cold box
A01A/B
Air
Adsorbers
LN2
GN2
EH03
Test heaters
2K / 4.5 K
LHe
Dewar
2K return
(GHe 3.3K)
CS return
(GHe 8.0K)
4.5K supply
(SHe 4.5K)
TS supply
(GHe 35K)
TS return
(GHe 55K)
Warm-up return
Cool down
（GHe 80K）
Maximum capacity
  1000W @2K
  350W @4.5K
  3750W @35K
  121.8 L/h
Turn-down
  350W @2K
  100W @4.5K
  1000W@35K
Liquefaction
  970 L/h

## Slide 26: Cryoplant Schedule

## Slide 27: Layout - Cryogenic test facility
HTB1
HTB2
VTC1
VTC2
UTC1
GTC1
CTC1
MTC1
VTC4
VTC3
HTB4
HTB3
UTC2
CTC2
BTC2
VTC: Vertical Test Cryostat
HTB: Horizontal Test Bench
UTC: Undulator Test Cryostat
CTC: Cavity Test Cryostat
GTC: General Test Cryostat
MTC: Magnet Test Cryostat
BTC: Backup Test Cryostat
EVB: End Valve Box
EVB1
EVB2
Cryogenic transfer line
Test Hall 1#
Test Hall 2#
So far, 15 test cryostats (benches) in total have been proposed

## Slide 28: Layout - Cryoplant
HTB1
HTB2
VTC1
VTC2
UTC1
GTC1
CTC1
MTC1
EVB1
VTC4
VTC3
HTB4
HTB3
UTC2
CTC2
BTC2
EVB2
GHe Storage
LN2 Dewar
Cold box
Warm compressor
LHe Dewar
VLP Pumps
ORS
Warm compressor
Recovery and Purification
Test Hall 1#
Test Hall 2#
Cryofactory

## Slide 29: Cryogenic system preliminary layout
Cold box
VLP pumps
Warm compressors
ORS
Dewar
Transfer
Line
Purifier
Recovery compressors
Transfer
Line
Valve boxes
Helium Inventory
Test Hall 1#
Test Hall 2#

## Slide 30: Cryogenic distribution system
From Cold Box
End Valve Box 1
End Valve Box 2
Splitting Box
Multi-channel Transfer Lines
Multi-channel Transfer Lines
9 Valve Box
6 Valve Box
Pipe line | Pressure | Temperature
 | barA | K
A/C | 3 | 4.6
B | 0.0275 | 3.5
D | 1.3 | 8
E | 14.24 | 35
F | 13.74 | 55
G1 | 15 | 80
H | 1.3 | 4.6-300

## Slide 31: Cryogenic distribution system PFD
300-80K
80-45K
45-4.6K
300K
80K
80K
4.6K
4.6K
2K operation
4.6K
35K

## Slide 32: Outline
1. Introduction to SHINE facility
2. Cryogenic system for SHINE facility
  Conceptual design
  Preliminary layout
3. Cryogenic system for SHINE test facility
  Refrigerator process and layout
  Cryogenic distribution system
4. Summary
Notes: In my presentation, the SHINE facility will be briefly introduced in the beginning, and afterwards I will talk a little bit about the conceptual design and preliminary layout of the cryogenic system for the SHINE facility. Next I will concentrate on the cryogenic system for the test facility within SHINE project.

## Slide 33: Summary
SHINE is a newly proposed MHz high rep-rate XFEL based on an 8 GeV CW SRF linac;
Three Cryoplants with 4kW@2K will be built for SHINE facility;
One cryoplant with 1kW@2K and corresponding distribution system is being built for SHINE test facility

## Slide 34
Thank you!

## Slide 35: Key components – Warm compressor
2
3
1
35K Shield
4.5K Cold mass
0.4 bar
1.05 bar
15.0 bar
Comp. | Flow | Power
HP x2 | 303g/s | 1065kW
VLPx5 | 50.5g/s | 92.5kW
 |  | 1157.5kW
2 Kaeser skids HSD842 model
Oil-lubricated screw compressors
Each skid contains 2 screws
1 screw with VFD for optimized power consumption
Water cooled
Length | Wide | Height | Weight
m | m | m | kg
4.37 | 2.15 | 2.35 | 10100
3.57 | 2.15 | 2.35 | 8600
Notes: By using a variable frequency driver (integrated in an additional cabinet beside the main compressor box, refer to above Figure 1), the compressor processed flow can be adjusted to the refrigeration need.

## Slide 36: Key components – VLP pumps
Length | Wide | Height | Weight
m | m | m | kg
7.5 | 2.2 | 2.0 | 6500
2
3
1
35K Shield
4.5K Cold mass
0.4 bar
1.05 bar
15.0 bar
Comp. | Flow | Power
HP x2 | 303g/s | 1065kW
VLPx5 | 50.5g/s | 92.5kW
 |  | 1157.5kW