## Slide 1: Phase shifter design for Macro Pixel ASIC
Jian Wang wangjian@ustc.edu.cn
State Key Laboratory of Particle Detection and Electronics
University of Science and Technology of China
Southern Methodist University

## Slide 2: Outline
Background
Interface
Digital flow
Phase shifter custom design for 320 MHz clock
Post-simulation results
Summary

## Slide 3: CMS Tracker will be upgraded during Phase II
  To exploit the very high interaction rate and integrated luminosity, reaching 3000 fb-1, major upgrades to CMS are necessary
  HL-LHC will operate at 14 TeV centre of mass energy with a peak luminosity of 5x10^34cm-2s-1

## Slide 4: Pt modules and Pixels compose the Tracker
Tracker Layout by G.Bianchi, N.De Maio and S.Mersi
140 mm
70 mm
130 mm
130 mm
Z
Ф
2 Strip module
Strips 5 cm x 90 um
r > 40 cm
TID ~ 40 Mrad
Pixel Detector (RD53)
Pixels 50um x 50um or 100um x 100um
r < 20 cm
TID ~ 1 Grad
No high-pT information
Pixel + Strip module
Pixels 1.5mm x 100um
Strip 2.5cm x 100um
r < 20 cm
TID ~ 100 Mrad

## Slide 5: Pixel + Strip module readout scheme
STRIP
PIXEL
wire bonds
wire bonds
bump bonds
ShortStrip ASIC (SSA):
Strip Readout only
MacroPixel ASIC (MPA):
Pixel readout +
Correlation +
Data storage
Front-End Hybrid
3x
Barrel Layers

## Slide 6: Pixel + Strip module exploded view
ShortStripASIC x 8
Concentrator IC (CIC)
Data aggregation
MacroPixelASIC x 16
Pixelated Layer
Strip Layer
LP-GBT and VTRx+
Data transmission through the optical link
DC-DC converters
PS module is fully integrate entity

## Slide 7: Data Readout block diagram of SSA + MPA
FE
SRAM
Memories
Stub Finding
Logic
Binary
Readout
FE
Binary
Readout
High pT
information
All tracks
information
L1 Data
Encoders
@ L1 trigger rate (1 MHz)
@ Bunch crossing frequency (40 MHz)
SSA
MPA
PIXEL
STRIP

## Slide 8: Tracker Back-end data transmission optimization
320 Mbps
High pT
Information
All tracks
Information
LP-GBT
1600 Mbps
Macro
Pixel
ASIC
.
.
.
.
.
Total of 8 MPAs
(send out data every 2 BX)
320 Mbps
1600 Mbps
Macro
Pixel
ASIC
1600 Mbps
Concentrator
IC
(sends out data every 8 BX)
1600 Mbps
Data transmission frequency 320 MHz with differential lines
SPECIFICATION DEFINITION ON GOING

## Slide 9: MPA Block Diagram
The Macro Pixel ASIC (MPA) is a pixel readout ASIC for the Phase II Outer Tracker upgrade of CMS.
It features the novel technique for high-pT particle recognition which allows the generation of data for the Trigger.
The design requires two Delay Lines highlighted in the picture on the right and described in the next slides.

## Slide 10: Phase Shiter for Clock Deskew
Application: Remove the skew on the event sampling clock among the chips in the same module.
Specifications:
  Resolution = 200-400 ps
  Input Frequency = 320 MHz
  Jitter < 10 ps
  Closed-Loop (Delay-locked loop)

## Slide 11: Phase Shifter integration
The delayed 320 MHz clock is used to sample the 40 MHz clock. The clock generated is the 40 MHz clock for the event sampling. A re-sampling is carried out on the data output with the not-delayed 40 MHz clock to be realigned with the input 320 MHz used for data transmission.
Phase Shifter
Command Decoder
CLK320
T1 commands
CLK40
Sampling CLK40

## Slide 12: Interface
Control Logics
(digital part)
Phase Shifter
(analog part)
dllEnable
dllForcedown
dllReset
dllChargePumpCurrent[3:0]
dllClockSelect[3:0]
dllLateA
dllLateB
dllLateC
clock @320 MHz
clkOut
The Control Logics initialize the Phase Shifter and select which phase to output.
The Phase Shifter generates 16 equally-spaced phases with a resolution of 208.3 ps at 320 MHz

## Slide 13: Digital flow
After power on, digital logics should reset LPF to VDD by disabling the whole
custom part, i.e. pulling down the “dllEnable” signal. The reset time is less than
200 ns. After resetting, delay cell has a minimal delay.
Then the logics gives a low level “dllForceDown” to force the charge pump to discharge the LPF. Thus the delay will increase.
After the control voltage on the LPF drops to a value that dllLate changes its
level from high to low, release the “dllForceDown” signal and give the loop
control back to DLL.
The control voltage will continue to drop until DLL is locked. Then it will change
according to the switching of up and down signals.

## Slide 14: Phase Shifter custom design for 320 MHz clock
[0]
[1]
[2]
[3]
[4]
[5]
[6]
[7]
[8]
[12]
[13]
[16]
dllChargePumpCurrent[3:0]
dllLateA
dllForceDown
Reference
clock
[10]
[9]
[11]
[14]
[15]
dllLateB
dllLateC
dllReset
dllEnable
clkDelay
The delay line is composed of 17 delay cells. The last one is dummy.
The delay resolution is T/15 that is
clockSelect[3:0]
16:1 MUX
D
CLK
down
up
Phase
detector
Charge
Pump
clkOut
Voltage controlled delay line
LPF

## Slide 15: Schematic and layout
Delay line
And
16:1 MUX
Phase
detector
Charge
Pump
LPF
Schematic:
layout:
~100um x 400um

## Slide 16: Test bench
320 MHz clock inputs. Run post-simulations in three corners: nominal corner, fastest corner—C2, slowest corner—C15. Minimal current setting.
The control voltage is initialized to a value to make DLL locked at the beginning of simulation.
The clockDelaySelect[3:0] change in turns so that the clkOut comes from tap0 to tap15 successively.

## Slide 17: Corner definition of MPA
TYPICAL: TT, 1 V, 25 C
FAST: FF, 1.1 V 0 C
SLOW LOW TEMPERATURE: SS, 0.9 V, -40 C
SLOW HIGH TEMPERATURE: SS, 0.9 V, 50 C

## Slide 18: Results in Typical corner
DLL functionality:
DLL is locked. The rising edges of two inputs of the phase detector are very close to each other.
Phase shifting:
1 LSB = 208.3 ps.
DNL = 0.008 LSB.
INL = 0.01 LSB.
Jitter =2.99 ps.
Power dissipation
is 1.007 mW.
dn
up
vCtrl
clkDelay
And
clkRef
Chart: Phase shifting in typical corner
 | 208.0175 | 207.5623 | 208.5599 | 207.8424 | 208.6063 | 209.3641 | 206.8402 | 206.8175 | 209.3791 | 207.0091 | 208.21 | 209.7131 | 209.1846 | 208.1657 | 206.714
 | 208.0175 | 207.5623 | 208.5599 | 207.8424 | 208.6063 | 209.3641 | 206.8402 | 206.8175 | 209.3791 | 207.0091 | 208.21 | 209.7131 | 209.1846 | 208.1657 | 206.714

## Slide 19: Results in Fast corner
DLL functionality:
DLL is locked. The rising edges of two inputs of the phase detector are very close to each other.
Phase shifting:
1 LSB = 208.3 ps.
DNL = 0.008 LSB.
INL = 0.009 LSB.
Jitter = 3.03ps.
Power dissipation
is 1.447 mW.
dn
up
vCtrl
clkDelay
And
clkRef
Chart: Phase shifting in fast corner
 | 207.744 | 208.612 | 208.7586 | 208.3589 | 208.9331 | 208.0461 | 206.7354 | 207.335 | 208.0977 | 208.4002 | 209.7366 | 209.732 | 207.7157 | 209.3478 | 208.0156

## Slide 20: Results in slow low temperature corner
DLL functionality:
DLL is locked. The rising edges of two inputs of the phase detector are very close to each other.
Phase shifting:
1 LSB = 208.3 ps.
DNL = 0.01 LSB.
INL = 0.03 LSB.
Jitter = 2.93ps.
Power dissipation
is 0.68mW.
dn
up
vCtrl
clkDelay
And
clkRef
Chart: Phase shifting in slow low temperature corner
 | 207.6063 | 206.248 | 208.502 | 207.1653 | 207.8077 | 209.0236 | 207.7726 | 205.9096 | 208.6449 | 206.5345 | 208.4353 | 209.7629 | 207.6224 | 209.4935 | 207.086

## Slide 21: Results in slow high temperature corner
DLL functionality:
DLL is locked. The rising edges of two inputs of the phase detector are very close to each other.
Phase shifting:
1 LSB = 208.3 ps.
DNL = 0.01 LSB.
INL = 0.04 LSB.
Jitter = 2.38ps.
Power dissipation
is 0.75mW.
dn
up
vCtrl
clkDelay
And
clkRef
Chart: Phase shifting in slow high temperature corner
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
 | 207.5552 | 206.0818 | 208.5779 | 207.0574 | 207.7172 | 209.2639 | 208.2902 | 205.7901 | 207.9747 | 206.2333 | 209.1084 | 209.478 | 207.6142 | 209.3618 | 206.3365

## Slide 22: Summary
Phase shifter for 320 MHz :
  Resolution:
  Power dissipation:
  DNL:
  INL:
  Jitter:
  Lock time: 150 us
  Layout size: