## Slide 1: Summary of Session 2: Vibration measurements
Session 2: Vibration measurements
Convener: Lin ZHANG (SLAC)
Location: C305
14:00 NSLS-II Site Vibration Measurements and Girder Support System Design for Mechanical Stability 40'
Speaker: Charles Spataro (BNL)
14:40 Ambient Ground Motion Measurement and the Preliminary Analysis for HEPS 30'
Speaker: Fang YAN (IHEP)
15:10 Mechanical Stability Issues in SSRF Storage Ring 40'
Speaker: Rongbing Deng (SINAP)

## Slide 2: Highlights
Ground vibration measurements
  Versus time: day, week, weekend (NSLS-II, ESRF, but not SSRF)
  Spectral: peak at 3 Hz
Source identification
  Decay with distance (NSLS-II, HEPS, ESRF)
  Traffics
  Utilities (pumps, air conditioning,…) (vibration isolation, distance)
Magnet-Girder Assembly
  NSLS-II
  SSRF (f1=21 Hz)
Thermal stability in Storage ring tunnel
  NSLS-II: ±0.75C
  SSRF: ±0.2C

## Slide 3: Discussion and Suggestions
Measurement instruments
  Sensors: geophone,…
  DAC
Data processing
  Spectral analysis
Results comparison validation
  “Round robin”
Gound vibration properties
  Vibration spectra
  Wave propagation speed
  Soil parameters: E, ν
Magnet-Girder design
  Great care on Girder design
  Care should be taken on magnet support design
Source identification
  Advanced spectral analysis can give much information

## Slide 4: Vibration propagation
Mechanical (air) acoustic  ground
(Helicopter flying over Soleil site, 1996)
Doppler Effects :
Vs : sound speed
Δf/f ~ 1/8 
Vhelico ~ 42 m/s
~ 151 km/h
  Spectrogram of vertical acceleration (dB.µm/s2)
X 10
X 3