## Slide 1: Vibration study of magnet girder of the HEPS-TF
Wang Zihao
11-13 December 2017
GM 2017

## Slide 2: Outline
Overview
Design of auto-tuning girder
  Modal analysis
  Experimental modal analysis
Optimization of girder model
Summary

## Slide 3: Overview
QUAD
DOUBLET
QUAD
DOUBLET
L-BEND
L-BEND
L-BEND
L-BEND
STRAIGHT
MULTIPLET
STRAIGHT
MULTIPLET
FODO
SECTION
HEPS Storage ring consists of 48-7BA.
Circumference ~1296m.
Each arc section ~27 m.
Girders provide firm support and
  precise positioning for magnets.
7 Magnet-Girder modules with 4 sizes.
  Each module pre-assembled,
  components aligned, prior to
  installation in tunnel.
one arc section

## Slide 4: Overview
Very Low Emittance Stringent Alignment Requirements
Positioning Tolerance | Transverse(RMS) | Vertical(RMS)
Magnet to Magnet | 30μm | 30μm
Girder to Girder | 50μm | 50μm
Girder should be capable of doing beam-based alignment to minimize magnet position error as much as possible. |  | 
HEPS-TF solve key technical difficulties of HEPS
The study of auto-tuning girder is one of the key techniques of HEPS-TF

## Slide 5: Design of Auto-tuning Girder
QUAD
DOUBLET
QUAD
DOUBLET
L-BEND
L-BEND
L-BEND
L-BEND
STRAIGHT
MULTIPLET
STRAIGHT
MULTIPLET
FODO
SECTION
Specifications:
Magnet Girder :
  6-point supported
Prototypes :
3300mm
Parameter | Specification
Resolution | 3μm
Adjusting range | X/Z：4mm Y：10mm
Natural frequency | 30Hz
Locking
Mechanism
Electronic Level
Cam Mover
Ball transfer Unit
Length gauge
Pedestal
Girder body
  Motor + Cam
  Sensor feedback control adjustment
  Multi-point support
  Automatic locking

## Slide 6: Modal Analysis
Uncoupled equation
Solving eigenvalue
Single degree of freedom system
(frequency response function curve)
(model)

## Slide 7: Modal Analysis
order | Natural frequency /HZ | Modal shapes
1 | 34.3 | lateral
2 | 40.1 | pitch
3 | 50.5 | longitudinal
4 | 53.3 | Yaw + pitch
5 | 55.6 | Yaw + pitch (counter to 4th )
6 | 73.7 | Roll (elastomer mode)
Finite element modal analysis results:
The 1st five orders are rigid modes, and the 6th appears elastomer mode.
The frequency range is 30Hz-80Hz.
The 1st natural frequency is larger than the specification. So we use this model to design.
Node displacement map of 1st modal shape
Meshing maps
Model simplification:
1. remove the bolts
2. contact mode is bonded
Cam mover & ball transfer unit

## Slide 8: Experimental Modal Analysis
Experimental modal analysis is based on the response and excitation force of system.
Modal shape

## Slide 9: Experimental Modal Analysis
Natural frequency range
Simulated modal shape
According to modal analysis results:
Type of hammer head (rubber)
Position of the hammer & measuring point layout

## Slide 10: Experimental Modal Analysis
Tested the natural frequency and modal shapes under different condition.
with/without loads
with/without locking mechanism
Locking mechanism is effective but not enough.
The fixed mode of baseplate has little effect on natural frequency.
Fixed mode 1
Fixed mode 2
x
z
y
axis | without loads unlocked | With loads unlocked | With loads locked
Z | 42.2Hz (pitch) | 23.6Hz (pitch） | 27.2Hz (pitch)
X | 24.2Hz (lateral) | 17.3Hz (lateral) | 22.8Hz (lateral)
Y | 23.6Hz (longitudinal) | 19.7Hz (longitudinal) | 28Hz (longitudinal)
locking mechanism

## Slide 11: Experimental Modal Analysis VS Modal Analysis
order | Simulation |  | Test |  | Error
 | Natural frequency Hz | Modal shapes | Natural frequency Hz | Modal shapes | 
1 | 34.3 | lateral | 17.3 | lateral | 98%
2 | 40.1 | pitch | 19.7 | longitudinal | 104%
3 | 50.5 | longitudinal | 21.3 | yaw | 137%
4 | 53.3 | Yaw + pitch | 23.6 | pitch | 126%
5 | 55.6 | Yaw + pitch (counter to 4th ) | 27.8 | vertical | 100%
6 | 73.7 | roll | 42.6 | roll | 73%
Results :
1. Except the 1st and 6th orders, modal shapes are all different.
2. From the experimental results, the first six orders modal shapes are all rigid-body modes.

## Slide 12: Optimization of girder model
elastic
elastic-plastic
plastic
gravity load
Contact stiffness
After some work:

## Slide 13: Optimization of girder model
Mode order | Natural frequency/Hz | Mode shape
1 | 20.179 | Lateral
2 | 22.583 | Pitch
3 | 23.516 | Longitudinal
4 | 26.011 | Yaw
5 | 28.245 | Vertical
6 | 44.427 | Roll
pitch
roll
yaw
Lateral
Longitudinal
Vertical
Results:
Direction | Natural frequency/Hz |  | Error | Mode shape
 | Simulation | Test |  | 
Z | 22.6 | 23.6 | 4.2% | pitch
X | 20.2 | 17.3 | 16.8% | lateral
Y | 23.5 | 19.7 | 19.3% | longitudinal
1.The modal shapes of two results are agree with each other.
2.The error rate is less than 20%

## Slide 14: Optimization of girder model
Direction | Original | Case 1 |  | Case 2 |  | Case 3 | 
 | Natural frequency Hz | Natural frequency Hz | improve | Natural frequency Hz | improve | Natural frequency Hz | improve
Z | 20.2 | 50.3 | 149% | 21 | 4% | 20.6 | 2%
Y | 22.6 | 52.7 | 133% | 23.2 | 3% | 22.9 | 1%
X | 23.5 | 64.3 | 173% | 27.3 | 16% | 24 | 2%
Case 1: removing girder body & loads.
Case 2: removing cam & bearings.
Case 3: only pedestals.
According to simulation results of 1st modal shape
Maybe , improving cam structure is a good method to increase the whole
natural frequency.

## Slide 15: Summary
1. Modal analysis and experimental modal analysis can interact with each other.
2. The fixed mode of baseplate has little effect on natural.
3. Locking mechanism is effective for increasing natural frequency of girder but not enough .
4. Cam mover is a weaker part than the other parts, improving cam structure is a good method to increase the natural frequency.
Next research plan:
1. we will consider other locking methods.
2. we will be able to match the simulation with the test.

## Slide 16
Thanks for your attention！