## Slide 1: Fast Orbit Feedback System for HEPS (Cooperation work among all related systems)
Dapeng Jin
Control System
Dec. 12, 2017

## Slide 2: Outline
1
Components involved
2
Preliminary design of the FOFB
3
Preliminary results of simulation
4
Further considerations
5
Summary

## Slide 3
Components involved

## Slide 4: Illustration of the FOFB
BPMs
Physics simulation, feedback logic
Power supplies, fast correctors, vacuum chambers

## Slide 5: Further Illustration of the FOFB
Integration && Feedback Logic
Power Supplies
BPMs
Fast Correctors
Vacuum Chambers

## Slide 6: FOFB Control Loop & Algorithm

## Slide 7: Layout of BPMs and fast correctors
3 fast correctors
There are 13 BPMs, 3 or 4 fast correctors per cell.

## Slide 8
Preliminary Design of the FOFB

## Slide 9: Overall Structure

## Slide 10: Design Considerations
  Core chip selection : UltraScale+/UltraScale from Xilinx
  Clock frequencies of logics and DSPs, up to 1GHz frequency is desired, at least 800MHz. Current level is between 600 MHz to 800MHz.
  GTH transceivers together with optical transceivers working above 10Gb/s for global communication, and above 5Gb/s for BPM data collection. Multi channels will be used.
  Cable routing around the ring to minimize delay.
  Parallel data transmission to PS controllers to minimize delay.

## Slide 11: Design Considerations
  Global timing synchronized data acquisition, transmission and logics.
  Ripple, effective resolution, accuracy and stability of the power supplies are very important.
  Parameters consistency for the fast correctors, power supplies and vacuum chambers are very important. The same, the best.
  Local linearity and hysteresis error of the fast correctors need to be concerned.

## Slide 12: Preliminary Time Consumption Estimate
  BPM data acquisition and treatment : ~ 5s.
  Global optical cable delay : ~ 10s for ~ 2km cables.
  Serialization/Deserialization for half the ring : ~ 7.2s for 24 nodes.
  Global data packets transmission : ~ 1 s.
  Matrix calculation : ~ 20s.
  Step response of power supplies : ~ 70s to 95% amplitude.
  Step response of fast correctors : ~ 70s to 95% amplitude.
  Vacuum chambers : Inconnel 625, thickness 0.8mm, step response : ~ 129s to 95% amplitude.

## Slide 13
Preliminary Results of Simulation

## Slide 14: Error Modeling
Ground vibration
Power supply ripple

## Slide 15: Feedback Algorithm and Parameters used
+
PID
R-1
delay
PS
magnet
chamber
R
BPM
+
yd +
-
+
+
y
e
n
PID PI controller
R response matrix
Delay calculation delay 40s
PS step response : 70s to 95% amplitude
Magnet same as PS
chamber 0.8mm thick Inconnel 625, inner diameter 22mm
n noise
BPM delay 2.5s

## Slide 16: Components Modeling
+
a = -0.1433;
b = 8.038*1000;
c = 1.001;
d = 0.00307*1000;
f= -0.8693;
g = 152.4*1000;
Vacuum chamber : 0.8mm thick
Inconnel 625,
inner diameter
22mm.

## Slide 17: Components Modeling
a=42.8*1000;

## Slide 18: Components Modeling
System performance:
System performance will be studied by the frequency-amplitude curve of this function.
transfer function for PID controller:

## Slide 19: PI Tuning

## Slide 20: PI Tuning

## Slide 21: PSD w/ & w/o FOFB

## Slide 22: PSD w/ & w/o FOFB : Zoom In

## Slide 23: Present Results and Further to Do
Present results with the parameters used
  Effective bandwidth up to ~ 500Hz.
  Almost no effect to noise ~ 800Hz.
  Negative effect to noise ~ 1kHz.
Further to do
  Lower thickness of the vacuum chambers down to 0.5mm.
  Lower delay of calculations down to 10s.
  Lower conductance fast correctors with less magnetic poles.

## Slide 24
Further Considerations

## Slide 25: Further Considerations
  Control with overshoot is must to increase the response speed.
  Possible positions of the control with overshoot : Just before data output to PS controllers or in the PS controller. Parameters should be easily adjustable.
  Balance among performance, cost, difficulty, complexity, reliability, availability, scalability and maintainability.

## Slide 26
Summary

## Slide 27: Summary
Preliminary design and simulation results have been carried out till now.
A bandwidth of 500 Hz can be possibly achieved.
A bandwidth of 800 Hz or higher is desired with some difficulties.
Much further work need to be done to make a good balance.
Tight cooperation among all related systems is the key to success.
Thank you!