## Slide 1: Summary Session 4: Vibration Suppression Techniques: 1
Vibration measurements at KEKB/SuperKEKB, and experience with vibration damping material
  Site Vibrations dominated by a 3Hz Eigenmode of the Soil System
  Testing the Effect of a Damping Alloy Material
  Both by Simulations and Measurements
  Characterization of a Cryostat with a Clear Tone at 14Hz
  Several Tests, with Damping and Different kinds of Screw Connections with Good Results
  Some Analysis Show the possibility of being Saved by Correlated Motions
  Real Testing to Commence soon will Show the Results of the Efforts
Notes: Mika Masuzawa

## Slide 2: Summary Session 4: Vibration Suppression Techniques: 2
Ambient Micro-vibration Control Technology for HEPS
  Some Ambitious Plans for Systematically Testing Different Configurations of Slap Thicknesses and Foundations
  This Provide a Good Collection of Information for Adjusting the FEA Models for the Soil at the Site
  Test of Production Techniques, Gain of Experience for Planning Phase
  Very Good Questions and Discussions Regarding how to Set and Define Tolerances
Notes: SUN Ning

## Slide 3: Summary Session 4: Vibration Suppression Techniques: 3
This Work is on Dimensioning for Sufficient Control of Settlements in the Structures due to Loading
Systematic Work Involving both FEA and Tests
The Methods are More Environmental Friendly
All the data is obtained form Geotechnical investigation report!
Cement is Used Instead of Lime Due to its Better Settlement Performance…
Together with The Dynamical Tests: Good Work to Find how You Get Most Stability For Your Money
Notes: XU ZhaoGang

## Slide 4: Summary Session 4: Vibration Suppression Techniques: 4
Vibration study of magnet girder of the HEPS-TF
  7BA Design, Still Considering Two Different Schemes
  Modal Analysis, Both by FEA and Prototype Testing (Goal: 30Hz)
  There are some Thoughts on How to Model and to Improve the Design in Order to Increate Stiffness, Especially Contact Stiffness
  Cam Structure is the Weakest Link, Work on Improving the Design
Notes: Wang Zihao

## Slide 5
The impact of vibration on BPM measurement, BEPCII
  Despite Being in a Busy Area, the Vibration Level is Very Low!
  But the Quadrupoles are Still Vibrating a Lot
  Different Sensors Used for Testing, Showing Similar Spectral Behavior
  Also FA Data from the BPM show this
  A New BPM Compact Support was Investigated at a BPM Test Bench
  The Importance of Fixing Components to the Floor was Seen
Summary Session 4: Vibration Suppression Techniques: 5

## Slide 6: Summary Session 4: Vibration Suppression Techniques: Comments 1
We All have Similar Challenges!
FEA is a Great Tool, but Difficult to Master for Real Life Predictions!
Using Real Testing in order to Adjust FEA Models is a Must
Setting Meaningful and Useable Stability Tolerances is Difficult
  Vibration Levels
  Frequency Content
  Eigenfrequencies
Contact Stiffness Modelling is one of the Key Challenges in FEA
You Need to take Some Reasonable Assumptions, There is No Unambiguous Truth
It is Tempting To Lower Ambitions Regarding Performance, But be Careful – Trust Yourself and Your Calculations
Notes: Concluding Remarks:

## Slide 7: Vibration Suppression Techniques: Comments: 2
The Green Field Vibration Level Should be Considered as a Future Goal
Isolate ALL Your Own Sources and Tell Your Neighbors to do The Same!
Stability Is Vital for Our New Sources!
  Make That Clear to Your Colleagues and Surroundings!
Organizing a Workshop Like This was a Really Good Idea!
  Sharing Knowledge With other Geeks!
  Sparring
  New Ideas Popping up
  New Contacts…
  …
Thank You For A very Well Organized Workshop!

## Slide 8
Calculations: Per Jørstad and Peter Persson, LTH
The (true) Story behind the MAX IV Bumps

## Slide 9: THANKS!