## Slide 1
Summary of session 1

## Slide 2: 5 talks in session1
Qing Qin (IHEP) Progress of the HEPS projects
Lin Zhang(SLAC) Beam stability consideration for low emittance storage ring
Masaru Takao(JASRI) Beam orbit stability issues at the Spring-8 storage ring
Chih-Hsien Huang(NSRRC) Beam orbit stability issues for user operations at TPS
Brian Norsk Jensen(MAX lab) Update for the MAX IV stability task force.

## Slide 3: In Qing Qin’s(IHEP) Talk
The performance of the HEPS is introduced.
The progress of HEPS is given
  01/2016, CDR study & writing
  02/2017, CD0 completed & submitted to CAS
  03/2017, internal review of CD0, modify CD0 report
  05/2017, CD0 submitted to National Development & Reform Commission
  06/2017, CD1 study and report writing started
  26/06/2017, national review of CD0
  12/2017, CD0 approved & CD1 report will be submitted
  02/2017, national review of CD1
  06/2018, national review of CD2
  11/2018, project construction starts, and will completed in 6.5 years
Parameter | Value | Unit
Beam energy | 6 | GeV
Beam current | 200 | mA
Circumference | 1360.4 | m
Partition number Jx /Jy/Jz | 1.51/1.0/1.49 | 
Horizontal natural emittance | 58.4 | pm∙rad
Transverse tune (x/y) | 107.37/82.43 | 
Natural chromaticity (x/y) | -214/-133 | 
Corrected chromaticity (x/y) | +5/+5 | 
No. of cell / long straight section | 48/48 | 
Length of LSS | 6.15 | m
Beta function @ mid-LSS (x/y) | 8.9/4.1 | m
Damping time (x/y/z) | 18.3/27.8/18.7 | ms
U0 per turn (w/o ID) | 1.959 | MeV
U0 per turn (w/10 IDs) | 2.5 | MeV
Natural energy spread | 8.20×10-4 | 
Momentum compaction factor | 3.43×10-5 | 
RF frequency | 166.6/499.8 | MHz
RF voltage (swap-out injection) | 2.65/0.575 | MV
Harmonic number | 756 | 
Bunch length with 3rd harm. cavity | 31.6 | mm

## Slide 4: In Qing Qin’s(IHEP) Talk
Light sources in China
BSRF (1st G mid energy) HLS(2nd G low energy) SSRF, TPS(3rd G mid energy） HEPS（4th G high energy）
Hefei Light source
Shanghai Synchrotron Radiation Facility

## Slide 5: In Qing Qin’s(IHEP) Talk
Key technologies to HEPS
Oscillating-line alignment tech
10ppm high accuracy PS
Injection Kicker PS
166MHz SC RF

## Slide 6: Lin Zhang’s (SLAC) Talk
Gives an overview of orbit stability requirement for DLSR. ESRF-EBS as an example.
Gives an overview of ground vibration.
Overview of Magnet-Girder assembly + Damping device
Overview of FOFB

## Slide 7: Beam stability requirement
Small emittance  small beam size
Beam size ~ f(emittance, β-function, energy spread σγ and dispersion function η):
  RMS beam size:
  RMS divergence:
Beam position motion 
  Larger apparent beam
  Macroscopic “emittance growth”
Beam stability requirements
  Emittance growth: Δε/ε0 < 20%
  Beam position stability:
x
y
Δσx
Δσy
Mainly in 0.01Hz ~ 100Hz
3rd Vs 4th GLS
H plane needs a little bit improvement
V plane already satisfied.

## Slide 8: Ground vibration
In frequency domain
3 frequency ranges
Low ( f < 1 Hz)
  Ocean waves
  micro seismic activities
Intermediate (1<f<100 Hz)
  Mechanical resonant frequencies
  Traffic, machine operations, water flow, wind,…
High ( f >100 Hz)
  Generated by small electro-mechanical structures
  Cooling flow
  Vibro-acoustic
  Much smaller level
Low frequency
Intermediate frequency
High frequency
Intermediate frequency is important ：
1、A lot of man made noise in 1<f<100 Hz
2、 Intermediate frequency vibration amplitude is relative large
3、Photon users are sensitive to 1<f<100 Hz vibrations.

## Slide 9: Ground vibration
Data source:
  W. Bialowons & H. Ehrlichmann, DESY, 2006
  R. Bartolini et al., EPAC2008
  Soleil private communication
  L. Zhang
Soleil, Diamond
SLAC tunnel
LCLS FEE, day

## Slide 10: Magnet-girder assembly + damping device
Overview on magnet-girder assembly
?
ESRF EBS 4 vertical motorized jacks, stiffer hori. Manual adj. 42 1.0~1.1

## Slide 11: Damping device – damping link
Passive Damping systems can be (effective) used when TFs2M&G > 2 and f1<20 Hz
  Damping links at ESRF TFs2M&G = 2.2
   TFs2M&G * fdamping = 1.3
L. Zhang et al., EPAC2000
L. Zhang et al., PAC2001

## Slide 12: Damping device – damping pad
  Damping pads (shim) at APS TFs2M&G = 9
   TFs2M&G * fdamping = 3 1.5 (+shim)
C. Doose, S. Sharma, MEDSI 2002
S. Sharma, WAGM 2005
  Magnet-Girder assembly, combining with damping device: TFs2M&G * fdamping < 1.5 ( ~ 1 is possible)
2mm thick
steel plate
0.5mm thin
steel plate
0.18mm VEM
cross section (not in scale)
Thermal drift  not applied

## Slide 13: Electron beam stability & Feedback efficiency
Different ground vibration level, and e-beam motion between ESRF and Soleil, but feedback efficiencies are comparable in both vertical and horizontal directions, and both 4000 Hz or 100 Hz band width

## Slide 14: Work can be done to stable the beam
Design and optimization to reach the stability criterion:
Δx =TFQ2e * TFG2M * TFs2G * TFgr2s * xgr
Ground vibration
Slab design
Magnet girder design
Storage ring Lattice design
Δx = TFQ2e * fFOFB * TFs2M&G * fdamping * TFgr2s* xgr < 0.1σx
Ground vibration
Slab design
Magnet girder design
Fast orbit feedback
(fFOFB )
Damping device
(fdamping)
< 0.1σx
Storage ring Lattice design

## Slide 15: Masaru Takao’s (JASRI) talk
Sources of beam orbit fluctuation and the efforts to suppression them at Spring 8.
Improvement of orbit feedback system

## Slide 16: Sources of vibration at Spring-8 and improvement
1、Klystron PS ripple at 2KHz
2、Quad PS ripple 50ppm  3ppm
3、Temperature fluctuation of cooling water
Fast
Slow
+/- 1ºC +/- 0.3ºC @1998 (+/-0.1ºC @present)
4、Wall plug electric power
5、Earth tide; Atmospheric temperature; Atmospheric pressure; Earthquake.

## Slide 17: Feedback system improvement at Spring 8
 | New Circuits | Old Circuits
Resolution | 0.1 μm | 0.3 μm
Measurement Cycle in user operation | 7 s (1 s @present) | 30 s
16bit DAC
16bit DAC
Att
Sum
Mag
VME
1/32
PS
 | Max. Kick Angle | Min. Step
H | 31 μrad | 1 nrad
V | 16 μrad | 0.5 nrad
H, V: ~ 4,5 mm r.m.s
H, V: ~ 1mm r.m.s
Improvement on BPM and Steering PS

## Slide 18: Chih-Hsien Huang’s (TPS) Talk
Relationship of ground motion to the beam motion.
Hunting 29Hz, 40Hz, 60Hz, 3Hz noises.
FOFB system performance at TPS

## Slide 19: Relationship of ground motion to the beam motion
0.1~ 1 Hz ground vibration, the integrated RMS is in the order of mm. The motion is almost coherent in all ring.
0.1~ 0.5 Hz horizontal vibration Creates dispersive orbit, which may related to Lower alpha of the lattice.
For the frequency between 1 to 4 Hz, the integrated rms ground motion is < 100 nm in vertical. The components motion excited by the ground is almost in phase within one cell.
The location variation of the crane disturbs the beam orbit.
Thickness of the floor slab is 160 cm in the tunnel and 80 cm in the experiment hall, respectively. The increase of the thickness of floor slab can reduce the ground motion induced by mechanical vibration, especially higher than 4 Hz.

## Slide 20: Hunting 29Hz, 40Hz, 60Hz, 3Hz noises
  Dry pump: Induction motor induced vibration ~ 29 Hz
    Turn off dry pumps => solved!
  Vacuum chamber vibration due to cooling water: ~ 40 Hz
    Lower the flow rate reduce the amplitude.
  Cooling fan, SRF transmitter: ~ 60 Hz
  Booster PS : ~ 3 Hz
3 Hz beam motion.
-1BPM-Corr * [Dx]
Corrector vs. BPM Response Matrix R
To hunting the noise: Match the frequeny
Inverse Response matrix to location the noise

## Slide 21: FOFB system performance at TPS
After removing error sources and before applying FOFB, the integrated RMS displacement from 1-100 Hz was around 2 mm in both horizontal and vertical directions for the ID BPM.
When the FOFB was turned on, the integrated RMS became smaller than 0.5 mm from 1 to 100 Hz.

## Slide 22: Brian Norsk Jensen’s (MAX lab) Talk
A effective a one-man band to stable the beam at MAX IV
Many passive works to reduce the vibration.

## Slide 23: Civil Engineering
Notes: Most tools are for measuring vibrations and mechanical stability

## Slide 24: Ground vibration & Beam
MAX IV
Electron Beam, Integrated Values, NO FOFB
Already stratify 3GLS
However MAX IV is 4GLS
They needs 200~300 nm stability

## Slide 25: passive works to reduce the vibration
Increase eigen freuqency
Isolation

## Slide 26: Summary
The geological conditions and the environment is important for LS stability.
Passive method is more reliable than feedback. Pile, Slab, Gird, Damping link(pad), isolation.
It common issues that we will face : PS ripple, water flow, temperature, ground vibration, we needs to hunt the source and to eliminate them.
FOFB is essential for high performance of orbit stability.