## Slide 1
Welcome to IHEP
IHEP, Dec. 11 – 13
Workshop on Ambient Ground Motion and Vibration Suppression for Low Emittance Storage Ring

## Slide 2: Progress of the High Energy Photon Source Project
Qing Qin
Institute of High Energy Physics, CAS
Dec. 11, 2017

## Slide 3: Outlines
Introduction
Accelerator physics issues
Key technologies to HEPS
Project progress
Summary

## Slide 4: 1. Introduction
Photon source – A powerful tool to probe the nature, required with widely tunable frequency range from infrared to hard X-ray

## Slide 5: Storage ring-based synchrotron radiation light source
Developed in China from 1980s, BEPC/BSRF, HLS, SSRF, and TLS/TPS
BSRF
1GLS
HLS
2GLS
SSRF
3GLS
Beijing Synchrotron Radiation Facility
Hefei Light source
Shanghai Synchrotron Radiation Facility
TPS
3GLS
Taiwan Photon Source

## Slide 6: Trends of light source
Lower emittances (  0.1 nmrad)
Higher brilliances (↗2~3 orders)
More advanced beam lines and end-stations (Better resolutions, higher speeds, etc.)
SR-based research centers
Sirius, Brazil, 518 m, 3 GeV, 0.27 nm
MAX IV, Sweden, 528 m, 3 GeV, 0.33 nm
ESRF-EBS, France, 844 m, 6 GeV, 0.13 nm

## Slide 7: New light source in China — High energy, high brightness
Users increased as the development of Chinese sciences and economy
SSRF
A new photon science research center at the north China
About 80 km from IHEP
IHEP
e.g. Increase of structure biology users in China

## Slide 8: Two steps
R&D of HEPS project
  One of the 16 large scientific facilities in the list of National Development and Reform Commission in the 12th 5-year plan.
  Scheduled from 2011 to 2015, but delayed.
  Officially started from Feb. 2016, and will be completed on Oct. 2018.
  Total budget: 321.6 M RMB (~48 M USD)
HEPS project
  Passed the review of the proposals for the large scientific facility, and shortlisted the 13th 5-year plan of the National Development and Reform Commission of China
  Expected to start the construction in late 2018, completed at 2024. The whole project finished in mid-2025 after commissioning.
  Total budget: 4.5-5 B RMB (~0.7 B USD)

## Slide 9: Design goal of the HEPS (high energy photon source)
Main parameters | Unit | Value
Beam energy | GeV | 6
Circumference | m | ~1360
Emittance | pm.rad | < 100
Beam current | mA | 200
Injection |  | Top-up
Brightness | Phs/s/mm2 /mrad2/0.1%BW | >1022
HEPS

## Slide 10: 2. Accelerator physics issues
Linear lattice design
  find an optimized qusi-DLSR design for the HEPS storage ring.
    compromised between Chinese technology level and innovations (e.g., way to get the lowest emittance)
    compromise between user requirements and accelerator performance
  give a detailed parameter list and tolerance budget table for hardware systems.
Hybrid 7-BA lattice, adopts aggressively strong focusing which results in a compact layout as well as an ultra-low emittance. This allows practical and cost effective storage ring design, even when the natural emittance is reduced down to approaching the diffraction limit of hard X-rays

## Slide 11
48 identical hybrid 7BAs.
Each 7BA cell is about 27 m.
48 dispersion-free 6-m straight sections, with beta functions of 9/3.2 m.
4 outer dipoles with long. gradients; 3 inner dipoles with defocusing gradients.
Neighboring 3 inner dipoles, high-gradient quadrupoles (~ 80 T/m).
6 sextupoles and 2 octupoles in one 7BA.
Parameter | Value | Unit
Beam energy | 6 | GeV
Beam current | 200 | mA
Circumference | 1360.4 | m
Partition number Jx /Jy/Jz | 1.51/1.0/1.49 | 
Horizontal natural emittance | 58.4 | pm∙rad
Transverse tune (x/y) | 107.37/82.43 | 
Natural chromaticity (x/y) | -214/-133 | 
Corrected chromaticity (x/y) | +5/+5 | 
No. of cell / long straight section | 48/48 | 
Length of LSS | 6.15 | m
Beta function @ mid-LSS (x/y) | 8.9/4.1 | m
Damping time (x/y/z) | 18.3/27.8/18.7 | ms
U0 per turn (w/o ID) | 1.959 | MeV
U0 per turn (w/10 IDs) | 2.5 | MeV
Natural energy spread | 8.20×10-4 | 
Momentum compaction factor | 3.43×10-5 | 
RF frequency | 166.6/499.8 | MHz
RF voltage (swap-out injection) | 2.65/0.575 | MV
Harmonic number | 756 | 
Bunch length with 3rd harm. cavity | 31.6 | mm

## Slide 12: Dynamic aperture study
Nonlinear optimization w/ 4 families of multipoles (grid-scan)
  Effective on-momentum DA: ~2.5 mm in x and 3.5 mm in y;
  effective MA: ~3%.
  Effective DA/MA is required not only the motion remains stable after tracking over a few thousand turns (traditional definition of the DA or MA), but the tune footprint is bounded by the integer and half integer resonances nearest to the nominal tunes of the storage ring.
y (mm)
x (mm)
ux
uy
x (mm)
d

## Slide 13: Nonlinearity study
Half-integer resonances
  Experimental (G. Wang et al., IPAC16) and numerical (M. Borland et al., IPAC15) studies show that the half-integer resonances can be safely crossed even w/ errors.
  For HEPS, keeping the probability of MA reduction due to crossing of half-integer resonances below 1%, the rms beta beating should be smaller than 1.5% in x and 2.5% in y plane, respectively.
  Within the effective DA or MA, not only the motion remains stable after tracking over a few thousand turns, but also the tune footprint is bounded by the integer and half integer resonances nearest to the nominal tunes.
  One can avoid too optimistic estimation of the nonlinear performance of the actual machine, when having only the bare lattice in hand.
MA reduction probability (%) for the HEPS (Left: caused by horizontal half- integer resonances, Right: caused by vertical half integer resonances. Y. Jiao, Z. Duan, NIM-A, 841, 2017
Integer resonances
  always fatal to dynamics and can never be crossed

## Slide 14: ‘Effective’DA&MA: limited by IRs and HIRs
This can provide a quick and reasonable measure of the realistic acceptance of a DLSR while with only the bare lattice in hand！
DA defined in a conventional sense
‘Effective’ DA
This will facilitate the optimization of a DLSR design with MOGA to find multi rather than single “optimal” solutions.
ated error modeling and lattice calibration can then select one most robust design from these solutions.
In this way, we find an efficient approach to separate the optimization and evaluation of the lattice processes.
Y. Jiao and Z. Duan, arXiv:1606.07191.
Submitted to NIM-A.
Y. Jiao, Z. Duan and G. Xu, IPAC 2017, WEPAB055, 2706-2708.

## Slide 15: Injection design – On-axis injection schemes
On-axis transverse injection (swap-out)
Major challenge:
A full charge injector to replace stored bunches in storage ring,
in particular, HEPS timing mode requires a bunch charge of ~15 nC, generation and acceleration of such high charge bunches is nontrivial.
swap-out
schematic plot of the kicker pulse shape
On-axis longitudinal injection (accumulation)
Major challenge:
Generation of a RF acceptance region to keep both injected and stored bunch with a large enough temporal separation, so as to accommodate the kicker pulse.
longitudinal injection
bunch spacing = 6ns for HEPS
injected bunch
injected bunch

## Slide 16: On-axis longitudinal injection schemes for HEPS
166 MHz + 500 MHz active RF system
Manipulation of RF voltages and phases in an injection period of ~ 200 ms
injection mode
circulating bunch
injected bunch
operation mode
Challenges:
Operational issues with frequent RF ramping.
Substantial brightness drop (~20%) due to the short bunches at the injection mode.
166 MHz + 333 MHz (2nd harmonic) + 500 MHz (3rd harmonic) RF systems
A substantial increase in RF acceptance compared to what is achievable with a double RF system.
Challenge: requires a large enough (~ 2mm) dynamic aperture at large synchrotron amplitude( ~ 3%)

## Slide 17: Error tolerance study
Lattice model – 7-BA, 7 girders, 12 hori. and 10 vert. correctors, 4 skew quads, and 13 BPMs
Error assign
  Multipole field components (1e-3) of magnets
  Alignment error (30mm on the same girder, 50mm on different girder) and rotation (100mrad)
  BPM resolution (0.5mm)
Alignment error is dominant
Dispersion in vertical and coupling should be controlled by correcting with skew quads
  From a max. 30 pm∙rad increase reduced to 1 pm∙rad increase.

## Slide 18: ID effect
Setup kick maps with Hamiltonian-Jacobin methods for 14 undulators to be installed in the first stage of HEPS.
Planar undulator
Elliptically polarizing undulator
Induced tune shift on the order of 0.003.
Obvious DA reduction, but not affects on-axis injection.

## Slide 19: Collective effects – Impedance model
Longitudinal wake potential (sz =3mm)
Impedance model is setup for instability studies
The longitudinal impedance is dominated by large number elements, e.g., flanges, BPMs.
The transverse impedance is dominated by the resistive wall impedance due to the small aperture of beam pipe.
More impedance contributors will be included in the further studies.
Geometrical contributions |  |  | 
Elements | Number | Elements | Number
RF cavities | 4 | LFB kicker | 1
Harmonic RFs | 2 | TFB kicker | 1
Flanges | 1000 | Inj. kickers | 10
Bellows | 400 | Ext. kickers | 4
Vacuum pumps | 288 | IDs | 15
BPMs | 768 | Transitions | 360

## Slide 20: Collective effects – single bunch instability
Microwave instability
  The Keil-Schnell criterion gives threshold bunch current of 0.2 mA.
  Simulation studies shows that the threshold intensity is around 0.8 mA (3.5 nC) with harmonic cavity. Above threshold, turbulent distributions are observed.
TMCI
  For Gaussian bunch, the instability is evaluated
  with Eigen Mode analysis.
  The threshold bunch intensity is ~0.1 mA with ξ = 0.
  A positive chromaticity is required.
bunch charge=15nC

## Slide 21: 3. Key technologies to HEPS – supported by HEPS-TF
Magnets
  High-gradient quadrupole
  Gradient: 88T/m
  Longitudinal gradient dipole
  Combined function magnets: dipole+quad

## Slide 22
166.6 MHz SRF cavity – for longitudinal injection
  Tested in March 15, 2017
  85 MV/m, 130 mT, 2.3 nΩ

## Slide 23
High accurate power supplies
10ppm high accuracy PS
Prototype of dynamic PS (acc. =0.1)
DPSCM-II high acc. ADC plate

## Slide 24
Mechanics & alignment
  Auto-control high precision tunable girder
Oscillating-line alignment tech.
支架I型总装配体
凸轮机构

## Slide 25
Injection kicker & power supply
  Physics and structure design for the strip-line kicker, on-line test
  DSRD rapid pulse PS – Test of single-level circuit & structure design for 6-level iterated circuit

## Slide 26
Vacuum technique
  NEG coating device,
  still in progress
  Photon absorber

## Slide 27: High-resolution X-ray monochromator
Characterization of precision of the goniometers
Controller of goniometers
Goniometers and laser interferometer
two kinds of techniques:
Gluing
Anode-bonding
Checked by zygo :
Online test:
4-inch Si crystal
Spherically bent Si(111)/(110)/(100) analyzers (R=1m)

## Slide 28: High Heat Load Monochromator
Project timeline:
  Fabricate: finished in April, 2017.
  Offline test: April, 2017-June, 2017.
  Online test: Oct. 2017-Nov. 2017.
Performance test:
  Mono: mechanical, vacuum, basic operations, performance of stability, thermal leakage and heat extraction power.
  Cryogenic cooling system: pressure stability and basic operations.
  Control system: safety protection, PID flow rate control and basic operations.
Inside of the chamber
Scene of the offline test
Mono
Laser interferometer
Cryo cooler

## Slide 29: Micro- & nano- focusing optics
High Energy Compound Refractive Lenses
Knife edge scan
CCD imaging, Focal length: 3m
8.5μm
10.6 gain
Online testing @SSRF
BL13W1 (50keV X-ray)
400µm

## Slide 30: Nano-positioning and scanning system
Characterization of the Z-stage
the device under measurement
Sub-nano steps 0.7 nm with a load of 1 kg
Resolution：0.7 nm
Travel range： 1 mm
Load capacity： 1 kg

## Slide 31: High repetition time-resolved experimental system
Storage ring –hybrid fill pattern
Dedicated mode 250mA,
Top-up, 1.243MHz
4mA camshaft single bunch
Colliding mode: 500-700mA, Top-off, 1.263MHz
~100bunch, 5-7mA/bunch
Single bunch
Single bunch
SR pulse width 100ps
Laser repetition up to 611kHz
Timing jitter < 0.6ps
XRD and XAS experiment

## Slide 32: Rapid-loading DAC system
XRD system for fast dDAC experiments in SSRF
X-ray
Lead shielding
Beam
stop
Pilatus3-6M
X-ray
dDAC
SSRF-18U

## Slide 33: 4. Project progress (HEPS)
Milestones of HEPS
  01/2016, CDR study & writing
  02/2017, CD0 completed & submitted to CAS
  03/2017, internal review of CD0, modify CD0 report
  05/2017, CD0 submitted to National Development & Reform Commission
  06/2017, CD1 study and report writing started
  26/06/2017, national review of CD0
  12/2017, CD0 approved & CD1 report will be submitted
  02/2017, national review of CD1
  06/2018, national review of CD2
  11/2018, project construction starts, and will completed in 6.5 years

## Slide 34: Design of the injector to HEPS
Linac design
  Electron gun, buncher, accelerating tube, etc.
  Bunch distribution at the linac exit
  Phase & position distribution of central bunch
Beam dynamics simulation & AP design
Design of accelerating structure & MW element
Physics design of various kind of magnets
Design of other systems of linac

## Slide 35
Design of booster
  Dynamic aperture study
  Single bunch current limit
  Effect on orbit error at low energy to injection
  Effect of magnetic errors to tunes
  Chromaticity variation due to ripple
Lattice design & nonlinear tracking study
Magnetic errors effects to injection and beam store
Simulation on impedance, modification of AP parameters to get required bunch charge
Fit to the swap-out & long. on-axis injection
  Mom. Acceptance @low energy

## Slide 36
Design on injection and extraction
  Pulse distribution at BTS line
Lattice design of injection and extraction sections
Simulation on injection
Physics design of key elements
Fit the requirements of swap-out & long. on-axis injection
  Slotted kicker

## Slide 37
Design on key hardware of booster
Design of various magnets
7 kinds of magnet support
Injector 2D layout in general
Linac mechanics design
air loading & pressure analysis
vacuum chamber design & temp. deform calculation
Design on RF system integration
HOM calculation

## Slide 38: Beamlines for the phase-I of HEPS
1 | High energy X-ray diffraction | High energy, low emmitance
2 | CDI and XPCS | 
3 | NRS and IXS | 
4 | Nano-probe | 
5 | Time-resolved techniques | 
6 | Hard X-ray imaging | 
7 | High-pressure | 
8 | Protein crystallography | Large users communities
9 | XAFS | 
10 | In situ surface diffraction and scattering | 
11 | High throughtput SAXS | 
12 | Ultrahigh resolution Electronic-Structure Spectroscopy | Application in industry, medicine, etc.
13 | Medium energy X-ray micro-spectroscopy | 
14 | Structure and spectrum imaging | 

## Slide 39: The site for HEPS
Huairou District, Beijing area (near the venue of the USR workshop in Oct 2012, Hairou), ~100 km northeast of IHEP
Ground motion at the area were measured
BASIC: An area of 233 acres, including:
HEPS
SECUF (Synergized Extreme Condition User Facility)
Simulation Facility for the Earth
Series research platforms in energy, environment, biology, materials, etc.
UCAS
HEPS
High-Tech Zone , Huairou, Beijing

## Slide 40: Site, construction & buildings

## Slide 41: Platform for Advanced Photon Sciences (PAPS)
Supported by Beijing Municipality (~0.5 B RMB), 05/17 – 05/20
Research in accelerator and X-ray optic techniques
Testing infrastructure (magnets, RF, pre-alignment, vacuum, ID) of HEPS

## Slide 42: 5. Summary
A high energy photon source is requested by users, aiming at the lowest emittance and highest brightness in the exiting synchrotron light sources.
The R&D of the HEPS project is being carried on, and will be finished by the end of Oct 2018.
The HEPS is scheduled to start the construction by the end of 2018, and will be completed in mid of 2025.
The AP design and key technologies development for the HEPS are now under way.
Ground motion and vibration reduction is critical to HEPS

## Slide 43: Thanks for your attentions!