## Slide 1: CEPC Injector Damping Ring
Cai Meng, Dou Wang, Jingru Zhang,
Dianjun Gong, Jiyuan Zhang, Jie Gao
CEPC CDR internal review, Feb 10, 2018 . A415, IHEP.

## Slide 2: Outline
Introduction of CEPC linac
  Parameters
  layout
Damping Ring design
  Why
  Parameters and layout
  ECS/BCS
Summary

## Slide 3: Introduction
Linac design principles
  Simplicity
  High Availability (necessary hot-standby backups,10%-20%) and Reliability
  meet requirements of Booster
CEPC linac
Parameter | Symbol | Unit | Value
e- /e+ beam energy | Ee-/Ee+ | GeV | 10
Repetition rate | frep | Hz | 100
e- /e+ bunch population | Ne-/Ne+ |  | >9.4×109
 |  | nC | >1.5
Energy spread (e- /e+ ) | σE |  | <2×10-3
Emittance (e- /e+ ) | εr | nm | < 120
e- beam energy on Target |  | GeV | 4
e- bunch charge on Target |  | nC | 10
Length
R&D
Positron source
ECS/ shorter bunch length
Positron source/DR

## Slide 4: Introduction
CEPC linac
Emittance: RMS
  300 nm@6GeV  300nm@10GeV  120nm@10GeV  ? @10GeV
  3500mm-mrad 5800mm-mrad 2350 mm-mrad
Positron source
  Capture emittance

## Slide 5: Introduction
Accelerating tube
  Aperture: 25 mm
Norm. RMS. Emittance
  2500 mm-mrad
Energy: >200 MeV
Positron yield
  Ne+/Ne- ~=0.55 [-6°,14°,235 MeV,265 MeV]
Emittance
  Bunch charge
  Collimation
  120 nm
CEPC linac
Only energy cutoff
Deceleration
Acceleration
SuperKEKB commissioning results
D1
A1
SuperKEKB

## Slide 6: Damping Ring
Smaller emittance requirement possibility and update potential
  Damping Ring for positron linac
Emittance budget for Linac: One-bunch-per-pulse
  Enough margin with high transmission efficiency
  Decrease beam loss at low energy part (collimation)
  100 Hz kicker?  Reliability
Emittance for booster
  Easy injection design and high efficiency
  Beam lifetime
  Damping time at high energy(?)
CEPC Accelerator CDR mini-review
  Strongly Suggesttion @ Katsunobu Oide
Why
@Dou Wang

## Slide 7: Damping Ring
DR V1.0 | Unit | Value
Energy | GeV | 1.1
Circumference | M | 58.5
Repetition frequency | Hz | 100
Bending radius | M | 3.6
Dipole strength B0 | T | 1.01
U0 | keV | 35.8
Damping time x/y/z | Ms | 12/12/6
0 | % | 0.049
0 | mm.mrad | 302
Nature z | mm | 7 (23ps)
Extract z | mm | 7 (23ps)
inj | mm.mrad | 2500
ext x/y | mm.mrad | 716/471
inj /ext | % | 0.5/0.07
Energy acceptance by RF | % | 1.0
fRF | MHz | 650
VRF | MV | 1.8
Preliminary design
Energy
  1.1 GeV
  SuperKEKB DR: CSR
Repetition frequency
  100 Hz 10ms
  One bunch

## Slide 8: Damping Ring
Lattice
FODO length (m) | 2.4
Phase per cell | 60
Dipole length (m) | 0.71
Dipole strength (T) | 1.0
Quadrupole length (m) | 0.2
Quadrupole strength (m-2) | 4.1
Sextupole length (m) | 0.06
@Dou Wang

## Slide 9: Damping Ring
Lattice

## Slide 10: Damping Ring
DA
@Dou Wang
Red：7 times injected beam size (rms)

## Slide 11: Damping Ring
SC cavity and NC cavity
  Because of the small beam current and beam power, choose 4-cell 650MHz NC cavity.
  This cavity is scaled from 5-cell 500MHz HERA-type cavity.
RF parameters
 | SCRF | NCRF
Circumference [m] | 58.5 | 58.5
Beam energy [GeV] | 1.1 | 1.1
SR loss/ turn [keV] | 35.8 | 35.8
Revolution frequency [MHz] | 5.12 | 5.12
SR power / beam [W] | 550.4 | 550.4
Momentum compactor | 7.82E-02 | 7.82E-02
Beam current [mA] | 15.4 | 15.4
Bunch charge [nC] | 3 | 3
Number of bunches per revolution | 1 | 1
RF voltage [MV] | 1.8 | 1.8
RF frequency [MHz] | 650 | 650
RF wave length [m] | 0.461 | 0.461
Bucket length [ns] | 1.538 | 1.538
Harmonic number | 127 | 127
Revolution time [ns] | 195.1 | 195.1
Bunch population [1E10] | 1.88 | 1.88
Bunch charge [nC] | 3 | 3
Natrue Bunch length [mm] | 7 | 7
RF energy acceptance [%] | 1 | 1
Acc. Phase [deg] | 88.86 | 88.86
Syn. Tune | 0.010 | 0.010
Synchrotron oscillation period [us] | 19.3 | 19.3
Longitudinal damping time [ms] | 6.0 | 6.0
@Dianjun Gong

## Slide 12: Damping Ring
Damping ring lattice
  4 1m-long spaces for RF
  2 4-cell NC cavity.
  Acc. gradient is 1MV/m
  Input power is 63kW
RF parameters
 | SCRF | NCRF
Type of Cavity | SCRF | NCRF(HERA-type)
number of cell/ cavity | 1 | 4
Cavity effective length [m] | 0.23 | 0.92
RF section length [m] | 1 | 1
Cavity number | 1 | 2
Cavity voltage [MV] | 1.8 | 0.9
Cavity Acc. Gradient [MV/m] | 7.83 | 0.98
Q0 | 1.00E+10 | 29500
R/Q [Ohm] | 103 | 440
Input power/ cavity [W] | 550 | 62679
Pb [W] | 550 | 550
Pc/ cavity [W] | 3 | 62404
Coupling Coefficient | 176 | 1.01
Optimal QL | 5.68E+07 | 2.92E+04
Cavity bandwidth at optimal QL [Hz] | 11 | 2.2E+04
Detuning angle [deg] | -88.86 | -12.45
Filling time [us] | 2.78E+04 | 14.3
Optimal detuning at optimal QL [Hz] | -287.49 | -2452.99
Cavity stored energy [J] | 7.7 | 0.5
@Dianjun Gong

## Slide 13: Damping Ring
Coherent synchrotron radiation
  High energy
  Larger momentum compaction
  Longer bunch length
Electron Cloud Instability
Instability

## Slide 14: Damping Ring
Injection (DR)
  Small energy spread
  Large bunch length
  Energy compression system (ECS)
Extraction (Linac)
  small bunch length: 7mm 1 mm
    Energy spread <1%
    R56: -600mm
  Bunch compression system (BCS)
ECS/BCS

## Slide 15: Damping Ring
C-Chicane
  Rectangular dipole
  Bending angle: θ
  Bend radius: ρ
  Length: a, b
Chicane

## Slide 16: Damping Ring
 | Unit | Value
bend radius ρ | m | 3.7
bending angle | degree | 25
a | m | 0.5
b | m | 0.6
Dx | mm | 1049
R56 | mm | -684
H | m | 0.926
L | m | 7.855
Chicane

## Slide 17: Positron Linac

## Slide 18: Summary
Damping ring is new addition in injector for smaller emittance requirement possibility and update potential.
Preliminary damping ring design is proposed.
ECS and BCS is considered.
Further study is necessary and needed.