## Slide 1
Status of MFT Disks
Ni Fang, Dong Wang, Jun Liu – CCNU
The 5th China LHC Physics Workshop
– 2019, October 26th

## Slide 2: Outline
Motivation
ALICE MFT upgrade
-- Electronic readout board(disk0~disk4)
-- Other components(Support & Heat Exchangers & Ladders)
-- DISKs Performance test (Power dropout & High speed signal)
Summary

## Slide 3
Briefly introduce ALICE
ALICE (A Large Ion Collider Experiment) detects quark-gluon plasma, a state of matter thought to have formed just after the big bang
stuides properties of strongly interacting matter (quark-gluon plasma)
MFT
（Muon Forward Tracker）

## Slide 4
Motivation

## Slide 5: The MFT Detector
Zoom out
General layout of the MFT half-barrel and its environment
Zoom out of the MFT half-barrel
MFT is a sub detector of ALICE in front of the FIT and absorber
MFT is composed by 5 disks
Each disk is a couple of front and back PCB fixed on a mechanical support
Several FPC with detection sensors are connected on each PCB(front & back)

## Slide 6
MFT Mechanical Structure Breakdown
920 silicon pixel sensors (0.4 m2) in 280 ladders of 2 to 5 sensors each.
DISK0~DISK4
Sensor
(2 to 5)

## Slide 7: Disk0/1
Electronic board layout and physical map
Four-layer board design
support high-speed signals of 1.6Gb/s
Layout
Physical map
This is the fourth（Final）
vision of disk0/1
This prototype has been
produced in May,2019
We have sent 16 pieces
to France for test.
Length : 29.4cm
Width : 7.2cm

## Slide 8
Disk2
Six-layer board design
Electronic board physical map and layout
support high-speed signals of 1.6Gb/s
Layout
Physical map
This prototype has been
produced in June,2019
We have sent 8 pieces
of PCB to France
Length : 29.4cm
Width : 8.5cm

## Slide 9: Disk3
Four-layer board design
support high-speed signals of 1.6Gb/s
Electronic board physical map and layout
Layout
Physical map
This prototype has been
produced in September,2019
We have sent 8 pieces
of PCB to France
Length : 44.0cm
Width : 16.1cm

## Slide 10
Disk4
support high-speed signals of 1.6Gb/s
Four-layer board design
Electronic board physical map and layout
Layout
Physical map
This prototype has been
produced in July,2019
We have sent 8 pieces
of PCB to France
Length : 44.0cm
Width : 17.5cm

## Slide 11
Physical map of other brackets and heat sinks
Thermal performance results
Ladder
Disk support
Assembled
Heat exchangers
Ladder
PCB
(DISK0-DISK4)
Support

## Slide 12
Disk Power dropout testing
This shows a test for the second vision of disk0/1.
We use this power to provide power, and a Sliding resistance as load.
The difference between Actual input and Actual output should be smaller than 5 percent of Actual input.

## Slide 13
Disk Power dropout testing

## Slide 14
This is the Power dropout reasult for disk01.
The power for every zone is different and they have different shape copper on the layers, which reasults the Irregularity between zones.
In fact, Power dropout is required to be below 5%.
Disk Power dropout testing

## Slide 15
Disk High speed signal test
Full scale setup
-- Using most of pre-prod elements
-- BER measurements in PRBS mode at 1.2Gb/s
-- 68 hours without errors ; BER = 1.5 10-14
Zoom out
Zoom out

## Slide 16: Status
Electronic Boards | Waiting | Schematic Under design | PCB layout Under design | Prototype Produced
disk0/1 PCB--version 1 |  |  |  | 
… |  |  |  | 
disk0/1PCB--Final version |  |  |  | Produced 16 blocks
disk2 PCB--version 1 |  |  |  | 
… |  |  |  | 
disk2 PCB--Final version |  |  |  | Produced 8 blocks
disk3 PCB--version 1 |  |  |  | 
… |  |  |  | 
disk3 PCB--Final version |  |  |  | Produced 8 blocks
disk4 PCB--version 1 |  |  |  | 
… |  |  |  | 
disk4 PCB--Final version |  |  |  | Produced 8 blocks
The electronic interconnect board has been fully produced and tested well.

## Slide 17: Summary
Thanks for your attention
All current electronic board designs are completed including spare boards
Cooperate with partners for assembly and testing