## Slide 1: “GPU for realtime processing in HEP experiments”
Piero Vicini (INFN)
On behalf of GAP collaboration
Beijing, 17.5.2013

## Slide 2: GAP Realtime
GAP (GPU Application Project) for Realtime in HEP and medical imaging is a 3 years project funded by the Italian minister of research started in the beginning of April.
It involves three groups (~20 people): INFN Pisa (G.Lamanna), Ferrara (M.Fiorini) and Roma (A.Messina) with the partecipation of the Apenet Roma Group.
Several position will be opened to work on GAP. Contact us for further information (http://web2.infn.it/gap ).

## Slide 3: GAP Realtime
“Realization of an innovative system for complex calculations and pattern recognition in real time by using commercial graphics processors (GPU). Application in High Energy Physics experiments to select rare events and in medical imaging for CT, PET and NMR.”
For what concern HEP we will study the GPU application in low level hardware triggers with reduced latency and high level software triggers.
We will consider the NA62 L0 and the ATLAS high level muon trigger as “physics cases” for our studies.

## Slide 4: NA62: Overview
Main goal: BR measurement of the ultrarare K→ pnn (BRSM=(8.5±0.7)·10-11)
Stringent test of SM, golden mode for search and characterization of New Physics
Novel technique: kaon decay in flight, O(100) events in 2 years of data taking
Huge background:
  Hermetic veto system
  Efficient PID
Weak signal signature:
  High resolution measurement of kaon and pion momentum
Ultra rare decay:
  High intensity beam
  Efficient and selective trigger system

## Slide 5: The NA62 TDAQ system
L0 trigger
Trigger primitives
Data
CDR
O(KHz)
EB
GigaEth SWITCH
L1/L2
PC
RICH
MUV
CEDAR
LKR
STRAWS
LAV
L0TP
L0
1 MHz
1 MHz
10 MHz
10 MHz
L1/L2
PC
L1/L2
PC
L1/L2
PC
L1/L2
PC
L1/L2
PC
L1/L2
PC
100 kHz
L1 trigger
L1/2
L0: Hardware synchronous level. 10 MHz to 1 MHz. Max latency 1 ms.
L1: Software level. “Single detector”. 1 MHz to 100 kHz
L2: Software level. “Complete information level”. 100 kHz to few kHz.
Notes: At L1/L2 GPU can reduce number of computing systems required
At L0 completely different problems…..

## Slide 6: Two problems to use GPU at L0
Computing power: Is the GPU fast enough to take trigger decision at tens of MHz events rate?
Latency: Is the GPU latency per event small enough to cope with the tiny latency of a low level trigger system? Is the latency stable enough for usage in synchronous trigger systems?

## Slide 7: GPU computing power

## Slide 8: GPU processing
GPU
GPU
MEM
Chipset
CPU
SYSTEM
MEM
PCIe
GbE
20 events data (1404 byte) sent from Readout board to the GbE NIC are stored in a receiving host kernel buffer.
T=0 start of send operation on the Readout Board.
μs

## Slide 9: GPU processing
GPU
GPU
MEM
Chipset
CPU
SYSTEM
MEM
PCIe
GbE
μs
Data are copied from kernel buffer to a user space buffer.
99

## Slide 10: GPU processing
GPU
GPU
MEM
Chipset
CPU
SYSTEM
MEM
PCIe
GbE
104
μs
Data are copied from system memory to GPU memory
Notes: Latency control: le due soluzioni… fare disegnino come alessandro con le varie componenti e far vedere le due soluzioni quali problemi affrontano

## Slide 11: GPU processing
GPU
GPU
MEM
Chipset
CPU
SYSTEM
MEM
PCIe
GbE
134
Ring pattern-matching GPU Kernel is executed, results are stored in device memory.
μs

## Slide 12: GPU processing
GPU
GPU
MEM
Chipset
CPU
SYSTEM
MEM
PCIe
GbE
Results are copied from GPU memory to system memory (322 bytes – 20 results)
139
μs

## Slide 13: GPU processing: open problems (1)
GPU
GPU
MEM
Chipset
CPU
SYSTEM
MEM
PCIe
GbE
109
μs
latcomm ≅ 110 μs
4 x latproc

## Slide 14: GPU processing: open problems(2)
GPU
GPU
MEM
Chipset
CPU
SYSTEM
MEM
PCIe
GbE
109
μs
Fluctuations on the GbE component of latcomm may hinder the real-time requisite, even at low events count.
sockperf: Summary: Latency is 99.129 usec sockperf: Total 100816 observations; each percentile contains 1008.16 observations
sockperf: ---> <MAX> observation = 657.743 sockperf: ---> percentile 99.99 = 474.758 sockperf: ---> percentile 99.90 = 201.321 sockperf: ---> percentile 99.50 = 163.819 sockperf: ---> percentile 99.00 = 149.694 sockperf: ---> percentile 95.00 = 116.730 sockperf: ---> percentile 90.00 = 105.027 sockperf: ---> percentile 75.00 = 97.578 sockperf: ---> percentile 50.00 = 96.023 sockperf: ---> percentile 25.00 = 95.775 sockperf: ---> <MIN> observation = 64.141

## Slide 15: Two approaches: PF_RING driver
Fast packet capturing from standard NIC (PF_RING driver from www.ntop.org. The author is in the GAP collaboration.)
The data are written directly on the user space memory.
Skip redundant copy in the kernel memory space.
Both for 1 Gb/s and 10 Gb/s
Latency fluctuations could be reduced using RTOS (under study).
NIC
GPU
chipset
CPU
RAM
PCI express
VRAM

## Slide 16: Two approaches: NaNet (1)
NaNet derived from APEnet+ design.
3D Torus network for HPC hybrid parallel computing platform
GPU Direct RDMA support at HW level
  First not-NVIDIA device having P2P connection with a GPU.
  Joint development with NVIDIA.
High-end FPGA based
  PCI Gen2 x8 card
  6 fully bidirectional Torus links @34Gbps

## Slide 17: Two approaches: NaNet(2)
Multiple link tech support
  apelink bidir 34 Gbps
  1 GbE
  Future interconnection standards
New features:
  UDP offload: extract the payload from UDP packets
  NaNet Controller: encapsulate the UDP payload in a newly forged APEnet+ packet and send it to the RX NI logic
  Low latency receiving GPU buffer management
  Implemented either on APEnet+ card and ALTERA dev kit
Lonardo A. “Building a Low-latency, Real-time, GPU-based Stream Processing System” GTC2013 Conference

## Slide 18: NaNet preliminary results
In the 1 GbE link L0 GPU-based Trigger Processor prototype the sweet spot between latency and throughput is in the region of 70-100 Kb of event data buffer size, corresponding to 1000-1500 events.
Sustained Bandwidth ~119.7 MB/s
NaNet transit time (7.3 ms ÷ 8.6 ms)

## Slide 19: First application: RICH
~17 m RICH
1 Atm Neon
Light focused by two mirrors on two spots equipped with ~1000 PMs each (pixel 18 mm)
3s p-m separation in 15-35 GeV/c, ~18 hits per ring in average
~100 ps time resolution, ~10 MHz events rate
Time reference for trigger
Vessel diameter 4→3.4 m
Beam
Beam Pipe
Mirror Mosaic (17 m focal length)
Volume ~ 200 m3
2 × ~1000 PM

## Slide 20: Algorithms for single ring search
DOMH/POMH: Each PM (1000) is considered as the center of a circle. For each center an histogram is constructed with the distances btw center and hits.
HOUGH: Each hit is the center of a test circle with a given radius. The ring center is the best matching point of the test circles. Voting procedure in a 3D parameters space

## Slide 21: Algorithms for single ring search
TRIPL: In each thread the center of the ring is computed using three points (“triplets”) .For the same event, several triplets (but not all the possible) are examined at the same time. The final center is obtained by averaging the obtained center positions
MATH: Translation of the ring to centroid. In this system a least square method can be used. The circle condition can be reduced to a linear system , analitically solvable, without any iterative procedure.

## Slide 22: Processing time
The MATH algorithm gives 50 ns/event processing time for packet of >1000 events.
The performance on DOMH (the most resource-dependent algorithm) is compared on several Video Cards
The gain due to different generation of video cards can be clearly recognized.

## Slide 23: Processing time stability
The stability of the execution time is an important parameter in a synchronous system
The GPU (Tesla C1060, MATH algorithm) shows a “quasi deterministic” behavior with very small tails.
The GPU temperature, during long runs, rises in different way on the different chips, but the computing performances aren’t affected.

## Slide 24: Data transfer time
The data transfer time significantly influence the total latency
It depends on the number of events to transfer
The transfer time is quite stable (double peak structure in GPUCPU transfer)
Using page locked memory the processing and data transfer can be parallelized (double data transfer engine on Tesla C2050)

## Slide 25: TESLA C1060
On TESLA C1060 the results both in computing time and total latency are very encouraging
About 300 us for 1000 events
Throughput about 300 MB/s
“Fast online triggering in high-energy physics experiments using GPUs” Nucl.Instrum.Meth.A662:49-54,2012

## Slide 26: TESLA C2050 (Fermi) & GTX680 (Kepler)
On TESLA C2050 and GTX680 improves (x4 and x8 respectivelly)
The data trasfer latency improves a lot thanks to the streaming and the PCI-express gen3

## Slide 27: Multirings
Most of the 3 tracks, which are background, have max 2 rings per spot
Standard multiple rings fit methods aren’t suitable for us, since we need:
  Trackless
  Non iterative
  High resolution
  Fast: ~1 us (1 MHz input rate)
New approach use the Ptolemy’s theorem (from the first book of the Almagest)
“A quadrilater is cyclic (the vertex lie on a circle) if and only
if is valid the relation:
AD*BC+AB*DC=AC*BD “

## Slide 28: Almagest algorithm description
28
A
B
C
D
D
D
Select a triplet randomly (1 triplet per point = N+M triplets in parallel)
If the point satisfy the Ptolemy theorem, it is considered for a fast algebraic fit (i.e. math, riemann sphere, Taubin, … ).
Each thread converges to a candidate center point. Each candidate is associated to Q quadrilaters contributing to his definition
For the center candidates with Q greater than a threshold, the points at distance R are considered for a more precise re-fit.
Consider a fourth point: if the point doesn’t satisfy the Ptolemy theorem reject it

## Slide 29: Almagest algorithm results
The real position of the two generated rings is:
1 (6.65, 6.15) R=11.0
2 (8.42,4.59) R=12.6
The fitted position of the two rings is:
1 (7.29, 6.57) R=11.6
2 (8.44,4.34) R=12.26
Fitting time on Tesla C1060: 1.5 us/event

## Slide 30: The ATLAS experiment

## Slide 31: The ATLAS Trigger System
L1: information from muon and calorimeter detectors processed by custom electronics
L2: Region of Interests with L1 signal, information from all sub-detector, dedicated software algorithms
EF: full event reconstruction, offline software reconstruction
~60 ms
~1 s

## Slide 32: ATLAS: as study case for GPU sw trigger
The ATLAS trigger system has to cope with the very demanding conditions of the LHC experiments in terms of rate, latency, and event size.
The increase in LHC luminosity and in the number of overlapping events poses new challenges to the trigger system, and new solutions have to be developed for the fore coming upgrades (2018-2022)
GPUs are an appealing solution to be explored for such experiments, especially for the high level trigger where the time budget is not marginal and one can profit from the highly parallel GPU architecture
We intend to study the performance of some of the ATLAS high level trigger algorithms as implements on GPUs, in particular those concerning muon identification and reconstruction.

## Slide 33: High level muon triggers
L2 muon identification is based on:
  track reconstruction in the muon spectrometer and in conjunction with the inner detector (<3ms)
  Isolation of the muon track in a given cone both based on ID tracks and calorimeter energy (~10ms)
For both track and energy reconstruction:
  Algorithm execution time grows at least linear with pileup
  naturally parallelizable
Algorithm purity also depends on the width of the cone:
  Reconstruction within the cone easily parallelizable

## Slide 34: Conclusions (1)
The GAP project aims at studying the possibility to use GPUs in realtime applications.
In HEP triggers this will be studied in the L0 of NA62 and in the muon HLT of ATLAS.
For the moment we focused on the online ring reconstruction in the RICH for NA62.
The results on both throughput and latency are encouraging to build a full scale demonstrator.

## Slide 35: Conclusions (2)
The ATLAS high level trigger offers an interesting opportunity to study the impact of GPUs in the sw triggers of LHC experiments.
Several trigger algorithms are heavily affected by pileup, this effect can be mitigated by having algorithms with a parallel structure.
As for the offline reconstruction, the next hw generation for HLT will be based on vector and/or parallel processors: the GPUs would be a good partner to speedup the online processing in high pileup/high intensity environment.

## Slide 36: Realtime?