## Slide 1: Future Circular Collider Study FCC-ee SC-RF System
F. Zimmermann/CERN
Prepared by Erk Jensen/CERN
Many thanks to: M. Benedikt, A. Butterworth, O. Brunner, R. Calaga, S. Claudet, R. Garoby, F. Gerigk, P. Lebrun, E. Montesinos, D. Schulte, E. Shaposhnikova, I. Syratchev, M. Vretenar, J. Wenninger

## Slide 2: FCC Study – Scope (1)
A conceptual design study of options for a future high-energy frontier circular collider at CERN for the post-LHC era shall be carried out, implementing the request in the 2013 update of the European Strategy for Particle Physics.
Many results of the study will be site independent.
The design study shall be organised on a world-wide international collaboration basis under the auspices of the European Committee for Future Accelerators (ECFA) and shall be available in time for the next update of the European Strategy for Particle Physics, foreseen by 2018.

## Slide 3: FCC Study – Scope (2)
The main emphasis of the conceptual design study shall be the long-term goal of a hadron collider with a centre-of-mass energy of the order of 100 TeV in a new tunnel of 80 - 100 km circumference for the purpose of studying physics at the highest energies.
The conceptual design study shall also include a lepton collider and its detectors, as a potential intermediate step towards realization of the hadron facility. Potential synergies with linear collider detector designs should be considered.
Options for e-p scenarios and their impact on the infrastructure shall be examined at conceptual level.
The study shall include cost and energy optimisation, industrialisation aspects and provide implementation scenarios, including schedule and cost profiles.

## Slide 4: FCC Study – Scope (3)
Forming an international collaboration to study:
pp-collider (FCC-hh)  defining infrastructure requirements
e+e- collider (FCC-ee) as potential intermediate step
p-e (FCC-he) option
80-100 km infrastructure in Geneva area
~16 T  100 TeV pp in 100 km
~20 T  100 TeV pp in 80 km

## Slide 5: Collaboration forming
FCC kick-off meeting in Geneva (Feb. 2014)
  International community informed and invited
  Discussions launched on collaboration, scope, etc
Preparation of legal framework for collaboration
  General Memorandum of Understanding
  Specific Addenda adapted for each contribution
Preparation meeting for International Collaboration Board
  Took place 9-10 Sep 2014 at CERN
  Work status, governance structure, organisation
Preparation of H2020 Design Study proposal “EuroCirCol”
  Submitted to EU on 2 Sep 2014
Next: 1st Yearly FCC Workshop, 23 – 27 March 2015, Washington DC
  Followed by review ~2 months later, begin June 2015

## Slide 6: FCC Kick-off Meeting

## Slide 7: FCC Parameters
High-energy hadron collider FCC-hh as long-term goal
Seems only approach to get to 100 TeV range in the coming decades
High energy and luminosity at affordable power consumption
Lead time design & construction > 20 years (LHC study started 1983!)
 Must start studying now to be ready for 2035/2040
Lepton collider FCC-ee as potential intermediate step
Would provide/share part of infrastructure
Important precision measurements indicating the energy scale at which new physics is expected
Search for new physics in rare decays of Z, W, H, t and rare processes
Lepton-hadron collider FCC-he as option
  High precision deep inelastic scattering and Higgs physics

## Slide 8: FCC-hh parameters
PRELIMINARY
Energy 100 TeV c.m.
Dipole field ~ 16 T (design limit) [20 T option]
Circumference ~ 100 km
#IPs 2 main (tune shift) + 2
Beam-beam tune shift 0.01 (total)
Bunch spacing 25 ns [5 ns option]
Bunch population (25 ns) p
#bunches
Stored beam energy 8.2 GJ/beam
Emittance , normalised
Luminosity
[conservative option]
Synchroton radiation arc 26 W/m/aperture (filling fact. 78% in arc)
Longit. emit damping time 0.5 h

## Slide 9: FCC-hh Design Challenges

## Slide 10: FCC-hh SR Heat Load
High synchrotron radiation load on beam pipe
  Up to 26 W/m/aperture in arcs, total of ~5 MW for the collider
  (LHC has a total of 1W/m/aperture from different sources)
Three strategies to deal with this
  LHC-type beam screen
    Cooling efficiency depends on screen temperature, higher temperature creates larger impedance  40-60 K?
  Open midplane magnets
    Synergies with muon collider developments
  Photon stops
    dedicated warm photon stops for efficient cooling between dipoles
    as developed by FNAL for VLHC
http://inspirehep.net/record/628096/files/fermilab-conf-03-244.pdf
Also P. Bauer et al., "Report on the First Cryogenic Photon Stop Experiment," FNAL TD-03-021, May 2003

## Slide 11: FCC-hh High-Field Magnet R&D
FHC baseline is 16T Nb3Sn technology for ~100 TeV c.m. in ~100 km
Goal: 16T short dipole models by 2018 (America, Asia, Europe)
Develop Nb3Sn-based 16 T dipole technology,
with sufficient aperture (~40 mm) and
accelerator features (field quality, protect-ability, cycled operation).
In parallel conductor developments
Goal: Demonstrate HTS/LTS 20 T dipole technology in two steps:
a field record attempt to break the 20 T barrier (no aperture), and
a 5 T insert, with sufficient aperture (40 mm) and accel. features
In parallel HTS development targeting 20 T.
HTS insert, generating o(5 T) additional field, in an outsert of large aperture o(100 mm)

## Slide 12: EuroCirCol Proposal
EuroCirCol forms the heart of the hadron collider design and the feasibility study of its key technologies.
Work packages include high field magnets, arc design, interaction regions and cryogenic beam vacuum – infrastructure aspects, implementation and cost.
It does not include SC-RF intentionally (to keep the focus narrow).

## Slide 13: FCC-ee parameters
Design choice: max. synchrotron radiation power set to 50 MW/beam
  Defines the max. beam current at each energy.
  4 Physics working points
  Optimization at each energy (bunch number & current, emittance, etc).
For FCC-ee-H and FCC-ee-t the beam lifetime of ~few minutes is dominated by Beamstrahlung (momentum acceptance of 2%).
Parameter | FCC-ee-Z | FCC-ee-WW | FCC-ee-H | FCC-ee-ttbar | LEP2
E/beam (GeV) | 45 | 80 | 120 | 175 | 104
I (mA) | 1450 | 152 | 30 | 6.6 | 3
Bunches/beam | 16700 | 4490 | 170 | 160 | 4
Bunch popul. [1011] | 1.8 | 0.7 | 3.7 | 0.86 | 4.2
L (1034 cm-2s-1) | 28.0 | 12.0 | 4.5 | 1.2 | 0.012

## Slide 14: Why back to circular?
High potential of the rings at ‘low’ energy (includes ZH)
CEPC (2 IPs)
FCC-ee (4 IPs)
ILC
CLIC

## Slide 15: FCC-ee Design Challenges
Short beam lifetime from Bhabha scattering and high luminosity
  Top-up injection
Lifetime limits from Beamstrahlung
  Flat beams (very small vertical emittance, b* ~ 1 mm)
  Final focus with large (~2%) energy acceptance
Machine layout for high currents, large #bunches at Z pole and WW.
  Two rings and size of the RF system.
Polarization and continuous high precision energy calibration at Z pole and WW, where natural polarization times are ~ 15 hours.
RF System ! 100 MW cw!
  RF system scalable to this size
  RF power conversion effiency

## Slide 16: FCC-ee RF System
Main RF parameters
Synchrotron radiation power: 50 MW per beam
Energy loss per turn: 7.5 GeV (at 175 GeV, t)
Beam current up to 1.4 A (at 45 GeV, Z)
Up to 7500 bunches of up to 4 x 1011 e per ring.
CW operation with top-up operation, injectors and top-up booster pulsed
Basic choices for RF system and RF system size:
Frequency range (200 … 800) MHz with 400 MHz as starting point, Harmonics of 40 MHz required, harmonics of 200 MHz preferred
Preferred technology: Thin films on Cu substrate (allows scaling to very large overall size)
System dimension compared to LHC:
  LHC 400 MHz  2 MV and ~250 kW per cavity, (8 cavities per beam)
  Lepton collider ~600 cavities 20 MV / 180 kW RF  12 GV / 100 MW

## Slide 17: Compare: LEP-II RF System
*) Plus 56 copper cavities (130 MV) driven by 8 klystrons
Frequency | 352.209 MHz
Number of cavities *) | 288
Total accelerating voltage *) | 3600 MV
Number of klystrons *) | 36
Total cryomodule length | 817 m
Cavities per klystron | 8
Average (nom.) power per klystron | 0.6 (1.3) MW
Average power per cavity | 90 kW
Circumference | 26.7 km
Beam energy | 104.5 GeV
Energy loss per turn | 3.4 GeV
Beam current | 5 mA
Synchrotron radiation power | 17 MW
Available cooling power | 53 kW @ 4.5K
RF system surface | 7 tennis courts

## Slide 18: FCC RF R&D Subjects
Superconducting RF
Cavity technology
Cryomodules
Large RF Systems
Availability
Operational aspects
Energy Efficiency
Efficient power sources
Lowering cryogenic load
Energy recovery?
Power couplers
Reliability
Cavity optimization
Maintainability

## Slide 19: Superconducting RF: General Considerations
FHC-ee total power needed per beam:
Also: need to maintain longitudinal focusing with sufficient momentum acceptance to keep good beam lifetime
Energy | for | for
Energy |  | 

## Slide 20: FHC-ee @175 GeV in numbers
cf. LEP2: 812 m
cf. LHC cryoplant capacity @ 1.9 K: 18 kW
Input power couplers!
 | 5-cell cavity
Gradient | 
Active length | 
Voltage/cavity | 
Number of cavities | 
Number of cryomodules | 
Total length cryomodules | 
Dynamic heat load per cavity @ : | 
Total dynamic heat load | 
CW RF power per cavity | 
Matched | 
Gradient | 
Active length | 
Voltage/cavity | 
Number of cavities | 
Number of cryomodules | 
Total length cryomodules | 
Total dynamic heat load | 
CW RF power per cavity | 

## Slide 21: Superconducting RF
Superconducting RF
  Minimize residual resistance , maximize  surface physics, technology, materials, fabrication techniques, shape optimisation, operating optimisation.
  Todays investment in R&D may pay off significantly!
Example: 800 MHz 5-cell cavity for 18 MV, is the cryogenic power at ambient temperature. Thanks: R. Calaga, S. Claudet, P. Lebrun!
x 4.4
Technology
x 1.6

## Slide 22: Superconducting RF
Superconducting RF – technology (2 examples )
  Push coating techniques – on Cu substrate – performance reach?
  Coating with Nb3Sn on Nb looks promising – note potential at 4.2 K (left)
  New treatment techniques – N2 processing (right)
Sam Posen et al. (Cornell): “Theoretical Field Limits for Multi-Layer Superconductors”, SRF 2013
Anna Grasselino et al. (FNAL): “New Insights on the Physics of RF Surface Resistance and a Cure for the Medium Field Q-Slope”, SRF 2013
MV/m

## Slide 23: Superconducting RF Power couplers
Test of RF couplers (CEA)
Cylindrical
window
Disk
window
Coupler development for SPL (704 MHz)
2 designs currently under test: cylindrical and disk windows
Design goal: 1 MW 10% duty cycle for SPL
Cylindrical window design uses LHC coupler ceramic window with tapered outer conductor
LHC windows () routinely tested to CW!

## Slide 24: FCC: Areas of SRF R&D work
Cavity design
  200 MHz
  400 MHz
  800 MHz
  Cavity for sample tests (quadrupole resonator, …)
  Small single-cell test cavities (6 GHz?)
Power couplers
  Design, engineering,
  Multipactor study & suppression
Cavity technology
  Forming & fabrication techniques
  Coating techniques
    Diode sputtering Nb on Cu
    Magnetron sputtering
    HiPIMS
    Coating Nb3Sn on Nb
    …
  Joining techniques
  Chemistry
  Heat treatments
  He
HOM Dampers
  HOM spectrum, impedances
  Beam dynamics
  HOM couplers and filters, dampers
  -vessel design and engineering
Tuners
  Design and engineering
CM design and engineering
  Magnetic and thermal shields, …
  CM for 200 MHz
  CM for 400 MHz
  CM for 800 MHz
  Alternative designs (SS He-vessel?)
  CM for testing
Diagnostics for validation tests
  -mapping
  Quench localisation
  …
Experimental verification
  Sample preparation
  Sample tests (quadrupole resonator)
  Single-cell small cavity testing (6 GHz?)
  Vertical tests
  Horizontal tests
Infrastructures (operation, upgrade, maintenance)
  Manufacturing
  EB Welding
  Vacuum brazing
  Chemistry & cleaning, rinsing
  Heat treatments
  Cryogenics
  Vacuum
  Cryolab
  SM18
  Other test-facilities
  & cleaning

## Slide 25: CERN present SRF work
New Coating Technologies:
HIPIMS on 1.3 GHz cavities
Coll. S. Calatroni and G. Terenziani
Cavity Diagnostic Developments with OSTs
Master Thesis B. Peters
Fundamental SRF studies using the Quadrupole Resonator
PhD Thesis S. Aull

## Slide 26: CERN EB Welding machine
O. Capatina

## Slide 27: CERN SRF Infrastructure (1)
O. Capatina, L. Marques, K. Schirm
Electro-polishing High pressure rinsing

## Slide 28: CERN SRF Infrastructure (2)
Cavity RF Test Area
Helium tank
Service module in horizontal bunker

## Slide 29: CERN SRF Infrastructure (3)
Existing clean room upgrade and extension New clean room facility – HIE-ISOLDE
High-pressure rinsing
Clean room layout
Ultra-pure water station

## Slide 30: CERN SRF Infrastructure (4)
Fundamental research
Quench localization via second sound on SPL cavities
Optical Inspection Bench
J. Chambrillon, K. Liao, B. Peters, K. Schirm

## Slide 31: CERN SRF Infrastructure (5)
F. Pillon, S. Mikulas, K. Schirm
Bead-pull measurement setup for field mapping
Cell-by-cell tuning system

## Slide 32: SC RF R&D Opportunities
FCC-ee will need 100 MW of continuous RF power; this sets the scale of the RF system. Assuming a CW power limit for an FPC of 100 kW (for the sake of scaling), this would need about 1,000 FPC’s and the same order of magnitude of cavities – so we’re talking about a large system.
The SCRF R&D for FCC blends into a wider SCRF R&D program at CERN, which includes work for LHC, HL-LHC, HIE-ISOLDE, SPL and ERL-TF. This allows taking maximum advantage of synergies between projects and sharing of experts and infrastructures.
The area of R&D identified as key for the FCC is the study and development of advanced coating techniques. Cu cavities with sputtered Nb coatings were used at LEP, are used in LHC and will be used in HIE-ISOLDE. The present-day performance of these cavities in terms of maximum accelerating gradient and is moderate compared to advanced bulk Nb cavities, whereas clear advantages arise from the good thermal conductivity and stability of Cu.
The above examples demonstrate that there is still exciting physics out there to be discovered and technologies to be developed. The European Strategy encourages us to undertake this R&D.

## Slide 33: Energy Conversion Efficiency
For FCC-ee of major importance – CW RF requires at least from the grid to produce (in addition to cryogenic power mentioned above)
Study more energy efficient methods to convert!
wall plug
DC
klystron eff.
useable RF
beam
loss
loss
loss
loss
Φ & loss
minimize losses!
recover waste RF power!
recover beam power!

## Slide 34: Study of high klystrons
Recent studies make look possible; the key seems bunching with “core oscillations”
A.Yu. Baikov et al.: “Simulation of Conditions for the Maximal Efficiency of Decimeter-Wave Klystrons”, Technical Physics Vol. 59#3, 2014
I. Guzilov: “BAC method of increasing efficiency”, CLIC Workshop 2014: https://indico.cern.ch/event/275412/
From: Baikov, Marrelli, Syratchev, private communictation
Efficiencies (left) and klystron length (right) of 10 MW L-band klystrons. Blue: stat-of-the art klystrons, Red: Optimization utilizing “core oscillation bunching”

## Slide 35: IOTs
Inductive Output Tube: density modulation with a grid (like a tetrode) output to a cavity (like in a klystron). IOT shorter, less gain than klystron. IOT in 70 kW class used for DVB transmitters.
Klystrons reach maximum efficiency only in saturation.
  Is it necessary to back-off in operation? (we did during LEP2!)
IOTs (Inductive Output Tubes) may be better in this respect:
Illustration from CPI

## Slide 36: MB-IOT Study
CPI (Communications&Power Industries) have built a 1 MW range MB IOT demonstrator 10 years ago.
ESS Lund have now revived this research, jointly with CERN
M.R.F. Jensen et al.: “Applications of High Power Induction Output Tues in High Intensity Superconducting Proton Linacs”, IVEC2013, Paris

## Slide 37: Summary
The areas of R&D identified to prepare technology for the Future Circular Collider are
  Superconducting RF R&D
    focus on Nb on Cu, but explore alternatives!
  High Efficiency RF power generation
  Design of complex systems for high availability
In all these areas, the R&D has significant synergies with ongoing studies and projects, with which the R&D should be coordinated.
Thank you very much!

## Slide 38: spare slides

## Slide 39: Superconducting RF: Choice of frequency (-ies)
FCC-hh – beam dynamics considerations!
  A combination of a system with a system looks like a good starting point, which would allow for both long bunches (?) and short bunch spacings (of ). The harmonic system would allow to control the bunch profile. Possible bunch spacings: integer multiple of .
  Limiting bunch lengths to , a combination & would be a better choice (stability)
FCC-ee
  lower than : cavities become huge, mechanically less stable and need a lot of He! Compact cavities would have to be studied! Smaller impedance
  larger than : multi-cell cavities with critical BBU limit – more wakefield effects! Larger impedance
  BCS resistance , power sources tend to have larger efficiency at lower .
  Going to would have several advantages:
    Operate at 4 K and provocatively argue for coated cavities (more advantages). Requires investment into R&D to push to higher at high gradient.
    Fairly confident we can aim at , so SS will be slightly longer than for sheet Nb cavities.
    Use LHC power coupler (tuneable for better matching) – CW (x2 if you use two couplers/cavity for higher currents)
    HOM power would be much less. LHC type damping system could be used with warm ferrites outside to strongly damp HOMs.
The choice of frequencies is still open, but we would like to limit us to harmonics of – presently looking at combinations of and systems.

## Slide 40: FCC Organization
Physics and Experiments
Accelerators
Infrastructures and Operation
Implementation and Planning
Study and Quality Management
Hadron Collider Physics
Hadron Collider Experiments
Lepton Collider Physics
Lepton Collider Experiments
Lepton-Hadron Collider Physics
Lepton-Hadron Collider Experiment
Hadron Injectors
Hadron Collider
Lepton Injectors
Lepton Collider
Lepton-Hadron Collider
Technology R&D
Civil Engineering
Technical Infrastructures
Operation and Energy Efficiency
Integration
Computing and Data Services
Safety, RP and Environment
Project Risk Assessment
Implementation Scenarios
Cost Models
Study Administration
Communications
Conceptual Design Report

## Slide 41: FCC Technology R&D excerpt from WBS:
1.6.1 | 16 T Superconducting Magnet Program
1.6.1.1 | Accelerator magnet design study for hadron collider
1.6.1.2 | Nb3Sn material R&D
1.6.1.3 | 16 T short model construction
1.6.1.4 | 16 T support technologies
1.6.1.5 | Magnet/collider integration studies
1.6.2 | 20 T Superconducting Magnet Program
1.6.2.1 | 5 T HTS insert
1.6.2.2 | HTS Material R&D
1.6.2.3 | 20 T magnet design
1.6.3 | 100 MW RF Program
1.6.3.1 | SC-RF R&D
 | Cavity design and production technologies
 | Cryo-module and ancillary systems design
 | Optimisation of cryogenic power consumption
1.6.3.2 | High efficiency RF power generation
 | Multi-beam klystron demonstrator
 | Klystron working point for optimum efficiency
1.6.4 | Specific Technologies Program
1.6.4.1 | More efficient, compact and higher capacity helium cryo-plants
1.6.4.2 | Non conventional cryogen mixtures for efficient refrigeration below 100 K
… | …

## Slide 42: RF Systems
Availability/reliability/maintainability/operability
  LHC experience: We do not reach the predicted integrated luminosity because of trips (with long recovery)
  Some of these trips avoidable by system design
  … if not avoidable, MTTR can be minimized by design!
  Relevant for both FHC-hh and FHC-ee:
    Even if the RF System of FHC is “like LHC”, it is about 3 to 4 times as large and complex!
  Apply methods developed for nuclear power plants, chemistry plants, hospital emergency installations, aircraft carriers and airplanes! This probably has to be done in any case.
  Specifically for RF systems, fail-safe designs must be developed – these system can reach MTBF !

## Slide 43: R&D on high availability systems
I’m a non-expert, so just some personal thoughts here:
Look at what has been done already (Myrrha, Eurisol, …)
A model must be developed that can predict the impact of a component/subsystem failure on the overall system performance.
The model must include built-in redundancy and fault tolerance on overall reliability (to allow for optimization)
It must include reliable MTTF and MTTR data of components/subsystems to allow.
The model must include cost (power, efficiency) of these measures to allow overall optimisation (wrong: to pay the double to avoid a 10% down-time!)
One example: Solid-state power amplifiers could allow intervention during operation!