## Slide 1: AHCAL cellsize optimization
石禹坤

## Slide 2: OutLine
Outline
  Background and setup
  Marlin arbor and Cluster building
  Pion and KLong separation
  Simple PFA method
  Conclusion and plan

## Slide 3: Background and setup
PFA
  The optimal detector to detect different kinds of particle
  Match or dismatch particle cluster with track is very important
  Cellsize is crucial for particle identification
Charged particle
65%
photon
25%
Neutral hadron
10%

## Slide 4: Background and setup
Geometry Setup
  ECAL
    30 layers
    Absorber:2.8mm tungsten
    SI:10×10×0.5mm3
    PCB:2mm
  AHCAL
    40 layers
    Absorber:20mm Fe
    Scintillator:10×10×3mm3
    PCB:2mm
Notes: Fe λ=168mm X0=17.7mm Rm=16.8mm tungsten X0=3.5mm

## Slide 5: Background and setup
Incident particle
  10 Gev pion-
  10 GeV KLong: abundant in H-gg event
Feature of KLong
  KLong usually doesn’t deposit significant energy in ECAL so that it doesn’t have a ‘stick’ in the front
  KLong is fatter than pion
Single KLong event
Overlay particle event
pion
KLong

## Slide 6: Marlin arbor and Cluster building
SimuCalorimeter Hit
ClusterAB1st
Calorimeter Hit
EHBushes
digitization
arbor
Bush merge

## Slide 7: Marlin arbor and Cluster building
Digitization
  Combine small cell into the size we want
arbor
  6 parameter in total
  EE connection(xy direction and z direction)
  EH connection
  HH connection(xy direction and z direction)
  EE Seed connection

## Slide 8: Marlin arbor and Cluster building
Bush merge
  Merge small cluster into core and fragment
  Cluster Seed:hit closest to origin point in cluster
  Cluster COG:center of energy gravity
  Joint:close hits from different cluster
  Cluster depth:distance from cluster Seed to ECAL surface
  Connection of EE,EH,HH clusters has different cut on cluster Seed difference,COG difference,number of joints,transSeed difference
  Only deeper cluster can be merge into shallower cluster

## Slide 9: Marlin arbor and Cluster building
For single pion event in 10mm cellsize
Number of Joint
with largest energy cluster
transSeeddistance
Largest cluster
energy
Distance between
Cluster COG and
track

## Slide 10: Pion and KLong separation
Real situation
  Charged particle: track can provide energy and direction
  Uncharged particle: even don’t know the number of them
Strategy for pion, K in MC
  Assume that the incident direction is the track in Simplified geometry
  Pion, K candidate selection
    Pion candidate: cluster closet to track and energy >mean - 3σ
    K candidate: cluster doesn’t match pion track with largest cluster energy
  Efficiency for pion, K
    Pion:| energy pioncandidate – meanpion| <3σ && distance(COG) to track<80mm
    K::|energy Kcandidate – meanK| <3σ && distance to track<80mm
Apply selection and calculate efficiency for both single particle and di particle event

## Slide 11: Pion and KLong separation
Fail events
  Head and tail
  confusion
Head and tail
confusion

## Slide 12: Pion and KLong separation
Successful event
  Pion K distance 30mm
Pion 8.3GeV
KLong 13.2GeV
Pion 12.8GeV
KLong 5.3GeV

## Slide 13: Pion and KLong separation
70mm cellsize
  Incident position
    pion:0mm
    Klong:0mm
Pion 7.8GeV
KLong 8.4GeV
fail
fail

## Slide 14: Pion and KLong separation
70mm cellsize
  Incident position
    pion:75mm
    Klong:0mm
Pion 11.7GeV
Klong 11.8GeV
Pion 9.9GeV
Klong 14.4GeV

## Slide 15: Pion and KLong separation
fail
Pion 11.3GeV
Klong 5.1GeV
fail
Klong 11.2GeV
Pion 4.5GeV

## Slide 16: Pion and KLong separation
Pion energy distribution
Pion candidate energy
K(0mm)-pion(0mm)
Real pion energy
K(0mm)-pion(0mm)
Pion candidate energy
K(0mm)-pion(100mm)
Real pion energy
Single pion event

## Slide 17: Pion and KLong separation
KLong energy distribution
KLong candidate energy
K(0mm)-pion(0mm)
Real KLong energy
K(0mm)-pion(0mm)
KLong candidate energy
K(0mm)-pion(100mm)
Real KLong energy
Single Klong event

## Slide 18: Pion and KLong separation
The cluster chose as particle is called as ‘core’
Distance between Cluster COG and Core
  Distance is calculated with energy weight and threshold 0.5GeV for a single event
  Reflect the size of core to some extent
Pion single event
MPV:23.69mm
KLong single event
MPV:22.81mm

## Slide 19: Pion and KLong separation
  Straight Line is efficiency of single particle
  Marker is efficiency of di particle event
  particle distance is the distance of 2 particle on ECAL surface
10mm cellsize

## Slide 20: Pion and KLong separation
Different cellsize
  Keep the energy mean of single particle similar, apply different energy mean for different cellsize
  Energy sigma stays unchanged as 10mm cellsize situation
Pion reconstruction efficiency
KLong reconstruction efficiency

## Slide 21: Pion and KLong separation
Critical Distance
  The distance which has 80% efficiency is define as critical distance
  Since core size is about 23mm,such result seems reasonable
Pion and K reconstruction efficiency
Critical distance – HCAL cellsize

## Slide 22: Simple PFA method
Simple PFA method
  PFA:E = pion track + KLong
  Real situation:E = pion track + part of pion fragment + KLong
KLong
pion
Pion core
Pion fragment
KLong fragment
KLong core
fragment

## Slide 23: Simple PFA method
PFA energy
K(0mm)-pi(0mm)
PFA energy
K(0mm)-pi(500mm)
Total Cluster energy
Total Hit energy

## Slide 24: Simple PFA method
Energy resolution
  Total Hit energy resolution
  Total cluster energy resolution
  PFA method:pion fragment has ~25% of total pion energy which makes a big trouble
10mm cellsize
50mm cellsize
Critical distance

## Slide 25: Simple PFA method
  CellSize doesn’t have significant influence on energy resolution
  30mm seems to be a good choice

## Slide 26: Cellsize optimization
Conclusion
  30mm cellsize seems reasonable but the difference between 2 kinds of critical distance should be figure out
Plan
  Find the reason why 2 kinds of critical distance behave unlikely
  Full PFA with AHCAL on baseline(jet energy resolution, particle separation)

## Slide 27
backup

## Slide 28: Cellsize optimization
Other cell size
  Adjust single particle event energy mean similar to 10mm cellsize
20mm cellsize

## Slide 29: Cellsize optimization
30mm cellsize
40mm cellsize

## Slide 30: Cellsize optimization
70mm cellsize
50mm cellsize

## Slide 32
70%
80%