## Slide 1: Status of sensor design for MOST1 project
Yunpeng Lu
On behalf of the design team
2019-8-14

## Slide 2: CMOS Sensor Design
MOST mid-term review in Aug. 2018
  Insufficient manpower
  Two chips, two schemes
Combination of two schemes
  Small pixel: Low power FE + Rolling shutter Readout
  Improve spatial resolution further
  Targeting on low power and readout speed as well
Design team
  IHEP, CCNU, Dalian Minzu Unv., Shandong Unv.
  Working together on a mask area：10.4mm*6.1mm
  Started Sep. 2018

## Slide 3: Design specification
In order of priority：
Spatial resolution
  <3um
  Initial pixel size 16um*20um
  FPN < 20e
Power consumption
  100mW/cm2（MOST1 specification）
  Measureable
Readout speed
  100ns/row （ MOST1 specification ）
  Measureable
TID tolerance

## Slide 4: Readout scheme
D Q
CLK
RST
Row decoder
D Q
CLK
RST
D Q
CLK
RST
row n
row n+1
Priority Encoder
Priority Encoder
col. 0
col. 63
...
Addr[5:0]
Valid
Multiplexer
Addr[5:0]
Valid
...
Serializer & LVDS
Level 1 buffer
Level 2 buffer
col. 64
col. 127
...
D flip-flop to register a HIT
Shared column lines
End of column Priority Encoder
  Zero suppression
  64 columns processed during readout of one row
Multiplexer controlled by FPGA
  Flexible readout control
2018.10.15deleted

## Slide 5: Pixel design variants
0.5
8.2
mm
1.7
mm
5.1 mm
.5
BK1
BK3
BK4
BK2
PE1
PE3
PE4
PE2
Sector 0
Sector 1
Sector 2
Sector 3
Sector | Diode | Front-end | Pixel digital | Pixel layout
0 | 2 + 2 μm | FE_V0 | DGT_V0 | 16×26 μm2
1 | 2 + 2 μm | FE_V0 | DGT_V1 | 16× 26 μm2
2 | 2 + 2 μm | FE_V0 | DGT_V2 | 16× 23.11 μm2
3 | 2 + 2 μm | FE_V1 | DGT_V0 | 16×26 μm2
Diode, minimum size
Front-end, 2 versions
  FE_V0, FE_V1 (20nA, 60nA)
Pixel digital, 3 versions
  DGT_V0，DGT_V1， DGT_V2
Pixel area
  16×26 μm2
  16×23.2 μm2

## Slide 6
Wrap up this month.
Submit next month.