## Slide 1: The Pointing Calibration of WFCTA telescopes
Lingling Ma
IHEP
LHAASO Collaboration Meeting
10. 2019 ZhuHai

## Slide 2: Outline
Introduction of LHAASO-WFCTA
Why should we calibrate the pointing of WFCTA
How to calibrate the pointing of WFCTA
The accuracy of the calibration
Summary

## Slide 3: Introduction of LHAASO-WFCTA
Wide Field of view Cherenkov Telescope Array
  Pixel：SiPM + Weston Cone
    32 X 32，0.5°X 0.5°
  FOV: 16°X 16°
  Pointing：vertical

## Slide 4: Why should we calibrate the pointing of WFCTA
The reconstruction of the Shower-Detector-Plane depends on the pointing of WFCTA
The pointing accuracy effects the energy reconstruction and composition discriminations

## Slide 5: How to calibrate the pointing of WFCTA
The base of
a sipm V.S. time
Bright stars
Cherenkov light
Star light
City background light
The SiPMs on the trace of a bright star is lighted one by one
Bright Stars with well know positions can be used as a guider of the WFCTA

## Slide 6: Star Catalog
TD1 with wavelength 297 nm Catalog is used.
The positions are given by B1950
The positions should be converted to now
The differences in Ra direction
0.8degree
The differences in Dec directions

## Slide 7: Star and data selection criteria
Star selection criteria
  Flux higher than 10^-10erg/s
  Do not have neighbors within 2degrees
Data selection criteria
  The peaks caused by stars should be higher than 4 pe
  The rms of peaks caused by the same stars in Ra and Dec should be less than 0.1degrees
  The distance to the mean position of peaks caused by the same star should be less than 0.2degree

## Slide 8: Method of the calibration
Get the rough pointing of telescopes by maximum matches between the stars and the peaks.
Get the accurate pointing of telescopes by the least square fitting. (Pointing and shift of the camera center)

## Slide 9: results and accuracy
 | Zenith | Azimuth | Shift X | Shitf Y
TEL 3 | 31.30 | 18.96 | 0.02 | 0.02
TEL 4 | 0.86 | -15.8 | -0.24 | 0.09
TEL 5 | -30.28 | -45.15 | 0.01 | 0.02
TEL 6 | 30.28 | -69.89 | 0.07 | 0.02
0.06degree
0.05degree

## Slide 10: Stability study By Tel 3
 | Zenith | Azimuth | Shift X | Shift Y
3. Oct. | 31.30 | 18.96 | 0.02 | 0.02
4. Oct. | 31.28 | 19.09 | 0.02 | -0.02
9. Oct. | 31.13 | 18.89 | 0.02 | 0.09
11. Oct. | 31.08 | 18.95 | -0.01 | 0.13

## Slide 11: Summary
Pointing of four WFCTA telescopes are calibrated by bright stars.
  The pointing error after calibration of bright stars: 0.05°
  The Stability of the method is studied by four days data
0.1degrees in azimuth and zenith

## Slide 12: 3号望远镜
1003
1004
1009
1011
3号望远镜

## Slide 13: 4号望远镜
1003
1004
1009
1011

## Slide 14: 5号望远镜
1003

## Slide 15: 6号望远镜
1003
1004
1011