## Slide 1: CEPC high luminosity lattice and related progress
Yiwei Wang
for the CEPC Accelerator Physics Group
CEPC day, 27 Sep 2019, IHEP

## Slide 2
Outline
  Lattice design for a higher luminosity
  Progress of dynamic aperture optimization
Summary
Notes: difficulties

## Slide 3
D. Wang
et al
 | Higgs (CDR) | Higgs (high) | 
Number of IPs | 2 | 2 | 
Beam energy (GeV) | 120 | 120 | 
Circumference (km) | 100 | 100 | 
Synchrotron radiation loss/turn (GeV) | 1.73 | 1.68 | The filling factor of bends should be increased to get a even lower SR with smaller emiitance.
Crossing angle at IP (mrad) | 16.5×2 | 16.5×2 | 
Piwinski angle | 3.48 | 3.78 | 
Number of particles/bunch Ne (1010) | 15.0 | 17.0 | single bunch charge increased thus larger momentum acceptance required
Bunch number (bunch spacing) | 242 (0.68s) | 218 (0.76s) | 
Beam current (mA) | 17.4 | 17.8 | 
Synchrotron radiation power /beam (MW) | 30 | 30 | 
Bending radius (km) | 10.7 | 10.7 | 
Momentum compact (10-5) | 1.11 | 0.91 | 
 function at IP x* / y* (m) | 0.36/0.0015 | 0.33/0.001 | much larger natural chromaticity
Emittance ex/ey (nm) | 1.21/0.0024 | 0.89/0.0018 | 
Beam size at IP sx /sy (m) | 20.9/0.06 | 17.1/0.042 | 
Beam-beam parameters x/y | 0.018/0.109 | 0.024/0.113 | 
RF voltage VRF (GV) | 2.17 | 2.4 | 
RF frequency f RF (MHz) (harmonic) | 650 (216816) | 650 (216816) | 
Natural bunch length z (mm) | 2.72 | 2.2 | 
Bunch length z (mm) | 4.4 | 3.93 | 
HOM power/cavity (2 cell) (kw) | 0.46 | 0.58 | 
Energy spread (%) | 0.134 | 0.19 | 
Energy acceptance requirement (%) | 1.35 | 1.7 | larger momentum acceptance required
Energy acceptance by RF (%) | 2.06 | 3.0 | 
Photon number due to beamstrahlung | 0.082 | 0.104 | 
Beamstruhlung lifetime /quantum lifetime* (min) | 80/80 | 30/50 | 
Lifetime (hour) | 0.43 | 0.22 | 
F (hour glass) | 0.89 | 0.85 | 
Luminosity/IP L (1034cm-2s-1) | 2.93 | 5.2 | 

## Slide 4: Lattice design with luminosity of
  Fit parameter list with luminosity of
  Stronger optimization and stricter hardware requirement should be made to get enough dynamic aperture
Optimization of the quadrupole radiation effect
  Interaction region: longer QD0/QF1
  ARC region: longer quadrupoles
  Reduction of dynamic aperture requirement from injection
  Straight section region: larger x at injection point
Maximization of bend filling factor to minimize the synchrotron radiation loss per turn
  ARC region: sextupoles in two rings changed from staggered to parallel; The left drifts are used for longer bend.
  RF region: shorter phase tuning sections

## Slide 5
Optimization of the quadrupole radiation effect
L*= 2.2 m
LQD0 = 2×1.5 m+0.08m
D = 0.23 m
LQF1 = 2.0 m
The dynamic aperture reduction due to the damping and fluctuation is significant especially on the vertical plane.
Radiation power due to quadrupoles:
  contribution of QD0 dominant
  longer QD0 will significantly decreased the power on vertical plane and thus help to increase the dynamic aperture: QD0/QF1 2m/1.48m => 3m/2m
  longer ARC quadrupoles: 2m => 3m
  With longer QD0, the vertical dynamic aperture increased around 30%
L*= 2.2 m
LQD0 = 2 m
D = 0.23 m
LQF1 = 1.48 m

## Slide 6
The requirements of the Final Focus quadrupoles (QDa,QDb and QF1) are based on the L* of 2.2 m, beam crossing angle of 33 mrad.
Design considerations
The field gradient of quadrupoles is reduced compared to that in CDR, and the development of QDa is the most challenging.
Design of quadrupoles and anti-solenoid is similar to that in CDR.
Space for the corrector coil is available inside the bore of quadrupole.
Iron yoke is used in quadrupoles to eliminate the field crosstalk from the two apertures.
Table 1: Requirements of Interaction Region quadrupole magnets for Higgs
Magnet | Central field gradient (T/m) | Magnetic length (m) | Width of GFR (mm) | Minimal distance between two aperture beam lines (mm)
QDa | 77.5 | 1.5 | 19.2 | 72.61
QDb | 77.5 | 1.5 | 22.0 | 124.75
QF1 | 63.4 | 2.0 | 30.9 | 181.85
Y. Zhu, S. Bai

## Slide 7
Design progress of QDa
The design of QDa is based on two layers cos2θ quadrupole coil using Rutherford cable with iron yoke.
The QDa single aperture cross section is optimized with four coil blocks in two layers separated by wedges, and there are 25 turns in each pole.
The excitation current of QDa is 1240A,and each multipole field in single aperture is smaller than 1×10-4.
2D flux lines (1/4 cross section)
Magnetic flux density distribution
Y. Zhu

## Slide 8
Optics design of Interaction region
local chromaticity correction of both plane, asymmetric layout 1), crab-waist collision 2)
L*=2.2m, C =33mrad, GQD0 =77 T/m, GQF1 =63 T/m, LQD0 =3.0m, LQF1 =2.0m
IP upstream of IR: Ec < 120 keV within 400m, last bend Ec = 25.5keV (45 keV CDR)
IP downstream of IR: Ec < 300 keV within 250m, last bend Ec = 36.6keV (97 keV CDR)
1) K. Oide et al., ICHEP16.
2) M. Zobov et al., Phys. Rev. Lett. 104, 174801(2010).

## Slide 9
Maximization of the bend filling factor in the ARC
1.1m+L+0.7m
1.1m+L+0.7m
1.1m+L+0.7m
1.1m+L+0.7m
Bend: L -> L+0.7m, L+1.8m
Quad: 2m -> 3m
SF: 0.7m
SD: 1.4m
Corr: 0.3m (drift 0.15m)
Drift: 0.2m
SF
SF
SD
SD
L+0.7m
L+0.7m
L+0.7m
1.1m+L+0.7m
1.1m+L+0.7m
1.1m+L+0.7m
1.1m+L+0.7m
1.1m+L+0.7m
1.1m+L+0.7m
L+0.7m
Corr
Corr
Corr
Corr
Corr
Corr
Corr
Corr
Corr
Corr
Corr
Corr
Corr
Corr

## Slide 10: Optics design of ARC region
  FODO cell, 90/90, non-interleaved sextupole scheme, period =5cells
  Cell length reduced from 69m to 62m
Twin-aperture of dipoles and quadrupoles* is adopt in the arc region to reduce the their power. The distance between two beams is 0.35m.
*Ref: A. Milanese,
PRAB 19, 112401 (2016)

## Slide 11: Optics design of RF region
Common RF cavities for e- and e+ ring (Higgs)
RF region divided into two sections for bypassing half numbers of cavities in W&Z mode
An electrostatic separator combined with a dipole magnet to avoid bending of incoming beam (ref: K. Oide, ICHEP16)
  The radiation due to imperfect cancelation from incoming beam is tolerable for SCRF cavities.
Shorter phase tuning sections to increase the length of ARC region
Ec maximum around 19 keV
3.4 W for 8 components
Power of 0.1W may hit when top-up injection
Esep= 2.0 MV/m
Bdip=66.7 G
L= (4+1)m8
x= 11.1 cm at the entrance of quad
phase tuning
phase tuning
cavities
cavities
Separation
Separation

## Slide 12: Reduction of dynamic aperture requirement from injection
Horizontal DA requirement with off-axis injection
Trying to relax the dynamic aperture requirement of the off-axis injection scheme
  Smaller injected emittance from booster
  Larger x at injection point
by Xiaohao CUI
Ɛbooster=Ɛcollider
Ɛbooster=3Ɛcollider

## Slide 13
Larger x at injection point
  x increased from 600m to 1800m
  Increased horizontal chromaticity is small and the results of DA are almost the same.
Reduction of dynamic aperture requirement from injection (cont.)
*based on CDR lattice

## Slide 14
Optics of the collider ring
  An preliminary optics fulfilling requirements of the new parameters list, geometry, photon background and key hardware was got.
Circumference=100,001 m
Qx/Qy=391.11/393.22

## Slide 15
Optimization of dynamic aperture
Start point of the optimization
  Nonlinearity optimized term by term with 10 families of sextupoles in the IR and 4 families of sextupoles in the ARC.
Dynamic aperture further optimized with MODE
  Higgs dynamic aperture with 90% survival of 100 samples
  Including radiation damping, fluctuation, energy sawtooth and tapering, beam-beam effects, w/o error
  145 turns (2 damping times), 4 initial phases

## Slide 16
Different versions of lattice
  To make sure the effect of changement, different versions were studied
  V1, bx*=0.36m, by*=0.001m, ex=1.1nm rad: 15**1.5%
  V2, bx*=0.33m, by*=0.001m, ex=0.89nm rad: 17**1.5% (benefit from smaller nonlinearity in IR and smaller beam size)
  V3, bx*=0.33m, by*=0.001m, ex=0.89nm rad, shorten the RF region: 18**1.5%
  V4, bx*=0.33m, by*=0.001m, ex=0.89nm rad, shorten the RF region, add octupole and decapole for vertical chromaticity correction: 18**1.5%
  V5, bx*=0.33m, by*=0.001m, ex=0.89nm rad, shorten the RF region, add octupole and decapole for vertical chromaticity correction, add multipoles for vertical chromaticity correction : 11**1.3%
J. Wu,
Y. Zhang,
et al
Notes: difficulties

## Slide 17
Status of DA optimization
J. Wu,
Y. Zhang,
et al
 | Higgs(CDR) | Higgs(high) |  | 
Number of particles/bunch Ne (1010) | 15 | 17 | 12 | 
Bunch number | 242 | 218 | 309 | 
Energy acceptance requirement (%) | 1.35 | 1.7 | 1.2 | 1.0
Energy acceptance status (%) (w/o, w/ error) | 1.8, 1.4 | 1.5, ~1.2 |  | 
Luminosity/IP L (1034cm-2s-1) | 2.93 | 5.2 | 3.5 | 3.0
CDR: w/o errors
new: 18 w/o errors
  V4, bx*=0.33m, by*=0.001m, ex=0.89nm rad, shorten the RF region, add octupole and decapole for vertical chromaticity correction, lattice+beam beam+SR fluctuation, w/o error: 18**1.5%
Notes: difficulties

## Slide 18
Further optimization of DA
Recent studies show that the distortion of beta and dispersion due to energy deviation may hurt the dynamic aperture.
The break down of –I in the IR may be another source.
Lower SR from last bend allows to increase the dispersion at multipole for high order chromaticity correction.
A code to generate lattice of whole collider ring automatically are almost finished.
  parameters of lattice can be modified slightly
  will be integrated into direct DA optimization
Notes: difficulties

## Slide 19: Summary
  Lattices for a higher luminosity has been designed.
  Stronger optimization and stricter hardware requirement had be made in order to get enough dynamic aperture
Without error, a momentum acceptance of 1.5% achieved which correspond to luminosity around 3.5*1034cm-2s-1 .
  Further optimization are undergoing for the designed luminosity 5.2*1034cm-2s-1 .
Relaxed requirement of errors compared with CDR and stronger corrections made. The survived seeds increased. (B. Wang, Y. Wei)
  work will be done with the new lattice