## Slide 1: CEPC injection/extraction physics and hardware design status
Jinhui Chen, X.H. Cui, D. Wang
Injection group
2019-11-01

## Slide 2
Overview of the CEPC injection and extraction systems

## Slide 3: Layout of the accelerator complex
The CEPC accelerator complex consists of a Linac, which including a small damping ring for positron beams, several transport lines, a booster ring and 2 storage rings, all 3 of which are in a single tunnel.
1.2km
10-120GeV
120GeV
120GeV
e+
e-
100km
Damping ring

## Slide 4: CEPC injection and extraction systems
DR injection and Extraction system(e+)
Booster LE injection system (e+,e-)
Booster Extraction system1 (e+,e-)
Collider off-axis injection system (e+,e-)
Booster Extraction system2 (e+,e-)
Booster HE injection system (e+,e-)
Collider swap out injection system (e+,e-)
Collider swap out extraction system (e+,e-)
Collider beam dump system(e+,e-)
There are 9 injection and extraction sub-systems in CEPC accelerator complex, including:
Off-axis injection
(in W and Z mode)
On-axis injection
(only in Higgs mode)
Linac
DR
Booster
Collider
120GeV
1.1GeV
10~120GeV
dump
①
⑨
④
②
⑥
③
⑧
⑦
⑤

## Slide 5
Damping ring

## Slide 6: DR injection and extraction system
On-axis bunch-by-bunch injection
Injection and extraction systems are totally occupied 2 long straight sections.
Storage Beam
Injection Beam
Septum Plate 6mm
Lambertson: length=0.5m, deflection angle=100mrad, B=0.72T
thickness of septum sheet=6mm Leakage field=<5E-4(0.8mm) Beam-Stay-clear(HxV)=25x15mm
Fast kicker: pulse width<250ns, repetition rate=100Hz, length=0.25m, deflection angle=1.5mrad, B=0.02T, Beam-Stay-clear(HxV)=16x9.4mm??
7.6mm
7.6mm
10ms
125ns
1.1GeV，75.4m
250ns
Inj.& ext. straight sections
Q
Q
1.25m
5m
0.5m
0.25m
ϴv=1.5mrad
2.7m
0.3m
21.2mm
Side view
Q
Q
ϴH=100mrad
25mm
150mm
Top view
Lambertson
kicker
17.15mm?
21.95mm
Q
Q

## Slide 7: Alternative inj.&ext. scheme of DR
Inj.
ext.
DR
Linac
Side view
DR
Linac
Top view
LMS
LMS
LMS
LMS
Kicker
Kicker
Inj. & ext.
RF
Sharing kicker and straight section
CDR

## Slide 8: Parameters of Hardware
 | Injection | extraction
Energy（GeV） | 1.1 | 1.1
Bunch number | 2 | 2
Bunch spacing（ns） | 125 | 125
Injection（extraction）mode | Bunch by bunch | Bunch by bunch
Kicker repetition rate (Hz) | 100 | 100
Kicker pulse width (ns) | <250 | <250
Kicker rise（fall）time (ns) | <125 | <125
Timing delay(ns) | <125 | <125
Kick angle (mrad) | 1.5 | 1.5
Kicker Integral magnetic field strength (Tm) | 0.006 | 0.006
Kicker Beam-Stay-clear(HxV)（mm） | 44x44? | 44x44?
Kicker good field region (HxV)（mm） |  | 
Kicker field uniformity（%） |  | 
Septum deflection angle（mrad） | 100 | 100
Septum Integral magnetic field strength （Tm） | 0.36 | 0.36
Septum board thickness（mm） | 10 | 10
Circulating Beam-Stay-clear(HxV)（mm） |  | 
Injected beam-stay-clear（HXV）（mm） |  | 
Septum good field region (HxV)（mm） |  | 
septum field uniformity（%） |  | 
Kicker: vertical strip-line kicker or slotted pipe kicker
Septa: horizontal Lambertson magnet

## Slide 9: Strip-line kicker Design
Kick strength
  Total kick angle: θ=1.5mrad
  E=1.1GeV, d=44mm, g=1 =>U*L>36.3kV∙m
  Total strip-line kicker electrode length L=1m =>U>36.3kV(or ±18kV)
Here, θ is kick angle(rad)；E is beam energy(eV)；U is applied pulse voltage for both electrodes(V)；l is strip-line length；d is the distance between the electrodes，g is the geometry factor, determined by the shape of the electrode. w is the strip-line width.
Kick speed
  Min bunch spacing - τ=125ns
    Electrode length l<18.75m => l= 1m
    Electrical pulse Width 6.7ns< tp <243.3ns =>Flat-top ttop >6.7ns, Rise/fall Time tr/tf <118.3ns

## Slide 10: DR Injection& Extraction Kicker System
Main design Specification | Unit | extraction | injection
Kick angle | mrad | 1.5 | 1.5
Kick direction | - | Vertical | Vertical
Length of Strip-line kicker electrode | mm | 1000 | 1000
Gap of Strip-line kicker electrode | mm | 44 | 44
Quantity of Strip-line kicker | - | 1 | 1
Amplitude of electrical pulse | kV | ±18 | ±18
Rise time of electrical pulse（10%-90%） | ns | <100 | <100
Flat top of electrical pulse (90%) | ns | >7 | >7
Fall time of electrical pulse(90%-10%） | ns | <100 | <100
1000mm
Strip-line kicker
fast pulser

## Slide 11: Lambertson design
DS
US
DS
US
0.4m

## Slide 12
Booster ring

## Slide 13: Booster injection and extraction
Booster operating mode | Higgs |  |  | W |  | Z | 
Beam energy（GeV） | 10 | 120 |  | 10 | 80 | 10 | 45.5
Function | Injection （both） | Extraction （off-axis） | Inj./Ext. （on-axis） | Injection （off-axis） | Extraction （off-axis） | Injection （off-axis） | Extraction （off-axis）
Bunch number | 242（in half ring） |  | 7（in half ring） | 1524（uniform） |  | 6000 | 
Min. bunch spacing （ns） | 680 |  | 23800 | 220 |  | 25 | 
Bunch number per train× train number | - |  | - | - | - | 80×75 | 
Train spacing （ns） | - |  | - | - | - | 2460 | 
Injection（extraction）mode | Bunch by bunch |  |  | Bunch by bunch |  | Bunch by bunch | Train by train
Kicker repetition rate (Hz) | 100 | 1000 |  | 100 | 1000 | 100 | 1000
Kicker pulse width (ns) | 1360 |  |  | 440 |  | 50 | <6900
Kicker flat top（ns） | - |  |  | - |  | - | >1980
Kicker rise（fall）time (ns) | <680 |  |  | <220 |  | <25 | <2460
Timing delay(ns) | <680 |  | <23800 | <220 |  | <2460 | <4400
injection（extraction）period (s) | 2.42 | 0.242 | 0.007 | 15.24 | 1.5 | 60 | 0.075
Kick angle (mrad) | 0.11 | 0.2 | 0.1 | 0.11 | 0.2 | 0.11 | 0.2
Kick Integral field strength (Tm) | 0.004 | 0.08 | 0.04 | 0.004 | 0.05 | 0.004 | 0.03
Beam pipe aperture Φ（mm） | 55 |  |  |  |  |  | 
Considering the compatibility of three operating modes:
Function | LE-Injection （both） | HE-Extraction （off-axis） | HE-Inj./Ext. （on-axis）
Kicker repetition rate (Hz) | 100 | 1000 | 1000
Kicker pulse width (ns) | 50 | 440~2420(Adjustable) | 1360
Kicker flat top（ns） | - | 0~1980(Adjustable) | -
Kicker rise（fall）time(ns) | <25 | <220 | <680
injection（extraction）period (s) | 60 | 1.5 | 0.007
Kick angle (mrad) | 0.11 | 0.2 | 0.1
Kick Integral field strength (Tm) | 0.004 | 0.08 | 0.04
Beam pipe aperture Φ（mm） | 55 | 55 | 55
50ns,100Hz
200ns
40~2000ns
200ns
1kHz
1360ns,1kHz

## Slide 14: Booster LE injection
Q
Q
22.5m
195.7m
2m
0.2m
ϴV=0.11mrad
123m
48m
30mm
Side view
Q
Q
ϴH=22mrad
5mm
500mm
Top view
Lambertson
kicker
16.47mm?
30.22mm
On-axis bunch-by-bunch injection
50ns,100Hz
Storage Beam
Injection Beam
Septum Plate 10mm
10mm
10mm
Kicker: vertical strip-line kicker driven by DSRD pulser
Septa: horizontal Lambertson magnet

## Slide 15: Booster HE extraction for off-axis inject into SR
Q
Q
24m
210.7m
15m
0.7m
ϴH=0.2mrad
123m
48m
30mm
Side view
Q
Q
ϴV=26mrad
?mm
600mm
Top view
Lambertson
kicker
5.4mm
33mm
Train by train, bunch-by-bunch extraction
Storage Beam
Injection Beam
Septum Plate 10mm
10mm
10mm
200ns
40~2000ns
200ns
1kHz
Kicker: horizontal vacuum out delay-line dipole kicker(coating ceramic vacuum chamber) driven by PFN-based solid-state pulser
Septum: vertical Lambertson magnet

## Slide 16: On-axis swap-out injection layout1
Booster
E- SR
Side view
Booster
E- SR
Top view
LMS
LMS
LMS
LMS
LMS
LMS
LMS
LMS
Dipole Kicker
Dipole Kicker
Kicker
Kicker
Kicker
Kicker
down
up
down
up
in
out
in
Off-axis injection is used in the high-energy reinjection of the booster, the dipole kicker and nonlinear kicker(NLK) can not compatible. So the layout is un-reasonable.
Need to modify the globle layout??
Pulsed sextupole + ceramic vacuum chamber
NLK
NLK

## Slide 17: On-axis swap-out injection layout2
Off-axis injection is used in the high-energy reinjection into the booster. Both puled multipole injection and pulsed bump injection are suit.
On-axis swap out injection is applied in SR. A set of dipole kicker can serve both injection and extraction process.
Booster
E- SR
Side view
Booster
E- SR
Top view
LMS
LMS
LMS
LMS
LMS
LMS
LMS
LMS
Kicker
Kicker
Kicker
NLK
NLK
Kicker
down
up
down
up
out
out
in
1360ns,1kHz
Ext. dipole kicker: horizontal ferrite core vacuum out kicker+coating ceramic chamber+LC resonance pulser
Inj. NLK: horizontal NLK or Pulsed sextupole+coating ceramic chamber+LC resonance pulser
Septum: Vertical Lambertson magnet
NLK or Pulsed sextupole magnet+ ceramic vacuum chamber
Dipole kicker+ ceramic vacuum chamber
0.333ms,1kHz

## Slide 18: Booster HE extraction For SR swap-out injection
Ext. dipole kicker: horizontal ferrite core vacuum out kicker+coating ceramic chamber+LC resonance pulser
Septa: Vertical Lambertson magnet
Q
Q
24m?
225.7m
35m
0.7m
ϴH=0.1mrad
123m
43m
20mm
Side view
Q
Q
ϴV=26mrad
?mm
450mm
Top view
Lambertson
Dipole kicker
7.7mm
23.5mm
Storage Beam
Injection Beam
Septum Plate 10mm
5mm
5mm
1360ns,1kHz

## Slide 19: Booster HE re-injection For SR swap-out injection
Inj. NLK: horizontal NLK or Pulsed sextupole+coating ceramic chamber+LC resonance pulser
Septa: Vertical Lambertson magnet
Storage Beam
Injection Beam
Septum Plate 10mm
5mm
5mm
Q
Q
?m
?m
35m
？m
ϴH=0.1mrad
123m
?m
?mm
Side view
Q
Q
ϴV=26mrad
?mm
450mm
Top view
Lambertson
NLK
?mm
?mm
0.333ms,1kHz

## Slide 20
Collider ring

## Slide 21: Collider ring
Booster operating mode | Higgs |  |  | W |  | Z | 
Beam energy（GeV） | 120 |  |  | 80 |  | 45.5 | 
Function | Injection （off-axis） | Injection （on-axis） | Extraction （dump） | Injection （off-axis） | Extraction （dump） | Injection （off-axis） | Extraction （dump）
Bunch number | 242（in half ring）- 7 |  |  | 1524（uniform） |  | 12000 | 
Min. bunch spacing （ns） | 680 |  |  | 220 |  | 25 | 
Bunch number per train× train number | - |  |  | - |  | 80×150 | 
Train spacing （ns） | - |  |  | - |  | 245 | 
Injection（extraction）mode | Bunch by bunch |  |  | Bunch by bunch |  | Train by train | 
Kicker repetition rate (Hz) | 1000 |  |  | 1000 |  | 1000 | 
Kicker pulse width (ns) | 1360 |  |  | 440 |  | <2460 | 
Kicker flat top（ns） | - |  |  | - |  | >1980 | 
Kicker rise（fall）time (ns) | <680 |  |  | <220 |  | <245 | 
Timing delay(ns) | <680 | <23800 | <680 | <220 |  | <4400 | 
injection（extraction）period (s) | 0.242 | 0.007 | 0.242 | 1.5 |  | 0.15 | 
Kick angle (mrad) | 0.1 | 0.2 | 0.2 | 0.1 | 0.2 | 0.1 | 0.2
Kick Integral field strength (Tm) | 0.04 | 0.08 | 0.08 | 0.027 | 0.05 | 0.015 | 0.03
Beam pipe aperture HxV（mm） | 75×56 |  |  |  |  |  | 
Function | Injection （on-axis） | Injection （off-axis） | Extraction （dump）
Kicker repetition rate (Hz) | 1000 | 1000 | 1000
Kicker pulse width (ns) | 1360 | 440~2420(Adjustable) | 440~2420(Adjustable)
Kicker flat top（ns） | - | 0~1980(Adjustable) | 0~1980(Adjustable)
Kicker rise（fall）time(ns) | <680 | <220 | <220
injection（extraction）period (s) | 0.007 | 1.5 | 1.5
Kick angle (mrad) | 0.2 | 0.1 | 0.2
Kick Integral field strength (Tm) | 0.08 | 0.04 | 0.08
Beam pipe aperture HxV（mm） | 75×56 | 75×56 | 75×56
200ns
40~2000ns
200ns
1kHz
1360ns,1kHz
Considering the compatibility of three operating modes:
200ns
40~2000ns
200ns
1kHz

## Slide 22: SR On-axis swap-out injection
Booster
E- SR
Side view
Booster
E- SR
Top view
LMS
LMS
LMS
LMS
LMS
LMS
LMS
LMS
Kicker
Kicker
Kicker
NLK
NLK
Kicker
down
up
down
up
out
out
in

## Slide 23: SR on-axis swap out injection
Q
Q
?m
?m
35m
？m
ϴH=0.1mrad
?m
?m
?mm
Side view
Q
Q
ϴV=26mrad
?mm
?mm
Top view
Lambertson
Dipole kicker
?mm
?mm
Lambertson
？m
35m
injection
injection
extraction
extraction
Dipole kicker: horizontal ferrite core vacuum out kicker+coating ceramic chamber+LC resonance pulser
Septa: Vertical Lambertson magnet
1360ns,1kHz
Storage Beam
Injection Beam
Septum Plate ?mm
?mm
?mm

## Slide 24: SR Off-axis injection-pulsed local bump scheme
200ns
40~2000ns
200ns
1kHz
Storage Beam
Injection Beam
Septum Plate 2mm
5mm
3mm
Q
Q
?m
?m
35m
0.7m
ϴH=0.1mrad
125m
25m
10mm
Side view
Q
Q
ϴV=26mrad
?mm
450mm
Top view
Lambertson
kicker
?mm
10mm
kicker
Dipole kicker: horizontal vacuum out delay-line kicker+coating ceramic chamber+PFN-based solid-state pulser
Septa: Vertical Lambertson magnet

## Slide 25: SR Off-axis injection-pulsed multipole injection scheme
200ns
40~2000ns
200ns
1kHz
Q
Q
?m
?m
35m
0.7m
ϴH=0.1mrad
125m
25m
10mm
Side view
Q
Q
ϴV=26mrad
?mm
450mm
Top view
Lambertson
NLK
?mm
13.5mm
Storage Beam
Injection Beam
Septum Plate 2mm
5mm
3mm
NLK kicker: horizontal vacuum out delay-line NLK kicker+coating ceramic chamber+PFN-based solid-state pulser
Septa: Vertical Lambertson magnet

## Slide 26: Dump extraction
Q
Q
?m
?m
35m
0.7m
ϴH=0.11mrad
125m
25m
20mm
Side view
Q
Q
ϴV=26mrad
?mm
450mm
Top view
Lambertson
kicker
?mm
23.85mm
Train by train,bunch-by-bunch extraction
Storage Beam
Injection Beam
Septum Plate 10mm
5mm
5mm
200ns
40~2000ns
200ns
1kHz
Dipole kicker: horizontal vacuum out delay-line kicker+coating ceramic chamber+PFN-based solid-state pulser
Septa: Vertical Lambertson magnet

## Slide 27: RF region beam separating system
k1
k2
k4
k3
165us
165us
k1
k2
k3
k4
165us
CW=6.06kHz, 50%
In Higgs mode，E- E+ beams only fill half ring respectively. So, it is possible to separate e- /e+ beams by kickers.
4 sets of Kicker locate at both sides of RF region, K1 and k4 applied for E+ beam,K2 and K3 applied for E- beam;
The waveform of kicker pulsers is square wave with a duty cycle of 50%, pulse width of 165 us and a frequency of 6.06 kHz;
The phase difference of K1 (K3) and K2(K4) is π.

## Slide 28: Beam separating system layout
kick strength ：203 Gauss
Total efficient length：40 m
Max. separating distance：0.0265m
Beam clearance（H/V）：31.146 mm/5.339 mm
kickers
septums
Last e+ Bunch
First e- Bunch
Dipole kicker: horizontal vacuum out delay-line kicker+coating ceramic chamber+PFN-based solid-state pulser
Septa: horizontal vacuum out DC septum magnet
septa
k1
RFC
RFC
K2
K1

## Slide 29: Challenge of new beam separating system
Kicker pulser requirements are special:
  Flat-top dropping
  Amplitude long term stability
overshoot
Top-drop
Tail
Amplitude drift
165us
165us
165us
CW=6.06kHz,50%
Ideal waveform ：
Practical waveform：
Delay-line kicker model

## Slide 30
Hardware designs for CEPC injection and extraction systems

## Slide 31: Main types of hardware
Strip-line kicker and DSRD based short pulsed PS
  The similar hardware was developed in HEPS-TF progress.
Vacuum out distributed parameter (delay-line) dipole kicker magnet with metallic coating ceramic vacuum chamber and Solid-state adjustable pulse width PFN based Pulser
  The structure of delay-line kicker is complicated; the kind of kicker helps to achieve ideal trapezoid waveform.
  This kind of kicker and pulser need a R&D progress for us
Vacuum out lumped parameter dipole kicker magnet with metallic coating ceramic vacuum chamber and Solid-state LC discharge half-sine Pulser
  It is easy than last type one.
Pulsed sextupole magnet with metallic coating ceramic vacuum chamber and Solid-state LC discharge half-sine Pulser
  It need to R&D for us (tentative)
Vacuum out distributed parameter nonlinear kicker(NLK) with metallic coating ceramic vacuum chamber and Solid-state adjustable pulse width PFN based Pulser
  New proposed
Constant amplitude continuous square wave pulser for RF region beam separating kicker
  New proposed
  R&D effort: flat top dropping compensate topology and amplitude long term stability controlling technique
Lambertson septa
  The similar hardware was developed in HEPS, CSNS, BEPC

## Slide 32: Hardware R&D Plan
Component | description | Number(set) | Budget(RMB) | schedule
Vacuum chamber | Coated ceramic vacuum chamber | 1 | 100k | 24 M
Dipole kicker | Vacuum out distributed parameter dipole kicker magnet | 1 | 200k | 24 M
NLK | Vacuum out distributed parameter NLK magnet | 1 | 300k | 12 M
Trapezoid pluser | Solid-state pulse width adjustable trapezoid pulser | 1 | 300k | 36 M
CW pulser | continuous square wave pulser | 1 | 300k | 36 M
Based on the mastered technology, the key technical problems to be solved and the key components to be developed for CEPC injection and extraction system are proposed:
Year | 2019 | 2020 |  |  |  | 2021 |  |  |  | 2022 |  |  |  | 2023 |  |  | 
Quarter | 4th | 1st | 2nd | 3rd | 4th | 1st | 2nd | 3rd | 4th | 1st | 2nd | 3rd | 4th | 1st | 2nd | 3rd | 4th
Vacuum chamber |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Dipole kicker |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
NLK |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Trapezoid pluser |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CW pulser |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 33
END

## Slide 34
Back up slides

## Slide 35: Prototype kicker passed acceptance test of HEPS-TF
Pusle voltage=18kV
FWHM=1.92ns
Vacuum =2E-9~2E-8Torr
Kicker HV test bench
HV pulser
Kicker HV test reult：
Kicker electrical pulse：
Rise time（10%-90%）<641ps，
Fall time（90%-10%）<1.5ns。
pluse edge slowing down due to kicker insertion：
rise time (10%-90%)≈86.6ps,
Fall time (90%-10%) ≈ 35ps。
Kicker transmission characteristics test result
Feed through
D shape blades
Outer body
Cooling water tube
End cover
Vacuum leak test
after brazing
750mm
Ion pump
kicker

## Slide 36: Prototype pulser passed acceptance test of HEPS-TF
DSRD housing
6 stage inductive adder
4ns
V=17kV,
FWHM=5ns,
Tr(10-90%)<2.6ns,
Tf(90-10%)<3.2ns,
Bottom width(3%-3%)<10ns
PFL=0.3m
±18kV pulsers installed in 19 inch cabinet

## Slide 37: Distributed parameter (delay-line) dipole kicker

## Slide 38
To get an high excitation efficiency, all the kicker magnets will have a window type cores made by two C-type ferrite blocks.
All the kicker magnets will be put inside the vacuum tanks so that the fast pulsed field can directly kick the beam without time delay and amplitude attenuation.
To avoid the coupling between particle beam and the ferrite blocks, two thin copper plates will be inserted between the touched surfaces of two C-type blocks.
Lumped parameter dipole kicker magnet
Wen Kang

## Slide 39: Lambertson

## Slide 40
There are two types of septum magnets often used for beam injection and extraction of accelerators. One is C-type septum magnet, another is Lambertson type septum magnet.
Due to high reliability and stability, Lambertson magnets are selected as the septum magnet for the beam injection and extraction of all the CEPC accelerators.
Preliminary design of septum magnets
By using several shielding measures, the leakage field along the orbit of the circulating beam can be reduced down to 5E-4 of the main field in the magnet gap.
Wen Kang

## Slide 41: Comparison Between on-axis and off-axis injection

## Slide 42: Comparison Between 2 off-axis Schemes
Pulsed Local Bump Injection
Pulsed septum field Injection

## Slide 43: Comparison Between 2 off-axis Schemes
Pulsed septum field Injection
Pulsed Local Bump Injection
By
x
I
S

## Slide 44: DA Requirement for OFF-axis injection

## Slide 45: From dipole to multi-pole to NLK
1999, University of Maryland, College Park,
Pulsed Panofsky quadrupole for UMER injection
2004, KEK-PF
Proposal of pulsed quadrupole for KEK-PF-AR injection
2005, KEK-PF
Pulsed quadrupole test at KEK-PF-AR injection
2006, KEK-PF
Proposal of pulsed sextupole for KEK-PF-AR injection
2008-2011, KEK-PF
pulsed sextupole test at KEK-PF-AR injection
2009, NSLSII
Design consideration on pulsed sextupole
Pulsed Multi-pole
2010-2011, MAXIV
Proposal of pulsed sextupole in MAXIV injection
2012, SSRF
Study on pulsed sextupole injeciton
2012, HEPS
Study on pulsed sextupole injection by Wenkang, Yijiao
2008-2011, BESSY
Proposal 4-wire NLK for BESSYII
Test first prototype on BESSY, be not successful for beam impedance
2011-2016, BESSY
Proposal a new NLK design, and test on
BESSY successfully(in vacuum)
NLK(MIK)
2011-2017, MAXIV-SOLEIL
R&D NLK for MAXIV in association with BESSY (out of vacuum)
2010-2017, ALS
R&D NLK for ALS-U accumulating ring
Base on BESSY design(out of vacuum)
2014-2017,
Study on NLK by IHEP, NSRL, ESRF, DIAMOND
2011, SPRING-8
Proposal 4 Strip-line NLK

## Slide 47: Nonlinear Kicker
By
Stored
beam
Injected
beam
x